## Slide 1
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 11
Interrupt, Timer and PWM
Exercises ANS
Z. Gu
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Interrupt
Suppose register i (i ≤ 12) is initialized to have a value of i (e.g. r0 = 0, r1= 1, r2 = 2, r3 = 3, etc.). Assume the main stack (MSP) is used. (Recall: in the interrupt handler, if LR = 0xFFFFFFF9, then the main stack (MSP) is used. If LR = 0xFFFFFFFD, then the process stack (PSP) is used. ) The program status register (PSR) = 0x00000020, PC = 0x08000020, and LR = 0x20008020, when the interrupt occurs.
(1) Show the stack content immediately before the PUSH instruction runs. Suppose the stack pointer SP, i.e. MSP in this case, was 0x20000600 immediately before the system timer interrupt occurs
(2) What are the values of these registers (R0-R12, LR, SP, PC, and PSR) immediately after the interrupt exits?
SysTick_Handler PROC EXPORT SysTick_Handler PUSH {lr, r0, r7} ADD r0, r0, #1 ADD r1, r1, #1 ADD r2, r2, #1 ADD r3, r3, #1 ADD r4, r4, #1 ADD r5, r5, #1 ADD r6, r6, #1 ADD r7, r7, #1 ADD r8, r8, #1 ADD r9, r9, #1 ADD r10, r10, #1 ADD r11, r11, #1 ADD r12, r12, #1 POP {r0, r7, pc} ENDP

## Slide 3: Interrupt ANS
(1)
0x20000600 | 
0x200005FC | 0x00000020 (PSR)
0x200005F8 | 0x08000020 (PC)
0x200005F4 | 0x20008020 (LR)
0x200005F0 | 12 (R12)
0x200005EC | 3 (R3)
0x200005E8 | 2 (R2)
0x200005E4 | 1 (R1)
0x200005E0 | 0 (R0)
0x200005DC | 

## Slide 4: Summary of Equations
Timer clock frequency vs. CPU Clock Frequency
Timer frequency with up-counting or down-counting mode:
PWM duty cycle for Mode 1 (Low-True):
Timer frequency with center-aligned counting mode:
PWM duty cycle for Mode 2 (High-True):

## Slide 5: Maximum timer counter value
If timer clock frequency is MHz, timer interrupt frequency is KHz, what is the maximum timer counter value?
ANS: Timer clock freuency = 24 Mhz, Timer interrupt frequency KHz
If timer clock frequency is MHz, timer interrupt frequency is Hz, what is the maximum timer counter value?
ANS: