## Slide 1
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 15
Timer and PWM
Z. Gu
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: System Timer (SysTick)
A timer is a hardware module that generates periodic clock ticks at a fixed time interval
Example Usages:
  To measure time elapsed, e.g., to implement a time delay function Delay (e.g., 100ms).
  To implement periodic polling to check peripheral device status, or to implement CPU scheduler, which periodically selects a new process, from the ready queue, to run next.
Fixed time interval
time
SysTick interrupts
Notes: {{Pause=2}} The system timer, also called System Tick, or, SysTick, is to generate SysTick interrupts at a fixed time interval. {{Pause=1}} Here I give two example applications of the system timer. {{Pause=1}} The first example is that, the system timer can measure time elapsed. For instance, software can use the system timer, to implement a time delay function. {{Pause=1}} The second example is that we can execute some specific tasks periodically. For instance, we can use system timer, to implement periodic polling, to check peripheral status, or read external inputs, with a regular timed interval. In addition, operating systems rely on the system timer to implement CPU scheduler. In order to support multitasking and improve the CPU utilization, the CPU scheduler periodically selects a new process, from the ready queue, to run next.

## Slide 3: System Timer (SysTick)
System timer (SysTick) is a standard hardware component built into ARM Cortex-M.
This hardware periodically interrupts the processor to execute the following ISR:
Processor
Core
NVIC
Peripherals
I/O pins
IRQs
IRQs
System
Exceptions
System Timer
SysTick IRQ
ARM Cortex-M
Microcontroller
void SysTick_Handler(void){
...
}
Notes: {{Pause=2}} The system timer is a standard hardware component, built into ARM Cortex processors. Almost all ARM Cortex processors have the system timer component. If enabled, the system timer can periodically generate SysTick interrupt requests. The Nested Vectored Interrupt Controller (NVIC) monitors and handles all interrupt requests based on their priority levels. For SysTick interrupts, N V I C forces the core to execute, the interrupt service routine named SysTick Handler.

## Slide 4: Timer: Prescaler (PSC)
Reload Value
Timer
Counter
fCK_PSC
ISR
Timer Interrupt
Reload
PSC
ARR
Prescaler
fCK_CNT
CPU Clock
The 16-bit PSC register holds the frequency pre-scaler value in the range of [0, 216-1=65535]. The CPU Clock Frequency fCK_PSC is divided by a constant integer, PSC+1, in the range of [1, 216=65536], to generate the Timer Clock with frequency fCK_CNT that drives the Timer Counter. The prescaler serves as a “frequency divider” that enables tradeoffs between timer resolution and timer range. Larger PSC value leads to slower timer clock rate, coarser timer resolution, and larger timer range.
The 16-bit Auto-Reload Register (ARR) holds the maximum timer counter value in the range of [0, 65535].
CPU clock and timer clock: measured in MHz/GHz; Timer Clock: measured in Hz, e.g., the Linux OS timer frequency is 100Hz (period=10ms). Since each timer interrupt triggers an ISR software execution, it is not realistic to have timer frequency higher than 1KHz.
Timer Clock
or
Notes: A timer is a hardware component in ARM Cortex-M microprocessor. Each timer has a special register, which is called the timer counter. The counter runs freely. If enabled, it automatically counts upwards or downwards, under the driven of a clock source. Pay attention. It is hardware, not software, which keeps repeatedly incrementing or decrementing the counter value. For each rising edge in the clock signal, the value of the counter increments or decrements by one automatically. That is why, we say the counter of a timer, is the free-running counter.
By updating the PSC register, we set the timer to be clocked at the rate we desire. The PSC register holds the frequency pre-scaler value, or the frequency divider. The frequency of the clock source is divided by a constant integer, PSC plus 1, before the input clock is fed to the counter. The prescaler enables a tradeoff between timer resolution and timer range. High timer resolution requires a high clock rate. However, high clock rates cause the timer to overflow or underflow more quickly.

## Slide 5: 3 Modes
A timer can be configured in 3 modes:
  Up-counting mode
  Down-counting mode
  Center-aligned counting mode（Alternating up-counting and down-counting）
Related registers include:
  Counter register (TIMx_CNT)
  Prescaler register (TIMx_PSC)
  Auto-reload register (TIMx_ARR)
  Their values are denoted as CNT, PSC and ARR.

## Slide 6: Up-counting Mode
ARR = 6
Timer
clock
Counter
Counter overflow
Update event (UEV)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Counter overflow
Counter overflow
Counter overflow
Auto-Reload Register ARR=6. In up-counting mode, the counter counts up, from 0 to 6. When the counter is reset to 0 from 6, counter overflow occurs, and a Update event (UEV) is generated. On the next clock cycle, the counter counts up again. The Timer Period is 1+ARR clock ticks, with duration of (1+ARR)*Clock Period.
Timer Period = (ARR + 1) * Clock Period
= 7 * Clock Period
Notes: We can configure the timer to repeatedly count up, count down, or, count up and down. Let’s first take a look at the up-counting mode. The auto-reload register (ARR) holds the maximum counter value, which is also called the auto-reload value. The counter counts from 0 to the auto-reload value, then restarts from 0, and generates a counter overflow event. This figure shows an example of the counter behavior when ARR is 6, and the repetition counter is not used. In the up-counting mode, the counter rolls over and is reset when it exceeds 6. When the counter resets, it triggers a counter overflow and an update event (UEV). After that, a new period starts. The counting period is determined by the auto-reload value, as well as the clock period.
, RCR = 0

## Slide 7: Down-counting Mode
ARR = 6
Counter
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Counter underflow
Counter underflow
Counter underflow
Counter underflow
Update event (UEV)
Timer Period = (ARR + 1) * Clock Period
= 7 * Clock Period
ARR=6. In down-counting mode, the counter counts down, from 6 to 0. When the counter is reset to 6 from 0, counter underflow occurs, and a UEV is generated. On the next clock cycle, the counts down again. The Timer Period is 1+ARR clock ticks, with duration of (1+ARR)*Clock Period.
Timer
clock
Notes: In the down-counting mode, the counter counts from the auto-reloaded value down to 0. After the counter has reached 0, hardware automatically reloads the counter with the auto-reloaded value, and generate a counter underflow event and an update event (UEV). The counting period of the down-counting mode is exactly the same as the counting period of the up-counting mode.
, RCR = 0

## Slide 8: Center-aligned Counting Mode
ARR = 6
Counter
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Counter overflow
Counter overflow
Counter underflow
Counter underflow
Timer Period = 2 * ARR * Clock Period
= 12 * Clock Period
ARR=6. In center-aligned counting mode, the counter first counts up, from 0 to 6, then counts down, from 6, to 0. When the counter makes transition from 1 to 0, a UEV (Update Event) is generated. On the next clock cycle, the counter repeats the up/down counting process. The Timer Period is 2*ARR clock ticks, with duration of 2*ARR*Clock Period.
Counter underflow
Update event (UEV)
Timer
clock
Notes: In center-aligned mode, the counter counts from 0 to the auto-reload value minus 1, generates a counter overflow event, then counts from the auto-reload value down to 1 and generates a counter underflow event. Then it restarts counting
from 0. In this mode, the counting direction changes automatically on counter overflow and underflow. , RCR = 0

## Slide 9: Pulse-Width Modulation (PWM) as DAC
A closed-loop control system consisting of a CPU-based controller (digital) interacting with a physical plant (analog) needs
  Sensors with ADC (Analog-to-Digital Convertor) functionality to convert analog signals into digital domain, e.g., temperature, humidity…
  Actuators with DAC (Digital-to-Analog Convertor) functionality to convert digital signals into analog domain, e.g., output voltage to control a motor
PWM is a type of DAC. It uses a rectangular waveform to periodically switch on and off a voltage source to produce a desired average voltage output.
Controller (Digital)
Physical Plant
(Analog)
Sensor w/ ADC
Actuator w/ DAC

## Slide 10: Pulse-Width Modulation (PWM)
(Analog-to-Digital Convertor) The “Pulse Width” in PWM refers to the time interval when the output signal is On; the Duty Cycle is the percentage of time that the output signal is On (“the pulse width”):
Higher Duty Cycle means higher average output:

## Slide 11: Pulse-Width Modulation (PWM)
The PWM output signal is determined by:
  Reference signal stored in Compare and Capture Register (CCR); and the PWM mode
PWM mode 1 (Low True): if the timer counter is lower than the reference signal stored in CCR, the PWM output is on; otherwise it is off.
  Higher CCR  higher duty cycle
PWM mode 2 (High True): if the timer counter is higher than the reference signal stored in CCR, the PWM output is on; otherwise it is off.
  Higher CCR  lower duty cycle
Notes: Comparison between timer counter (CNT) and given reference value stored in
A single timer can generate up to 4 PWM signals with independent duty cycles and identical frequency.
Polarity bit
When multiple PWM signals are generated by the same timer, all rising edges occur at the same time. That is why it is called edge-aligned.

## Slide 12: PWM Mode: Rigorous Definition
PWM Mode | Timer Counting Mode | On | Off
Mode 1 (Low True) | Up-counting | CNT < CCR | CNT ≥ CCR
 | Down-counting | CNT ≤ CCR | CNT > CCR
Mode 2 (High True) | Up-counting | CNT ≥ CCR | CNT < CCR
 | Down-counting | CNT > CCR | CNT ≤ CCR

## Slide 13: PWM Mode 1 (Low-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Up-counting mode, ARR = 6, CCR = 3
Clock
Counter
CCR = 3
Timer Period = (ARR + 1) * Clock Period = 7 * Clock Period
Duty Cycle =
CCR
ARR + 1
=
3
7
PWM
Output
Timer Output =
High if counter < CCR
Low if counter ≥ CCR
Mode 1
Notes: A single timer can generate up to 4 PWM signals with independent duty cycles and identical frequency. When multiple PWM signals are generated by the same timer, all rising edges occur at the same time. That is why it is called edge-aligned. , RCR = 0

## Slide 14: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Up-counting mode, ARR = 6, CCR = 3
Clock
Counter
CCR = 3
Timer Period = (ARR + 1) * Clock Period = 7 * Clock Period
Duty Cycle = 1 -
CCR
ARR + 1
=
4
7
PWM
Output
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 15: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Up-counting mode, ARR = 6, CCR = 5
Clock
Counter
CCR = 5
Duty Cycle = 1 -
CCR
ARR + 1
=
2
7
Timer Period = (ARR + 1) * Clock Period = 7 * Clock Period
PWM
Output
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
Mode 2

## Slide 16: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Center-aligned mode, ARR = 6, CCR = 3
Clock
Counter
CCR = 3
Duty Cycle = 1 -
CCR
ARR
Timer Period = 2 * ARR * Clock Period = 12 * Clock Period
=
1
2
PWM
Output
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
PWM Mode | Counting Mode | On | Off
Mode 1 | Up-counting | CNT < CCR | CNT ≥ CCR
 | Down-counting | CNT ≤ CCR | CNT > CCR
Mode 2 | Up-counting | CNT ≥ CCR | CNT < CCR
 | Down-counting | CNT > CCR | CNT ≤ CCR
The timer counter value of 3 corresponds to different PWM outputs depending on the phase (up-counting or down-counting)

## Slide 17: PWM Mode 2 (High-True)
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
Center-aligned mode, ARR = 6, CCR = 1
Clock
Counter
CCR = 1
Duty Cycle = 1 -
CCR
ARR
=
5
6
Timer Period = 2 * ARR * Clock Period = 12 * Clock Period
PWM
Output
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
PWM Mode | Counting Mode | On | Off
Mode 1 | Up-counting | CNT < CCR | CNT ≥ CCR
 | Down-counting | CNT ≤ CCR | CNT > CCR
Mode 2 | Up-counting | CNT ≥ CCR | CNT < CCR
 | Down-counting | CNT > CCR | CNT ≤ CCR
The timer counter value of 1 corresponds to different PWM outputs depending on the phase (up-counting or down-counting)

## Slide 18: Up-Counting, PWM Mode 1: Left Edge-aligned
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3
Clock
Counter
CCR = 3
PWM
Output 1
CCR = 6
PWM
Output 2
CCR = 3
CCR = 6
All rising edges occur at the same time!
PWM Period
Left-aligned
In the up-counting mode, when multiple PWM signals are generated by the same timer, the PWM pulses are left edge aligned, because all rising edges are aligned to the left side of the PWM period.
Notes: {{Pause=2}} In the up-counting mode, when multiple PWM signals are generated by the same timer, all rising edges occur at the same time. {{Pause=1}} That is why the up-counting mode is edge-aligned. This example shows the PWM output when CCR is 3 and 6. All rising edges of the PWM signals are aligned with the overflow events of the timer counter. {{Pause=1}} More specifically, the PWM outputs are left edge aligned, because all pulses are aligned to the left side of the PWM period. The outputs go to their active state at the beginning of the period, {{Pause=0.5}} stay on, for an amount of time determined by their duty cycle, {{Pause=0.5}} then turn off for the remainder of the period. After that, this process repeats. {{Pause=0.5}} In summary, If a timer is configured to count up, its PWM signals are edge-aligned, and more specifically, left-aligned.

## Slide 19: Up-Counting, PWM Mode 2: Right Edge-aligned
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Upcounting mode, ARR = 6, CCR = 3
CCR = 3
Clock
Counter
All falling edges occur at the same time!
CCR = 5
CCR = 5
CCR = 3
PWM Period
Right-aligned
In the down-counting mode, when multiple PWM signals are generated by the same timer, the PWM pulses are right edge aligned, because all falling edges are aligned to the right side of the PWM period.
PWM
Output 1
PWM
Output 2
Notes: {{Pause=2}} When multiple PWM signals are generated by the same timer in mode 2, all falling edges occur at the same time. That is why mode 2 is edge-aligned. This example shows the PWM output when CCR is 3, and 5. {{Pause=1}} All falling edges of the PWM signals are aligned with the overflow events. {{Pause=1.5}} More specifically, the PWM outputs are right edge aligned, because all pulses are aligned to the right side of the PWM period.

## Slide 20: Center-aligned Counting, PWM Mode 2: Center aligned
Center-aligned counting mode, ARR = 6, CCR = 3
0
1
2
3
4
5
6
0
1
2
3
4
5
1
2
3
4
5
6
0
1
2
3
4
5
CCR = 3
Clock
Counter
CCR = 1
PWM signals are center aligned!
CCR = 1
CCR = 3
PWM Period
Center-aligned
Timer Output =
Low if counter < CCR
High if counter ≥ CCR
PWM
Output 1
PWM
Output 2
In the center-aligned counting mode, when multiple PWM signals are generated by the same timer, the PWM pulses are center aligned, because their centers are aligned with peaks of the timer counter.
Notes: {{Pause=2}} When a timer generates multiple PWM signals, the centers of the PWM pulses are aligned with, the peak value of the timer counter. In other words, the active pulse of, all output channels, are placed at the center of each PWM period. {{Pause=2}} Center-aligned PWM signals are often used in electronic circuits, such as motor control and power supplies. The signals are symmetrical and thus have less harmonics. It helps reduce noise interference and power consumption.

## Slide 21: PWM Pulse Alignment
PWM Mode | Timer Counting Mode | Pulse Alignment
Mode 1 (Low True) | Up-counting | Left edge
 | Down-counting | Right edge
 | Center-aligned Counting | Center aligned
Mode 2 (High True) | Up-counting | Right edge
 | Down-counting | Left edge
 | Center-aligned Counting | Center aligned
Can you work out the down-counting cases by hand?

## Slide 22: Summary of Equations
Timer clock frequency vs. CPU Clock Frequency
Timer frequency with up-counting or down-counting mode:
PWM duty cycle for Mode 1 (Low-True):
Timer frequency with center-aligned counting mode:
PWM duty cycle for Mode 2 (High-True):

## Slide 23: Quiz: Calculating ARR
Suppose Timer Clock Frequency = 80MHz
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 24: Quiz Answer: Calculating ARR
Suppose Timer Clock Frequency = 80MHz
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
But a 16-bit ARR register has value range of [0, 65535], so ARR value of 799999 or 400000 is out of range  cannot generate a 10ms timer from a 80MHz Timer Clock!
Solution: use prescaler (PSC) to reduce Timer Clock Frequency
For up-counting or down-counting mode:
For center-aligned counting mode:
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 25: Quiz: Calculating ARR with prescaler
Suppose CPU Clock Frequency = 80MHz, PSC=79
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 26: Quiz Answer: Calculating ARR with prescaler
Suppose CPU Clock Frequency = 80MHz, prescaler PSC=79
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
For center-aligned counting mode:
With prescaler, the ARR value of 9999 or 5000 is now within the range of 16-bit ARR register.
For up-counting or down-counting mode:
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 27: Quiz
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.

## Slide 28: Quiz Answer
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.
= 0.1 MHz

## Slide 29: Quiz
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Timer Clock Frequency, and Timer Frequency, assuming up-counting mode?

## Slide 30: Quiz Answer
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Timer Clock Frequency, and Timer Frequency, assuming up-counting mode?
PSC, ARR are both in the range [0, 216-1=65535].
(A realistic Timer Frequency should not be higher than 1KHz, as mentioned before.)
=

## Slide 31: Quiz
Suppose a 16-bit timer has the following settings
    CPU Clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.

## Slide 32: Quiz Answer
Suppose a 16-bit timer has the following setting
    CPU clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.
=
PWM output is high on when the counter is 499, 500, 501, …, 1999, a total of 1501 cycles. (This statement is not required in the exam.)