## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises ANS

## Slide 2: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
Review
Notes: Yes. For a standard full-descending ARM/Thumb-2 stack, SP is decremented before each store during PUSH (pre-decrement), and incremented after each load during POP (post-increment); slides should reflect SP moving down before writing and up after reading.duetorun+1
Correct rule to apply
PUSH: STMDB/STMFD sp!, {...} semantics — SP moves down first, then values are stored starting at the new SP; lowest-numbered register goes to the lowest address.documentation-service.arm+1
POP: LDMIA/LDMFD sp!, {...} semantics — values are read starting at SP, then SP moves up after the block; lowest-numbered register is loaded from the lowest address.developer.arm+1
https://duetorun.com/blog/20230614/arm-stack-modes/
https://developer.arm.com/documentation/107656/latest/Registers/Registers-in-the-register-bank/R13--Stack-Pointer--SP-/Stack-memory
https://documentation-service.arm.com/static/65798111b52744113be5cda1?token=
https://developer.arm.com/documentation/dui0231/latest/thumb-instruction-reference/thumb-memory-access-instructions/push-and-pop
https://developer.arm.com/documentation/dui0801/a/Cacbgchh
https://stackoverflow.com/questions/70008529/i-cannot-understand-how-the-arm-stack-operations-work
https://www.scs.stanford.edu/~zyedidia/docs/arm/extras/annot/subroutines.hohl-arm-asm.pdf
https://stackoverflow.com/questions/47109767/push-and-pop-order-in-arm/47109995
https://shankarrajagopal.github.io/theory/Module_5_good_one.pdf
https://developer.arm.com/documentation/dui0489/e/arm-and-thumb-instructions/memory-access-instructions/push-and-pop
https://www.embeddedrelated.com/showthread/comp.arch.embedded/200819-1.php
http://www.cs.emory.edu/~cheung/Courses/255/Syllabus/7-ARM/SLIDES/s53.html
https://bob.cs.sonoma.edu/testing/sec-stack.html
https://stackoverflow.com/questions/57031401/why-push-first-decreases-the-stack-pointer
https://azeria-labs.com/functions-and-the-stack-part-7/
http://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture5/lecture5-4-2.html
https://web.eecs.umich.edu/~prabal/teaching/eecs373-f10/readings/ARMv7-M_ARM.pdf
https://users.ece.utexas.edu/~valvano/mspm0/Arm_Architecture_v6m_Reference_Manual.pdf
http://homepage.cs.uiowa.edu/~jones/compiler/notes/27.shtml

## Slide 3: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Pop multiple registers
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
Review

## Slide 4: Stack
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=?, r1=?

## Slide 5: Stack ANS
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
r2=2
r1=1
SP
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=1, r1=2
Stack contains only the values like 2, 1… I write r2=2, r1=1 in the figures for illustration purposes only.

## Slide 6: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3} (same as POP {r0, r1, r2, r3})
What is in registers ?

## Slide 7: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3}
Draw stack after each instruction. What is in registers after execution?
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
After POP {r0-r3}
r0=?, r1=?, r2=?, r3=?

## Slide 8: Stack ANS
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3}
Draw stack after each instruction. What is in registers after execution?
SP
r2=2
r1=1
SP
r2=2
r1=1
r3=3
r0=0
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
SP
After POP {r0-r3}
r0=0, r1=3, r2=1, r3=2

## Slide 9: What is Wrong?
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 10: What is Wrong? ANS
Return result should be put into r0, not r1
BX lr returns to caller
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r0, r3 BX lr ENDP

## Slide 11: toLower
Caller Program
#include <stdio.h> extern int mystery(int); /* mystery assembler routine */ int main(void) { static const char str[] = "Hello, World!"; const int len = sizeof(str)/sizeof(str[0]); char newstr[len]; int i; for (i = 0; i < len; i++) newstr[i] = toLower (str[i]); printf("%s\n", newstr); return 0; }
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Consider the following C program that converts all ASCII letters to lower case. Write the toLower function in ARMv7 assembly code.
Callee Program Assembly
.text .global toLower toLower:
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 12: toLower ANS
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Callee Program Assembly
.text .global toLower toLower: cmp r0, #'A' @ if c < 'A' -> skip_adjust blt skip_adjust cmp r0, #'Z' @ if c > 'Z' -> skip_adjust bgt skip_adjust add r0, r0, #('a' - 'A') @ c += 32 skip_adjust: bx lr
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)