## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
ARM Instruction References
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: NZCV Flags in xPSR
N (negative) – set (1) when a signed result is negative, otherwise cleared (0).
Z (zero) – set (1) when a result is 0, otherwise cleared (0).
C (carry) – set (1) when an add-based operation produces an overflow, when a subtract-based operation doesn’t require a borrow; when shifting, holds the last bit that’s been shifted out; otherwise cleared (0).
V (overflow) – set (1) when an add- or subtract-based operation generates a signed overflow, otherwise cleared (0).
Notes: https://eclecticlight.co/2021/06/23/code-in-arm-assembly-controlling-flow/

## Slide 3: Common ARM Instructions
Type of Instruction | ARM Assembly | Register Transfer Language Description
Memory Access (Load and Store) | LDR r4, Mem | [r4] ← [Mem] ; Mem is a global variable label
 | STR r4, Mem | [Mem] ← [r4]
 | LDR r4, [r3] | [r4] ← [[r3]] ; register indirect
 | STR r4, [r3, #4] | [[r3] + 4] ← [r4] ; register indirect with offset
Move | MOV r4, r2 | [r4] ← [r2]
 | MOV r4, #10 | [r4] ← 10 ; 8-bit literal, can be shifted
Load Address | ADR r4, Mem | [r4] ← load address of label Mem
Arithmetic Instruction | ADD r4, r2, r3 | [r4] ← [r2] + [r3]
 | MUL r4, r2, r3 | [r4] ← [r2] * [r3] (32-bit product)
 | SUB r4, r2, r3 | [r4] ← [r2] - [r3]
Compare (sets condition codes) | CMP r4, r2 | 
Conditional Branch | BGT LABEL (BGE, BLT, BLE, BEQ, BNE) | Branch to LABEL based on condition codes
Unconditional Branch | B LABELAlways Branch to LABEL | 
Notes: (and psuedo-instructions)

## Slide 4
Type of Instruction | ARM Assembly | Register Transfer Language Description
ARM Logical Instructions | AND r4, r2, r3 | [r4] ← [r2] (bit-wise AND) [r3]
 | AND r4, r2, #0xFF000000 | [r4] ← [r2] (bit-wise AND) FF000000
 | ORR r4, r2, r3 | [r4] ← [r2] (bit-wise OR) [r3]
 | EOR r4, r2, r3 | [r4] ← [r2] (bit-wise XOR) [r3]
 | BIC r4, r2, r3 | [r4] ← [r2] (bit-wise AND) (NOT [r3]) (clear bits set in r3)
 | MOVN r4, r2 | [r4] ← (NOT) [r2] (Flip all bits)
ARM Shift and Rotate Instructions | MOV r4, r5, LSL #3 | r4 ← logical shift left r5 by 3 positions. (Shift in zeros)
 | MOV r4, r5, LSL r6 | r4 ← logical shift left r5 by the number of positions specified in register r6
 | MOV r4, r5, LSR #3 | r4 ←logical shift right r5 by 3 positions. (Shift in zeros)
 | MOV r4, r5, ASR #3 | r4 ← arithmetic shift right r5 by 3 positions. (Shift with sign-extend)
 | MOV r4, r5, ROR #3 | r4 ← rotate right r5 by 3 positions. (Circulate shift)
 | AND r4, r5, r6, LSL #2 | Shifts can operate on 3rd register operand of arithmetic or logical instruction, e.g., r4 ← r5 AND (logical shift left r6 by 8 positions)
Notes: (and psuedo-instructions)

## Slide 5: Ch6 ARM Flow Control: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 6: Ch6 ARM Flow Control: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 7: Ch6 ARM Flow Control: Conditional Execution
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 8: Ch8 ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | Yes | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | Receives return address on BL call to procedure
r15 (PC) | Program counter | N/A | Do not directly change PC
Notes: LR does not have to contain the same value after a subroutine has completed.