## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Flow Control in Assembly
Exercises ANS
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Q1
Write ARMv7 assembly for pseudocode
  if (r0 != r1) r2 = r2 + r2
ANS A:
  CMP r0, r1
  BEQ skip
  ADD r2, r2, r2
  skip:
ANS B:
  CMP r0, r1 ; Compare r0 and r1
  ADDNE r2, r2, r2 ; r2 = r2 + r2 if Not Equal
Notes: Compare r0 and r1
@ Branch to skip if r0 == r1 (skip the addition)
@ r2 = r2 + r2 (only executed if r0 != r1)

## Slide 3: Q1 ANS
Write ARMv7 assembly for pseudocode
  r1 = (r0 >> 4) & 15
ANS:
  MOV r1, r0, LSR #4
  AND r1, r1, #15
Notes: Alternative solution:
  AND r1, r0, #0xF0
  MOV r1, r1, LSR #4

## Slide 4: Q2
What is r0 equal to after running this program:
  MOV r0, #10
  MOV r1, #7
  MOV r2, #5
  CMP r1, r2
  ADDGT r0, r0, #100

## Slide 5: Q2 ANS
What is r0 equal to after running this program:
  MOV r0, #10 @ Load immediate value 10 into r0
  MOV r1, #7 @ Load immediate value 7 into r1
  MOV r2, #5 @ Load immediate value 5 into r2
  CMP r1, r2 @ Compare r1 and r2 (compute r1-r2, set flags)
  ADDGT r0, r0,100 @ Add 100 to r0 only if r1 > r2 (Greater Than)
This code sets r0 to 10, compares 7 and 5. Since 7 > 5, adds 100 to the base value of 10 to get 110
Notes: bx lr @ Branch and exchange, return to caller

## Slide 6: Q3
save[] is an array of 32-bit integers. Assume that i and k correspond to registers r1 and r2, and the base of the array save is in r0. Write the ARMv7 assembly code corresponding to this C code.
  while (save[i] == k)
  i += 1;

## Slide 7: Q3 ANS
C code:
  while (save[i] == k)
  i += 1;
ANS:
  @ r0 = &save[0] (base address of array)
  @ r1 = i (index)
  @ r2 = k (value to compare)
  loop:
  LDR r3, [r0, r1, LSL #2] @ r3 = save[i], 32-bit loads with index scaled by 4
  CMP r3, r2 @ compare save[i] with k
  BNE done @ exit loop if save[i] != k
  ADD r1, r1, #1 @ i += 1
  B loop @ repeat
  done:

## Slide 8: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 9: Conditional Instructions
Write the following ARMv7 instructions:
  Add registers r3 and r6 only if N is clear (from a previous instruction). Store the result in register r7.
  Multiply registers r7 and r12, put the results in register r3 only if C is set and Z is clear (from a previous instruction)
  Compare registers r6 and r8 only if Z is clear (from a previous instruction)
Notes: After a CMP/CMN or SUBS/ADDS used as an unsigned compare where the first operand is strictly greater than the second; for example, after CMP r0, r1, HI means r0 > r1 when treated as unsigned.

## Slide 10: Conditional Instructions ANS
Write the following ARMv7 instructions:
  Add registers r3 and r6 only if N is clear. Store the result in register r7.
  Multiply registers r7 and r12, put the results in register r3 only if C is set and Z is clear
  Compare registers r6 and r8 only if Z is clear
ANS:
  @ Plus, Positive or Zero, (N=0). Add r3 and r6 only if N is clear, store in r7
  ADDPL r7, r3, r6
  @ HI, Unsigned Higher, (C=1 & Z=0). Multiply r7 and r12, put result in r3 only if C is set and Z is clear
  MULHI r3, r7, r12
  @ NE, Not equal (Z=0). Compare r6 and r8 only if Z is clear
  CMPNE r6, r8
Notes: After a CMP/CMN or SUBS/ADDS used as an unsigned compare where the first operand is strictly greater than the second; for example, after CMP r0, r1, HI means r0 > r1 when treated as unsigned.

## Slide 11: Assembly to C
Write the equivalent C program for the following assembly code, assuming registers and C variables are related as (x=r0, y=r1). ( Variables in C are in memory, and load/store assembly instructions are omitted here for brevity.) For example:
Assembly Program | C Program
CMP r0, #5 MOVEQ r0, #10 BLEQ fn | if (x == 5) { x = 10; fn(x); }
Assembly Program | C Program
CMP r0, #0 MOVLE r0, #0 MOVGT r0, #1 | 
Assembly Program | C rogram
CMP r0, #'A’ CMPNE r0, #'B' MOVEQ r1, #1 | 

## Slide 12: Assembly to C ANS
Write the equivalent C program for the following assembly code, assuming registers and C variables are related as (x=r0, y=r1). ( Variables in C are in memory, and load/store assembly instructions are omitted here for brevity.)
Assembly Program | C Program
CMP r0, #5 MOVEQ r0, #10 BLEQ fn | if (x == 5) { x = 10; fn(x); }
Assembly Program | C Program
CMP r0, #0 MOVLE r0, #0 MOVGT r0, #1 | if (x <= 0) x = 0; else x = 1;
Assembly Program | C Program
CMP r0, #'A’ CMPNE r0, #'B' MOVEQ r1, #1 | if (c == ‘A’ ¦¦ c == 'B') y = 1;

## Slide 13: Conditional Execution
Rewrite the assembly program to use conditional execution statements.
Assembly Program | Assembly Program with Cond. Exec
CMP r3, #0 BEQ next ADD r0, r0, r1 SUB r0, r0, r2 next ... | 

## Slide 14: Conditional Execution ANS
Rewrite the assembly program to use conditional execution statements.
Assembly Program | Assembly Program with Cond. Exec
CMP r3, #0 BEQ next ADD r0, r0, r1 SUB r0, r0, r2 next ... | CMP r3, #0 ADDNE r0, r0, r1 SUBNE r0, r0, r2 ...

## Slide 15: C to Assembly
C Program | Assembly Program
//Calculate x such that 2^x = 128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE DONE

## Slide 16: C to Assembly ANS
C Program | Assembly Program
//Calculate x such that 2^x = 128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE CMP r0, #128 ; r0-128 BEQ DONE ; if (pow==128) exit loop LSL r0, r0, #1 ; pow = pow * 2 ADD r1, r1, #1 ; x = x + 1 B WHILE ; repeat loop DONE

## Slide 17: C to Assembly
For an array of 32‑bit ints, each element is 4 bytes, so element i lives at base + i*4, which is implemented as base + (i << 2) via LSL #2 in the addressing mode
BPL “Branch if PLus” branches when the N (negative) flag N == 0, meaning the prior result was positive or zero
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i=i-1) array[i] = array[i] * 8; | ; R0 = array base address, R1 = i MOV R0, 0x60000000 MOV R1, #199 FOR

## Slide 18: C to Assembly ANS
For an array of 32‑bit ints, each element is 4 bytes, so element i lives at base + i*4, which is implemented as base + (i << 2) via LSL #2 in the addressing mode
BPL “Branch if PLus” branches when the N (negative) flag N == 0, meaning the prior result was positive or zero
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i = i - 1) array[i] = array[i] * 8; | ; R0 = array base address, R1 = i MOV R0, 0x60000000 MOV R1, #199 FOR LDR R2, [R0, R1, LSL #2] ;R2 = array(i) LSL R2, R2, #3 ; R2 = R2<<3 = R2*8 STR R2, [R0, R1, LSL #2] ;array(i) = R2 SUBS R1, R1, #1 ; i=i-1 and set flags BPL FOR ; if (i >= 0) repeat loop

## Slide 19: Assembly Programming
Write a program that reverses the bits in a register, such that the register containing d31,d30,d29...d1,d0 now contains d0,d1,...d29,d30,d3.

## Slide 20: Assembly Programming ANS
ANS:
  @ Reverse bits in r0, result in r1
  MOV r1, #0 @ Initialize result
  MOV r2, #32 @ Bit counter
  reverse_loop:
  CMP r2, #0
  BEQ reverse_end
  LSL r1, r1, #1 @ Shift result left
  AND r3, r0, #1 @ Get LSB of r0
  ORR r1, r1, r3 @ Add to result
  LSR r0, r0, #1 @ Shift r0 right
  SUB r2, r2, #1 @ Decrement counter
  B reverse_loop
  reverse_end:
Example with 8 bits:
Let input r0 = 0b1011_0010
Initialize r1 = 0, r2 = 8 (bit counter), and r3 is the scratch for the extracted bit; the loop body runs 8 times.
Iteration 1
LSL r1, r1, #1: r1 = 0 << 1 = 0.
AND r3, r0, #1: r3 = 0b1011_0010 & 1 = 0 (LSB of r0 is 0).
ORR r1, r1, r3: r1 = 0 | 0 = 0.
LSR r0, r0, #1: r0 = 0b0101_1001 (shift right, next LSB becomes current).
SUB r2, r2, #1: r2 = 7.
Effect: The first output bit appears at the LSB of r1 and equals original d0.
Iteration 2
LSL r1: r1 = 0 << 1 = 0.
AND r3, r0, #1: r3 = 0b0101_1001 & 1 = 1 (new LSB is 1).
ORR r1, r1, r3: r1 = 0 | 1 = 1 (now r1 = 0b0000_0001).
LSR r0: r0 = 0b0010_1100.
SUB r2: r2 = 6.
Effect: r1 now holds bits “d0 d1”.
On each subsequent iteration, r1 is shifted left before inserting the next bit, so earlier bits move toward the MSB while the newly inserted bit always starts at the LSB; over the whole loop, this builds the reversed word with the earliest extracted bits ending up toward the MSB by the end.

## Slide 21: Assembly Programming
Write the equivalent assembly program for this piece of code in C
  for (i=0; i<8; i++){
  a[i] = b[7-i];
  }
ANS:
  @ for (i=0; i<8; i++) { a[i] = b[7-i]; }
  @ Assume r0 = base address of a, r1 = base address of b
  MOV r2, #0 @ i = 0
  loop_start:
  …
  loop_end:

## Slide 22: Assembly Programming ANS
Write the equivalent assembly program for this piece of code in C
  for (i=0; i<8; i++){
  a[i] = b[7-i];
  }
ANS:
  @ for (i=0; i<8; i++) { a[i] = b[7-i]; }
  @ Assume r0 = base address of a, r1 = base address of b
  MOV r2, #0 @ i = 0
  loop_start:
  CMP r2, #8
  BGE loop_end
  RSB r3, r2, #7 @ r3 = 7 - i
  LDR r4, [r1, r3, LSL#2] @ Load b[7-i]
  STR r4, [r0, r2, LSL#2] @ Store to a[i]
  ADD r2, r2, #1 @ i++
  B loop_start
  loop_end:

## Slide 23: Test for Equal
Give the different methods to test if two values held in registers r0 and r1 are equal.

## Slide 24: Test for Equal ANS
Give the different methods to test if two values held in registers r0 and r1 are equal.
ANS:
  @ Method 1: Compare instruction
  CMP r0, r1
  @ Method 2: Exclusive OR
  EORS r2, r0, r1 @ If equal, result is zero and Z flag set
  @ Method 3: Subtract and test
  SUBS r2, r0, r1 @ If equal, result is zero and Z flag set