## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises

## Slide 2: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
Review
Notes: Yes. For a standard full-descending ARM/Thumb-2 stack, SP is decremented before each store during PUSH (pre-decrement), and incremented after each load during POP (post-increment); slides should reflect SP moving down before writing and up after reading.duetorun+1
Correct rule to apply
PUSH: STMDB/STMFD sp!, {...} semantics — SP moves down first, then values are stored starting at the new SP; lowest-numbered register goes to the lowest address.documentation-service.arm+1
POP: LDMIA/LDMFD sp!, {...} semantics — values are read starting at SP, then SP moves up after the block; lowest-numbered register is loaded from the lowest address.developer.arm+1
https://duetorun.com/blog/20230614/arm-stack-modes/
https://developer.arm.com/documentation/107656/latest/Registers/Registers-in-the-register-bank/R13--Stack-Pointer--SP-/Stack-memory
https://documentation-service.arm.com/static/65798111b52744113be5cda1?token=
https://developer.arm.com/documentation/dui0231/latest/thumb-instruction-reference/thumb-memory-access-instructions/push-and-pop
https://developer.arm.com/documentation/dui0801/a/Cacbgchh
https://stackoverflow.com/questions/70008529/i-cannot-understand-how-the-arm-stack-operations-work
https://www.scs.stanford.edu/~zyedidia/docs/arm/extras/annot/subroutines.hohl-arm-asm.pdf
https://stackoverflow.com/questions/47109767/push-and-pop-order-in-arm/47109995
https://shankarrajagopal.github.io/theory/Module_5_good_one.pdf
https://developer.arm.com/documentation/dui0489/e/arm-and-thumb-instructions/memory-access-instructions/push-and-pop
https://www.embeddedrelated.com/showthread/comp.arch.embedded/200819-1.php
http://www.cs.emory.edu/~cheung/Courses/255/Syllabus/7-ARM/SLIDES/s53.html
https://bob.cs.sonoma.edu/testing/sec-stack.html
https://stackoverflow.com/questions/57031401/why-push-first-decreases-the-stack-pointer
https://azeria-labs.com/functions-and-the-stack-part-7/
http://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture5/lecture5-4-2.html
https://web.eecs.umich.edu/~prabal/teaching/eecs373-f10/readings/ARMv7-M_ARM.pdf
https://users.ece.utexas.edu/~valvano/mspm0/Arm_Architecture_v6m_Reference_Manual.pdf
http://homepage.cs.uiowa.edu/~jones/compiler/notes/27.shtml

## Slide 3: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Pop multiple registers
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
Review

## Slide 4: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 5: Stack
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=?, r1=?

## Slide 6: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3} (same as POP {r0, r1, r2, r3})
Draw stack after each instruction. What is in registers after execution?
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
After POP {r0-r3}
r0=?, r1=?, r2=?, r3=?

## Slide 7: What is Wrong?
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 8: toLower
Caller Program
#include <stdio.h> extern int mystery(int); /* mystery assembler routine */ int main(void) { static const char str[] = "Hello, World!"; const int len = sizeof(str)/sizeof(str[0]); char newstr[len]; int i; for (i = 0; i < len; i++) newstr[i] = toLower (str[i]); printf("%s\n", newstr); return 0; }
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Consider the following C program that converts all ASCII letters to lower case. Write the toLower function in ARMv7 assembly code.
Callee Program Assembly
.text .global toLower toLower:
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 9: If Then Else
Translate the following program into ARMv7 assembly.
  int foo(int x, int y) {
  if ((x+y) < 0)
  return 0;
  else return 1;
  }
ANS:
  @ int foo(int x, int y) - returns 0 if (x+y) < 0, else 1
  @ x in r0, y in r1, return in r0
  foo:
  …
  BX lr

## Slide 10: Factorial
Write an assembly program to calculate the factorial of a number, corresponding to the following C programs. One recursive version, one iterative version. (In the exams, I may provide most of the code and let you fill in the blanks.)
//Recursive algorithms for Factorial
#include <stdint.h>
uint32_t fact_rec(uint32_t n) {
if (n <= 1) {
return 1;
}
return n * fact_rec(n - 1);
}
//Iterative algorithms for Factorial
#include <stdint.h>
uint32_t fact_iter(uint32_t n) {
uint32_t acc = 1;
if (n <= 1) {
return 1;
}
while (n > 1) {
acc *= n;
n -= 1;
}
return acc;
}