## Slide 1: ECE 319K Introduction to Embedded Systems
Lecture 6: Exam 1 review
Bard, Gerstlauer, Cuevas, Holt, Telang, Tiwari, Valvano, Yerraballi
  Exam 1: Thu-Feb 20, 2025 7:00PM - 8:30PM

## Slide 2: Agenda
Exam 1
  Exam 1, Thu-Feb 20, 2025 7:00PM - 8:30PM.
  Closed book, no calculator.
  See handout at end of each exam
Topics
  Memory access
  Registers and stack
  Arithmetic operations
  Shift operations
  Logic operations
  Control structures
  Functions
  Arrays
Bard, Erez, Gerstlauer, Valvano, Holt, Yerraballi, Telang, Cuevas, Tiwari

## Slide 3: Exam 1 What to study?
Labs 1-3
  Arrays in C and assembly
Book chapters 1-3, eBook Chapters 1-3
  See reading assignments for Labs 1-3
Canvas Quizzes up through 10/4
Old exams
  Familiarize reference sheet with old exams
    Instructions, pseudops, I/O registers
AAPCS
Bard, Erez, Gerstlauer, Valvano, Holt, Yerraballi, Telang, Cuevas, Tiwari

## Slide 4: Exam 1 What not to study?
Divide algorithm
Stepper motor, solid state relay
.macro
SysTick, TimerG,
no pointers in C
  Yes to pointers in assembly
printf
LED interface with ULN2003B driver
No NZVC bits
  Yes to CMP, ANDS..SUBS followed by Bxx
.align
Structs
FSM
Bard, Erez, Gerstlauer, Valvano, Holt, Yerraballi, Telang, Cuevas, Tiwari

## Slide 5: Memory Access
Signed or Unsigned
8/16/32 bits
  LDRB
  LDRSB
  LDRH
  LDRSH
  LDR
  STRB
  STRH
  STR
What do the following instructions do?
LDR R1,[R2]
LDRB R1,[R2,#2]
LDRSB R1,[R2,R3]
LDRH R1,[R2,R3]
What is the difference?
LDR R0,=100
MOV R0,#100

## Slide 6: Stack access
SP points to data
Push
  SP = SP-4
  Store at SP
POP
  Read at SP
  SP = SP+4
Order of data (one push or pop)
  Smaller register number at lower address
  Larger register number at higher address

## Slide 7: Activity
Initially, let R0=0, R1=1, R2=2
Execute PUSH {R1,R2}
Draw stack
Execute POP {R0,R1}
Draw stack
SP
SP
Initially After PUSH After POP

## Slide 8: Instapoll Lec 6
Initially, let R0=0, R1=1, R2=2, R3=3
Execute
PUSH {R1,R2}
PUSH {R3,R0}
POP {R0-R3}
What is in register ?

## Slide 9: AAPCS, Registers and stack
Save LR before calling another function
Input parameters in R0,R1,R2,R3
Output parameter in R0
Balance the stack
PUSH {R4,R5} same as PUSH {R5,R4}
Freely use R0,R1,R2,R3,R12
Save, use, restore R4-R11
Fun1: PUSH {R4,LR}
BL Fun2
POP {R4,PC}
Fun3: PUSH {R4-R7}
//stuff using R4-R7
POP {R4-R7}
BX LR

## Slide 10: Arithmetic, logical, shift
ADDS
SUBS
RSBS
MULS
LSLS
LSRS
ASRS
ANDS
ORRS
BICS
EORS
How do you tell what operands are possible?
ADDS R0,R1,#3
ANDS R0,R1,#3 //not allowed (see handout)
MULS R0,R1,#3 //not allowed (see handout)
LSL R0,R1,#3

## Slide 11: Control Operations
If-then
If-then-else
Do-while
While
CMP R0,#0
Bxx Target
CMP R0,#0
Bxx Yes
No: //not true
//
B done
Yes: //true
//
done:
loop:
//body
CMP R0,#0
Bxx loop
loop: CMP R0,#0
Bxx done
//body
B loop
done:
BEQ
BNE
BLO
BLS
BHI
BHS
BEQ
BNE
BLT
BLE
BGT
BGE

## Slide 12: Special cases
If-then with bit mask
Do-while with counter
MOVS R1,#4
ANDS R0,R1
BEQ Target
MOVS R1,#4
ANDS R0,R1
BNE Target
loop:
//stuff
SUBS R0,#1
BNE loop

## Slide 13: Arrays
Base
  Pointer passed in a register
Precision
  8 bits n=1 byte
  16 bits n=2 bytes
  32 bits n=4 bytes
Size
  Fixed and known
  Passed in another register
Value
  Character
  Unsigned integer
  Signed integer
0 ≤ I < Size
Base+n*I

## Slide 14: Pointers (???)
Definition
  uint16_t *p1;
  int32_t *p2;
Initialization
  p1 = &data;
  p2 = buffer;
Write access
  *p1 = 5;
  *p2 = 5;
  p2[i] = 0;
Read access
  x = *p1
  y = *p2;
  y = p2[i];
Pointer math
  p2++;
0 ≤ I < Size
Base+n*I
  uint16_t data;
  uint16_t x;
  int32_t buffer[100];
  int32_t y;
  int i=0;

## Slide 15: Examples
Simple programs
  Clear, set, toggle, swap bits
  Check if a bit is high or low
  Logic, shift
  Add, sub, multiply, and divide
Array programs
  Min, max, sum, product, difference, average
  Search for element
  Replace one element with another
  Copy from one to another
Bard, Erez, Gerstlauer, Valvano, Holt, Yerraballi, Telang, Cuevas, Tiwari

## Slide 16: Strategies
Understand the question
  What are the inputs?
  What is the output?
Design
  Understand complexity
    If-then
    Single loop
    Double loop
  Pseudo code
Implementation
  AAPCS
Debug it
  Single step your code in your mind
  Do the inputs generate proper outputs?
Bard, Erez, Gerstlauer, Valvano, Holt, Yerraballi, Telang, Cuevas, Tiwari