## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises ANS

## Slide 2: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
Review
Notes: Yes. For a standard full-descending ARM/Thumb-2 stack, SP is decremented before each store during PUSH (pre-decrement), and incremented after each load during POP (post-increment); slides should reflect SP moving down before writing and up after reading.duetorun+1
Correct rule to apply
PUSH: STMDB/STMFD sp!, {...} semantics — SP moves down first, then values are stored starting at the new SP; lowest-numbered register goes to the lowest address.documentation-service.arm+1
POP: LDMIA/LDMFD sp!, {...} semantics — values are read starting at SP, then SP moves up after the block; lowest-numbered register is loaded from the lowest address.developer.arm+1
https://duetorun.com/blog/20230614/arm-stack-modes/
https://developer.arm.com/documentation/107656/latest/Registers/Registers-in-the-register-bank/R13--Stack-Pointer--SP-/Stack-memory
https://documentation-service.arm.com/static/65798111b52744113be5cda1?token=
https://developer.arm.com/documentation/dui0231/latest/thumb-instruction-reference/thumb-memory-access-instructions/push-and-pop
https://developer.arm.com/documentation/dui0801/a/Cacbgchh
https://stackoverflow.com/questions/70008529/i-cannot-understand-how-the-arm-stack-operations-work
https://www.scs.stanford.edu/~zyedidia/docs/arm/extras/annot/subroutines.hohl-arm-asm.pdf
https://stackoverflow.com/questions/47109767/push-and-pop-order-in-arm/47109995
https://shankarrajagopal.github.io/theory/Module_5_good_one.pdf
https://developer.arm.com/documentation/dui0489/e/arm-and-thumb-instructions/memory-access-instructions/push-and-pop
https://www.embeddedrelated.com/showthread/comp.arch.embedded/200819-1.php
http://www.cs.emory.edu/~cheung/Courses/255/Syllabus/7-ARM/SLIDES/s53.html
https://bob.cs.sonoma.edu/testing/sec-stack.html
https://stackoverflow.com/questions/57031401/why-push-first-decreases-the-stack-pointer
https://azeria-labs.com/functions-and-the-stack-part-7/
http://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture5/lecture5-4-2.html
https://web.eecs.umich.edu/~prabal/teaching/eecs373-f10/readings/ARMv7-M_ARM.pdf
https://users.ece.utexas.edu/~valvano/mspm0/Arm_Architecture_v6m_Reference_Manual.pdf
http://homepage.cs.uiowa.edu/~jones/compiler/notes/27.shtml

## Slide 3: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Pop multiple registers
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
Review

## Slide 4: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 5: Stack
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=?, r1=?

## Slide 6: Stack ANS
Initially, let r0=0, r1=1, r2=2.
a) Execute PUSH {r1,r2}. Draw stack.
b) Execute POP {r0,r1}. Draw stack.
SP
r2=2
r1=1
SP
SP
After PUSH {r1,r2}
After POP {r0,r1},
r0=1, r1=2
Stack contains only the values like 2, 1… I write r2=2, r1=1 in the figures for illustration purposes only.

## Slide 7: Stack
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3} (same as POP {r0, r1, r2, r3})
Draw stack after each instruction. What is in registers after execution?
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
After POP {r0-r3}
r0=?, r1=?, r2=?, r3=?

## Slide 8: Stack ANS
Initially, let r0=0, r1=1, r2=2, r3=3
Execute
PUSH {r1,r2}
PUSH {r3,r0}
POP {r0-r3}
Draw stack after each instruction. What is in registers after execution?
SP
r2=2
r1=1
SP
r2=2
r1=1
r3=3
r0=0
SP
After PUSH {r1,r2}
After PUSH {r3,r0}
SP
After POP {r0-r3}
r0=0, r1=3, r2=1, r3=2

## Slide 9: Stack
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx
R1==0x11111111
R2==0x22222222
Before execution
What is content of stack, and position of SP, after PUSH {R2,R1}?
What are the values of R1/R2 after POP {R2}?

## Slide 10: Stack ANS
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
0x22222222
0x11111111
R1==0x11111111
R2==0x22222222
Before execution
Stack content and SP shown in figure
After POP {R2}, R1==0x11111111, R2==0x22222222

## Slide 11: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 13: Argument Passing
Which registers are used to pass the arguments and return the result?
long fun (short a1, char a2, double a3, int a4, char a5)
Registers
Stack in Memory

## Slide 14: Argument Passing ANS
Which registers are used to pass the arguments and return the result?
Each argument of 8-bit char, or 16-bit short, is passed in 1 32-bit register; cannot use 1 register to pass more than 1 arguments
long fun (short a1, char a2, double a3, int a4, char a5)
a1 | a2 | a3
a4 | a5 |  |  |  |  | 
Registers
Stack in Memory

## Slide 15: What’s wrong? Passing arguments and Returning Value
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOV r0, #5 ; e32
MOV r0, #1 ; a8
MOV r1, #2 ; b8
MOV r2, #3 ; c16
MOV r3, #4 ; d16
BL sum
...
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
ADD r0, r0, r1 ; add e32
BX LR
ENDP

## Slide 16: What’s wrong? Passing arguments and Returning Value ANS
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOV r0, #5 ; e32
PUSH {r0}
MOV r0, #1 ; a8
MOV r1, #2 ; b8
MOV r2, #3 ; c16
MOV r3, #4 ; d16
BL sum
...
POP {r0}
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
LDR r1, [sp, #0] ; read argument e32
ADD r0, r0, r1 ; add e32
BX LR
ENDP
The caller is responsible to pop extra arguments out of the stack after the subroutine returns.

## Slide 17: Passing arguments and Returning Value
a64
b8
c16
d16
Subroutine
Register:
Register;
Register:
Return Value
Register R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack
Fill in register names.
Register:

## Slide 18: Passing arguments and Returning Value ANS
a64
b8
c16
d16
Subroutine
Register r1:r0
Register r2
Register r3
Return Value
Register R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack
Fill in register names.

## Slide 19: What is Wrong?
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 20: What is Wrong? ANS
Return result should be put into r0, not r1
BX lr returns to caller
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r0, r3 BX lr ENDP

## Slide 21: toLower
Caller Program
#include <stdio.h> extern int mystery(int); /* mystery assembler routine */ int main(void) { static const char str[] = "Hello, World!"; const int len = sizeof(str)/sizeof(str[0]); char newstr[len]; int i; for (i = 0; i < len; i++) newstr[i] = toLower (str[i]); printf("%s\n", newstr); return 0; }
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Consider the following C program that converts all ASCII letters to lower case. Write the toLower function in ARMv7 assembly code.
Callee Program Assembly
.text .global toLower toLower:
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 22: toLower ANS
Callee Program
int toLower (int c) { if (c >= 'A' && c <= 'Z') c += 'a' - 'A'; return c; }
Callee Program Assembly
.text .global toLower toLower: cmp r0, #'A' @ if c < 'A' -> skip_adjust blt skip_adjust cmp r0, #'Z' @ if c > 'Z' -> skip_adjust bgt skip_adjust add r0, r0, #('a' - 'A') @ c += 32 skip_adjust: bx lr
Notes: @ int mystery2(int c)
@ r0: c -> returns r0
.text
.align 2
.global mystery2
mystery2:
cmp r0, #'A' @ c ? 'A'
blt 1f @ if c < 'A' -> skip add
cmp r0, #'Z' @ c ? 'Z'
bgt 1f @ if c > 'Z' -> skip add
add r0, r0, #('a' - 'A') @ c += 32 (ASCII delta)
1:
bx lr @ return c (possibly adjusted)

## Slide 23: If Then Else
Translate the following program into ARMv7 assembly.
C Program | Assembly Program
int foo(int x, int y) { if (x+y < 0) return 0; else return 1; } | @ int foo(int x, int y) - returns 0 if (x+y) < 0, else 1 @ x in r0, y in r1, return in r0 foo: … BX lr

## Slide 24: If Then Else ANS
Straight-line with conditional execution
foo: ADD r2, r0, r1 ; r2 = x + y CMP r2, #0 ; sets N,Z,V,C for signed compare to 0 MOVLT r0, #0 ; if (x+y) < 0 -> r0 = 0 MOVGE r0, #1 ; else r0 = 1 BX lr
Conditional branch to label w/ CMP
foo: ADD r2, r0, r1 CMP r2, #0 BLT .Lneg MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Combine add and compare with ADDS
foo: ADDS r2, r0, r1 ; r2 = x + y, sets flags from the sum MOVMI r0, #0 ; MI means N==1 (negative) MOVPL r0, #1 ; PL means N==0 (non-negative) BX lr
No temp register r2, reuse r0
foo: ADDS r0, r0, r1 ; r0 = x + y, flags set MOVMI r0, #0 MOVPL r0, #1 BX lr
Conditional branch to label w/ ADDS
foo: ADDS r2, r0, r1 BMI .Lneg ; if negative MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Notes: Straight-line with conditional execution
foo: ADD r2, r0, r1 ; r2 = x + y CMP r2, #0 ; sets N,Z,V,C for signed compare to 0 MOVLT r0, #0 ; if (x+y) < 0 -> r0 = 0 MOVGE r0, #1 ; else r0 = 1 BX lr
Conditional branch to label
foo: ADD r2, r0, r1 CMP r2, #0 BLT .Lneg MOV r0, #1 BX lr .Lneg: MOV r0, #0 BX lr
Calling convention: inputs x,y in r0,r1; result in r0; lr holds return address; no callee-saved registers are clobbered.
Choose MI/PL (based on N) or LT/GE (signed) consistently; both are correct when flags come from the sum or a compare to zero.
For Thumb-2, prefer conditional branches or the IT block variant if permitted by assembler; for classic ARM state, full conditional MOVs avoid branches.

## Slide 25: Factorial
Fill in the blanks (TODO) for the assembly programs for calculating the factorial of a number, corresponding to the following C programs. One recursive version, one iterative version.
//Recursive algorithms for Factorial
#include <stdint.h>
uint32_t fact_rec(uint32_t n) {
if (n <= 1) {
return 1;
}
return n * fact_rec(n - 1);
}
//Iterative algorithms for Factorial
#include <stdint.h>
uint32_t fact_iter(uint32_t n) {
uint32_t acc = 1;
if (n <= 1) {
return 1;
}
while (n > 1) {
acc *= n;
n -= 1;
}
return acc;
}
Notes: (In the exams, I may provide most of the code and let you fill in the blanks.)

## Slide 26: Factorial
% uint32_t fact_iter(uint32_t n);
% r0 = n, returns r0 = n!
.global fact_iter
fact_iter:
PUSH {r4, lr} % save callee-saved we’ll use and return addr
MOV r1, r0 % r1 = n (loop counter)
MOV r0, #1 % r0 = acc = 1
CMP r1, #1
BLS .Ldone_iter % if n <= 1, return 1
.Lloop_iter:
% TODO
.Ldone_iter:
POP {r4, lr}
BX lr
% uint32_t factorial(uint32_t n);
% r0: n
% returns r0: n!
factorial:
CMP r0, #1 % if (n <= 1) ...
BLE base_case % ... return 1
PUSH {lr} % save return address for this frame
PUSH {r0} % save current n on stack (we'll need it after the recursive call)
SUB r0, r0, #1 % r0 = n - 1 (argument for recursive call)
BL factorial % r0 = factorial(n - 1)
POP {r1} % r1 = saved n (restore caller's n)
MUL r0, r0, r1 % r0 = factorial(n - 1) * n
POP {lr} % restore return address
BX lr % return with result in r0
base_case:
% TODO

## Slide 27: Factorial ANS
% uint32_t fact_iter(uint32_t n);
% r0 = n, returns r0 = n!
.global fact_iter
fact_iter:
PUSH {r4, lr} % save callee-saved we’ll use and return addr
MOV r1, r0 % r1 = n (loop counter)
MOV r0, #1 % r0 = acc = 1
CMP r1, #1
BLS .Ldone_iter % if n <= 1, return 1
.Lloop_iter:
MUL r0, r0, r1 % acc *= i
SUBS r1, r1, #1 % i--
BHI .Lloop_iter % continue while i > 1 (unsigned)
.Ldone_iter:
POP {r4, lr}
BX lr
% uint32_t factorial(uint32_t n);
% r0: n
% returns r0: n!
factorial:
CMP r0, #1 % if (n <= 1) ...
BLE base_case % ... return 1
PUSH {lr} % save return address for this frame
PUSH {r0} % save current n on stack (we'll need it after the recursive call)
SUB r0, r0, #1 % r0 = n - 1 (argument for recursive call)
BL factorial % r0 = factorial(n - 1)
POP {r1} % r1 = saved n (restore caller's n)
MUL r0, r0, r1 % r0 = factorial(n - 1) * n
POP {lr} % restore return address
BX lr % return with result in r0
base_case:
MOV r0, #1 % factorial(n) = 1 for n <= 1
BX lr % return
POP is used here because the function previously PUSHed registers that must be restored before returning; POP both restores those registers and fixes the stack pointer in one instruction.

## Slide 28: What is wrong?
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0], #2
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3 ; return result in r0
BX lr
ENDP

## Slide 29: What is wrong? ANS
int16_t sum_of_array(int16_t *pArray){
uint32_t i;
int32_t sum = 0;
for(i=0; i<64; i++) // array size = 64
sum += pArray[i];
return (int16_t) sum;
}
sum_of_array PROC
MOV r2, #0 ; loop index
MOV r3, #0 ; sum
B check
loop LDRSH r1, [r0], #2
ADD r3, r3, r1 ; sum += pArray[i]
ADD r2, r2, #1 ; i++
check CMP r2, #64
BLO loop ; branch if unsigned LOwer
MOV r0, r3, LSL #16
MOV r0, r0, ASR #16 ; r0 = (short) r3
BX lr
ENDP
The sum is limited to 16 bits!
0x12345678
0x00005678
0x1234ABCD
0xFFFFABCD
int32_t x = 0x12345678;
int16_t y = (int16_t) x;

## Slide 30: Explanations
These two lines sign-extend the lower 16 bits of r3 into a full 32-bit value in r0.
MOV r0, r3, LSL #16
  Shifts the value in r3 left by 16 bits.
  The lower 16 bits of r3 (the part we care about) move up into the upper 16 bits of r0.
  The bottom 16 bits of r0 become 0.
MOV r0, r0, ASR #16
  Shifts the value right by 16 bits, but preserves the sign (arithmetic shift).
  That means if bit 31 (the sign bit after the first shift) is 1, it fills with 1s; if 0, it fills with 0s.
  The result is a sign-extended 16-bit value from the original lower half of r3.
Examples:
r3 = 0x00001234
  LSL #16 → 0x12340000
  ASR #16 → 0x00001234
r3 = 0x0000ABCD
  LSL #16 → 0xABCD0000
  ASR #16 → 0xFFFFABCD
Can be replaced with a single instruction:
  SXTH r0, r3 ; r0 = (int16_t) r3, sign-extend