## Slide 1: L3 (CHAPTER 6) Programming in Assembly Part 2: Data Manipulation Exercises

## Slide 2: Memory Cell Contents with Endianness
Consider 4-byte data 0xA1B2C3D4 at memory address 0x100. Fill in the memory cell contents for Big-Endian and Little-Endian
MSB
LSB
Big-Endian
0x100
0x101
0x102
0x103
LSB
MSB
Little-Endian
0x100
0x101
0x102
0x103
Notes: Recall: memory address is Byte address, not bit address)

## Slide 3: Memory Cell Contents with Endianness ANS
4-byte data 0xA1B2C3D4 at memory address 0x100 (Recall: memory address is Byte address, not bit address)
MSB
LSB
D4
C3
B2
A1
Big-Endian
0x100
0x101
0x102
0x103
LSB
MSB
A1
B2
C3
D4
Little-Endian
0x100
0x101
0x102
0x103

## Slide 4: Load Instructions
LDR rt, [rs]
  fetch data from memory into register rt.
  The memory address is specified in register rs.
  For Example:
; Assume r0 = 0x08200004
; Load a word:
LDR r1, [r0] ; r1 = Memory.word[0x08200004]
Review

## Slide 5: Store Instructions
STR rt, [rs]:
  save data in register rt into memory
  The memory address is specified in a base register rs.
  For Example:
; Assume r0 = 0x08200004
; Store a word
STR r1, [r0] ; Memory.word[0x08200004] = r1
Review

## Slide 6: Question: Load-Modify-Store
; Assume the memory address of x is stored in r1. Write the assembler program for the C statement.
x = x + 1;
C statement
Notes: Assume x is a 32-bit integer stored in the memory

## Slide 7: Loading Constants: LDR
LDR rd,=constant
  A special “pseudo-operation” that will work for any constant up to 32 bits wide.
  You simply write what appears to be a regular ARM instruction (except that an equal sign is substituted for the pound sign) and let the assembler sort out the most efficient way to achieve your objective:
  Converted to MOV or MVN if possible
  Else converts to LDR rd,[pc,#imm]
Examples:
  LDR R1,=10 ;assembler replaces this by MOV R1,#10.
  LDR R1,=−15 ;assembler replaces this by MVN R1,#14.
  LDR R1,=−127435 ;assembler replaces this by a memory reference instruction that loads the constant −127435 from a separate memory location.
Review

## Slide 8: LDRH (Load Halfword)
32-bit Register |  |  |  |  |  |  | 
31 |  |  | 16 | 15 |  |  | 0
15 | 0
16-bit Memory Half-Word (unmodified) | 
0 0 | 0 0
. . . . . . . . . .
. . . . . . . . . .
When loading 8- or 16-bit data into a 32-bit register, the operand itself is always right justified within the register and its most significant bits filled according to whether the value is signed or unsigned. Unsigned operands less than 32 bits wide must fill the extra bit positions with zeroes (called “zero-filling”).
Review
Notes: when loading 8- or 16-bit data into a 32-bit register, the operand itself is always right
justified within the register and its most significant bits filled according to whether the
value is signed or unsigned

## Slide 9: LDRSH (Load Signed Halfword)
32-bit Register |  |  |  |  |  |  | 
31 |  |  | 16 | 15 |  |  | 0
15 | 0
16-bit Memory Half-Word (unmodified) | 
. . . . . . . . . .
. . . . . . . . . .
Signed operands less than 32 bits wide must fill the extra bit positions with copies of their sign bit
Review

## Slide 10: Load (from memory) Instructions
Load/Store Memory | Operation | Notes
LDR rd,<mem> | rd  mem32[address] | 
LDRB rd,<mem> | rd  mem8[address] | Zero fills
LDRH rd,<mem> | rd  mem16[address] | Zero fills
LDRSB rd,<mem> | rd  mem8[address] | Sign extends
LDRSH rd,<mem> | rd  mem16[address] | Sign extends
LDRD rt,rt2,<mem> | rt2. rt  mem64[address] | 
Review
Notes: These instructions never affect flags in xPSR!

## Slide 11: STRH (Store Halfword)
31 |  |  | 16 | 15 |  |  | 0
32-bit Register (unmodified) |  |  |  |  |  |  | 
16-bit Memory Half-Word | 
15 | 0
. . . . . . . . . .
Most-significant 16 bits are not written into memory
Writing a half-word result to address 104: The two memory bytes that should be written are at addresses 104 and 105. However, the 32-bit memory data bus is actually 4 bytes wide, corresponding to addresses 104, 105, 106, and 107. Each byte of the memory data bus has its own write enable; during the memory write cycle, the write-enable signals for addresses 106 and 107 are disabled so that only the bytes at addresses 104 and 105 are modified.
Review

## Slide 12: Store (to memory) Instructions
Load/Store Memory | Operation | Memory Byte Addresses Actually Written |  |  | 
STR rd,<mem> | rd  mem32[addr] | addr+3 | addr+2 | addr+1 | addr
STRB rd,<mem> | rd  mem8[addr] |  |  |  | addr
STRH rd,<mem> | rd  mem16[addr] |  |  | addr+1 | addr
STRD rt, rt2,<mem> | rt2.rt  mem64[addr] |  |  |  | 
Review
Notes: These instructions never affect flags in xPSR!

## Slide 13: LDR and STR
LDR | Load Word
LDRB | Load Byte
LDRH | Load Halfword
LDRSB | Load Signed Byte
LDRSH | Load Signed Halfword
STR | Store Word
STRB | Store Lower Byte
STRH | Store Lower Halfword
Review
Notes: Point out destination (reg) first for LDR, but destination (mem) last for STR. Different to Motorola, but it keeps the instruction mnemonic format consistent. Always have register loaded/stored first, then address accessed second
Size specifier comes out on MAS (memory access size) signal. Important that memory supports full range of accesses - especially important for writes where only the specified size should be written.
Special types of sign extended load - this is needed because ARM registers only hold 32-bit values. Draw diagram. No need for special store instructions though.
Instruction cycle timing:
STR LDR
7TDMI 2 cycles 3 cycles
9TDMI 1 cycle 1 cycle - interlock if used in next cycle
StrongARM1 1 cycle 1 cycle - interlock if used in next cycle
Xscale 1 cycle 1 cycle - interlock if used in next 2 cycles
Note size specifier comes after condition code.
Link: <address> explained on next slide.
Note that load/store instructions never set condition codes.

## Slide 14: Assume Little-Endianness
For the rest of the questions, assume Little-Endian ordering by default unless specified otherwise

## Slide 15: Question: Load a Byte, Half-word, Word
0x87
0x02000003
0x02000002
0x02000001
0x02000000
0xE1
0xE3
0x65
LDRB r1, [r0]
What does r1 contain: Load a Byte
0
31
LDRH r1, [r0]
What does r1 contain: Load a Halfword
0
31
LDR r1, [r0]
What does r1 contain: Load a Word
0
31
Little Endian
Assume
r0 = 0x02000000
r1
r1
r1
Use zero-filling for remaining Bytes

## Slide 16: Question: Sign Extension
0x87
0x20000003
0x20000002
0x20000001
0x20000000
0xE1
0xE3
0x65
LDRSB r1, [r0]
Load a Signed Byte. Sign-bit of 0xE1（11100001） is its leftmost bit (1),
so the left 3 Bytes of r1 are filled with all 1’s
0
31
LDRSH r1, [r0]
Load a Signed Halfword. Sign-bit of 0xE3E1
(1110001111100001） is its leftmost bit (1),so the left 3
Bytes of r1 are filled with all 1’s
0
31
Use sign-filling for remaining Bytes
Facilitate subsequent 32-bit signed arithmetic!
Little Endian
Assume
r0 = 0x02000000
r1
r1

## Slide 17: Address
Address accessed by LDR/STR is specified by a base register plus an offset
For word and unsigned byte accesses, offset can be
  An unsigned 12-bit immediate value (i.e. 0 - 4095 bytes). LDR r0,[r1,#8]
  A register, optionally shifted by an immediate value LDR r0,[r1,r2] LDR r0,[r1,r2,LSL#2]
This can be either added or subtracted from the base register: LDR r0,[r1,#-8] LDR r0,[r1,-r2] LDR r0,[r1,-r2,LSL#2]
For halfword and signed halfword / byte, offset can be:
  An unsigned 8 bit immediate value (i.e. 0-255 bytes).
  A register (unshifted).
Choice of pre-indexed or post-indexed addressing
Review
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 18: Addressing Modes
Offset addressing (most important):
  LDR R1,[R0] ;Load R1 from memory address R0
  LDR R1,[R0,#16] ;Load R1 from memory address R0+16
Auto-indexing with pre-indexed addressing mode:
  LDR R1,[R0,#16]! ;Load from memory address R0+16, then ;update R0 = R0+16
Auto-indexing with post-indexed addressing mode:
  LDR R1,[R0],#16 ;Load R0 from memory address R0, then
  ;update R0 = R0+16
Review
Notes: Program counter (PC)-relative addressing mode:
  LDR R0, [R15, #24] ;loads R0 with the word pointed at by PC+24

## Slide 19: Addressing Modes
Index Format | Example | Equivalent
offset | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Pre-index | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Post-index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4
Offset range is -255 to +255
Review
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 20: Question: LDR w/ Offset
What do r0 and r1 contain after: LDR r1, [r0, #4]
Offset range is -255 to +255

## Slide 21: Question: LDR w/ Post-index
What do r0 and r1 contain after: LDR r1, [r0], #4
Offset range is -255 to +255
Notes: “!” indicates “writeback” i.e. the base register is to be updated after the instruction.
No “!” for post-indexed because post-increment of base register always happens (otherwise the offset field would not be used at all).
Give C example:
int *ptr;
x = *ptr++;
Compiles to a single instruction:
LDR r0, [r1], #4

## Slide 22: Question: LDR w/ Pre-index
What do r0 and r1 contain after: LDR r1, [r0, #4]!
Offset range is -255 to +255
Notes: “!” indicates “writeback” i.e. the base register is to be updated after the instruction.
No “!” for post-indexed because post-increment of base register always happens (otherwise the offset field would not be used at all).
Give C example:
int *ptr;
x = *ptr++;
Compiles to a single instruction:
LDR r0, [r1], #4

## Slide 23: Question: LDRH
LDRH r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
?
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 24: Question: LDSB
What is r1 after: LDSB r1, [r0]
; r0 = 0x20008000
r1 before load
0x12345678
r1 after load
?
Memory Address | Memory Data
0x20008003 | 0x89
0x20008002 | 0xAB
0x20008001 | 0xCD
0x20008000 | 0xEF
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 25: Question: STR w/ Post-Index
What are r0, and memory content after: STR r1, [r0], #4
; r0 = 0x20008000, r1=0x76543210
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
r0 before store
0x20008000
r0 after store
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 26: Question: STR with Offset
What are r0, and memory content after: STR r1, [r0, #4]
; r0 = 0x20008000, r1=0x76543210
r0 before the store
0x20008000
r0 after the store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 27: Question: STR with Pre-Index
What are r0, and memory content after: STR r1, [r0, #4]!
; r0 = 0x20008000, r1=0x76543210
r0 before store
0x20008000
r0 after store
Memory Address | Memory Data
0x20008007 | 0x00
0x20008006 | 0x00
0x20008005 | 0x00
0x20008004 | 0x00
0x20008003 | 0x00
0x20008002 | 0x00
0x20008001 | 0x00
0x20008000 | 0x00
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 28: Question: LDR w/ Big Endian Ordering
LDR r11, [r0]
; r0 = 0x20008000
Memory Address | Memory Data
0x20008003 | 0xEE
0x20008002 | 0x8C
0x20008001 | 0x90
0x20008000 | 0xA7
r11 before load
0x12345678
r11 after load
?
What is r11 after load with Big-Endian ordering?
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 29: ARM ADR Pseudo-op
ADR pseudo-op generates instruction required to calculate address:
  ADR R1,x ;get memory address of variable x and put it in register R1
Review
Notes: Generate value by performing arithmetic on PC. Cannot refer to an address directly in an instruction.

## Slide 30: Example 1: Assignment
C:
  //assume x, a, b are 32-bit integer variables
  x = a - b;
Assembler:
ADR R4,a ; get address for a
LDR R0,[R4] ; get value of a
ADR R4,b ; get address for b, reusing R4
LDR R1,[R4] ; get value of b
SUB R0,R0,R1 ; subtract R1 from R0, and store result in R0
ADR R4,x ; get address for x
STR R0,[R4] ; store value of x into memory
Review
Notes: label1 ADR R4,c ; take memory address of variable c and put it ; into register R4
LDR R0,[R4] ; load content at memory address R4 into register ; R0
ADR R4,d
LDR R1,[R4]
SUB R0,R0,R1 ; subtract R1 from R0, and store result in R0 ; (R0 -= R1)

## Slide 31: Question: Programming
Q: Fill in the blanks of the following assembly program that implements the following C program snippet (assuming x, y and z are 32-bit ints):
  %Assembler Program
  ADR R4, x
  ...
  ADR R4, y
  ...
  ADR R4, z
  ...
  //C Program
  //assume x, y, z, are integer variables
  z=x+y;
  z=z2

## Slide 32: Question: Programming
Q: can you reduce the number of registers used in the assembler program?
  %Assembler Program
  ADR R4, x
  LDR R0, [R4]
  ADR R4, y
  LDR R1, [R4]
  ADD R2, R0, R1
  MUL R3, R2, R2
  ADR R4, z
  STR R3, [R4]
  //C Program
  //assume x, y, z, are integer variables
  z=x+y;
  z=z2