## Slide 1: L1 (CHAPTER 2) Data Representation Exercises
Acknowledgement: some slides taken from Yifeng Zhu’s courseware

## Slide 2: Question: Endianness
Q: Assume Big Endian ordering. If a 32-bit word resides at memory address N, what is the address of:
  (a) The MSB (Most Significant Byte)
  (b) The 16-bit half-word corresponding to the most significant half of the word
Q: Redo the question assuming Little Endian ordering.
MSB
LSB
Big-Endian
N
N+1
N+2
N+3
LSB
MSB
Little-Endian
N
N+1
N+2
N+3

## Slide 3: Question: Endianness
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
What are the memory address of these four words?
Word 3
Word 2
Word 1
Word 0

## Slide 4: Question: Endianness
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
?
The word stored at address 0x20008000
with Big-Endian ordering is
?
The word stored at address 0x20008000
with Little-Endian ordering is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 5: Data Alignment
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand:
Review

## Slide 6: Question: Data Alignment
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each).
  (a) What is the address of the most significant byte of the word at address 102, , assuming Little-Endian ordering?
  (b) What is the address of the most significant byte of the word at address 102, , assuming Little-Endian ordering?
  (b) How many memory cycles are required to read the word at address 102?
  (c) How many memory cycles are required to read the half word at address 102?

## Slide 7: Question: Data Alignment
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each). How many memory cycles are required to read each of the following from memory?
  (a) A 2-Byte operand read from decimal address 5
  (b) A 2-Byte operand read from decimal address 15
  (c) A 4-Byte operand read from decimal address 10
  (d) A 4-Byte operand read from decimal address 20

## Slide 8: Question: Memory Cycles
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide.
  It takes ____ memory cycle(s) to read a Byte from memory
  It takes ____ memory cycle(s) to read a half-word from memory
  It takes ____ memory cycle(s) to read a word from memory
  It takes ____ memory cycle(s) to read a double word from memory

## Slide 9: Question: Arrays
Q: If the first element of a one-dimensional array x[] is located in memory at address 0x12345678, what will be the address of the second element if the array x[] contains
  (a) chars
  (b) shorts
  (c) ints
  (c) longs

## Slide 14: Decimal, Binary and Hex
Decimal | Binary | Hex
0 | 0000 | 0x0
1 | 0001 | 0x1
2 | 0010 | 0x2
3 | 0011 | 0x3
4 | 0100 | 0x4
5 | 0101 | 0x5
6 | 0110 | 0x6
7 | 0111 | 0x7
8 | 1000 | 0x8
9 | 1001 | 0x9
10 | 1010 | 0xA
11 | 1011 | 0xB
12 | 1100 | 0xC
13 | 1101 | 0xD
14 | 1110 | 0xE
15 | 1111 | 0xF
Prefix 0x denotes hex
Review

## Slide 15: Question: Number Conversion
Q: Convert 0x3A56E2F8 into binary
Q: Convert binary number 0011 1010 into hex
0x3A
Decimal | Binary | Hex
0 | 0000 | 0x0
1 | 0001 | 0x1
2 | 0010 | 0x2
3 | 0011 | 0x3
4 | 0100 | 0x4
5 | 0101 | 0x5
6 | 0110 | 0x6
7 | 0111 | 0x7
8 | 1000 | 0x8
9 | 1001 | 0x9
10 | 1010 | 0xA
11 | 1011 | 0xB
12 | 1100 | 0xC
13 | 1101 | 0xD
14 | 1110 | 0xE
15 | 1111 | 0xF

## Slide 16: Adding two integers
-9
6
-3
01001
10110
10111
flip
+1
9
-9
00010
00011
flip
+1
3
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1
Hardware Adder
23
6
29
+
Two’s Complement Counterpart
Same bit patterns, different interpretation.
  Unsigned addition: 23+6=29
  Signed addition: -9+6=-3
This example shows that the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers.
Review
Notes: {{Pause=1}} We will use a very simple example to show that, the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers. {{Pause=0.5}}
Suppose we are adding negative nine and six. {{Pause=0.5}} These two signed numbers are represented in two’s complement in computers. {{Pause=0.5}}
Specifically, we can obtain the two’s complement representation of negative nine by flipping all bits and adding one. {{Pause=0.5}} The two’s complement of a positive number is itself. {{Pause=0.5}}
Let’s see what will happen if the hardware treats these two inputs as unsigned numbers. If these binary bits represent unsigned numbers, they are 23 and 6, respectively. Therefore, the hardware adds 23 and 6, and produces 29, in decimal, {{Pause=0.3}} or one, one, one, zero, one, in binary. {{Pause=0.5}}
If the output represents a signed integer in two’s complement, it actually represents negative 3. This can be proved by inverting all the bits and adding one. The result, negative three, is exactly the sum of the original signed inputs. {{Pause=0.5}}
This example shows that, without any modification, the hardware adder designed for adding unsigned numbers, works correctly for adding signed numbers.

## Slide 17: Signed Integers Method 3: Two’s Complement
Two’s Complement ():
TC of a number can be obtained by its bitwise NOT plus one.
 | Binary | Decimal
Original number | 00011 | 3
Step 1: Invert every bit | 11100 | 
Step 2: Add 1 | + 00001 | 
Two’s complement | 11101 | -3
Example 1: TC(3)
Review

## Slide 18: Signed Integer Representation Overview
Three ways to represent signed binary integers:
  Signed magnitude
  One’s complement ()
  Two’s complement ()
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero | Two zeroes () | Two zeroes () | One zero
Unique Numbers |  |  | 
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero |  |  | One zero
Unique Numbers |  |  | 
Review

## Slide 19: Question: 2’s Complement
For each of the following binary numbers in a 8-bit system, give the corresponding binary number of the negative of its value, for 2’s-complement system
(a) x=01010101
  TC(x)=10101011
(b) x=10101010
  TC(x)=01010110
(c) x=10000000
  TC(x)=10000000

## Slide 20: Question: Number Conversion
Q: What is the decimal value of binary number x=10100111 as either unsigned int, or signed int in 2’s complement representation?
  Unsigned int: 2^7+2^5+2^2+2^1+2^0= 167
  Signed int: 10100111=-89 flip 01011000 add 1 01011001=89
  01011001 flip 10100110 add1 10100111
What about x=11100001?
  Unsigned int: 225 = 2^7+2^6+2^5+2^0=
  Signed int: 00011110 + 1 = 00011111 = 31 so 11100001 = -31
What about x=10000000?
  Unsigned int: 128
  Signed int:-128

## Slide 21: Question: Number Conversion
Q: Which number is larger: 1001 or 0011 in binary?
  If unsigned int: 1001
  If signed int: 1001=-7 0011=3
  0111 = 7
Q: Which number is larger: 0xFFFFFFFF or 0x00000001 in hex?
  If unsigned int: 0xFFFFFFFF=2^32 – 1 0x00000001=1
  If signed int: 0xFFFFFFFF= 111111111111111111111 =-1
  invert: 0x00000000 add1: 0x00000001
  0x00000001=1

## Slide 22: Question: Number Range
Which range of decimals can be expressed with a 6-bit signed number (assuming Two’s complement representation)?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 23: Question: Number Range
Which range of decimals can be expressed with a 6-bit unsigned integer?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 24: Question: Integer arithmetic
Q: Consider a 4-bit system. What is the result of 1001 + 0011?
  1001 + 0011 = 1100
  Unsigned: 9+3=12
  Signed:-7+3=-4

## Slide 25: Summary of Carry and Overflow Flags
25
Carry flag C = 1 upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Bit | Name | Meaning after add or sub
N | negative | result is negative
Z | zero | result is zero
V | overflow | signed overflow
C | carry | unsigned overflow
31
0
N
Z
C
V
CPSR (Current Program Status Register)
Review
Notes: C is cleared upon an unsigned subtract if the answer is wrong

## Slide 26: Signed or unsigned
Whether the carry flag or the overflow flag should be used depends on the programmer’s intention.
uint a;
uint b;
…
c = a + b
…
C Program
Check the carry flag
for unsigned addition
int a;
int b;
…
c = a + b
…
C Program
Check the overflow flag
for signed addition
Review

## Slide 27: Question: Addition
Q: Consider a 4-bit system. What is the result of addition 1011+0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？
    Unsigned: 8+2+1=11 11+6=17, result 0001 = 1, Carry=1
    Signed: 1011=-5 -5+6=1, result 0001 = 1, overflow=0
  1011
  0110
  10001

## Slide 28: Question: Subtraction
Q: Q: Consider a 4-bit system. What is the result of subtraction 1011-0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？
    Unsigned: 11-6=5
    Signed: -5-6=-11 0101=5, overflow=1
1011
-0110
=0101

## Slide 29: Question: Subtraction
Q: Consider a 4-bit system. What is the result of subtraction 0110-1011, assuming either unsigned integers, or signed integers in 2’s-complement representation？
  Unsigned int: 6-11=11 carry=0 borrow=1
  Signed int 6-(-5)=-5 overflow=1
0110-1011=1011

## Slide 30: Question: True or False
1. Borrow is impossible when subtracting one unsigned number from another.
2. Overflow is impossible when subtracting two signed operands of the same sign.
3. There are two representations of zero in 2’s complement representation.
4. In 2’s complement, the absolute values of full-scale negative and full-scale positive are identical