## Slide 1: Dr. Yifeng Zhu
Volatile Qualifier in C
Embedded Systems with ARM Cortex-M
Microcontrollers in Assembly Language and C

## Slide 2: Compiler
Compiler can make aggressive optimization
  Cache results in register to reduce memory accesses
  Reorder computations
  Eliminate useless and redundant computations
C programs
Binary executable
01001
10101
11100
01011
Compiler
Performance, Performance, Performance!

## Slide 3
int flag = 0;
void SysTick_Handler(void){
flag = 1;
// Turn on the green LED
GPIOE->ODR |= GPIO_ODR_ODR_8;
}
int main(void){
GPIO_init();
SysTick_init();
while(flag == 0);
// Turn on the red LED
GPIOB->ODR |= GPIO_ODR_ODR_2;
while(1);
}
...
LDR r0, =flag ; Get memory address
LDR r1, [r0] ; Read memory
loop CMP r1, #0
BEQ loop
...
...
LDR r0, =flag ; Get memory address
loop LDR r1, [r0] ; Read memory
CMP r1, #0
BEQ loop
...
Without optimization
With optimization
A dead loop since flag was 0. Thus, the program is blocked here and failed to turn on the red LED.

## Slide 4
volatile int flag = 0;
void SysTick_Handler(void){
flag = 1;
// Turn on the green LED
GPIOE->ODR |= GPIO_ODR_ODR_8;
}
int main(void){
GPIO_init();
SysTick_init();
while(flag == 0);
// Turn on the red LED
GPIOB->ODR |= GPIO_ODR_ODR_2;
while(1);
}
...
LDR r0, =flag ; Get memory address
loop LDR r1, [r0] ; Read memory
CMP r1, #0
BEQ loop
...
With/without optimization
Solution

## Slide 5: Volatile variables
Qualifier volatile tells the compiler that this value may change at any time
  Do not apply any optimizations to remove reads or writes to these variables
Example:
volatile int x;
y = x + x + x + x;
y = 4 * x;
y = x << 2;
Compiler cannot optimize it as:
or
variable x
Memory
registers
ALU
CPU
This value may change any time.
The computation cannot complete within a single clock cycle and x can change any time.

## Slide 6: Volatile variables
Qualifier volatile tells the compiler that this value may change at any time
  Do not apply any optimizations to remove reads or writes to these variables
Memory
registers
ALU
CPU
A memory value may be changed anytime by hardware.
Input data registers:
GPIOB->IDR
SPI1->DR
USART1->DR
Status registers:
USART1->SR
Notes: Inform compiler that a variable may be changed by hardware, the kernel, another thread etc.

## Slide 7: Volatile variables
Qualifier volatile tells the compiler that this value may change at any time
  Do not apply any optimizations to remove reads or writes to these variables
Memory
registers
ALU
CPU
This value may be changed anytime by software.
Interrupt handlers
Another thread (with OS or RTOS)
Notes: Inform compiler that a variable may be changed by hardware, the kernel, another thread etc.

## Slide 8: Three Common Usages of volatile
ODR
BSRR
LCKR
MODER
OTYPER
OSPEEDR
PUPDR
AFR[0]
AFR[1]
BRR
ASCR
0x48000000
0x48000004
0x48000008
0x4800000C
0x48000010
0x48000014
0x48000018
0x4800001C
0x48000020
0x48000024
0x48000028
0x4800002C
IDR
#define GPIOA_IDR (*((uint32_t volatile *) 0x48000010))
GPIOA Peripheral Registers
void main(void){
...
// Read the input on pin 2
Pin2 = GPIOA_IDR >> 2;
...
}
Use volatile on accessing memory-mapped I/O registers

## Slide 9: Three Common Usages of volatile
Use volatile on accessing memory-mapped I/O registers
Use volatile on global variables accessed in interrupt service routines
Use volatile on global variables shared between multi-thread tasks
volatile uint32_t counter;
void SysTick_Handler(void){
counter++;
}
Notes: #define GPIOA_IDR ((uint32_t volatile *) 0x48000010)

## Slide 10: Summary
Volatile forces compiler to generate executable that performs actual memory reads and writes, instead of caching values in registers!
Read volatile variable X in C
LDR r0, =x
LDR r1, [r0]
Write to volatile variable X in C
LDR r0, =x
STR r1, [r0]

## Slide 11
“I hear and I forget.
I see and I remember.
I do and I understand.”
Confucius (Chinese philosopher, 551–479 BC)
Book Website:
web.eece.maine.edu/~zhu/book
Notes: Thank you for watching. Please visit the book website for more examples and tutorials. See you next time.

## Slide 12: Syntax of volatile keyword
Declare a variable volatile
volatile int x;
int volatile y;

## Slide 13: Pointers
int* pi;
int volatile* pvi;
int* volatile vpi;
int volatile* volatile vpvi;
Trick: Read from left to right
Notes: The devil is in the details.

## Slide 14: Pointers
A pointer to an int
int* pi;
A pointer to a volatile int
int volatile* pvi;
A volatile pointer to an int
int* volatile vpi;
A volatile pointer to a volatile int
int volatile* volatile vpvi;
Notes: The devil is in the details.