## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 17
Liquid-Crystal Display (LCD)

## Slide 2: HD44780 Connection Diagram (8-bit data bus)
Read/Write (RW) connects to the ground if processor does not read data from LCD
LED+ and LED- pins provide 5V voltage for backlights.
Enable (E) pin provides clock signal
Register Select (RS)
  RS = 0: data on the data bus is a command
  RS = 1: data on the data bus is actual data.

## Slide 3: HD44780 Connection Diagram (8-bit data bus)
Saves four pins for the processor
For each 8-bit data, transfer the upper 4 bits first and then the lower 4 bits.

## Slide 4: HD44780 Controller: Internal Diagram

## Slide 5: Clock Signal
On the falling edge of E (Enable), data are latched into the data or command register
  RS = 0: command; RS = 1: data
E is a data transmission clock signal provided by the processor
A nibble = 4 bits
For each byte, the upper nibble is sent out first.

## Slide 6: Generating Clock Signal
void LCD_Pulse(void) { LCD_Port->ODR ¦= 1<<LCD_EN; // Set E high Delay(4); // Delay 40us LCD_Port->ODR &= ~(1<<LCD_EN); // Set E low Delay(4); // Delay 40us }

## Slide 7: Example Signals
Sending “hello”

## Slide 8: Sending Command and Data
Sending Command to LCD | Sending Data to LCD
void LCD_SendCmd(uint8_t c) { // RS: 0 = command, 1 = data LCD_Port->ODR &= ~(1<<LCD_RS); // Send Upper 4 bits LCD_PutNibble( c >> 4 ); LCD_Pulse(); // Send Lower 4 bits LCD_PutNibble( c & 0xF ); LCD_Pulse(); // Return to default LCD_Port->ODR ¦= 1<<LCD_RS; } | void LCD_SendData(uint8_t c) { // RS defaults to 1 // Send Upper 4 bits LCD_PutNibble( c >> 4 ); LCD_Pulse(); // Send Lower 4 bits LCD_PutNibble( c & 0xF ); LCD_Pulse(); }

## Slide 9: Command Format
 | RS | RW | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 | 
LCD Commands | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | Clear screen and set DDRAM address to 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | - | Return home (set DDRAM address to 0)
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | I/D | S | Entry mode set
 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | D | C | B | Control on/off of display, cursor, and blink
 | 0 | 0 | 0 | 0 | 0 | 1 | SC | RL | - | - | Cursor/display shift
 | 0 | 0 | 0 | 0 | 0 | DL | N | F | - | - | Set of data length, lines, and font type
 | 0 | 0 | 0 | 1 | A5 | A4 | A3 | A2 | A1 | A0 | Set code generator CG-RAM address A5-A0
 | 0 | 0 | 1 | A6 | A5 | A4 | A3 | A2 | A1 | A0 | Set display memory DDRAM address A6-A0
 | 0 | 1 | BF | A6 | A5 | A4 | A3 | A2 | A1 | A0 | Ready busy flag (BF) and address A6-A0
 | 1 | 0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Write data D7-D0 to DDRAM or CG-RAM
 | 1 | 1 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Read data D7-D0 from DDRAM or CG-RAM

## Slide 10: LCD Initialization

## Slide 11: Customized Font
Smiling Face
// Select CGRAM and set address to 0x00
LCD_SendCmd(0x40 + 0x00);
Delay(4); // Wait > 39us
// Define smile face
LCD_SendData(0x00); // 1st row byte
LCD_SendData(0x0A); // 2nd row byte
LCD_SendData(0x0A); // 3rd row byte
LCD_SendData(0x0A); // 4th row byte
LCD_SendData(0x00); // 5th row byte
LCD_SendData(0x11); // 6th row byte
LCD_SendData(0x0E); // 7th row byte
LCD_SendData(0x00); // 8th row byte
// Select display RAM & set address to 0
LCD_SendCmd(0x80); // First character
Delay(4); // Wait > 39us
LCD_SendData(0x00); // Display the font