## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 22
USB: Universal Serial Bus

## Slide 2: USB Layers

## Slide 3: USB Connection
Four shielded wires: two for power (+5V, ground), two for data (D+, D-)
D+ and D- are twisted to cancel external electromagnetic interference
Standard A
Standard B
Image from wiki.com

## Slide 4: USB Speed Identification
USB supports four transmission speeds:
  low speed (1.5 Mbit/s = 187 KB/s)
  full speed (12 Mbit/s = 1.5 MB/s)
  high speed (480 Mbit/s = 60 MB/s)
  super speed (4.8 Gbit/s = 600 MB/s)
Full-speed mode (12 Mbits/s) identified by 1.5KΩ pull-up on D+
Low-speed mode (1.5Mbits/s) identified by 1.5KΩ pull-up on D-

## Slide 5: Non-Return-to-Zero Inverted (NRZI)
Logic 0: represented by a transition of the voltage level
Logic 1: represented by no transition

## Slide 6: Interface

## Slide 7: USB Descriptors

## Slide 8
Field Name | Size | Offset
bLength | 1 | 0
bDescriptorType | 1 | 1
bInterfaceNumber | 1 | 2
bAlternateSetting | 1 | 3
bNumEndpoints | 1 | 4
bInterfaceClass | 1 | 5
bInterfaceSubClass | 1 | 6
bInterfaceProtocol | 1 | 7
iInterface | 1 | 8
Field Name | Size | Offset
bLength | 1 | 0
bDescriptorType | 1 | 1
bEndpointAddress | 1 | 2
bmAttributes | 1 | 3
wMaxPacketSize | 2 | 4
bInterval | 1 | 6
Field Name | Size | Offset
bLength | 1 | 0
bDescriptorType | 1 | 1
wTotalLenght | 2 | 2
bNumInterfaces | 1 | 4
bConfigurationValue | 1 | 5
iConfiguration | 1 | 6
bmAttributes | 1 | 7
bMaxPower | 1 | 8
Field Name | Size | Offset
bLength | 1 | 0
bDescriptorType | 1 | 1
bcdUSB | 2 | 2
bDeviceClass | 1 | 4
bDeviceSubClass | 1 | 5
bDeviceProtocol | 1 | 6
bMaxPacketSize | 1 | 7
idVendor | 2 | 8
idProduct | 2 | 10
bcdDevice | 2 | 12
iManufacturer | 1 | 14
iProduct | 1 | 15
iSerialNumber | 1 | 16
bNumConfigurations | 1 | 17
Device descriptor
Configuration descriptor
Interface descriptor
Endpoint descriptor

## Slide 9: USB Enumeration
Detecting a device has been connected. When a USB device is plugged into a host, there is a change on the USB D+ or D- line since one of them is pulled up by the device.
Determining the USB speed. As introduced previously, pulling up D- via 1.5KΩ pull-up to 3V indicates a low-speed device. The same pull-up on D+ specifies a high-speed device.
Retrieving the device descriptor and determining what device is attached.
Retrieving all configuration descriptors. This process may take milliseconds to complete. The host selects one configuration.
Retrieving all interface descriptors.
Loading the corresponding device driver. This is typically handled by the operating systems on the host. The host typically uses idVendor and idProduct to match a driver.

## Slide 10: USB Enumeration
Format of Setup Request

## Slide 12: Human Interface Device

## Slide 13: GET HID Descriptor

## Slide 14: HID Report Format of Keyboard

## Slide 15: HID Report Format of Mouse