## Slide 1: L1 (CHAPTER 2) Data Representation
Acknowledgement: some slides taken from Yifeng Zhu’s courseware

## Slide 2: Bit, Byte, Half-word, Word, Double-Word

## Slide 3: Decimal, Binary and Hex
Decimal | Binary | Hex
0 | 0000 | 0x0
1 | 0001 | 0x1
2 | 0010 | 0x2
3 | 0011 | 0x3
4 | 0100 | 0x4
5 | 0101 | 0x5
6 | 0110 | 0x6
7 | 0111 | 0x7
8 | 1000 | 0x8
9 | 1001 | 0x9
10 | 1010 | 0xA
11 | 1011 | 0xB
12 | 1100 | 0xC
13 | 1101 | 0xD
14 | 1110 | 0xE
15 | 1111 | 0xF
Prefix 0x denotes hex

## Slide 4: Unsigned Integers
Convert from Binary to Decimal:
Five-bit binary code

## Slide 5: Unsigned Integers
Convert Decimal to Binary
5210 = 1101002
Example 1
3210 = 1000002
Example 2

## Slide 6: Carry/borrow flag bit for unsigned arithmetic
When adding two unsigned numbers in an n-bit system, a carry occurs if the result is larger than the maximum unsigned integer that can be represented (i.e. ).
When subtracting two unsigned numbers, borrow occurs if the result is negative, smaller than the smallest unsigned integer that can be represented (i.e. 0).
On ARM Cortex-M3 processors, the carry flag and the borrow flag are physically the same flag bit in the CPSR (Current Program Status Register).
  Carry = NOT Borrow

## Slide 7: Carry/borrow flag bit for unsigned arithmetic
For 5-bit system, a carry occurs when adding 28 and 6
If result of addition crosses the boundary between 0 and , the carry flag is set.
Carry flag = 1, since true result .
Notes: For unsigned numbers, the carry flag is set when adding two numbers and the result is larger than the maximum that can represented. For subtraction, the borrow bit is set when the result is positive, representing no borrowing occurs. The borrow bit is cleared when the result is negative. On the ARM processor, the carry bit and borrow bit are the same flag bit in the status register.

## Slide 8: Carry/borrow flag bit for unsigned arithmetic
For 5-bit system, a borrow occurs when subtracting 5 from 3.
If result of subtraction crosses the boundary between 0 and , the borrow flag is set.
Carry flag = 0 (Borrow flag = 1), since true result .
Notes: For unsigned numbers, the carry flag is set when adding two numbers and the result is larger than the maximum that can represented. For subtraction, the borrow bit is set when the result is positive, representing no borrowing occurs. The borrow bit is cleared when the result is negative. On the ARM processor, the carry bit and borrow bit are the same flag bit in the status register.
For subtraction, carry = NOT borrow.

## Slide 9: Signed Integer Representation Overview
Three ways to represent signed binary integers:
  Signed magnitude
  One’s complement ()
  Two’s complement ()
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero | Two zeroes () | Two zeroes () | One zero
Unique Numbers |  |  | 
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero |  |  | One zero
Unique Numbers |  |  | 

## Slide 10: Signed Integers Method 1: Signed magnitude
Example: in a 5-bit system
  +710 = 001112
  -710 = 101112
Two ways to represent zero
  +010 = 000002
  -010 = 100002
Not used in modern systems
  Hardware complexity
  Two zeros
Sign-and-Magnitude:
The most significant bit is the sign.
The rest bits are magnitude.

## Slide 11: Signed Integers Method 2: One’s Complement
One’s Complement ():
Example: in a 5-bit system
  +710 = 001112
  -710 = 110002
The one's complement representation of a negative binary number is the bitwise NOT of its positive counterpart.
  +710 + (-710) = 001112 + 110002
  = 111112
  = 25 - 1

## Slide 12: Signed Integers Method 3: Two’s Complement
Two’s Complement ():
TC of a number can be obtained by its bitwise NOT plus one.
 | Binary | Decimal
Original number | 00011 | 3
Step 1: Invert every bit | 11100 | 
Step 2: Add 1 | + 00001 | 
Two’s complement | 11101 | -3
Example 1: TC(3)

## Slide 13: Signed Integers Method 3: Two’s Complement
Two’s Complement (TC)
TC of a number can be obtained by its bitwise NOT plus one.
Example 2: TC(-3)
 | Binary | Decimal
Original number | 11101 | -3
Step 1: Invert every bit | 00010 | 
Step 2: Add 1 | + 00001 | 
Two’s complement | 00011 | 3

## Slide 14: Signed Integers Method 3: Two’s Complement
Two’s Complement (TC)
TC of a number can be obtained by its bitwise NOT plus one.
Example 2: TC(-16)
 | Binary | Decimal
Original number | 10000 | -16
Step 1: Invert every bit | 01111 | 
Step 2: Add 1 | + 10000 | 
Two’s complement | 10000 | -16
Negation of -16 in 5-bit two's complement wraps back to itself, meaning the most negative number's two's complement is itself. (Number range is [-16, 15], so 16 is out of range)

## Slide 15: Quiz
Calculate TC(-6) for 6-bit system
For a 6-bit two's complement number: the range of representable integers is from −32 to +31.
−16 in 6-bit two's complement is 110000
  Write 16 in binary: 010000
  Take the two's complement (invert bits and add 1):
  Invert bits: 101111, Add 1: 101111+1=110000
To take the negation of this (i.e., find the two's complement of 110000):
  Invert bits: 001111, Add 1: 001111+1=010000
  This is 16 in binary, so the negation of −16 is +16 as expected.
Unlike the 5-bit case where −16 is the minimum and its negation wraps onto itself, in 6 bits −16 behaves normally with correct negation.
Notes: For a 6-bit two's complement number:
The range of representable integers is from to .
To represent in 6 bits:
  Write in binary:
  Take the two's complement (invert bits and add 1):
    Invert bits:
    Add 1:
So, in 6-bit two's complement is .
To take the negation of this (i.e., find the two's complement of ):
Invert bits:
Add 1:
This is in binary, so the negation of is as expected.
Unlike the 5-bit case where is the minimum and its negation wraps onto itself, in 6 bits behaves normally with correct negation.
For a 6-bit two's complement number:
The range of representable integers is from −32 to +31.
To represent −16 in 6 bits:
  Write 16 in binary: 010000
  Take the two's complement (invert bits and add 1):
    Invert bits: 101111
    Add 1: 101111+1=110000
So, −16 in 6-bit two's complement is 110000.
To take the negation of this (i.e., find the two's complement of 110000):
Invert bits: 001111
Add 1: 001111+1=010000
This is 16 in binary, so the negation of −16 is +16 as expected.
Unlike the 5-bit case where −16 is the minimum and its negation wraps onto itself, in 6 bits −16 behaves normally with correct negation.

## Slide 16: Comparison: different signed reps
One’s complement representation
Range [-15,15]
Negative = invert all bits of a positive
Two’s Complement representation
Range [-16,15]
TC = invert all bits, then plus 1
Signed magnitude representation
Range [-15,15]
0 = positive
1 = negative

## Slide 17: Comparison: unsigned vs. signed
Unsigned int representation
Range [0, 31]
Two’s Complement representation
Range [-16,15]
TC = invert all bits, then plus 1

## Slide 18: Unsigned vs. Signed (TC)
 | Unsigned | Two’s Complement Signed
Range |  | 
Zero | One zero | One zero
Unique Numbers |  | 
 | Unsigned | Two’s Complement Signed
Range |  | 
Zero | One zero | One zero
Unique Numbers |  | 

## Slide 19: Two’s Complement for 8-bit System
8-bit signed Int (Two’s Complement) | 8-bit unsigned Int | Binary
-128 | 128 | 1000 0000
-127 | 129 | 1000 0001
… | … | …
-2 | 254 | 1111 1110
-1 | 255 | 1111 1111
0 | 0 | 0000 0000
1 | 1 | 0000 0001
… | … | ...
127 | 127 | 0111 1111
Note: Most significant bit (MSB) equals sign for signed int
15

## Slide 20: Sign Extension
Assignment differs for signed (above table) and unsigned numbers
  Compiler knows (from type declaration)
  Different assembly instructions for copying signed/unsigned data
Decimal | Binary |  | 
 | 4-bit | 8-bit | 32-bit
3ten | 0011two | 0000 0011two | 0000 0000 0000 0011two
-3ten | 1101two | 1111 1101two | 1111 1111 1111 1101two

## Slide 21: Overflow flag for signed arithmetic
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. ) or smaller than the minimum signed integer (i.e. ) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?

## Slide 22: Overflow flag for signed arithmetic
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign. Proof:
  A n-bit signed int has the range [-2n-1, 2n-1-1].
  2 operands with different signs: positive one in the range of [0, 2n-1-1], negative one in the range of [-2n-1, -1]. So the range of their sum must be [0-2n-1, 2n-1-1+(-1)]=[-2n-1, 2n-1-2] Î[-2n-1, 2n-1-1]
  2 operands with the same sign: if both are positive and in the range of [0, 2n-1-1], then the range of their difference must be [0-(2n-1-1), 2n-1-1-0]=[-(2n-1-1), 2n-1-1]; if both are negative and in the range of [-2n-1, -1], then the range of their difference must be [-2n-1-(-1), -1-(-2n-1)]=[-2n-1+1, 2n-1-1] Î [-2n-1, 2n-1-1]

## Slide 23: Overflow bit flag for signed arithmetic
An overflow occurs when adding two positive numbers and getting a negative result.
Overflow flag = 1, since true result .
Notes: For signed numbers represented in two’s complement, an overflow occurs only in two scenarios:
Add two positive numbers and get a negative result
Add two negative numbers and get a positive result

## Slide 24: Overflow bit flag for signed arithmetic
An overflow occurs when adding two negative numbers and getting a positive result.
Overflow flag = 1, since true result .
Notes: For signed numbers represented in two’s complement, an overflow occurs only in two scenarios:
Add two positive numbers and get a negative result
Add two negative numbers and get a positive result
C is cleared upon an unsigned subtract if the answer is wrong

## Slide 25: Carry and Overflow Flags in CPSR
25
Bit | Name | Meaning after add or sub
N | negative | result is negative
Z | zero | result is zero
V | overflow | signed overflow
C | carry | unsigned overflow
31
0
N
Z
C
V
CPSR (Current Program Status Register)
Notes: C is cleared upon an unsigned subtract if the answer is wrong

## Slide 26: Summary of Carry and Overflow Flags
26
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 | true result < 0  Carry flag=0 | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1  Overflow flag=1
Notes: C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 27: Signed or unsigned
Whether the carry flag or the overflow flag should be used depends on the programmer’s intention.
uint a;
uint b;
…
c = a+/-b
…
C Program
Check the carry/borrow
Flag for unsigned addition/
subtraction
int a;
int b;
…
c = a+/-b
…
C Program
Check the overflow flag
for signed addition/subtraction

## Slide 28: Signed or Unsigned
CPU does not know; it sets up both the carry flag and the overflow flag.
It is software’s (programmer/compiler) responsibility to interpret the flags.
  The C compiler uses either the carry or the overflow flag based on how this integer is declared in source code ( “uint” or “int”).
a = 0b10000
b = 0b10000
c = a + b
Are a and b signed or unsigned numbers?

## Slide 29: Signed or Unsigned
If unsigned:
uint a, b;
a = 16
b = 16
c = a + b
= 32 > 25-1
Carry flag set
a = 0b10000
b = 0b10000
c = a + b
Are a and b signed or unsigned numbers?
If signed:
int a, b;
a = -16
b = -16
c = a + b
= -32 < -24
Overflow flag set

## Slide 30: Why use Two’s Complement
Operation | Are signed and unsigned operations the same?
Addition | Yes
Subtraction | Yes
Multiplication | Yes if the product has the same number of bits as operands (not discussed in class)
Division | No (not discussed in class)
Two’s complement representation simplifies hardware
Notes: Why do we use two’s complement? {{Pause=0.5}} One of the advantages is that two’s complement can simplify the hardware implementation of arithmetic functions. If signed integers are represented in two’s complement, the hardware can ignore the sign of operands for addition or subtraction. If the product is required to keep the same number of bits as operands, the multiplication hardware can also ignore the sign of operands. This property of two’s complement simplifies the hardware design for addition, subtraction and multiplication. Note that this property does not hold true for division.

## Slide 31: Adding two integers
-9
6
-3
01001
10110
10111
flip
+1
9
-9
00010
00011
flip
+1
3
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1
Hardware Adder
23
6
29
+
Two’s Complement Counterpart
Same bit patterns, different interpretation.
  Unsigned addition: 23+6=29
  Signed addition: -9+6=-3
This example shows that the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers.
Notes: {{Pause=1}} We will use a very simple example to show that, the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers. {{Pause=0.5}}
Suppose we are adding negative nine and six. {{Pause=0.5}} These two signed numbers are represented in two’s complement in computers. {{Pause=0.5}}
Specifically, we can obtain the two’s complement representation of negative nine by flipping all bits and adding one. {{Pause=0.5}} The two’s complement of a positive number is itself. {{Pause=0.5}}
Let’s see what will happen if the hardware treats these two inputs as unsigned numbers. If these binary bits represent unsigned numbers, they are 23 and 6, respectively. Therefore, the hardware adds 23 and 6, and produces 29, in decimal, {{Pause=0.3}} or one, one, one, zero, one, in binary. {{Pause=0.5}}
If the output represents a signed integer in two’s complement, it actually represents negative 3. This can be proved by inverting all the bits and adding one. The result, negative three, is exactly the sum of the original signed inputs. {{Pause=0.5}}
This example shows that, without any modification, the hardware adder designed for adding unsigned numbers, works correctly for adding signed numbers.

## Slide 32: Subtracting two signed integers: (-9) - 6
-9
6
-15
01001
10110
10111
flip
+1
9
-9
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
Hardware Subtractor
23
6
17
-
01111
10000
10001
flip
+1
15
-15
1 | 0 | 0 | 0 | 1
Same bit patterns, different interpretation.
  Unsigned addition: 23-6=17
  Signed addition: -9+6=-15
This example shows that the hardware subtractor for subtracting unsigned numbers, also works correctly for subtracting signed numbers.
Notes: {{Pause=1}} Similarly, the same subtraction hardware works correctly for both signed and unsigned subtraction, even though the sign of input operands is not examined. {{Pause=0.3}} This example subtracts 6 from negative 9. The hardware ignores the sign of the inputs, and subtracts 6 from 23. The result is 17, in decimal, {{Pause=0.3}} or one, zero, zero, zero, one, in binary. If the result represents a signed integer in two’s complement, then the result is negative 15. This is exactly the result of subtracting the original signed integers.

## Slide 33: Two’s Complement Simplifies Hardware Implementation
In two’s complement, the same hardware works correctly for both signed and unsigned addition/subtraction.
If the product has the same number of bits as operands, the same hardware works correctly for both signed and unsigned multiplication.
However, this is not true for division.

## Slide 34: ASCII
Dec | Hex | Char | Dec | Hex | Char | Dec | Hex | Char | Dec | Hex | Char
0 | 00 | NUL | 32 | 20 | SP | 64 | 40 | @ | 96 | 60 | ‘
1 | 01 | SOH | 33 | 21 | ! | 65 | 41 | A | 97 | 61 | a
2 | 02 | STX | 34 | 22 | " | 66 | 42 | B | 98 | 62 | b
3 | 03 | ETX | 35 | 23 | # | 67 | 43 | C | 99 | 63 | c
4 | 04 | EOT | 36 | 24 | $ | 68 | 44 | D | 100 | 64 | d
5 | 05 | ENQ | 37 | 25 | % | 69 | 45 | E | 101 | 65 | e
6 | 06 | ACK | 38 | 26 | & | 70 | 46 | F | 102 | 66 | f
7 | 07 | BEL | 39 | 27 | ’ | 71 | 47 | G | 103 | 67 | g
8 | 08 | BS | 40 | 28 | ( | 72 | 48 | H | 104 | 68 | h
9 | 09 | HT | 41 | 29 | ) | 73 | 49 | I | 105 | 69 | i
10 | 0A | LF | 42 | 2A | * | 74 | 4A | J | 106 | 6A | j
11 | 0B | VT | 43 | 2B | + | 75 | 4B | K | 107 | 6B | k
12 | 0C | FF | 44 | 2C | , | 76 | 4C | L | 108 | 6C | l
13 | 0D | CR | 45 | 2D | - | 77 | 4D | M | 109 | 6D | m
14 | 0E | SO | 46 | 2E | . | 78 | 4E | N | 110 | 6E | n
15 | 0F | SI | 47 | 2F | / | 79 | 4F | O | 111 | 6F | o
16 | 10 | DLE | 48 | 30 | 0 | 80 | 50 | P | 112 | 70 | p
17 | 11 | DC1 | 49 | 31 | 1 | 81 | 51 | Q | 113 | 71 | q
18 | 12 | DC2 | 50 | 32 | 2 | 82 | 52 | R | 114 | 72 | r
19 | 13 | DC3 | 51 | 33 | 3 | 83 | 53 | S | 115 | 73 | s
20 | 14 | DC4 | 52 | 34 | 4 | 84 | 54 | T | 116 | 74 | t
21 | 15 | NAK | 53 | 35 | 5 | 85 | 55 | U | 117 | 75 | u
22 | 16 | SYN | 54 | 36 | 6 | 86 | 56 | V | 118 | 76 | v
23 | 17 | ETB | 55 | 37 | 7 | 87 | 57 | W | 119 | 77 | w
24 | 18 | CAN | 56 | 38 | 8 | 88 | 58 | X | 120 | 78 | x
25 | 19 | EM | 57 | 39 | 9 | 89 | 59 | Y | 121 | 79 | y
26 | 1A | SUB | 58 | 3A | : | 90 | 5A | Z | 122 | 7A | z
27 | 1B | ESC | 59 | 3B | ; | 91 | 5B | [ | 123 | 7B | {
28 | 1C | FS | 60 | 3C | < | 92 | 5C | \ | 124 | 7C | ¦
29 | 1D | GS | 61 | 3D | = | 93 | 5D | ] | 125 | 7D | }
30 | 1E | RS | 62 | 3E | > | 94 | 5E | ^ | 126 | 7E | ~
31 | 1F | US | 63 | 3F | ? | 95 | 5F | _ | 127 | 7F | DEL
American
Standard
Code for
Information
Interchange
Encoding 128 characters

## Slide 35: ASCII
Memory Address | Memory Content | Letter
str + 12  | 0x00 | \0
str + 11  | 0x79 | y
str + 10  | 0x6C | l
str + 9  | 0x62 | b
str + 8  | 0x6D | m
str + 7  | 0x65 | e
str + 6  | 0x73 | s
str + 5  | 0x73 | s
str + 4  | 0x41 | A
str + 3  | 0x20 | space
str + 2  | 0x4D | M
str + 1  | 0x52 | R
str  | 0x41 | A
char str[13] = “ARM Assembly”; // The length has to be at least 13 // even though it has 12 letters. The // NULL terminator should be included.

## Slide 36: String Comparison
Strings are compared based on their ASCII values
“j” < “jar” < “jargon” < “jargonize”
“CAT” < “Cat” < “DOG” < “Dog” < “cat” < “dog”
“12” < “123” < “2”< “AB” < “Ab” < “ab” < “abc”

## Slide 37: Find out String Length
Pointer dereference operator *
int strlen (char *pStr){ int i = 0; // loop until pStr[i] is NULL while( pStr[i] ) i++; return i; }
Array subscript operator [ ]
int strlen (char *pStr){ int i = 0; // loop until *pStr is NULL while( *pStr ) { i++; pStr++; } return i; }
Stings are terminated with a null character (NUL, ASCII value 0x00)

## Slide 38: Convert to Upper Case
Pointer dereference operator *
void toUpper(char *pStr){ for(char *p = pStr; *p; ++p){ if(*p >= ’a’ && *p <= ’z’) *p -= ‘a’ – ‘A’; //or: *p -= 32; } }
Array subscript operator [ ]
void toUpper(char *pStr){ char c = pStr[0]; for(int i = 0; c; i++, c = pStr[i];) { if(c >= ’a’ && c <= ’z’) pStr[i] -= ‘a’ – ‘A’; // or: pStr[i] -= 32; } }
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 4A | 4B | 4C | 4D | 4E | 4F | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 5A
a | b | c | d | e | f | g | h | i | j | k | l | m | n | o | p | q | r | s | t | u | v | w | x | y | z
61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 6A | 6B | 6C | 6D | 6E | 6F | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 7A
‘a’ – ‘A’ = 0x61 – 0x41 = 0x20 = 32

## Slide 39: Summary
Unsigned integer arithmetic
Signed integer arithmetic
  2’s complement
ASCII strings

## Slide 40: References
Lecture 1. Why use two's complement?
  https://www.youtube.com/watch?v=lJCefqV80ck&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=1
Lecture 2: Carry flag for unsigned addition and subtraction
  https://www.youtube.com/watch?v=MxGW2WurKuM&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=2
Lecture 3: Overflow flag for signed addition and subtraction
  https://www.youtube.com/watch?v=BIn6iyYIGio&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=3