## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 4
ARM Arithmetic and Logic Instructions
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: ARM Programming Model
31
0
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13: Stack Pointer (SP)
R14: Link Register (LR)
R15: Program Counter (PC)
N
Z
C
V
CPSR (Current Program Status Register)
Every arithmetic, logical, or shifting operation sets xPSR bits:
  N (negative), Z (zero), C (carry), V (overflow).

## Slide 3: Overview: Arithmetic and Logic Instructions
Shift : LSL (logic shift left), LSR (logic shift right), ASR (arithmetic shift right), ROR (rotate right), RRX (rotate right with extend)
Logic: AND (bitwise and), ORR (bitwise or), EOR (bitwise exclusive or), ORN (bitwise or not), MVN (move not)
Bit set/clear: BFC (bit field clear), BFI (bit field insert), BIC (bit clear), CLZ (count leading zeroes)
Bit/byte reordering: RBIT (reverse bit order in a word), REV (reverse byte order in a word), REV16 (reverse byte order in each half-word independently), REVSH (reverse byte order in each half-word independently)
Addition: ADD, ADC (add with carry)
Subtraction: SUB, RSB (reverse subtract), SBC (subtract with carry)
Multiplication: MUL (multiply), MLA (multiply-accumulate), MLS (multiply-subtract), SMULL (signed long multiply-accumulate), SMLAL (signed long multiply-accumulate), UMULL (unsigned long multiply-subtract), UMLAL (unsigned long multiply-subtract)
Division: SDIV (signed), UDIV (unsigned)
Saturation: SSAT (signed), USAT (unsigned)
Sign extension: SXTB (signed), SXTH, UXTB, UXTH
Bit field extract: SBFX (signed), UBFX (unsigned)
Syntax
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Notes: BIC bit clear
ORR bit set
AND bit mask
EOR bit invert
Comparisons produce no results - just set condition codes.
CMP like SUB
CMN like ADD (subtract of a negative number is the same as add)
TST like AND
TEQ like EOR (eor of identical numbers gives result of zero)
Generally single-cycle execution (except write to PC and register-controlled shift). Mention ARM NOP & Thumb NOP.
Explain RSB and RSC which do subtract in other order (e.g. y-x not x-y)
Does not include multiply (separate instr format). No divide - compiler uses run-time library or barrel shifter to perform division.
Can combine “S” bit with conditional execution, e.g.
ADDEQS r0, r1, r2

## Slide 4: Example: Add
  Unified Assembler Language (UAL) Syntax
ADD r1, r2, r3 ; r1 = r2 + r3
ADD r1, r2, #4 ; r1 = r2 + 4
  Traditional Thumb Syntax
ADD r1, r3 ; r1 = r1 + r3
ADD r1, #15 ; r1 = r1 + 15

## Slide 5: Commonly Used Arithmetic Operations
ADD {Rd,} Rn, Op2 | Add Rd  Rn + Op2
ADC {Rd,} Rn, Op2 | Add with carry Rd  Rn + Op2 + Carry
SUB {Rd,} Rn, Op2 | Subtract Rd  Rn - Op2
SBC {Rd,} Rn, Op2 | Subtract with carry Rd  Rn - Op2 + Carry - 1
RSB {Rd,} Rn, Op2 | Reverse subtract Rd  Op2 - Rn
MUL {Rd,} Rn, Rm | Multiply Rd  (Rn × Rm)[31:0]
MLA Rd, Rn, Rm, Ra | Multiply with accumulate Rd  (Ra + (Rn × Rm))[31:0]
MLS Rd, Rn, Rm, Ra | Multiply and subtract Rd  (Ra – (Rn × Rm))[31:0]
SDIV {Rd,} Rn, Rm | Signed divide Rd  Rn ÷ Rm
UDIV {Rd,} Rn, Rm | Unsigned divide Rd  Rn ÷ Rm
SSAT Rd, #n, Rm {,shift #s} | Signed saturate
USAT Rd, #n, Rm {,shift #s} | Unsigned saturate

## Slide 6: Instruction Suffix: S: Set Condition Flags
start
LDR r0, =0xFFFFFFFF
LDR r1, =0x00000001
ADDS r0, r0, r1
stop B stop
For most instructions, add a suffix S to update N, Z, C, V flags in APSR register.
  N - Negative
  Z - Zero
  C - Carry
  V - oVerflow
In this example, the Z and C bits are set.

## Slide 7: Instruction Suffix: S: Set Condition Flags
start
LDR r0, =0xFFFFFFFF
LDR r1, =0x00000001
ADDS r0, r0, r1
stop B stop
R0 = 0x00000000
N = 0, Z = 1, C = 1, V = 0
CPU sets both C and V:
  If r0 and r1 are unsigned int: 232-1+1, carry flag C=1
  If r0 and r1 are signed int: -1+1, overflow flag V=0
  CPU does not know about signed or unsigned integers
  Software is responsible to use C or V in follow-on code.

## Slide 8: Program Status Register (PSR)
Application PSR (APSR), Interrupt PSR (IPSR), Execution PSR (EPSR)
GE flags are only available on Cortex-M4 and M7
PSR is named CPSR (Current Program Status Register) in ARM7/ARM9 and ARMv4/ARMv5 processors: named xPSR (Extended Program Status Register) in ARM Cortex-M processors (ARMv7-M)
N
Z
C
V
ISR number
Reserved
Reserved
ICI/IT
Reserved
T
Reserved
ISR number
APSR
IPSR
EPSR
PSR
Q
ICI/IT
T
N
Z
C
V
Q
ICI/IT
ICI/IT
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
31
30
29
28
27
Combine them together into one register PSR = APSR + IPSR + EPSR
GE
Reserved
GE
Reserved
Notes: negative (N) - the result that set the condition code had a 1 in the most significant bit;
zero (Z) - the result that set the condition code was 0;
overflow (V) - the result that set the condition code overflowed; and
carry (C) - the result that set the condition code had a carry out of the most significant bit or a borrow into the most significant bit.
APSR provides program flow control through condition flags
IPSR provides interrupt/exception context awareness
EPSR provides low-level execution state control

## Slide 9: 64-bit Addition
start
; C = A + B
; Two 64-bit integers A (r1,r0) and B (r3,r2).
; Result C (r5, r4)
; A = 00000002FFFFFFFF
; B = 0000000400000001
LDR r0, =0xFFFFFFFF ; A’s lower 32 bits
LDR r1, =0x00000002 ; A’s upper 32 bits
LDR r2, =0x00000001 ; B’s lower 32 bits
LDR r3, =0x00000004 ; B’s upper 32 bits
; Add A to B
ADDS r4, r2, r0 ; C[31..0] = A[31..0] + B[31..0], update Carry
ADC r5, r3, r1 ; C[64..32] = A[64..32] + B[64..32] + Carry
stop B stop
r1
r0
r3
r2
r5
r4
A
B
C
ADDS “ADD and Set flags”: sets the carry flag C=1 if there is a carry
ADC “ADD with Carry” consumes that carry to complete the high‑half addition
A register can only store 32 bits
A 64-bit integer needs two registers
Split 64-bit addition into two 32-bit additions

## Slide 10: 64-bit Subtraction
start
; C = A - B
; Two 64-bit integers A (r1,r0) and B (r3,r2).
; Result C (r5, r4)
; A = 00000002FFFFFFFF
; B = 0000000400000001
LDR r0, =0xFFFFFFFF ; A’s lower 32 bits
LDR r1, =0x00000002 ; A’s upper 32 bits
LDR r2, =0x00000001 ; B’s lower 32 bits
LDR r3, =0x00000004 ; B’s upper 32 bits
; Subtract B from A
SUBS r4, r0, r2 ; C[31..0]= A[31..0] - B[31..0], update Carry
SBC r5, r1, r3 ; C[64..32]= A[64..32] - B[64..32] - Carry
stop B stop
r1
r0
r3
r2
r5
r4
A
B
C
SUBS “SUB and Set flags”: sets the carry flag C=0 if there is borrow (borrow flag=1)
SBC “SUB with Carry” consumes that carry to complete the high‑half addition
A register can only store 32 bits
A 64-bit integer needs two registers
Split 64-bit subtraction into two 32-bit subtractions

## Slide 11: Example: 64-bit Addition & Subtraction
0 0 0 0 0 0 0 2 F F F F F F F F
0 0 0 0 0 0 0 4 0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 7 0 0 0 0 0 0 0 0
Most-significant (Upper) 32 bits
Least-significant (Lower) 32 bits
+
64-bit Addition: Carry C=1
0 0 0 0 0 0 0 2 F F F F F F F F
0 0 0 0 0 0 0 4 0 0 0 0 0 0 0 1
F F F F F F F E F F F F F F F E
Most-significant (Upper) 32 bits
Least-significant (Lower) 32 bits
-
64-bit Subtraction: Borrow=0
(Carry C=1)

## Slide 12: Example: Short Multiplication and Division
MUL: Signed multiply
MUL r6, r4, r2 ; r6 = LSB32( r4 × r2 )
UMUL: Unsigned multiply
UMUL r6, r4, r2 ; r6 = LSB32( r4 × r2 )
MLA: Multiply with accumulation
MLA r6, r4, r1, r0 ; r6 = LSB32( r4 × r1 ) + r0
MLS: Multiply with subtract
MLS r6, r4, r1, r0 ; r6 = LSB32( r4 × r1 ) - r0
LSB32: Least significant 32 bits

## Slide 13: Example: Long Multiplication
UMULL RdLo, RdHi, Rn, Rm | Unsigned long multiply RdHi,RdLo  unsigned(Rn × Rm)
SMULL RdLo, RdHi, Rn, Rm | Signed long multiply RdHi,RdLo  signed(Rn × Rm)
UMLAL RdLo, RdHi, Rn, Rm | Unsigned multiply with accumulate RdHi,RdLo  unsigned(RdHi,RdLo + Rn × Rm)
SMLAL RdLo, RdHi, Rn, Rm | Signed multiply with accumulate RdHi,RdLo  signed(RdHi,RdLo + Rn × Rm)
UMULL r3, r4, r0, r1 ; r4:r3 = r0  r1, r4 = MSB bits, r3 = LSB bits
SMULL r3, r4, r0, r1 ; r4:r3 = r0  r1
UMLAL r3, r4, r0, r1 ; r4:r3 = r4:r3 + r0  r1
SMLAL r3, r4, r0, r1 ; r4:r3 = r4:r3 + r0  r1
The result has 64 bits, placed in two registers.

## Slide 14: Bitwise Logic
AND {Rd,} Rn, Op2 | Bitwise logic AND Rd  Rn & operand2
ORR {Rd,} Rn, Op2 | Bitwise logic OR Rd  Rn ¦ operand2
EOR {Rd,} Rn, Op2 | Bitwise logic exclusive OR Rd  Rn ^ operand2
ORN {Rd,} Rn, Op2 | Bitwise logic NOT OR Rd  Rn ¦ (NOT operand2)
BIC {Rd,} Rn, Op2 | Bit clear Rd  Rn & NOT operand2
BFC Rd, #lsb, #width | Bit field clear Rd[(width+lsb–1):lsb]  0
BFI Rd, Rn, #lsb, #width | Bit field insert Rd[(width+lsb–1):lsb]  Rn[(width-1):0]
MVN Rd, Op2 | Move NOT, logically negate all bits Rd  0xFFFFFFFF EOR Op2

## Slide 15: Example: AND r2, r0, r1
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
32 bits
r0
r1
r2
Bit-wise Logic AND
x | y | x AND y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 16: Example: ORR r2, r0, r1
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
32 bits
r0
r1
r2
Bit-wise Logic OR
x | y | x OR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 17: Example: BIC r2, r0, r1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
r0
NOT r1
r2
Bit Clear
r2 = r0 & NOT r1
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
r1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
NOT r1
Step 1:
Step 2:

## Slide 18: Example: BFC and BFI
Bit Field Clear (BFC) and Bit Field Insert (BFI).
Syntax
  BFC Rd, #lsb, #width
  BFI Rd, Rn, #lsb, #width
Examples:
  BFC R4, #8, #12
  ; Clear bit 8 to bit 19 (a total of 12 bits) of R4
  BFI R9, R2, #8, #12
  ; Replace bit 8 to bit 19 (12 bits) of R9
  ; with bit 0 to bit 11 (12 bits) from R2.

## Slide 19: Bit Operators (&, |, ~) vs Boolean Operators (&& ,||, !)
The Boolean operators perform word-wide operations, not bitwise.
For example,
  “0x10 & 0x01” = 0x00, but “0x10 && 0x01” = 0x01 (Any nonzero integer is considered true=0x01; false=0x00.)
  “~0x01” = 0xFFFFFFFE, but “!0x01” = 0x00. (Negation of true=0x01 is false=0x00.)
A && B | Boolean and | A & B | Bitwise and
A¦¦B | Boolean or | A¦B | Bitwise or
!B | Boolean not | ~B | Bitwise not

## Slide 20: Saturating Instruction: SSAT and USAT
Syntax (for n-bit system):
  op{cond} Rd, #n, Rm{, shift}
SSAT saturates a signed value to the signed range -2n-1 ≤ x ≤ 2n-1 -1.
USAT saturates a signed value to the unsigned range 0 ≤ x ≤ 2n - 1.
Examples:
  SSAT r2, #11, r1 ; output range: -210  r2  210
  USAT r2, #11, r3 ; output range: 0  r2  211

## Slide 21: Example of Saturation
Without saturation
With saturation
Assume data are limited to 16 bits

## Slide 22: Reverse Order
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF
RBIT Rd, Rn
Rn
Rd
LDR r0, =0x12345678 ; r0 = 0x12345678
RBIT r1, r0 ; Reverse bits, r1 = 0x1E6A2C48
Example:
0x12345678 = 0001 0010 0011 0100 0101 0110 0111 1000
0x1E6A2C48 = 0001 1110 0110 1010 0010 1100 0100 1000
Notes: Different from Big-Endian vs Little-Endian, which aff
he “=” form signals “load an immediate constant or address,” letting the assembler choose between synthesizing the value in-register or loading it from a literal pool.

## Slide 23: Reverse Order
REV Rd, Rn
Rn
Rd
LDR R0, =0x12345678 ; R0 = 0x12345678
REV R1, R0 ; R1 = 0x78563412
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF
0x12345678 = 0001 0010 0011 0100 0101 0110 0111 1000
0x1E6A2C48 = 0111 1000 0101 0110 0011 0100 0001 0010

## Slide 24: Reverse Order
REV16 Rd, Rn
Rn
Rd
LDR R0, =0x12345678 ; R0 = 0x12345678
REV16 R2, R0 ; R2 = 0x34127856
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF
0x12345678 = 0001 0010 0011 0100 0101 0110 0111 1000
0x1E6A2C48 = 0011 0100 0001 0010 0111 1000 0101 0110

## Slide 25: Reverse Order
REVSH Rd, Rn
Rn
Rd
LDR R0, =0x33448899 ; R0 = 0x33448899
REVSH R1, R0 ; R0 = 0xFFFF9988 %Sign bit of Byte 0 is 1
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF
0x12345678 = 0001 0010 0011 0100 0101 0110 0111 1000
0x1E6A2C48 = 1111 1111 1111 1111 1001 1001 1000 1000

## Slide 26: Sign and Zero Extension
int8_t a = -1; // a signed 8-bit integer, a = 0xFF
int16_t b = -2; // a signed 16-bit integer, b = 0xFFFE
int32_t c; // a signed 32-bit integer
c = a; // sign extension required, c = 0xFFFFFFFF
c = b; // sign extension required, c = 0xFFFFFFFE
a = 1111 1111
c = a = 1111 1111 1111 1111 1111 1111 1111 1111
b = 1111 1111 1111 1110
c = b = 1111 1111 1111 1111 1111 1111 1111 1110

## Slide 27: Sign and Zero Extension
LDR R0, =0x55AA8765
SXTB R1, R0 ; R1 = 0x00000065
SXTH R1, R0 ; R1 = 0xFFFF8765
UXTB R1, R0 ; R1 = 0x00000065
UXTH R1, R0 ; R1 = 0x00008765
SXTB {Rd,} Rm {,ROR #n} | Sign extend a byte Rd[31:0]  Sign Extend((Rm ROR (8 × n))[7:0])
SXTH {Rd,} Rm {,ROR #n} | Sign extend a half-word Rd[31:0]  Sign Extend((Rm ROR (8 × n))[15:0])
UXTB {Rd,} Rm {,ROR #n} | Zero extend a byte Rd[31:0]  Zero Extend((Rm ROR (8 × n))[7:0])
UXTH {Rd,} Rm {,ROR #n} | Zero extend a half-word Rd[31:0]  Zero Extend((Rm ROR (8 × n))[15:0])
0x55AA8765 = 0101 0101 1010 1010 1000 0111 0110 0101
0x00000065 = 0000 0000 0000 0000 0000 0000 0110 0101
0xFFFF8765 = 1111 1111 1111 1111 1000 0111 0110 0101
0x00008765 = 0000 0000 0000 0000 1000 0111 0110 0101
Notes: This pseudocode describes what certain ARM “sign-extend byte with rotate” instructions do (e.g., SXTB with optional ROR). It means:
Take register Rm, rotate it right by bits, where .
From that rotated value, extract the low byte bits [7:0].
Sign-extend that 8-bit value to 32 bits.
Write the 32-bit result into Rd.
Step-by-step:
ROR by multiples of 8 repositions one of the four bytes of Rm into the least-significant byte position without changing their bit order.
Index [7:0] selects that least-significant byte.
SignExtend interprets that byte as a signed 8-bit number: if bit 7 is 1, the upper 24 bits of Rd become 1’s; if bit 7 is 0, the upper 24 bits become 0’s.
Examples:
If Rm = 0xAABBCCDD and n = 0, rotate by 0: pick 0xDD; sign-extend → 0xFFFFFFDD because 0xDD has bit 7 set.
If Rm = 0xAABBCC7F and n = 1, rotate by 8: pick original 0xCC (now in [7:0]); sign-extend → 0xFFFFFFCC.
If Rm = 0x11223344 and n = 2, rotate by 16: pick original 0x22; sign-extend → 0x00000022.
If Rm = 0x80810002 and n = 3, rotate by 24: pick original 0x80; sign-extend → 0xFFFFFF80.
Intuition:
The rotate selects which byte (byte0..byte3) to extend: n=0→byte0, n=1→byte1, n=2→byte2, n=3→byte3.
Sign extension preserves the 8-bit signed value when placed into a 32-bit register.
https://devblogs.microsoft.com/oldnewthing/20210610-00/?p=105295
https://developer.arm.com/documentation/dui0801/latest/A64-General-Instructions/ADD--extended-register---A64-
https://www.reddit.com/r/RISCV/comments/tye2ak/sign_extension/
https://pages.cs.wisc.edu/~markhill/restricted/arm_isa_quick_reference.pdf
https://docs.openhwgroup.org/projects/cv32e40p-user-manual/en/latest/instruction_set_extensions.html
https://loongson.github.io/LoongArch-Documentation/LoongArch-Vol1-EN.html
https://www.ece.lsu.edu/alex/EE3755/fall09/MIPSNote1_1.htm
https://five-embeddev.com/riscv-bitmanip/1.0.0/bitmanip.html
https://en.wikipedia.org/wiki/Sign_extension
https://stackoverflow.com/questions/36706721/is-a-sign-or-zero-extension-required-when-adding-a-32bit-offset-to-a-pointer-for
This pseudocode describes what certain ARM “sign-extend byte with rotate” instructions do (e.g., SXTB with optional ROR). It means:
Take register Rm, rotate it right by 8×𝑛bits, where 𝑛∈{0ⓜ,1ⓜ,2ⓜ,3}.
From that rotated value, extract the low byte bits [7:0].
Sign-extend that 8-bit value to 32 bits.
Write the 32-bit result into Rd.
Step-by-step:
ROR by multiples of 8 repositions one of the four bytes of Rm into the least-significant byte position without changing their bit order.
Index [7:0] selects that least-significant byte.
SignExtend interprets that byte as a signed 8-bit number: if bit 7 is 1, the upper 24 bits of Rd become 1’s; if bit 7 is 0, the upper 24 bits become 0’s.
Examples:
If Rm = 0xAABBCCDD and n = 0, rotate by 0: pick 0xDD; sign-extend → 0xFFFFFFDD because 0xDD has bit 7 set.
If Rm = 0xAABBCC7F and n = 1, rotate by 8: pick original 0xCC (now in [7:0]); sign-extend → 0xFFFFFFCC.
If Rm = 0x11223344 and n = 2, rotate by 16: pick original 0x22; sign-extend → 0x00000022.
If Rm = 0x80810002 and n = 3, rotate by 24: pick original 0x80; sign-extend → 0xFFFFFF80.
Intuition:
The rotate selects which byte (byte0..byte3) to extend: n=0→byte0, n=1→byte1, n=2→byte2, n=3→byte3.
Sign extension preserves the 8-bit signed value when placed into a 32-bit register.
https://devblogs.microsoft.com/oldnewthing/20210610-00/?p=105295
https://developer.arm.com/documentation/dui0801/latest/A64-General-Instructions/ADD--extended-register---A64-
https://www.reddit.com/r/RISCV/comments/tye2ak/sign_extension/
https://pages.cs.wisc.edu/~markhill/restricted/arm_isa_quick_reference.pdf
https://docs.openhwgroup.org/projects/cv32e40p-user-manual/en/latest/instruction_set_extensions.html
https://loongson.github.io/LoongArch-Documentation/LoongArch-Vol1-EN.html
https://www.ece.lsu.edu/alex/EE3755/fall09/MIPSNote1_1.htm
https://five-embeddev.com/riscv-bitmanip/1.0.0/bitmanip.html
https://en.wikipedia.org/wiki/Sign_extension
https://stackoverflow.com/questions/36706721/is-a-sign-or-zero-extension-required-when-adding-a-32bit-offset-to-a-pointer-for

## Slide 28: Move Data between Registers
MOV r4, r5 ; Copy r5 to r4
MVN r4, r5 ; r4 = bitwise logical NOT of r5
MOV r1, r2, LSL #3 ; r1 = r2 << 3
MOV r0, PC ; Copy PC (r15) to r0
MOV r1, SP ; Copy SP (r14) to r1
MOV | Rd  operand2
MVN | Rd  NOT operand2
MRS Rd, spec_reg | Move from special register to general register
MSR spec_reg, Rm | Move from general register to special register

## Slide 29: Move Immediate Number to Register
MOVW r0, #0x4321 ; r0 = 0x00004321
MOVT r0, #0x8765 ; r0 = 0x87654321
MOVW Rd, #imm16 | Move Wide, Rd  #imm16
MOVT Rd, #imm16 | Move Top, Rd  #imm16 << 16
MOV Rd, #const | Move, Rd  const
MOVW writes 16-bit immediate into the low half of r0, and zeros upper halfword
MOVT writes 16-bit immediate into the high half of r0 without altering the low halfword
MOVT r0, #0x8765 ; r0 = 0x8765xxxx
MOVW r0, #0x4321 ; r0 = 0x00004321
Order does matter!
Example: Load a 32-bit number into a register
Notes:   Move Wide” writes the 16-bit immediate into the low half of r0 and clears the high half. After this, r0 = 0x00004321.
  Think of it as: r0[15:0] := 0x4321 and r0[31:16] := 0x0000.
MOVT r0, #0x8765
  “Move Top” writes a 16-bit immediate into the high half of r0 without altering the low half. After this, r0 = 0x87654321.

## Slide 30: Barrel Shifter
The second operand of ALU has a special hardware called Barrel shifter
Five shift and rotation operations:
  LSL, LSR, ASR, ROR, RRX
Use Barrel shifter to speed up multiplication and division
  Shifting left 1 bit multiplies a number by 2
r1, LSL #3 means “r1 shifted left by 3 bits,” i.e., r1 << 3, which is the same as multiplying r0 by 8.
  ADD r3, r2, r1, LSL #3 ; r3 = r2 + r1 << 3
Notes: Source Operand 2

## Slide 31: Use shifts to implement multiplication and division
Examples. r1 = r0 + (r0 << 3) = r0 + 8 × r0 = 9 × r0
  r1 = 9 × r0
  ADD r1, r0, r0, LSL #3 <=> MOV r2, #9 ; r2 = 9
  MUL r1, r0, r2 ; r1 = r0 * 9
ADD r1, r0, r0, LSR #3
; r1 = r0 + r0 >> 3 = r0 + r0/8 (unsigned)
ADD r1, r0, r0, ASR #3
; r1 = r0 + r0 >> 3 = r0 + r0/8 (signed)
MUL instruction takes only registers, not an immediate, so “MUL r1, r0, #9” is invalid syntax
Notes: LSL (logical shift left): Rd = Rm << s, zeros shift in on the right; effectively multiplies by for non‑overflowing values. Flags are updated only with the S suffix (e.g., LSLS).
LSR (logical shift right): Rd = Rm >> s, zeros shift in on the left; for unsigned values it divides by rounding down. Flags update only with the S suffix.
ASR vs LSR in ARM:
Purpose
  ASR (arithmetic shift right): shifts right and replicates the sign bit (bit 31) into the vacated high bits, preserving signed magnitude; models signed divide by with rounding toward negative infinity.
  LSR (logical shift right): shifts right and inserts zeros at the top, appropriate for unsigned values; models unsigned divide by with truncation.
Effects on values
  Example with negative signed value: r0 = 0xF0000000 (−268435456).
    ASR r1, r0, #4 → 0xFF000000 (still negative, sign kept).
    LSR r1, r0, #4 → 0x0F000000 (large positive, because zeros filled in).
  Example with positive value: r0 = 0x70000000.
    ASR r1, r0, #4 → 0x07000000.
    LSR r1, r0, #4 → 0x07000000.
When to use
  Use ASR for signed integers when dividing or scaling right so the sign is preserved.
  Use LSR for unsigned integers, bitfield extraction, and mask/pack operations.
Flags (with S suffix)
  N from result bit 31; Z if result is zero; C gets the last bit shifted out; V unchanged.
Handy patterns
  Signed rounding toward zero: add a bias before ASR for negatives, e.g., r += (r >> 31) & ((1<<n)-1); then ASR by n.
  Field extract: LSR then AND with a mask width, or use UBFX/SBFX if available.
https://developer.arm.com/documentation/dui0204/j/Cjacbgca
https://stackoverflow.com/questions/40193270/difference-between-asr-and-lsr
https://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture4/lecture4-3-3.html
https://www.youtube.com/watch?v=3tOgyQroCd4
https://www.reddit.com/r/learnprogramming/comments/1lmdk5/asrb_lsrw_btstb_explanation/
https://heyrick.eu/assembler/shift.html
https://mrjester.hapisan.com/04_MC68/Sect04Part06/Index.html
https://armasm.com/docs/bit-operations/shifting/
https://comp.sys.arm.narkive.com/ReVomvmp/lsr-asr-ror-rrx
LSL (logical shift left): Rd = Rm << s, zeros shift in on the right; effectively multiplies by 2^𝑠 for non‑overflowing values. Flags are updated only with the S suffix (e.g., LSLS).
LSR (logical shift right): Rd = Rm >> s, zeros shift in on the left; for unsigned values it divides by 2^𝑠 rounding down. Flags update only with the S suffix.
ASR vs LSR in ARM:
Purpose
  ASR (arithmetic shift right): shifts right and replicates the sign bit (bit 31) into the vacated high bits, preserving signed magnitude; models signed divide by 2^𝑛with rounding toward negative infinity.
  LSR (logical shift right): shifts right and inserts zeros at the top, appropriate for unsigned values; models unsigned divide by 2^𝑛with truncation.
Effects on values
  Example with negative signed value: r0 = 0xF0000000 (−268435456).
    ASR r1, r0, #4 → 0xFF000000 (still negative, sign kept).
    LSR r1, r0, #4 → 0x0F000000 (large positive, because zeros filled in).
  Example with positive value: r0 = 0x70000000.
    ASR r1, r0, #4 → 0x07000000.
    LSR r1, r0, #4 → 0x07000000.
When to use
  Use ASR for signed integers when dividing or scaling right so the sign is preserved.
  Use LSR for unsigned integers, bitfield extraction, and mask/pack operations.
Flags (with S suffix)
  N from result bit 31; Z if result is zero; C gets the last bit shifted out; V unchanged.
Handy patterns
  Signed rounding toward zero: add a bias before ASR for negatives, e.g., r += (r >> 31) & ((1<<n)-1); then ASR by n.
  Field extract: LSR then AND with a mask width, or use UBFX/SBFX if available.
https://developer.arm.com/documentation/dui0204/j/Cjacbgca
https://stackoverflow.com/questions/40193270/difference-between-asr-and-lsr
https://www-mdp.eng.cam.ac.uk/web/library/enginfo/mdp_micro/lecture4/lecture4-3-3.html
https://www.youtube.com/watch?v=3tOgyQroCd4
https://www.reddit.com/r/learnprogramming/comments/1lmdk5/asrb_lsrw_btstb_explanation/
https://heyrick.eu/assembler/shift.html
https://mrjester.hapisan.com/04_MC68/Sect04Part06/Index.html
https://armasm.com/docs/bit-operations/shifting/
https://comp.sys.arm.narkive.com/ReVomvmp/lsr-asr-ror-rrx

## Slide 32: Barrel Shifter
Logical Shift Left (LSL)
Arithmetic Shift Right (ASR)
Logical Shift Right (LSR)
Rotate Right (ROR)
Rotate Right Extended (RRX)
Why is there rotate right but no rotate left?
Rotate left can be replaced by a rotate right with a different rotate offset, e.g., ROL x, n equals ROR x, 32−n for 32-bit values
Notes: The diagram summarizes ARM’s barrel shifter, a datapath unit that applies shifts/rotates to an operand as part of many ALU instructions, or via standalone shift ops. It shows what each variant does to the data and to the carry flag.
LSL (logical shift left): moves bits toward the MSB, fills zeros on the right, and if flags are set, C receives the last bit shifted out of bit 31. This models multiply by for non-overflowing values.developer.arm+1
LSR (logical shift right): moves bits toward the LSB, fills zeros on the left, and C gets the last bit shifted out of bit 0 when flag-setting. This is unsigned division by .davespace+1
ASR (arithmetic shift right): shifts right while replicating the sign bit into the vacated top bits, preserving signedness; C gets the last bit shifted out of bit 0. This is signed division by with sign extension.developer.arm+1
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C receives the bit that wrapped. This is a pure rotation without data loss.developer.arm+1
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0. Useful for multiword shifts and certain crypto/bit-manip patterns.armasm+1
Why there’s no “rotate left”
Rotate-left can be expressed as rotate-right by the complementary amount: ROL x, n equals ROR x, 32−n for 32-bit values, so only ROR/rrx are needed.davespace+1
Usage tips
As an operand: ADD Rd, Rn, Rm, LSL #s performs the shift and add in one instruction using the barrel shifter.altmer.arts-union+1
Flags: With the S suffix, N and Z come from the result, C becomes the last bit shifted out (or the wrapped bit for ROR/RRX), and V is unchanged.stackoverflow+1
添加到后续问题
检查来源
https://developer.arm.com/documentation/den0013/latest/ARM-Thumb-Unified-Assembly-Language-Instructions/Data-processing-operations/Operand-2-and-the-barrel-shifter
https://www.davespace.co.uk/arm/introduction-to-arm/barrel-shifter.html
https://developer.arm.com/documentation/dui0204/j/Cjacbgca
https://armasm.com/docs/bit-operations/shifting/
http://altmer.arts-union.ru/3DO/docs/DevDocs/tktfldr/acbfldr/1acbc.html
https://stackoverflow.com/questions/66487890/why-different-ranges-of-permitted-shift-values-for-arm-lsl-vs-lsr
https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/25626b68-d7c8-45f3-b49c-0cf781caf953/image.jpg?AWSAccessKeyId=ASIA2F3EMEYEUILL727D&Signature=Cqm2JXG7dblHeBiRVNqnyQejMOc%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEDcaCXVzLWVhc3QtMSJHMEUCIA1qjOidmMRECFVULoTXY%2FGXcxrf44PZoTk27gNtqjSDAiEAsQAy1vwC0T2tfS8mUTrFQbGrQoRtYpM%2FdFzXJtQ83Bcq%2BgQIr%2F%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FARABGgw2OTk3NTMzMDk3MDUiDDgtuRQjgbze42a9AirOBEpBoI9JdczENp2Ntn5rCIKZRBY6ksKZIZNw2D%2B5%2FXP9hmu%2F5GHt2T2qunPg8T0UzKvTVbaFmkJzJKi1rJXtdS8x5XB2UsV4Kd6NU20HMR0rDw6jrh1f67a5j0Neu3n%2BQftDtxhLMxZrTNjGhBs1C974eCw3BnY4RHrXr20jEKkrgzr1K%2BGyrxhsmdhGznWI7kw6Y6la4%2FlSzYtNZLMkEf%2FabScGIbuvB%2FM%2FA7d9BVzP1ca8L6yPdlkF65dDTjhM2GQoxR1G1Ir90Qbu%2FG5jdaMjuIimqI3pPUAozeUwkOudEX1l%2B6Pwo9IdV67adHxGeMdE2Ajf%2FTkLB7vH53c3HlDITEs6kIFjVqyQSq3uS0wBWMnUp2CygIB0jtRE1z%2BdHztfDr6olTMWWTb70Rc%2FFW0y%2BbrpacdZl%2F83dk8WD3eW9LNDA5a4N%2FBMCskBYPNcu4%2FZWf%2BZDAzc%2Fsx6uLUsnFC6bU1hxH4d0ZD%2BOL7En2fpDipGbrGKgdIuLoBKM0t%2BJ%2FiCj69HIughIyxC1v6GXJjg6gOvZ9hDQ9FHv0iR0Whjfi02O7K%2FG0k8WMmWqpv1GSzakAzTZtMeYc1M%2F%2BAqqSitYE3Re6vSh18pXMAkFarp7d7hfxpI763FFndZHFHev95jkJfd06fP%2Fey7C6PPZ70IWYs4KIByG27bLTDrvlMnxCJ8FTWqt1Cvk7xyi4KcWd3NMAq2Ad15vQMFOzD4206xT9ftEuKk8Fh02TQOuIAbeT6AwnUWyvICizPWHlYhKpMeI71Pmf%2BRlud4jrj%2FMIvirMYGOpoBNfym9R2CHVS4%2BnxLODEhRnu8nGo7wFDNUmiWtORjxy3I5%2BRiMugcXgfTEhOKrHu9Ifm6Iw81v%2B0OgqkENTcNK%2Bltda6dEzYhTHI9UBH8Vx2ZmmOg6g%2BOc4wUw17r36RzU1aiGAdeVpZX7zKuWVtdosr3heaZACntInjZBtOuqK9tIffAyULLvT8Uo7kAbgyIAjY%2FmyQIC8XKWw%3D%3D&Expires=1758149168
https://www.youtube.com/watch?v=X560ZGrZ2qc
https://www.acsce.edu.in/acsce/wp-content/uploads/2020/03/MES-Module-2.pdf
https://www.rfwireless-world.com/interview-qa/barrel-shifter-in-arm-processors
The diagram summarizes ARM’s barrel shifter, a datapath unit that applies shifts/rotates to an operand as part of many ALU instructions, or via standalone shift ops. It shows what each variant does to the data and to the carry flag.
LSL (logical shift left): moves bits toward the MSB, fills zeros on the right, and if flags are set, C receives the last bit shifted out of bit 31. This models multiply by 2^𝑛for non-overflowing values.developer.arm+1
LSR (logical shift right): moves bits toward the LSB, fills zeros on the left, and C gets the last bit shifted out of bit 0 when flag-setting. This is unsigned division by 2^𝑛.davespace+1
ASR (arithmetic shift right): shifts right while replicating the sign bit into the vacated top bits, preserving signedness; C gets the last bit shifted out of bit 0. This is signed division by 2^𝑛with sign extension.developer.arm+1
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C receives the bit that wrapped. This is a pure rotation without data loss.developer.arm+1
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0. Useful for multiword shifts and certain crypto/bit-manip patterns.armasm+1
Why there’s no “rotate left”
Rotate-left can be expressed as rotate-right by the complementary amount: ROL x, n equals ROR x, 32−n for 32-bit values, so only ROR/rrx are needed.davespace+1
Usage tips
As an operand: ADD Rd, Rn, Rm, LSL #s performs the shift and add in one instruction using the barrel shifter.altmer.arts-union+1
Flags: With the S suffix, N and Z come from the result, C becomes the last bit shifted out (or the wrapped bit for ROR/RRX), and V is unchanged.stackoverflow+1
添加到后续问题
检查来源
https://developer.arm.com/documentation/den0013/latest/ARM-Thumb-Unified-Assembly-Language-Instructions/Data-processing-operations/Operand-2-and-the-barrel-shifter
https://www.davespace.co.uk/arm/introduction-to-arm/barrel-shifter.html
https://developer.arm.com/documentation/dui0204/j/Cjacbgca
https://armasm.com/docs/bit-operations/shifting/
http://altmer.arts-union.ru/3DO/docs/DevDocs/tktfldr/acbfldr/1acbc.html
https://stackoverflow.com/questions/66487890/why-different-ranges-of-permitted-shift-values-for-arm-lsl-vs-lsr
https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/25626b68-d7c8-45f3-b49c-0cf781caf953/image.jpg?AWSAccessKeyId=ASIA2F3EMEYEUILL727D&Signature=Cqm2JXG7dblHeBiRVNqnyQejMOc%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEDcaCXVzLWVhc3QtMSJHMEUCIA1qjOidmMRECFVULoTXY%2FGXcxrf44PZoTk27gNtqjSDAiEAsQAy1vwC0T2tfS8mUTrFQbGrQoRtYpM%2FdFzXJtQ83Bcq%2BgQIr%2F%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FARABGgw2OTk3NTMzMDk3MDUiDDgtuRQjgbze42a9AirOBEpBoI9JdczENp2Ntn5rCIKZRBY6ksKZIZNw2D%2B5%2FXP9hmu%2F5GHt2T2qunPg8T0UzKvTVbaFmkJzJKi1rJXtdS8x5XB2UsV4Kd6NU20HMR0rDw6jrh1f67a5j0Neu3n%2BQftDtxhLMxZrTNjGhBs1C974eCw3BnY4RHrXr20jEKkrgzr1K%2BGyrxhsmdhGznWI7kw6Y6la4%2FlSzYtNZLMkEf%2FabScGIbuvB%2FM%2FA7d9BVzP1ca8L6yPdlkF65dDTjhM2GQoxR1G1Ir90Qbu%2FG5jdaMjuIimqI3pPUAozeUwkOudEX1l%2B6Pwo9IdV67adHxGeMdE2Ajf%2FTkLB7vH53c3HlDITEs6kIFjVqyQSq3uS0wBWMnUp2CygIB0jtRE1z%2BdHztfDr6olTMWWTb70Rc%2FFW0y%2BbrpacdZl%2F83dk8WD3eW9LNDA5a4N%2FBMCskBYPNcu4%2FZWf%2BZDAzc%2Fsx6uLUsnFC6bU1hxH4d0ZD%2BOL7En2fpDipGbrGKgdIuLoBKM0t%2BJ%2FiCj69HIughIyxC1v6GXJjg6gOvZ9hDQ9FHv0iR0Whjfi02O7K%2FG0k8WMmWqpv1GSzakAzTZtMeYc1M%2F%2BAqqSitYE3Re6vSh18pXMAkFarp7d7hfxpI763FFndZHFHev95jkJfd06fP%2Fey7C6PPZ70IWYs4KIByG27bLTDrvlMnxCJ8FTWqt1Cvk7xyi4KcWd3NMAq2Ad15vQMFOzD4206xT9ftEuKk8Fh02TQOuIAbeT6AwnUWyvICizPWHlYhKpMeI71Pmf%2BRlud4jrj%2FMIvirMYGOpoBNfym9R2CHVS4%2BnxLODEhRnu8nGo7wFDNUmiWtORjxy3I5%2BRiMugcXgfTEhOKrHu9Ifm6Iw81v%2B0OgqkENTcNK%2Bltda6dEzYhTHI9UBH8Vx2ZmmOg6g%2BOc4wUw17r36RzU1aiGAdeVpZX7zKuWVtdosr3heaZACntInjZBtOuqK9tIffAyULLvT8Uo7kAbgyIAjY%2FmyQIC8XKWw%3D%3D&Expires=1758149168
https://www.youtube.com/watch?v=X560ZGrZ2qc
https://www.acsce.edu.in/acsce/wp-content/uploads/2020/03/MES-Module-2.pdf
https://www.rfwireless-world.com/interview-qa/barrel-shifter-in-arm-processors

## Slide 33: Barrel Shifter: Explanations
LSL (logical shift left): shifts left, fills zeros on the right; C gets the last bit shifted out of bit 31. This is multiply by for non-overflowing values.
LSR (logical shift right): shifts right, fills zeros on the left; C gets the last bit shifted out of bit 0. This is unsigned division by .
ASR (arithmetic shift right): shifts right, fills the sign bit on the left to preserving the sign; C gets the last bit shifted out of bit 0. This is signed division by with sign extension
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C receives the bit that wrapped. This is a pure rotation without data loss.
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0.
Notes: Useful for multiword shifts and certain crypto/bit-manip patterns
LSR (used here): Always fills with zeros, converting the negative value to a large positive number
ASR: Would preserve the sign bit, maintaining the negative value (-4096)

## Slide 34: Examples: shifting by 4
Logical Shift Left (LSL)
Logical Shift Right (LSR)
Arithmetic Shift Right (ASR)
Notes: https://www.davespace.co.uk/arm/introduction-to-arm/barrel-shifter.html

## Slide 35: Examples: shifting by 4
Rotate Right (ROR)
Rotate Right Extended (RRX)

## Slide 36: Barrel Shifter Examples
MOV r0, r0, LSL #1
  Multiply R0 by two.
MOV r1, r1, LSR #2
  Divide R1 by four (unsigned).
MOV r2, r2, ASR #2
  Divide R2 by four (signed).
MOV r3, r3, ROR #16
  Swap the top and bottom halves of R3.
ADD r4, r4, r4, LSL #4
  Multiply R4 by 17. (N = N + N * 16)
RSB r5, r5, r5, LSL #5
  Multiply R5 by 31. (N = N * 32 - N)
  Reverse-subtract using barrel shifter on the second operand, giving r5 = (r5 << 5) − r5
SUB r5, r5, r5, LSR #5
  Subtract using barrel shifter on the second operand, giving r5 − (r5 >> n)
Notes: RSB r5, r5, r5, LSL #5 computes a reverse-subtract using the barrel shifter on the second operand, giving r5 = (r5 << 5) − r5.
RSB is “Reverse SuBtract”: result = Operand2 − Rn, not Rn − Operand2.
Here, Rn is r5, and Operand2 is r5 logically shifted left by 5 bits.
Thus Operand2 = r5 × 2^5 = 32·r5, so the operation is r5 = 32·r5 − r5 = 31·r5.
No flags are updated because there is no S suffix.
Intuition and uses
It’s a strength-reduction trick: multiply by 31 using one instruction by combining a shift and a subtract in the ALU’s flexible operand path.
Equivalent sequences:
  SUB r5, r5, r5, LSR #? is different; SUB would compute r5 − (r5 >> n).
  RSB r5, r5, r5, LSL #k generally yields r5 = (2^k − 1)·r5. For k=5, multiplier is 31.
https://developer.arm.com/documentation/ddi0597/latest/Base-Instructions/RSB--RSBS--register---Reverse-Subtract--register--
https://developer.arm.com/documentation/dui0231/latest/arm-instruction-reference/arm-general-data-processing-instructions/add--sub--rsb--adc--sbc--and-rsc
https://stackoverflow.com/questions/42042832/what-does-this-rsb-instruction-do-with-an-extra-lsl-1-operand
https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf
https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf
https://web.cs.umass.edu/~weems/homepage/335-Notes/ewExternalFiles/Lecture%2015.pdf
https://cseweb.ucsd.edu/classes/wi14/cse30-c/lectures/PI_WI_14_CSE30_lecture_8_post.pdf
https://keleshev.com/compiling-to-assembly-from-scratch/07-arm-assembly-programming
https://salmanarif.bitbucket.io/visual/supported_instructions.html

## Slide 37: Integer Array Access with LSL
To calculate the address of element array[i] of 32-bit integers, we calculate (base address of array) + i*4 for an array of words. Since multiplication is a slow operation, we can shift i’s value left two bit positions. For example:
  ADR r3, ARRAY @ load base address of ARRAY into r3 (ARRAY contains 4-byte ints)
  MOV r2, #6 @ Suppose we want to access ARRAY[6]
  MOV r4, r2, LSL #2 @ logical shift i’s value in r2 by 2 to multiply its value by 4
  ADD r5, r3, r4 @ finish calculation of the address of element array[i] in r5
  LDR r6, [r5] @ load value of array[i] into r6 using the address in r5
Alternatively, we can perform this same address calculation with a single ADD:
  ADD r5, r3, r2, LSL #2 # calculate address of array[i] in r5 with single ADD
  LDR r6, [r5] # load the value of array[i] into r4 using the address in r5
Alternatively, ARM has some nice addressing modes to speedup array item access:
  LDR r6, [r3, r2, LSL #2] # load value of array[i] into r4

## Slide 38: Updating PSR Flags
N | Z | C | V
R<31> | IsZeroBit(R) | carry | unchanged
If “S” is present, the instruction update flags. Otherwise, the flags are not updated.
Let R be the final 32-bit result
LSLS
LSRS
ASRS
RORS

## Slide 39: Carry Flag Update
The carry flag captures the last bit shifted out of the register during shift operations, when the instruction explicitly updates flags (using S suffix like MOVS, LSLS, ASRS)
  LSLS (Logical Shift Left): Carry = the last bit shifted out from the MSB position (bit 31)
  LSRS (Logical Shift Right), ASRS (Arithmetic Shift Right): Carry = the last bit shifted out from the LSB position (bit 0)
  RORS (Rotate Right): Carry = bit that was rotated from bit 0 to bit 31
Notes: Carry = bit that was shifted out from bit 0
RRXS (Rotate Right Extended): Carry = bit that was rotated from bit 0 to bit 31

## Slide 40: Example 1: ANDS
Update carry flag C=1
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ANDS r2, r1, r0, LSL #1
N = 0, Z = 1, C = 1, V = 0
AND{S}<c><q> {<Rd>,} <Rn>, <Rm> {,<shift>}
r0 = 0xFFFFFF00
r1 = 0x00000001
r0, LSL #1 = 0xFFFFFE00
r2 = r1 AND (r0 << 1) = 0x00000001 AND 0xFFFFFE00 = 0x00000000
ANDS sets flags:
Z = 1 (result r2 is zero)
N = 0 (bit 31 of result r2 is 0)
C is unaffected by ANDS. It was set be previous shift to be C=1
V is unaffected by ANDS. Assume it was 0 before.
Notes: if ConditionPassed() then
EncodingSpecificOperations();
(shifted, carry) = Shift_C(R[m], shift_t, shift_n, APSR.C);
result = R[n] AND shifted;
R[d] = result;
if setflags then
APSR.N = result<31>;
APSR.Z = IsZeroBit(result);
APSR.C = carry;
// APSR.V unchanged

## Slide 41: Example 2: ADDS
Does NOT update carry flag
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ADDS r2, r1, r0, LSL #1
N = 1, Z = 0, C = 0, V = 0
ADD{S}<c><q> {<Rd>,} <Rn>, <Rm> {,<shift>}
r0 = 0xFFFFFF00
r1 = 0x00000001
r0, LSL #1 = 0xFFFFFE00
r2 = r1 + (r0 << 1) = 0x00000001 + 0xFFFFFE00 = 0xFFFFFE01
ADDS sets flags:
Z = 0 (result r2 is non-zero)
N = 1 (bit 31 of result r2 is 1)
C = 0 (there is no carry out from bit 31 for unsigned addition, when adding 0x00000001 and 0xFFFFFE00)
V=0 is (there is no overflow for signed addition, when adding 0x00000001 and 0xFFFFFE00. Recall: adding a positive (1) to a negative (0xFFFFFE00) cannot cause overflow.)
Notes: 0x00000001 + 0xFFFFFE00 = 0xFFFFFE01

## Slide 42: Set a Bit in C
a |= (1 << k)
a = a | (1 << k)
or
a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
a7 | a6 | 1 | a4 | a3 | a2 | a1 | a0
Example: k = 5
a
1 << k
a | (1 << k)
The other bits should not be affected.

## Slide 43: Set a Bit in Assembly
a |= (1 << 5)
Solution 1:
MOVS r4, #1 ; r4 = 1
LSLS r4, r4, #5 ; r4 = 1<<5
ORRS r0, r0, r4 ; r0 = r0 | 1<<5
Solution 2:
MOVS r4, #1 ; r4 = 1
ORRS r0, r0, r4, LSL #5 ; r0 = r0 | 1<<5

## Slide 44: Clear a Bit in C
a &= ~(1<<k)
a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
a7 | a6 | 0 | a4 | a3 | a2 | a1 | a0
Example: k = 5
a
~(1 << k)
a & ~(1<<k)
The other bits should not be affected.

## Slide 45: Clear a Bit in Assembly
a &= ~(1<<5)
Solution 2:
MOVS r4, #1 ; r4 = 1
MVNS r4, r4, LSL #5 ; r4 = not (1<<5)
ANDS r0, r0, r4 ; r0 = r0 & not (1<<5)
Solution 3:
MOVS r4, #1 ; r4 = 1
BICS r0, r0, r4, LSL #5 ; r0 = r0 & not (1<<5)
; BIC (Bit Clear) clears bit 5 of r0 (from r4=0x20)
Solution 1:
MOVS r4, #1 ; r4 = 1
LSLS r4, r4, #5 ; r4 = 1<<5 = 0x20
MVNS r4, r4 ; r4 = not (1<<5)
ANDS r0, r0, r4 ; r0 = r0 & not (1<<5)

## Slide 46: Toggle a Bit in C
a ^= 1<<k
a7 | a6 | a5 | a4 | A3 | a2 | a1 | a0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
a7 | a6 | NOT(a5) | A4 | a3 | a2 | a1 | a0
Example: k = 5
a
1 << k
a ^= 1<<k
a5 | 1 | a5⊕1
0 | 1 | 1
1 | 1 | 0
Truth table of Exclusive OR with one
Without knowing the initial value, a bit can be toggled by XORing it with a “1”
x | y | x XOR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: A bit can be ‘toggled’ (changed) – without knowing its initial value – by XORing it with a “1”.

## Slide 47: Toggle a Bit in Assembly
a ^= 1<<5
Solution:
MOVS r4, #1 ; r4 = 1
EORS r0, r0, r4, LSL #5 ; r0 = r0 ^ 1<<5
Notes: A bit can be ‘toggled’ (changed) – without knowing its initial value – by XORing it with a “1”.

## Slide 48: References
Lecture 25. Arithmetic and Logical Instructions
  https://www.youtube.com/watch?v=H-vOP2yRUj4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=25
Lecture 26. Updating NZCV bit flags
  https://www.youtube.com/watch?v=SGJibM1D2_A&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=26