## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Passing Parameters to Subroutines
via Registers

## Slide 2: Overview
How to call a subroutine?
How to return the control back to the caller?
How to pass arguments into a subroutine?
How to return a value in a subroutine?
How to preserve the running environment for the caller?

## Slide 3: Link Register (LR)
Link Register (LR) holds the return address of a subroutine
The processor copies LR to PC after the program is finished.
Link Register
Register Bank
Special Registers

## Slide 4: Call a Subroutine (BL)
Branch with Link
BL label
Step 1: LR = PC + 4
Step 2: PC = label
Notes:
  label is name of subroutine
  Compiler translates label to memory address
  After call, LR holds return address (the instruction following the call)
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 5: Return from a Subroutine (BX LR)
Branch and Exchange
BX LR
PC = LR
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 6: BL and BX
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
PC + 4
PC
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller
LR = PC + 4
PC = foo

## Slide 7: BL and BX
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
LR = PC + 4
PC = foo
PC = LR = PCold + 4
PCold + 4
PCold
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller

## Slide 8: Passing arguments and Returning Value
ARM Architecture Procedure Call Standard (AAPCS)
First four registers are used to pass argument values into a subroutine and to return a value from a subroutine
Argument #1
Argument #2
Argument #3
Argument #4
Subroutine
Register R0
Register R1
Register R2
Register R3
Return Value
Register R0

## Slide 9: Passing arguments and Returning Value

## Slide 10: Passing arguments and Returning Value
a8
b8
c16
d16
Subroutine
Register R0
Register R1
Register R2
Register R3
Return Value
Register R0
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16);

## Slide 11: Passing arguments and Returning Value
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16);
Caller
s = sum(1, 2, 3, 4);
MOVS r0, #1 ; a8
MOVS r1, #2 ; b8
MOVS r2, #3 ; c16
MOVS r3, #4 ; d16
BL sum
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
BX LR
ENDP

## Slide 12: Passing arguments and Returning Value
a8
b8
c16
d16
Subroutine
Register R0
Register R1
Register R2
Register R3
Return value
Register R0
uint32_t sum(uint8_t a, uint8_t b, uint16_t c, uint16_t d, uint32_t e);
Caller pushes e32 onto the stack
Callee loads (not pops) e32 from the stack
Caller pop e32 off the stack
e32

## Slide 13: Passing arguments and Returning Value
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16, uint32_t e32);
Caller
s = sum(1, 2, 3, 4, 5);
MOVS r0, #5 ; e32
PUSH {r0}
MOVS r0, #1 ; a8
MOVS r1, #2 ; b8
MOVS r2, #3 ; c16
MOVS r3, #4 ; d16
BL sum
...
POP {r0}
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
LDR r1, [sp, #0] ; read argument e32
ADD r0, r0, r1 ; add e32
BX LR
ENDP
The caller is responsible to pop extra arguments out of the stack after the subroutine returns.

## Slide 14: Passing arguments and Returning Value
a64
b8
c16
d16
Subroutine
Register R1:R0
Register R2
Register R3
Return Value
Register R0
uint64_t sum(uint64_t a64, uint8_t b8, uint16_t c16, uint16_t d16);
Caller pushes d16 onto stack
Callee reads d16 from stack

## Slide 15: Returning Value
uint32_t s32;
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16);
s32 = sum(1, 2, 3, 4) + 100;
MOVS r0, #1 ; 1st argument a8
MOVS r1, #2 ; 2nd argument b8
MOVS r2, #3 ; 3rd argument c16
MOVS r3, #4 ; 4th argument d16
BL sum ; result is returned in r0
ADDS r0, r0, #100
LDR r4, =s32 ; Get memory address of s32
STR r0, [r4] ; Save returned result to s32

## Slide 16: Callee Saved Registers vs Caller Saved Registers
Callee can freely modify R0, R1, R2, and R3
If caller expects their values are retained, caller should push them onto the stack before calling the callee
Caller expects these values are retained .
If Callee modifies them, callee must restore their values upon leaving the function.
Caller Saved Registers
Callee Saved Registers
Notes: Caller-saved registers - subprogram can use them as
scratch registers, but it must also save any needed values
before calling another subprogram.
Callee-saved registers - it can rely on an subprogram it calls not to change them (so a subprogram wishing to use these registers must save them on entry and restore them before it exits)

## Slide 17: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | Yes | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes/No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | Receives return address on BL call to procedure
r15 (PC) | Program counter | N/A | Do not directly change PC
Notes: LR does not have to contain the same value after a subroutine has completed.

## Slide 18: Common Coding Patterns
Callee returns a constant in r0.
  mov r0,#17 @ r0 is return value register
  bx lr @ return from function
Callee saves some registers, does some arithmetic, and returns the result in r0.
  push {r4-r7,lr}
  mov r4, #10
  mov r5, #100
  add r0,r4,r5
  pop {r4-r7,pc} @ pop saved lr value into PC to return from function
Callee calls another function (nested function calls)
  push {lr} @ must save LR if we call our own function
  mov r0, #123 @ r0 is first function parameter
  bl print_int @ call function print_int(123)
  pop {pc} @ pop saved lr into PC to return from function
Callee return: restore previously-pushed LR, then jump to LR (POP {lr}; BX lr), or equivalently, pop previously-pushed LR to PC
  POP {pc} ≡ POP {lr}; BX lr
Notes: Because loading the PC from the stack both restores the return address and performs a branch, and BX is the branch that also restores the correct instruction set state.
POP {pc} is defined to read a word from [sp], increment sp, and write that value into PC; writing PC causes an immediate control-flow change to that address, effectively “returning” to the caller [this is how POP-with-PC is specified on ARM/Thumb].
POP {lr}; BX lr does the same in two steps: first restore the saved return address into LR from the stack, then branch-exchange to LR, which updates PC and switches to ARM or Thumb according to bit 0 of LR, just like a return via PC does.
Therefore, POP {pc} ≡ POP {lr}; BX lr, because both end with PC loaded from the saved return address and state (Thumb/ARM) determined by the low bit of that address.
https://developer.arm.com/documentation/dui0489/e/arm-and-thumb-instructions/memory-access-instructions/push-and-pop
https://developer.arm.com/documentation/dui0231/latest/thumb-instruction-reference/thumb-memory-access-instructions/push-and-pop
https://stackoverflow.com/questions/16622877/arm-assembly-instructions-pop-what-means-as-return-of-a-function
https://www.cs.uaf.edu/2012/fall/cs301/lecture/11_26_ARM.html
https://ad2001.gitbook.io/a-noobs-guide-to-arm-exploitation/introduction-to-arm
https://duetorun.com/blog/20230614/arm-stack-modes/
https://keleshev.com/compiling-to-assembly-from-scratch/07-arm-assembly-programming
https://azeria-labs.com/functions-and-the-stack-part-7/

## Slide 19: Common Coding Patterns
Memory access: first put memory address into register, then load memory content at that address
  adr r2, mydata @Compute address of label mydata using a PC‑relative add and put that address in r2
  ldr r0,[r2] @Dereference that address, loading the 32‑bit word stored at mydata into r0; after this, r0 = 123.
  bx lr
  mydata:
  .word 123
Or
  ldr r2,=mydata @ pseudo‑instruction that loads absolute address of mydata from a nearby literal pool into r2
  ldr r0,[r2]
  bx lr
  mydata:
  .word 123
adr vs. ldr
  If mydata is in range for adr, both forms will leave r2 holding the same address at run time.
  Out‑of‑range labels: adr may fail; ldr =mydata still works.
Notes: https://www.cs.uaf.edu/2012/fall/cs301/lecture/11_26_ARM.html
It loads a PC‑relative address to a constant, reads the word stored there into r0, then returns.
adr r2, mydata: Compute the address of label mydata using a PC‑relative add and put that address in r2; adr is a pseudo‑instruction that forms a nearby address without touching memory.
ldr r0, [r2]: Dereference that address, loading the 32‑bit word stored at mydata into r0; after this, r0 = 123.
bx lr: Branch to the address in the link register (lr), i.e., return from the subroutine, preserving ARM/Thumb state via the low bit of lr.
mydata: .word 123: Assembles a 32‑bit literal 123 placed in the code/data section right after the code; adr targets this label so the code can read the literal at runtime.
Short answer: Not always. They can both put the address of mydata into r2, but they work differently and have different limits.
What adr does
adr r2, mydata computes the address of mydata relative to the current PC and places it in r2, producing position‑independent code.
It assembles to a single add/sub with PC and only works if mydata is within the encodable PC‑relative range for that instruction; otherwise it fails to assemble.
What ldr r2,=mydata does
ldr r2,=mydata is a pseudo‑instruction that typically loads the absolute address of mydata from a nearby literal pool into r2.
It is not limited by small PC‑relative ranges but costs an extra memory read and usually produces non‑position‑independent code unless using relocations suited for PIC.
When they are equivalent
If mydata is in range for adr, both forms will leave r2 holding the same address at run time.
When they differ
Out‑of‑range labels: adr may fail; ldr =mydata still works by using a literal pool entry.
Performance/side effects: adr is one instruction and no memory access; ldr =mydata fetches from memory and can be affected by literal pool placement and timing.
Code model: adr yields PC‑relative, PIC‑friendly code; ldr =mydata commonly yields absolute addresses unless assembled/linker‑relocated for PIC.
https://stackoverflow.com/questions/73851756/what-is-the-purpose-of-adr-instructions-in-arm
https://duetorun.com/blog/20230610/arm-adr-ldr/
https://en.eeworld.com.cn/news/mcu/eic302608.html
https://duetorun.com/blog/20230610/arm-adr2ldr/
https://www.youtube.com/watch?v=NJTlN2o2Xuo
https://www.youtube.com/watch?v=rvFqvlPukHg
https://stackoverflow.com/questions/73600196/why-use-adr-and-ldr-x2-var-to-get-the-address-of-a-variable
https://en.eeworld.com.cn/news/mcu/eic281184.html
https://developer.arm.com/documentation/dui0231/latest/writing-arm-and-thumb-assembly-language/loading-addresses-into-registers/direct-loading-with-adr-and-adrl
https://developer.arm.com/documentation/dui0489/latest/arm-and-thumb-instructions/adrl-pseudo-instruction

## Slide 20: Example: SSQ(3, 4)
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
...
int SSQ(int x, int y){
int z;
z = x*x + y*y;
return z;
}
R0: first argument
R1: second argument
R0: Return Value
Sum of Square:

## Slide 21: Example: SSQ(3, 4)
; Caller setup (passes x=3, y=4; calls SSQ; uses returned value)
MOV R0, #3 ; Load arg1 x=3 into R0
MOV R1, #4 ; Load arg2 y=4 into R1
BL SSQ ; Call SSQ: LR ← return address, PC ← SSQ entry; R0,R1 carry x,y
MOV R2, R0 ; Save returned result z from R0 into caller temp R2
B ENDL
...
; Callee (SSQ) computes z = x*x + y*y and returns it
SSQ PROC
MUL R2, R0, R0 ; R2 = R0 * R0 = x*x
MUL R3, R1, R1 ; R3 = R1 * R1 = y*y
ADD R2, R2, R3 ; R2 = (x*x) + (y*y) = z
MOV R0, R2 ; Move result z into R0
BX LR ; Return to caller: branch to address in LR
ENDP
; Register roles
; R0: x on entry, z on return
; R1: y on entry
; R2: temp for x*x and then z in callee; holds z in caller after MOV R2,R0
; R3: temp for y*y in callee

## Slide 22: Example: SSQ(3,4)
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
R0
R1
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
pc = 0x08000128
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013A
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 23: Example: SSQ(3, 4)
R0
R1
0x08000128
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
Notes: In fact, PC is 0x08000129 because bit 0 of PC should always be 1 for ARM Cortex-M to indicate thumb mode.

## Slide 24: Example: SSQ(3, 4)
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
3
R0
R1
0x08000128
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 25: Example: SSQ(3, 4)
3
R0
4
R1
0x0800012C
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 26: Example: SSQ(3, 4)
3
R0
4
R1
0x08000130
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 27: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
0x08000134
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
Address of the next instruction after the branch is saved into LR.
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address
Notes: In fact, LR is 0x08000135 because bit 0 of PC should always be 1 for ARM Cortex-M to indicate thumb mode.

## Slide 28: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 29: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013C
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 30: Example: SSQ(3, 4)
3
R0
4
R1
0x08000140
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 31: Example: SSQ(3, 4)
25
R0
4
R1
0x08000142
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 32: Example: SSQ(3, 4)
25
R0
4
R1
0x08000144
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 33: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
Copy LR to PC when returning from a subroutine!
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 34: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 35: Example: SSQ(3, 4)
25
R0
4
R1
0x08000136
PC
MOV R0,R2
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOV R0,#3
MOV R1,#4
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 36: Realities
In the previous example,
  PC is incremented by 2 or 4.
  The least significant bit of LR is always 0.
  Well, I lied!

## Slide 37: Realities
PC is always incremented by 4.
  Each time, 4 bytes are fetched from the instruction memory
  It is either two 16-bit instructions or one 32-bit instruction
    If bit [15-11] = 11101, 11110, or 11111, then, it is the first half-word of a 32-bit instruction. Otherwise, it is a 16-bit instruction.
The least significant bit of LR is always 1 for ARM Cortex-M
  This bit is used to control the processor mode:
    0 = ARM, 1 = THUMB
  Cortex-M only supports THUMB.

## Slide 38: Summary
How to call a subroutine?
  Branch with link: BL subroutine
How to return the control back to the caller?
  Branch and exchange: BX LR
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
How to return a value in a subroutine?
  Value is returned in r0
How to preserve the running environment for the caller?
  (to be covered)

## Slide 39: References
Lecture 29. Calling a subroutine
  https://www.youtube.com/watch?v=xt2Q9n1Udb4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=29
Lecture 30. Passing Arguments to a Subroutine
  https://www.youtube.com/watch?v=DGKjFKjxAYs&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=31