## Slide 1: Zonghua Gu
Fall 2025
General Purpose Input/Output (GPIO)
Acknowledgement: some slides taken from instructor resources of Daniel Lewis textbook

## Slide 2: Raspberry Pi GPIO pins

## Slide 3: Interfacing Peripherals
Port-mapped I/O
  Use special CPU instructions: Special_instruction Reg, Port
Memory-mapped I/O
  A simpler and more convenient way to interface I/O devices
  Each device registers is assigned to a memory address in the address space of the microprocessor
  Use native CPU load/store instructions: LDR/STR Reg, [Reg, #imm]
Core
0x48000024 | 
0x48000020 | 
0x4800001C | 
0x48000018 | 
0x48000014 | GPIO Data Output Register
0x48000010 | 
Memory Space
GPIO Output
Pin output
STR
ARM Cortex-M microprocessors use memory-mapped I/O.
Notes: Usually, each on-chip peripheral device has a few registers, such as control registers, status registers, data input registers, and data output registers. In general, there are two approaches to exchange data between the processor core, and a peripheral device, including {{Pause=0.5}} port-mapped I/O, and {{Pause=0.5}} memory-mapped I/O. Port-mapped I/O uses special CPU instructions, which are designed specifically for I/O operations. {{Pause=0.5}} On the other hand, memory-mapped I/O does not need any special instructions. Each register is assigned to a memory address, in the memory address space of the microprocessor. Memory-mapped I/O is performed by the native load and store instructions of the processor. Therefore, memory-mapped I/O is a more convenient way to interface I/O devices.
Here is an example of memory mapped I/O. Suppose we want to set the output of a G P I O pin to high, software can use the store instruction STR to set the corresponding bit in G P I O data output register to 1. When you write to this “special memory location”, the data you write, is sent to, the corresponding I/O device. {{Pause=0.5}} ARM Cortex-M microprocessors use memory-mapped I/O.

## Slide 4: Memory Map of Cortex-M4 (Pi uses Cortex-A53)
Code
SRAM
Peripheral
External Device
External RAM
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
4 GB
On-chip Flash, for code & data
On-chip RAM, for heap, stack, & code
AHB & APB, such as timers, GPIO
Off-chip memory for data
Such as SD card
NVIC, System Timer, SCB, vendor-specific memory
Notes: The memory address of ARM Cortex-M has a total of 32 bits, supporting 4 gigabytes of memory space. The memory space is divided into six different pre-defined regions. Each region is given for recommended usage. {{Pause=0.5}} The first region is code region. It is primarily used to store program code. It can also store data. The code region is on-chip memory, typically on-chip flash. The size of on-chip flash is limited to half a gigabyte. The actual size of the on-chip flash varies based on different venders and different chips. {{Pause=0.5}} The second region is SRAM. It is primarily used to store data, such as heaps and stacks. We can also put code here. It supports half a gigabyte. {{Pause=0.5}} The third region is peripheral. These peripherals include Advanced High Performance Bus peripherals, such as G P I O, and A D C, or Advanced Peripheral Bus peripherals, such as timers, and USART. {{Pause=0.5}} The next region is for external device, such as SD card. {{Pause=0.5}} The next is external RAM, which is executable region for data. It is off-chip memory, primarily used to store large data blocks. It has a total of 1 gigabyte. {{Pause=0.5}} The last region is system region, which includes the N V I C, system timer, system control block, and vendor-specific memory.

## Slide 5: Memory Map of STM32L4
Code
SRAM
Peripheral
External Device
External RAM
System
0x00000000
GPIO A (1 KB)
GPIO B (1 KB)
0x48000000
0x48000400
0x48000800
0x48000C00
GPIO C (1 KB)
GPIO D (1 KB)
0x48001000
0x40000000
0x60000000
…
…
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Notes: {{Pause=0.5}} Let’s take a look at the peripheral region. This region covers the memory addresses of all on-chip peripherals, such as G P I O, timers, USART, S P I, and A D C. {{Pause=0.5}} Specific mapping addresses are dependent on vendors and chips. We will use G P I O on STM 32 L4 as an example to illustrate the concept of memory-mapped I/O. For instance, on STM 32 L4, the registers of G P I O Port A, are mapped to a small memory region starting at, 48000000 in hex.

## Slide 6: Steps to using GPIO pins
1) Configure the pin as an input or an output
  A) Get the address of the appropriate GPSEL0 register
  B) ORR the current value with the value you want
1) Set or clear the pin
  A) Get the address of GPSET or GPCLR register
  B) ORR the current value with the value you want

## Slide 7: Memory-mapped GPIO Cortex-A53 (Pi)
GPCLR1
GPCLR0
///////////////////////
GPSET1
GPSET0
///////////////////////
GPSEL5
GPSEL4
GPSEL3
GPSEL2
GPSEL1
GPSEL0
GPIO_BASE
GPIO_BASE + 28
GPIO_BASE + 40
< --------------32 bits ------------->
P43 | P42 | P41 | P40 | P39 | P38 | P37 | P36 | P35 | P34 | P33 | P32
P11 | P10 | P9 | P8 | P7 | P6 | P5 | P4 | P3 | P2 | P1 | P0
P43 | P42 | P41 | P40 | P39 | P38 | P37 | P36 | P35 | P34 | P33 | P32
P11 | P10 | P9 | P8 | P7 | P6 | P5 | P4 | P3 | P2 | P1 | P0
Pin 3 | Pin 2 | Pin 1 | Pin 0
P31 | P30 | P29 | P28 | P27
P31 | P30 | P29 | P28 | P27
…
…
…
…
…
Pin 9
N/A
Pin 13 | Pin 12 | Pin 11 | Pin 10
Pin 23 | Pin 22 | Pin 21 | Pin 20
Pin 33 | Pin 32 | Pin 31 | Pin 30
Pin 43 | Pin 42 | Pin 41 | Pin 40
Pin 53 | Pin 52 | Pin 51 | Pin 50
Pin 19
Pin 29
Pin 39
Pin 49
N/A
N/A
N/A
N/A
N/A
N/A
N/A
N/A
N/A
N/A

## Slide 8: Thinking about memory addresses
GPSEL0
Pins 12-15
Pins 8-11
Pins 4-7
Pins 0-3
GPSEL0 (GPIO_BASE)
GPSEL0 + 1
GPSEL0 + 2
GPSEL0 + 3
GPSEL0 + 4

## Slide 9: GPSEL Registers on ARM-Cortex A53 (Pi)

## Slide 10: GPSEL0 Register
Pin 9 | Pin 8 | Pin 7 | Pin 6 | Pin 5 | Pin 4 | Pin 3 | Pin 2 | Pin 1 | Pin 0
How would we set pin 2 as an output in assembly?
LDR R1, =GPSEL0
LDR R2, [R1]
MOV R3, #1<<6
ORR R2, R3
STR R2, [R1]

## Slide 11: General Purpose Input/Output (GPIO)
ARM Cortex-M4
FPU
D Bus
I Bus
S Bus
SRAM
FLASH
AHB Bus Matrix
APB Bus Matrix
GPIO B
GPIO C
GPIO D
GPIO A
GPIO F
GPIO G
GPIO H
GPIO E
STM32L4
Timer
SPI
UART
…
Notes: {{Pause=2}} The ARM Cortex-M4 processor core, is connected to the other components via three buses, include the data bus, the instruction bus, and the system bus. These buses are connected to the Advanced high performance bus (AHB) matrix. AHB is the backbone bus. It is used for high-performance, high clock frequency system modules, such as on-chip flash, on-chip SRAM, as well as G P I O modules. The chip also has a bridge that connects AHB to Advanced Peripheral Bus (APB). APB is for low bandwidth peripherals. APB connects most of the peripheral devices in the system, such as UART, S P I, and timer.
{{Pause=1}} Here is the basic structure of a G P I O module. I will explain the details of this module in the next slide.

## Slide 12: Basic Structure of an I/O Port Bit Input and Output
Schmitt
trigger
Notes: {{Pause=2}} Most G P I O ports have 16 pins. This diagram shows the standard structure of one G P I O pin. It includes the basic structure for both digital input, and digital output. In this lecture, I will only focus on the digital output part. We will discuss the digital input in a separate lecture.

## Slide 13: Basic Structure of an I/O Port Bit: Output
Schmitt
trigger
Output Data Register
GPIO MODE Register
00 = Input, 01 = Output,
10 = AF, 11 = Analog (default)
GPIO Output Type Register (OTYPER)
0 = Output push-pull (default)
1 = Output open-drain
GPIO Pull-up/Pull-down Register (PUPDR)
00 = No pull-up, pull-down 01 = Pull-up
10 = Pull-down 11 = Reserved
Notes: {{Pause=2}} Here is the basic structure, that is designed for digital output, on one G P I O pin. There are four important registers related to output, including the output data register, {{Pause=1}} the mode register, {{Pause=1}} the data output type register, {{Pause=1}} and the pull-up pull-down register. In this slide, I only give a short overview of each registers. Detailed discussion will be presented in the next few slides. {{Pause=1}} We can use the mode register to configure the pin as output. {{Pause=1}} The output type register, sets the output pin as, either push-pull or open-drain. {{Pause=1}} The pull-up pull down register, specifies, whether the pin is pulled up to a high voltage by a resister, or the pin is pulled down to the ground via another resister.
{{Pause=1}} When the pin is configured as output, the value written to the output data register is output on the G P I O pin. {{Pause=1}} However, whether the pin has a high voltage output, a low voltage output, or a high impedance output, depends on the configuration of the output type register, and the pull-up pull-down register.

## Slide 14: GPIO Input: Pull Up and Pull Down
A digital input can have three states: High, Low, and High-Impedance (also called floating, tri-stated, HiZ)
Pull-Up
Pull-Down
If external input is HiZ, the input is read as a valid HIGH.
If external input is HiZ, the input is read as a valid LOW.

## Slide 15: GPIO Output: Push-Pull
GPIO Output = 1
Source current to external circuit

## Slide 16: GPIO Output: Push-Pull
GPIO Output = 0
Drain current from external circuit

## Slide 17: GPIO Output: Open-Drain
GPIO Output = 0
Drain current from external circuit

## Slide 18: GPIO Output: Open-Drain
Output = 1
GPIO Pin has high-impedance to external circuit

## Slide 19: Basic Structure of an I/O Port Bit Input and Output
Schmitt
trigger
Notes: {{Pause=2}} Again, here is the overall diagram of the G P I O module for one I/O pin. In this lecture, we will only focus on G P I O input.

## Slide 20: Basic Structure of an I/O Port Bit: Input
Input Data Register (IDR)
GPIO Pull-up/Pull-down Register (PUPDR)
00 = No pull-up, pull-down 01 = Pull-up
10 = Pull-down 11 = Reserved
Schmitt
trigger
Reduce noise
Increase slew rate
Notes: {{Pause=2}} Except the G P I O mode register, there are two other registers, which are related to G P I O input. They are the input data register (IDR), and the pull-up pull-down register (P U P D R).
{{Pause=1}} The input module, includes one important electronic component, called, Schmitt Trigger. The Schmitt trigger circuit is a special voltage comparator. It has two functions. First, it reduces noises, and provides a cleaner and more reliable signal. Second, it converts a slow signal edge, into a clean edge with instantaneous transition. Thus, it can increase the slew rate of signals.

## Slide 21: Schmitt Trigger
Analog signals
Noisy
Rise and fall slowly (small slew rate)
Threshold
Notes: {{Pause=2}} Let me explain the motivations of the Schmitt trigger. In practice, an analog signal often has electronic noise, introduced by various electronic components. The noise makes the signal fluctuate frequently. In addition, analog signal tends to rise or fall slowly, because of inherent parasitic capacitance, resistance, or induction in electronic circuits. Accordingly, analog signals tend to have small slew rates. The slew rate describes how fast a voltage changes. It is usually measured in volts per microsecond.

## Slide 22: Schmitt Trigger
Threshold
Notes: Let’s see what will happen, if we use a simple comparator, to convert the analog input signal, to a binary digital signal. The simple comparator compares the input voltage with a pre-defined threshold. If the input is larger than the threshold, then the comparator outputs high level. Otherwise, the comparator outputs low level. Here is the output of the simple comparator.

## Slide 23: Schmitt Trigger
Vin
Vout
Notes: {{Pause=2}} Different from the simple comparator, the Schmitt Trigger is a special circuit, which switches the output, based on two different thresholds. They are called the trigger high threshold, and the trigger low threshold. The output of a Schmitt Trigger depends on the current input, and the history of the input. When the input voltage increases from zero, the output remains low, until the input becomes larger than the high threshold. {{Pause=1}} Similarly, when the voltage decreases gradually, the output remains high, until the input becomes smaller than the low threshold. {{Pause=1}} Any fluctuation in the range between the high and low thresholds is ignored by the Schmitt trigger.
{{Pause=2}} This figure compares the output of the Schmitt Trigger, and the simple comparator. When the input signal fluctuates slightly, the output of the Schmitt Trigger does not switch its output level. For example, at the beginning, the output of Schmitt Trigger is low. When the input signal fluctuates, the output remains low as long as the input signal is lower than the high threshold. Similarly, if the current output is high, even thought the input fluctuates, the output remains high as long as the input is higher than the low threshold.
{{Pause=1}} From this simple example, we can see that, the Schmitt Trigger switches its output, much less frequently than the simple comparator. Accordingly, the Schmitt trigger helps eliminate noise in the input signal.