## Slide 1: L4 (CHAPTER 7) Programming in Assembly Part 3: Control Structures Exercises ANS
Acknowledgement: some slides taken from instructor resources of Daniel Lewis textbook

## Slide 2
Condition Code | Meaning | Requirements
EQ | Equal | Z = 1
NE | Not equal | Z = 0
CS | Carry set | C = 1
CC | Carry clear | C = 0
MI | Minus/negative | N = 1
PL | Plus/positive or zero (non-negative) | N = 0
VS | Overflow | V = 1
VC | No overflow | V = 0
HI | Unsigned > (“Higher”) | C = 1 && Z = 0
LS | Unsigned ≤ (“Lower or Same”) | C = 0 ¦¦ Z = 1
GE | Signed ≥ (“Greater than or Equal”) | N = V
LT | Signed < (“Less Than”) | N ≠ V
GT | Signed > (“Greater Than”) | Z = 0 && N = V
LE | Signed ≤ (“Less than or Equal”) | Z = 1 ¦¦ N ≠ V
AL | Always (unconditional) | only used with IT instruction
The condition is described as the state of a specific bit in the CPSR register. For example, when we compare two numbers a and b, and they turn out to be equal, we set the Zero bit (Z = 1), because a – b = 0. In this case we have EQual condition. If the first number was bigger, we would have a Greater Than condition and in the opposite case – Lower Than. There are more conditions, like Lower or Equal (LE), Greater or Equal (GE) and so on. Any one of these may be appended to any instruction mnemonic when used inside an If-Then-Else (IT) block.
Condition Codes
Review
Notes: Exceptions: CBZ, CBNZ, CMP, CMN, NEG, TST, or TEQ.
. (E.g., “IT NE followed by ADDNE” would add only if Z ≠ 0.)

## Slide 3: Another Example:
C code:
  if (a < b) {x = 5; y = c + d;} else {x = c - d;}
Assembler code:
True Block
{x=5;y=c+d;}
False Block
{x=c-d;}
BGE fblock
fblock
Compare a vs. b
after
B after
True Block
{x=5;y=c+d;}
False Block
{x=c-d;}
BLT tblock
tblock
Compare a vs. b
after
B after
Review

## Slide 4: Question: Conditional
C program:
  if (a == 0) {//True Block} else {//False Block}
Write the assembler program for the C program, given the snippets provided
    ADR R4,a
    LDR R0,[R4]
    __________
    __________
tblock % True Block
__________
fblock % False Block
after
    ADR R4,a
    LDR R0,[R4]
    __________
    __________
fblock % False Block
__________
tblock % True Block
after

## Slide 5: Answer: Conditional
C program:
  if (a == 0) {//True Block} else {//False Block}
Write the assembler program for the C program, given the snippets provided
    ADR R4,a
    LDR R0,[R4]
    CMP R0,#0
    BNE fblock
tblock % True Block
B after
fblock % False Block
after
    ADR R4,a
    LDR R0,[R4]
    CMP R0,#0
    BEQ tblock
fblock % False Block
B after
tblock % True Block
after

## Slide 6: Loops: Predetermined #Iterations
for (n = 0; n < 100; n++) { … //Loop body }
LDR R0,=0 top: CMP R0,#100 BGE done ;Branch greater than or equal to (n>=100) … ADD R0,R0,#1 B top done: | LDR R0,=0 top: … ADD R0,R0,#1 CMP R0,#100 BLT top ;Branch less than (n<100) done:
Assembler code (option 1):
Assembler code (option 2):
C code:
More efficient, with fewer branch instructions.
Review

## Slide 7: Question: Loop
Q: How many iterations does the following loop execute?
  （a）for (n=0; n<100; n +=2) {…}
  （b）for (n=0; n<100; n *=2) {…}
  （c）for (n=1; n<100; n *=2) {…}

## Slide 8: Answer: Loop
Q: How many iterations does the following loop execute?
  （a）for (n=0; n<100; n +=2) {…}
  （b）for (n=0; n<100; n *=2) {…}
  （c）for (n=1; n<100; n *=2) {…}
A: (a) 50 (b) infinite (c) 7 (since n=1,2,4,8,16,32,64)

## Slide 9: Question: Loop
Write the assembler code for the following C program
  For (n=1; n<100; n *=2) {…}

## Slide 10: Answer: Loop
Write the assembler code for the following C program
  For (n=1; n<100; n *=2) {…}
Assembler (option 1):
LDR R0,=0
top: CMP R0,#100
BGE done
…
MUL R0,R0,#2 B top done:
Assembler (option 2):
LDR R0,=0
top: …
MUL R0,R0,#2
CMP R0,#100
BLT top
done:

## Slide 11
Any of these may be applied to the 2nd operand register in Move / Add / Subtract, Compare, and Bitwise Groups.
<shift> | Meaning | Notes
LSL #n | Logical shift left by n bits | Zero fills; 0 ≤ n ≤ 31
LSR #n | Logical shift right by n bits | Zero fills; 1 ≤ n ≤ 32
ASR #n | Arithmetic shift right by n bits | Sign extends; 1 ≤ n ≤ 32
ROR #n | Rotate right by n bits | 1 ≤ n ≤ 32
RRX | Rotate right w/C by 1 bit | including C bit from CPSR
LSL #1
LSR #1
RRX
Shift Instructions
Review

## Slide 12: Answer: Loop with Shift Instruction
Write the assembler code for the following C program
  For (n=1; n<100; n *=2) {…}
Assembler (option 1):
LDR R0,=0
top: CMP R0,#100
BGE done
…
MOV R0, R0, LSL#1 B top done:
Assembler (option 2):
LDR R0,=0
top: …
MOV R0, R0, LSL#1
CMP R0,#100
BLT top
done: