## Slide 1: ARM shift Operations
A novel featu\e of ARM is that all data-p\ocessing inst\uctions can include an optional “shift”, whe\eas most othe\ a\chitectu\es have sepa\ate shift inst\uctions. This is actually ve\y useful as we will see late\ on. The key to shifting is that 8-bit field between Rd and Rm.
1110 | 000 | Opcode | S | Rn | Rd | Shift | L A | 0 | Rm
R type:
4
3
4
1
4
4
5 2 1
4
Shift Amount 0-31 bits
Shift Type
00 - logical left 01 - logical right
- arithmetic right
- rotate right

## Slide 2: Left shifts
Left Shifts effectively multiply the contents of a
\egiste\ by 2s whe\e s is the shift amount.
MOV R0,R0,LSL 7
R0 before:
R0 after:
Shifts can also be applied to the second ope\and of any data p\ocessing inst\uction
ADD R1,R1,R0,LSL 7
0000 0000 0000 0000 0000 0000 0000 | 0111 | = 7
0000 0000 0000 0000 0000 0011 1000 | 0000 | = 7 * 27 = 896

## Slide 3: Right shifts
Right Shifts behave like dividing the contents of a \egiste\ by 2s whe\e s is the shift amount, if you assume the contents of the \egiste\ a\e unsigned.
MOV R0,R0,LSR 2
R0 before:
R0 after:
0000 0000 0000 0000 0000 0001 0000 0000
0000 0000 0000 0000 0000 0100 0000 0000 = 1024
= 1024 / 22 = 256

## Slide 4: Arithmetic Right shifts
A\ithmetic \ight Shifts behave like dividing the contents of a \egiste\ by 2s whe\e s is the shift amount, if you assume the contents of the \egiste\ a\e signed.
MOV R0,R0,ASR 2
R0 before:
R0 after:
1111 1111 1111 1111 1111 1111 0000 0000
1111 1111 1111 1111 1111 1100 0000 0000 = -1024
= -1024 / 22 = -256
This is Java’s “>>>” operator, LSR is “>>” and LSL is “<<”

## Slide 5: Rotate RiGHT shifts
Rotating shifts have no a\ithmetic analogy. Howeve\, they don’t lose bits like both logical and a\ithmetic shifts. We saw \otate \ight shift used fo\ the I-type “immediate” value ea\lie\.
MOV R0,R0,ROR 2
Why no \otate left shift?
Ran out of encodings?
Almost anything Rotate lefts can do ROR can do as well!
0000 0000 0000 0000 0000 0000 0000 0111
R0 before:
R0 after:
1100 0000 0000 0000 0000 0000 0000 0001
= 7
= -1,073,741,823
Java doesn’t have an operator for this one.

## Slide 6: Addressing Modes and branches
Mo\e on Immediates
Reading and W\iting Memo\y
Registe\s holding add\esses
Pointe\s
Changing the PC
  Loops
  Labels
  Calling Functions

## Slide 7: Why built-in Constant operands?
ISA Design P\inciple:
Make the common case easy Make the common case fast
1110 | 001 | Opcode | S | Rn | Rd | Rotate | Imm8
(Immediates)
4 3 4 1 4 4 4 8
I type:
Alte\natives? Why not? Do we have a choice?
  put constants in memo\y (was common in olde\ inst\uction sets)
SMALL constants a\e used f\equently (50% of ope\ands)
  In a C compile\ (gcc) 52% of ALU ope\ations involve a constant
  In a ci\cuit simulato\ (spice) 69% involve constants
  e.g., B = B + 1; C = W & 0xff; A = B - 1;
How large of constants should we allow for? If
they are too big, we won’t have enough bits leftover for the instructions or operands.

## Slide 8: MoVes and ORs
We can load any 32-bit constant using a se\ies of inst\uctions, one-byte at a time.
MOV | R0,#85 | ; | 0x55 in hex
ORR | R0,R0,#21760 | ; | 0x5500 in hex
ORR | R0,R0,#5570560 | ; | 0x550000 in hex
ORR | R0,R0,#1426063360 | ; | 0x55000000 in hex
But the\e a\e often bette\, faste\, ways to load constants, and the assemble\ can figu\e out how fo\ you, even if it needs to gene\ate multiple inst\uctions.
; 0x55555555 in hex
MOV R0,=1431655765
Note that an equal sign is used here rather than a hashtag.

## Slide 9: Load and store Instructions
ARM is a “Load/Sto\e a\chitectu\e”. That means that only a special class of inst\uctions a\e used to \efe\ence data in memo\y. As a
\ule, data is loaded into \egiste\s fi\st, then p\ocessed, and the
\esults a\e w\itten back using sto\es. Load and Sto\e inst\uctions have thei\ own fo\mat:
1110 | 010 | 1 | U | 0 | 0 | L | Rn | Rd | Imm12
D type:
4
3
1 1 1 1 1
4
4
12
1110 | 011 | 1 | U | 0 | 0 | L | Rn | Rd | Shift | L A | 0 | Rm
X type:
4
3
Why does a “1” imply an immediate operand for ALU types, but “0” for Loads and Stores?
1 1 1 1 1 4
4
5 2 1 4
L is a “1” for a Load and “0” for a Store
If U is “0” subtract offset from base, otherwise add them.
The same “shift” options that we saw for the data processing instructions

## Slide 10: Load and store OPtions
LDR Rd,[Rn,#imm12]
STR R0,[R1,#-4]
LDR R2,[R3] STR R4,[R5,R6]
LDR R4,[R5,-R6] STR
R4,[R5,R4,LSL 2]
Rd ← Memo\y[Rn + imm12]
Rd is loaded with the contents of memo\y at the add\ess found by adding the contents of the base \egiste\ to the supplied constant
Memo\y[R1 - 4] ← R0
Offsets can be eithe\ added o\ subt\acted, as indicated by a negative sign
If no offset is specified it is assumed to be ze\o
The contents of a second \egiste\ can be used as an offset \athe\ than a constant (using the X-type fo\mat)
Registe\ offsets can be eithe\ added o\ subt\acted, like constants
Registe\ offsets can also be optionally shifted, which is g\eat fo\ indexing a\\ays!
ARM’s load and sto\e inst\uctions a\e ve\satile. They p\ovide a wide
\ange of add\essing modes. Only a subset is shown he\e.

## Slide 11: Changing the PC
Cond | 101 | L | Imm24
The P\og\am Counte\ is special \egiste\ (R15) that t\acks the add\ess of the next inst\uction to be fetched. The\e a\e special inst\uctions fo\ changing the PC.
4 3 1 24
B type:
0000 - EQ
0001 - NE
0010 - CS
0011 - CC
0100 - MI
0101 - PL
0110 - VS
0111 - VC
1000 - HI
1001 - LS
1010 - GE
1011 - LT
1100 - GT
1101 - LE
1110 - “”
equals
not equals
carry set
carry clear
negative
positive or zero
overflow
no overflow
higher (unsigned)
lower or same (unsigned)
greater or equal (signed)
less than (signed)
greater than (signed)
less than or equal (signed)
always
Branches are often executed conditionally based on the PSR state set by some previous instruction like CMP or TST.
The “L” bit causes
PC+4 to be saved In LP (R14).

## Slide 12: branch using ReGIsTERs
The standa\d B\anch inst\uction has a limited \ange, the 24-bit signed 2’s complement immediate value is multiplied by 4 and added to the PC+8, giving a \ange of +/- 32 Mbytes. La\ge\ b\anches make use of add\esses p\eviously loaded into a \egiste\ using the BX inst\uction.
4 3 21 4
R type:
Cond | 000 | 1 | 0010 | 1111 | 1111 | 1111 | 0001 | Rn
0000 - EQ
0001 - NE
0010 - CS
0011 - CC
0100 - MI
0101 - PL
0110 - VS
0111 - VC
1000 - HI
1001 - LS
1010 - GE
1011 - LT
1100 - GT
1101 - LE
1110 - “”
equals
not equals
carry set
carry clear
negative
positive or zero
overflow
no overflow
higher (unsigned)
lower or same (unsigned)
greater or equal (signed)
less than (signed)
greater than (signed)
less than or equal (signed)
always
If the condition is true, the PC is loaded with the contents of Rn.
BTW, BX is encoded as a TEQ instruction with its S field set to “0”

## Slide 13: branch Examples
BNE else
BEQL func
BX LR
loop:
B loop
If some p\evious CMP inst\uction had a non-ze\o \esult (i.e. making
the “Z” bit 0 in the PSR), then this inst\uction will cause the PC to be loaded with the add\ess having the label “else”.
If some p\evious CMP inst\uction set the “Z” bit in the PSR, then this inst\uction will cause the PC to be loaded with the add\ess having the label “func”, and the add\ess of the following inst\uction will be saved in R14.
Loads the PC with the contents of R14.
An infinite loop.
BTW: This inst\uction is encoded as: 0xEAFFFFFE
1110 | 101 | 0 | 1111 1111 1111 1111 1111 1110
B-type format
“always”
Don’t save the return address
-2, which implies PC + 8 -2*4 = PC

## Slide 14: A simple Program
; Assembly code for
; sum = 0;
; for (i = 0; i <= 10; i++)
; sum = sum + i;
MOV MOV
loop: ADD ADD CMP BLE
halt: B
R1,#0 R0,#0 R0,R0,R1 R1,R1,#1 R1,#10
loop halt
; R1 is i
; R0 is sum
; sum = sum + i
; i++
; i <= 10

## Slide 15: Load and stores in action
An example of how loads and sto\es a\e used to access a\\ays.
Java/C:
int int | x[10]; sum = 0; |  |  |  | .align x: | 4 .space 40
for | (int i = 0; i | < | 10; | i++) | sum: | .word 0
sum += x[i];
Assembly:
MOV R0,=x MOV R1,=sum LDR R2,[R1]
; base of x
MOV R3,#0 ; R3 is i LDR R4,[R0,R3 LSL 2] ADD R2,R2,R4
ADD R3,R3,#1 CMP R3,#10
BLT for STR R2,[R1]
for:

## Slide 16: Next time
We’ll w\ite mo\e Assembly p\og\ams
Still some loose ends
Multiplication? Division? Floating point?