## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Flow Control in Assembly

## Slide 2: Three Control Structures
Sequence Structure
  Computer executes statements (instructions), one after another, in the order listed in the program
Sequence Structure

## Slide 3: Three Control Structures
Selection Structure
  If-then-else
Loop Structure
  while loop
  for loop
Sequence Structure
Selection Structure
Loop Structure

## Slide 4: Review: Condition Flags
Negative bit
  N = 1 if most significant bit of result is 1
Zero bit
  Z = 1 if all bits of result are 0
Carry bit
  For unsigned addition, C = 1 if carry takes place
  For unsigned subtraction, C = 0 (carry = not borrow) if borrow takes place
  For shift/rotation, C = last bit shifted out
oVerflow bit
  V = 1 if adding 2 same-signed numbers produces a result with the opposite sign
    Positive + Positive = Negative, or
    Negative + negative = Positive
  Non-arithmetic operations does not touch V bit, such as MOV,AND,LSL,MUL
Reserved
ISR number
Program Status Register (PSR)
ICI/IT
T
N
Z
C
V
Q
ICI/IT
GE
Reserved

## Slide 5: Updating Condition Flags
Method 1: append with “S”
  ADD r0,r1,r2 → ADDS r0,r1,r2
  SUB r0,r1,r2 → SUBS r0, r1, r2
Method 2: using compare instructions
Instruction | Brief description | Flags
CMP | Compare | N,Z,C,V
CMN | Compare Negative | N,Z,C,V
TEQ | Test Equivalence | N,Z,C
TST | Test | N,Z,C

## Slide 6: Updating Condition Flags
Update the status flags
  No need to add S bit.
  No need to specify destination register.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 & operand2, but result not written
  TEQ operand1 ^ operand2, but result not written
Examples:
  CMP r0, r1
  TST r2, #5
Instruction | Operands | Brief description | Flags
CMP | Rn, Op2 | Compare | N,Z,C,V
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C

## Slide 7: Updating Condition Flags: CMP and CMN
CMP Rn, Operand2
CMN Rn, Operand2
Update N, Z, C and V according to the result
CMP subtracts Operand2 from Rn.
  Same as SUBS, except result is discarded.
CMN adds Operand2 to Rn.
  Same as ADDS, except result is discarded.

## Slide 8: Example of CMP
Area absolute, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
CMP r1, #0
RSBLT r1, r1, #0 ; r1 = -r1 if r1 < 0
done B done ; deadloop
ENDP
END
RSBLT r1, r1, #0:: conditional execution of the RSB instruction with the condition code LT. If the condition LT (less than) is true, then set r1=0−r1
Notes: Note: RSB = Reverse SuBtract

## Slide 9: Updating Condition Flags: TST and TEQ
TST Rn, Operand2 ; Bitwise AND
TEQ Rn, Operand2 ; Bitwise Exclusive OR
Update N and Z according to the result
Can update C during the calculation of Operand2
Do not affect V
TST performs bitwise AND on Rn and Operand2.
  Same as ANDS, except result is discarded.
TEQ performs bitwise Exclusive OR on Rn and Operand2.
  Same as EORS, except result is discarded.
x | y | x AND y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x XOR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10: Unconditional Branch Instructions
B label
  cause a branch to label.
BL label
  copy the address of the next instruction into r14 (lr, the link register), and
  cause a branch to label.
BX Rm
  branch to the address held in Rm
BLX Rm:
  copy the address of the next instruction into r14 (lr, the link register) and
  branch to the address held in Rm
Instruction | Operands | Brief description
B | label | Branch
BL | label | Branch with Link
BLX | Rm | Branch indirect with Link
BX | Rm | Branch indirect

## Slide 11: Unconditional Branch Instructions: A Simple Example
A label marks the location of an instruction
Labels helps human to read the code
In machine program, labels are converted to numeric offsets by assembler
MOVS r1, #1
B target ; Branch to target
MOVS r2, #2 ; Not executed
MOVS r3, #3 ; Not executed
MOVS r4, #4 ; Not executed
target MOVS r5, #5

## Slide 12: Condition Codes
The possible condition codes are listed below:
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Clear
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z==0
C==1
C==0
Z==1
Flags tested
N==1
N==0
V==1
V==0
C==1 and Z==0
C==0 or Z==1
N==V
N!=V
Z==0 and N==V
Z==1 or N!=V
    Note AL is the default and does not need to be specified
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 13: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | No overflow, implying the result is correct. The result is non-negative, Thus r0 – r1 ≥ 0, i.e., r0 ≥ r1 | No overflow, implying the result is correct. The result is negative. Thus r0 – r1 < 0, i.e., r0 < r1
V = 1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as non-negative and in fact it should be negative. Thus r0 – r1 < 0 in reality, i.e., r0 < r1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as negative and in fact it should be non-negative. Thus r0 – r1 ≥ 0 in reality., i.e. r0 ≥ r1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)
Notes: In the CPSR (Current Program Status Register) of ARM processors, the N and V flags are status flags used to reflect the result of operations:
N flag (Negative flag): This flag is set to 1 if the result of an operation is negative when interpreted as a signed number. In practice, it is set to the most significant bit (bit 31) of the result. If this bit is 1, the number is negative in two's complement representation. Otherwise, it is 0.sciencedirect+1youtube
V flag (Overflow flag): This flag is set to 1 if a signed overflow has occurred in the operation—meaning the signed result does not fit in the number of bits allowed. For example, adding two large positive signed integers that produce a negative result sets V. Likewise, subtracting a large negative from a large positive can also set V. It indicates that the sign bit has been corrupted due to overflow. If no overflow occurs, V is cleared to 0.armyoutube
Together, N and V help the processor and programmers detect and handle signed arithmetic conditions like overflow and sign changes, which are critical for signed condition codes and branching decisions.
https://arm-software.github.io/CMSIS_5/Core_A/html/group__CMSIS__CPSR.html
https://www.sciencedirect.com/topics/computer-science/current-program-status-register
https://developer.arm.com/documentation/ddi0406/b/System-Level-Architecture/The-System-Level-Programmers--Model/ARM-processor-modes-and-core-registers/Program-Status-Registers--PSRs-
https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/condition-codes-1-condition-flags-and-codes
https://goiabada.github.io/docs/sections/arm-cpu/flags.html
https://heyrick.eu/assembler/psr.html
https://users.ece.utexas.edu/~valvano/EE345M/Arm_EE382N_4.pdf
https://www.youtube.com/watch?v=28MMaELXRZ0
https://azeria-labs.com/arm-conditional-execution-and-branching-part-6/
https://ece.eng.wayne.edu/~smahmud/ECECourses/ECE5620/Manuals/ARM_InstructionSet.pdf

## Slide 14: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | r0 = +7 (00111) r1 = +3 (00011) r0 − r1 = +4 (00100); result non‑negative and no signed overflow, so N=0, V=0 ⇒ GE holds | r0 = +3 (00011) r1 = +7 (00111) r0 − r1 = −4 (11100) result negative with no overflow, so N=1, V=0 ⇒ LT holds
V = 1 | r0 = −10 (10110) r1 = +7 (00111) r0 − r1 = −17, outside range [−16,+15]; result is 00111 (decimal 7), whose sign bit is 0 so N=0, but signed overflow occurs so V=1 ⇒ LT holds | r0 = +10 (01010) r1 = −7 (11001) r0 − r1 = +17, outside range [−16,+15]; result is 10001 (decimal −15), whose sign bit is 1 so N=1, but signed overflow occurs so V=1 ⇒ GE holds
CMP r0, r1
perform subtraction r0 – r1, without saving the result
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)
Notes: In the CPSR (Current Program Status Register) of ARM processors, the N and V flags are status flags used to reflect the result of operations:
N flag (Negative flag): This flag is set to 1 if the result of an operation is negative when interpreted as a signed number. In practice, it is set to the most significant bit (bit 31) of the result. If this bit is 1, the number is negative in two's complement representation. Otherwise, it is 0.sciencedirect+1youtube
V flag (Overflow flag): This flag is set to 1 if a signed overflow has occurred in the operation—meaning the signed result does not fit in the number of bits allowed. For example, adding two large positive signed integers that produce a negative result sets V. Likewise, subtracting a large negative from a large positive can also set V. It indicates that the sign bit has been corrupted due to overflow. If no overflow occurs, V is cleared to 0.armyoutube
Together, N and V help the processor and programmers detect and handle signed arithmetic conditions like overflow and sign changes, which are critical for signed condition codes and branching decisions.
https://arm-software.github.io/CMSIS_5/Core_A/html/group__CMSIS__CPSR.html
https://www.sciencedirect.com/topics/computer-science/current-program-status-register
https://developer.arm.com/documentation/ddi0406/b/System-Level-Architecture/The-System-Level-Programmers--Model/ARM-processor-modes-and-core-registers/Program-Status-Registers--PSRs-
https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/condition-codes-1-condition-flags-and-codes
https://goiabada.github.io/docs/sections/arm-cpu/flags.html
https://heyrick.eu/assembler/psr.html
https://users.ece.utexas.edu/~valvano/EE345M/Arm_EE382N_4.pdf
https://www.youtube.com/watch?v=28MMaELXRZ0
https://azeria-labs.com/arm-conditional-execution-and-branching-part-6/
https://ece.eng.wayne.edu/~smahmud/ECECourses/ECE5620/Manuals/ARM_InstructionSet.pdf

## Slide 15: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | r0 ≥ r1 | r0 < r1
V = 1 | r0 < r1 | r0 ≥ r1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 16: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | 1 | 0
V = 1 | 0 | 1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 17: Signed vs. Unsigned Comparison
Conditional codes applied to branch instructions
Compare | Signed | Unsigned
> | BGT | BHI
>= | BGE | BHS
< | BLT | BLO
<= | BLE | BLS
== | BEQ | 
!= | BNE | 
Compare | Signed | Unsigned
> | GT | HI
≥ | GE | HS
< | LT | LO
≤ | LE | LS
== | EQ | 
≠ | NE | 

## Slide 18: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V
Notes: Here are concrete unsigned compare examples for the two branch conditions after a CMP x, y:
BHI (unsigned higher): C=1 and Z=0
Example 1: x=9 (0b1001), y=3 (0b0011). After CMP x,y the CPU computes x−y=6 without borrow, so C=1, and result≠0 so Z=0 ⇒ BHI is taken (x>y).developer.arm+1
Example 2: x=0x00FF, y=0x0001. Subtraction has no borrow (C=1) and nonzero result (Z=0) ⇒ unsigned higher, branch taken.dmulholl+1
Example 3: x=42, y=41. No borrow (C=1) and not equal (Z=0) ⇒ BHI taken.eng.auburn+1
BLS (unsigned lower or same): C=0 or Z=1
Example 1 (lower): x=3 (0b0011), y=9 (0b1001). Subtraction x−y needs a borrow, so C=0 ⇒ BLS taken (x<y).princeton+1
Example 2 (same): x=0xABCD, y=0xABCD. Subtraction yields zero, so Z=1 (and C=1 for CMP), thus “same”, and BLS is taken.developer.arm+1
Example 3 (lower): x=0, y=1. Borrow occurs (C=0), Z=0 ⇒ BLS taken.princeton+1
How to read the flags after CMP
CMP x,y sets flags from x−y: C=1 means no unsigned borrow (x≥y), C=0 means borrow occurred (x<y), and Z=1 means equality. BHI requires (C=1 and Z=0) meaning strictly greater; BLS requires (C=0 or Z=1) meaning ≤.dmulholl+1
https://developer.arm.com/documentation/dui0473/latest/condition-codes/condition-code-suffixes-and-related-flags
https://www.cs.princeton.edu/courses/archive/fall20/cos217/precepts/19assemlang/conditionflags.pdf
https://www.dmulholl.com/notes/arm-condition-flags.html
https://www.eng.auburn.edu/~nelson/courses/elec2220/slides/ARM%20prog%20model%205%20flowcontrol.pdf
https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/9dd766a6-c32c-4026-a164-0ffe7e7c9039/image.jpg?AWSAccessKeyId=ASIA2F3EMEYEYVC6Y2YM&Signature=Yp%2FAqhMlv5CD8NmMqYq318hZBX8%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEDMaCXVzLWVhc3QtMSJHMEUCIQDwOsOuBMDyKtF4dIXkDd%2Bi4vRKTrULzok8G7%2BLD01BlAIgBHlPHz9%2Bz6uEC1AgBh5%2BjH%2BZr5kEbtUZWfLUEHXsD6sq%2BgQIrP%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FARABGgw2OTk3NTMzMDk3MDUiDLRqFJAgBJUp6W%2BDKyrOBF0ysku%2FO8entYRcBcZivjDF%2BZnqrmM3X9QUlwtE8JqyNinP3zBLzDAEfze1WjiUNe42AtNcM6eNTB%2BroipKN8GOLxFNrvXePYqCgsj94Tfru7XL4WDSBbBZiNoUvVjAMh2EAFvA%2B42sZ7PzWncZpdZojIKk27t%2F1MA%2BgDpOFUOfRiCZjz41N7WZ9SRaLJzx29CYiFs1XaaPA3kbl8krSRU%2B2LYwJQ2bW8Pp%2BKQZysSMS6TJoKyeGQtmS97Q3OWsogoKYN757ScSecP%2F%2FlaUOScvktXhOM%2Br77gASkU128OQm9tNfMtY0qBdKgQDtqmF6NTFSlf2dKHHJ9Wq%2BpX4alV76juzP8RnPS7qTO5c28tw2vfptVM2SXAz%2F%2B13%2BRDPKQnL3Zt8SpNrqCLQEs%2BcZ%2BxhRjk2ANfaKdw6xF6SsFEBQVYO31NJqcpOOfdgOrFYAtc3wXhUdJ0%2FLX4mr2HxKitDOFXbiZgVikuph45iI1RKxd5CQDdeBj127YUK3eS0IhF82WiPbRFOygqBVE%2FfreSXfjlNDvtjs2zeBebluyNxmjt86otMe3CE5alb4t2UI46HuL77Z6bX6UstBuVoHqmhweAX9I5H6Xu93ms%2BDovmDoOeRAQ8SItZfAyy%2FPWAfs1JEUYSaNGLB%2ByFhj8mFcHxWyMfzZV3jQPyDqfxQijfR%2FFaMOl0cq8pPszbKnyTtFIYoOOYg3%2Bo82YmDw8u%2BO6NMA84%2BYjuuPBGGelwICnZOMCUZIYHm%2F2WjDEj%2BnZf%2BGNQ1W%2B%2BLeZ%2FOry7ZSKcMLmKrMYGOpoBB8dN%2BSOnzXKvSiinrvV8CexOzKNc4oRvjlrLKmbXRm5YWiq6d0%2FrdYzxiXrnX3kBa9VBjOvWNKdblWSSjh4oicEANx8PIcCvyAj91LH9EKRAmTBnFKU19H6SOjqO3FOdePeJXE5Q1wPhrRliAMHbi9vRLrlgDlYXAthkE%2FC2kvzYDjQ2WVVGQRZn%2B5Gv7oipqCrGkbwBgk0rfg%3D%3D&Expires=1758138626
https://developer.arm.com/documentation/dui0379/e/arm-and-thumb-instructions/condition-codes
https://armasm.com/docs/branches-and-conditionals/conditionals/
https://cseweb.ucsd.edu/classes/fa15/cse30/lectures/ARM_control_transfer_detailed.pdf
https://azeria-labs.com/arm-conditional-execution-and-branching-part-6/
https://stackoverflow.com/questions/52681110/questions-about-it-conditional-codes-in-assembly
https://publish.obsidian.md/cynixia/ARM+Instruction+Encoding

## Slide 19: Number Interpretation
If they represent signed numbers, the latter is greater
(1 > -1).
If they represent unsigned numbers, the former is greater
(4294967295 > 1).
Which is greater?
0xFFFFFFFF or 0x00000001

## Slide 20: Which is Greater: 0xFFFFFFFF or 0x00000001?
signed int x, y ; x = -1;
y = 1; if (x > y)
...
unsigned int x, y ;
x = 4294967295;
y = 1;
if (x > y)
...
BLE: Branch if less than or equal, signed ≤
BLS: Branch if lower or same, unsigned ≤
It’s software’s responsibility to tell computer how to interpret data:
If written in C, declare the signed vs unsigned variable
If written in Assembly, use signed vs unsigned branch instructions
MOV r6, #0xFFFFFFFF MOV r5, #0x00000001
CMP r5, r6 BLE Then_Clause
...
MOV r6, #0xFFFFFFFF MOV r5, #0x00000001
CMP r5, r6 BLS Then_Clause
...
Notes: Yes—MOV can be used instead of MOVS here, because CMP sets the flags needed for BLE/BLS, and the preceding MOV/MOVS that load r6 and r5 do not need to affect APSR for the compare-and-branch to work.arm+1
Specifically, CMP updates N, Z, C, V based on r5 − r6, and BLE/BLS test those flags; therefore, whether the earlier loads used MOV or MOVS is irrelevant to the branch decision as long as CMP immediately precedes it.eng.auburn+1
Use MOVS only if the move itself must set flags for a following conditional, which is not the case in the shown pattern where flags come solely from CMP.developer.arm+1
Summary for the snippet:
Replace “MOVS r6, #0xFFFFFFFF” with “MOV r6, #0xFFFFFFFF” safely.csie.ntu+1
Replace “MOVS r5, #0x00000001” with “MOV r5, #0x00000001” safely.developer.arm+1
Keep “CMP r5, r6” then “BLE/BLS …”, because CMP is the instruction that defines flags for signed BLE or unsigned BLS.armasm+1
https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/condition-codes-1-condition-flags-and-codes
https://armasm.com/docs/branches-and-conditionals/conditionals/
https://www.eng.auburn.edu/~nelson/courses/elec2220/slides/ARM%20prog%20model%205%20flowcontrol.pdf
https://developer.arm.com/documentation/den0042/latest/Unified-Assembly-Language-Instructions/Instruction-set-basics/Conditional-execution
https://azeria-labs.com/arm-conditional-execution-and-branching-part-6/
https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf
https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/b510844e-5870-455a-95b1-295f00e5f0e6/image.jpg?AWSAccessKeyId=ASIA2F3EMEYEZ2SIECMP&Signature=o6xlK7h8cbRJdcd1sOO8qTLYptQ%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEDMaCXVzLWVhc3QtMSJHMEUCIAUXBCCVRCs5WcDDZG86JMfMIIX1CPn4xuBrgTMCkWmIAiEA3ZoWrSD9v5qV2YQfaCj8J7dubreoXUJ1iLB%2FNzc8TeAq%2BgQIrP%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FARABGgw2OTk3NTMzMDk3MDUiDK29IBJPfnt%2FHqfTRirOBOTWQ%2FopIptKRvezzfLQtzZocgQxr%2FU0C6Ev75otOOoDF7mChUJk7gJgJNy1FHRI5vfUzOthPQMKVeP0TfLbrAInHf2agUA8K%2B2PTps0kxg1tO0Mg9OcPUFQZ7luV%2FDWrnXR0sSQnSRgrOsvXNxaYF5plANJ4rtT1NhoQzjBoPmpLDyf2ulC3FZBzpt8u5HstRfm8E23%2BaSmlyYZJ39g3b8Vy%2ByKGfUf%2BqYgWAK%2Famqm9cugjHfbfVisOmhurVy3pd5QiTyIHriDiGe9o4VXeQUjsS4ZjJlmrFATYOXfxK04xz%2BaFpqCbIQxRtPnBOkmMDTANJfeAdvsM96XTOJFIaLQahScx8HoiiUHzIq7H4nTjwBi45BkYwxtDh6ytiXp3cMvX2KaWj5H%2BK0%2FuPX30vyO3RHfBLHZbDl5Z8KYHzDgE0Jc9XYpA90RI5yKnY6kfWmY7MI2A7AaMTpodo%2F%2BBjgaKSziMLrpGEb9H%2FUNnhQodR8PvWtY57zhnwOt1cJiT0i92UewHJJOLRH9mUjY%2FO0rk07g5rB%2BdfWVUvieWW7Vmon9yDxgvGGOUu4da1eOQalap8sWpyoe9qpEF9AUwlhc79v1h3D1Ji4V41mRqjSbP1er92blZ8m5gGnM3uiGu2g9uD7yR1XMiNU5BV%2Bg2W%2Ft9IKU0bwgjGDzDA4DIHaKoDaoHsMZIh%2B%2BD1AYIHuYjzDuVbHbo1XioSP541dgfDgt1hTsrLmBYRjnQfXXGQy%2F97eS9FQPSRsjHw2%2F468FmVoVKdWhdYz%2F9x%2FcyMs9MICIrMYGOpoBSpPwC5%2Fk%2FZbTmfpm34dzo8KIIxAD1dPPSvB%2FMRzg146icCW%2B1wSyhA%2Fans8Yo5PCj%2BkssNzcNsN5B1opYn4oiYL5pLCQwU%2B66pbLpfdNcDy4xIFlPNG0vZ8DNyzMLGldnaUeWZctmLSBbt3%2Fwd65E2fqdWpKjrAWO5bLnwXX8NWaqLh67LwlOytGABPlmsyhWQEj99HTmDOrNQ%3D%3D&Expires=1758137046
https://stackoverflow.com/questions/45898438/understanding-cmp-instruction
https://www.dmulholl.com/notes/arm-condition-flags.html
https://www.cs.princeton.edu/courses/archive/spr19/cos217/lectures/14_Assembly2.pdf

## Slide 21: If-then Statement
C Program
// a is signed integer if (a < 0 ) { a = 0 – a; } x = x + 1;
; r1 = a (signed integer), r2 = x
CMP r1, #0 ; Compare a with 0
BGE endif ; Go to endif if a ≥ 0
then RSB r1, r1, #0 ; a = - a;
endif ADD r2, r2, #1 ; x = x + 1
Implementation 1:

## Slide 22: If-then Statement
; r1 = a, r2 = x
CMP r1, #0 ; Compare a with 0
RSBLT r1, r1, #0 ; a = 0 - a if a < 0
ADD r2, r2, #1 ; x = x + 1
Implementation 2:
C Program
// a is signed integer if (a < 0 ) { a = 0 – a; } x = x + 1;
RSBLT r1, r1, #0:: conditional execution of the RSB instruction with the condition code LT. If the condition LT (less than) is true, then set r1=0−r1
Notes: RSBLT r1, r1, #0 is a conditional execution of the RSB (Reverse Subtract) instruction with the condition code LT.

## Slide 23: Compound Boolean Expression
x > 20 && x < 25
x == 20 || x == 25
!(x == 20 || x == 25)
C Program | Assembly Program
// x is a signed integer if(x <= 20 ¦¦ x >= 25){ a = 1 } | ; r0 = x CMP r0, #20 ; compare x and 20 BLE then ; go to then if x ≤ 20 CMP r0, #25 ; compare x and 25 BLT endif ; go to endif if x < 25 then MOV r1, #1 ; a = 1 endif
Logical OR operator (||) employs short-circuit evaluation, meaning it evaluates expressions from left to right and stops as soon as the result of the entire expression is determined. For (cond1||cond2): If cond1 evaluates to true (non-zero), the overall result of the || operation is already known to be true, so cond2 is not evaluated. If cond1 evaluates to false (zero), the evaluation proceeds to the next operand cond2.

## Slide 24: If-then-else
C Program
if (a == 1) b = 3; else b = 4;
; r1 = a, r2 = b
CMP r1, #1 ; compare a and 1
BNE else ; go to else if a ≠ 1
then MOV r2, #3 ; b = 3
B endif ; go to endif
else MOV r2, #4 ; b = 4
endif

## Slide 25: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
B check
loop ADD r1, r1, r0 ; sum += i
ADD r0, r0, #1 ; i++
check CMP r0, #10 ; check whether i < 10
BLT loop ; loop if signed less than
endloop
Implementation 1:

## Slide 26: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
loop CMP r0, #10 ; check whether i < 10
BGE endloop ; skip if ≥
ADD r1, r1, r0 ; sum += i
ADD r0, r0, #1 ; i++
B loop
endloop
Implementation 2:

## Slide 27: Combined Program Status Registers (xPSR)
Notes: The Q flag is sticky in that, when set to 1 by an instruction, it remains set until explicitly cleared to 0 by an MSR instruction writing to the CPSR. Instructions cannot execute conditionally on the status of the Q flag.
Saturation arithmetic is a version of arithmetic in which all operations such as addition and multiplication are limited to a fixed range between a minimum and maximum value. If the result of an operation is greater than the maximum it is set ("clamped") to the maximum, while if it is below the minimum it is clamped to the minimum. The name comes from how the value becomes "saturated" once it reaches the extreme values; further additions to a maximum or subtractions from a minimum will not change the result.
For example, if the valid range of values is from -100 to 100, the following operations produce the following values:
60 + 43 = 100
(60 + 43) − 150 = −50
43 − 150 = −100
60 + (43 − 150) = −40
10 × 11 = 100
99 × 99 = 100
30 × (5 − 1) = 100
30×5 − 30×1 = 70
Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 28: Condition Codes
The possible condition codes are listed below:
    Note AL is the default and does not need to be specified
Not equal
Unsigned higher or same
Unsigned lower
Negative
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Signed Less than
Signed Greater than
Signed Less than or equal
Always
Signed Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 29: Conditional Execution
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 30: Conditional Execution Example: Signed Int
int32_t a; //a is signed int
...
if (a <= 0)
y = -1;
else
y = 1;
CMP r0, #0
MOVLE r1, #-1 ; executed if LE
MOVGT r1, #1 ; executed if GT
LE: Signed Less than or Equal
GT: Signed Greater Than
a ⟶ r0
y ⟶ r1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 31: Conditional Execution Example: Signed Int
int32_t a;
...
if (a==1 || a==7 || a==11)
y = 1;
else
y = -1;
CMP r0, #1
CMPNE r0, #7 ; executed if r0 != 1
CMPNE r0, #11 ; executed if r0 != 7
MOVEQ r1, #1
MOVNE r1, #-1
a ⟶ r0
y ⟶ r1
CMP r0, #1 compares a with 1 and sets Z=1 if equal, else Z=0.
CMPNE r0, #7 runs only if the previous compare was not equal, and if it runs, it refreshes the flags by comparing a with 7.
CMPNE r0, #11 runs only if a was not 1 and not 7, and if it runs, it compares a with 11 to set Z accordingly.
MOVEQ r1, #1 executes only when Z=1 from any of the comparisons, so y becomes 1 if a matched 1, 7, or 11.
MOVNE r1, #-1 executes only when Z=0 after all relevant compares, so y becomes -1 when none of the values matched.
Notes: NE: Not Equal
EQ: Equal
Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 32: Compound Boolean Expression: Signed Int
C Program | Assembly Program
int32_t x; ... if(x <= 20 ¦¦ x >= 25){ a = 1; } | ; x ⟶ r0, a ⟶ r1 CMP r0, #20 ; compare x and 20 MOVLE r1, #1 ; a=1 if less or equal CMP r0, #25 ; compare x and 25 MOVGE r1, #1 ; a=1 if greater or equal endif

## Slide 33: Example 1: Greatest Common Divider (GCD)
; suppose r0 = a and r1 = b
gcd CMP r0, r1 ; a > b?
BEQ end ; if a = b, done
BLO less ; a < b
SUB r0, r0, r1 ; a = a – b
B gcd
less SUB r1, r1, r0 ; b = b – a
B gcd
end
Euclid’s Algorithm
gcd CMP r0, r1
SUBHI r0, r0, r1
SUBLO r1, r1, r0
BNE gcd
uint32_t a, b;
while (a != b ) {
if (a > b)
a = a – b;
else
b = b – a;
}
Explanation of above short version:
CMP r0, r1 compares r0 and r1, setting Z=1 if r0 == r1, which is the termination condition when tested by BNE later
SUBHI r0, r0, r1 executes only if the previous compare set HI (unsigned “higher”), i.e., r0 > r1 for unsigned ints r0 and r1
SUBLO r1, r1, r0 executes only if the previous compare of unsigned ints set LO (unsigned “lower”), i.e., r0 < r1 for unsigned ints r0 and r1
BNE gcd branches back to the label if Z=0 from the CMP, i.e., while r0 != r1; when they become equal, Z=1 and the loop falls through, leaving r0 == r1 == gcd(a, b)

## Slide 34: Example 2
int foo(int x, int y) {
if ( x + y < 0 )
return 0;
else
return 1;
}
foo ADDS r0, r0, r1
BPL PosOrZ
MOV r0, #0
done MOV pc, lr
PosOrZ MOV r0, r1
B done
foo ADDS r0, r0, r1 ; r1 = x + y, setting CCs
MOVPL r0, #1 ; return 1 if n bit = 0
MOVMI r0, #0 ; return 0 if n bit = 1
MOV pc, lr ; exit foo function
BPL PosOrZ: Branch to PosOrZ if condition PL is true (N == 0 indicating Positive or Zero) for ADDS r0, r0, r1
MOVPL r0, #1: conditional move that executes only when condition PL is true
MOVMI r0, #0: conditional move that executes only when condition MI (N == 1 indicating Negative) is true
Notes: BPL label
Branch if PLus (Positive or Zero)

## Slide 35: Combination
Except that it does not change the status flags, CBZ Rn,label is equivalent to:
  CMP Rn, #0
  BEQ label
Except that it does not change the status flags, CBNZ Rn,label is equivalent to:
  CMP Rn, #0
  BNE label
Instruction | Operands | Brief description
CBZ | Rn, label | Compare and Branch if Zero
CBNZ | Rn, label | Compare and Branch if Non-Zero

## Slide 36: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: ?? | Output: ??

## Slide 37: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: 0, 1 Break: break out of the loop | Output: 0, 1, 3, 4 Continue: skip the current loop iteration

## Slide 38: Break and Continue
C Program | Assembly Program
// Find string length char str[] = "hello"; int len = 0; for( ; ; ) { if (*str == '\0') break; str++; len++; } | ; r0 = string memory address ; r1 = string length MOV r1, #0 ; len = 0 loop LDRB r2, [r1] CBNZ r2, notZero B endloop notZero ADD r0, r0, #1 ; str++ ADD r1, r1, #1 ; len++ B loop endloop

## Slide 39: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 40: Summary: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 41: Summary: Conditionally Executed
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V