## Slide 1: Zonghua Gu
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 5
Memory Access
Exercises ANS
Fall 2025
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Question: Endianness
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
What are the memory address of these four words?
Word 3
Word 2
Word 1
Word 0

## Slide 3: Answer: Endianness
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
0x0012
Addr
=
0x0008
Addr
=
0x0004
Addr
=
0x0000
Word 3
Word 2
Word 1
Word 0
What are the memory address of these four words?
Same as the address of the lowest-address Byte
(this is true for either Little-Endian or Big-Endian ordering)

## Slide 4: Question: Endianness
Q: Assume Big-Endian ordering. If a 32-bit word resides at memory address N, what is the address of:
  (a) The MSB (Most Significant Byte)
  (b) The 16-bit half-word corresponding to the most significant half of the word
Q: Redo the question assuming Little-Endian ordering.
MSB
LSB
Big-Endian
N
N+1
N+2
N+3
LSB
MSB
Little-Endian
N
N+1
N+2
N+3

## Slide 5: Answer: Endianness
A: With Big-Endian ordering:
  (a) Address of MSB: N
  (b) Address of 16-bit half-word corresponding to the most significant half of the word: N (the half-word has address range of [N, N+1], so its address is N)
With Little-Endian ordering:
  (a) Address of MSB: N+3
  (b) Address of 16-bit half-word corresponding to the most significant half of the word: N+2 (the half-word has address range of [N+2, N+3], so its address is N+2)
MSB
LSB
Big-Endian
LSB
MSB
Little-Endian
N
N+1
N+2
N+3
N
N+1
N+2
N+3

## Slide 6: Question: Endianness
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
?
The word stored at address 0x20008000
with Big-Endian ordering is
?
The word stored at address 0x20008000
with Little-Endian ordering is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 7: Answer: Endianness
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
0xEE8C90A7
The word stored at address 0x20008000
with Big-Endian ordering is
0xA7908CEE
The word stored at address 0x20008000
with Little-Endian ordering is
Endianness only specifies byte order, not bit order in a byte!
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 8: Endianness
LDR r11, [r0]
; r0 = 0x20008000
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
r11 before load
0x12345678
r11 after load w/ Big-Endian ordering
r11 after load w/ Little-Endian ordering
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 9: Endianness ANS
LDR r11, [r0]
; r0 = 0x20008000
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
r11 before load
0x12345678
r11 after load w/ Big-Endian ordering
r11 after load w/ Little-Endian ordering
0xA7908CEE
0xEE8C90A7
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 10: Data Alignment
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand:
Review

## Slide 11: Question: Data Alignment
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each). How many memory cycles are required to read each of the following from memory?
  (a) A 2-Byte operand read from decimal address 5
  (b) A 2-Byte operand read from decimal address 15
  (c) A 4-Byte operand read from decimal address 10
  (d) A 4-Byte operand read from decimal address 20

## Slide 12: Answer: Data Align
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. How many memory cycles are required to read each of the following from memory?
  (a) A 2-Byte operand read from decimal address 5
  (b) A 2-Byte operand read from decimal address 15
  (c) A 4-Byte operand read from decimal address 10
  (d) A 4-Byte operand read from decimal address 20
A: (a) The operand contains memory content in address range [5,6]. It can be read in 1 memory cycle; the memory controller returns a word in address range [4,7]. The operand can be obtained via 1-Byte offset addressing into the word.
(b) The operand contains memory content in address range [15,16]. It can be read in 2 memory cycles; the memory controller returns 2 words in address ranges [12,15] and [16, 19], which can be combined to return a word in address range [14,17]. The operand can be obtained via 1-Byte offset addressing into the word.
(c) The operand contains memory content in address range [10,13]. It can be read in 2 memory cycles; the memory controller returns 2 words in address ranges [8,11] and [12, 15], which can be combined to return a word with address range [10,13].
(d) The operand contains memory content in address range [20,23]. Since 20%4=0, it is well-aligned, and can be read in 1 memory cycle.

## Slide 13: Question: Data Align
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each).
  (a) What is the address of MSB of the word at address 102, , assuming Little-Endian ordering?
  (b) What is the address of LSB of the word at address 102, , assuming Little-Endian ordering?
  (b) How many memory cycles are required to read the word at address 102?
  (c) How many memory cycles are required to read the half word at address 102?

## Slide 14: Answer: Data Align
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each).
  (a) What is the address of MSB of the word at address 102, , assuming Little-Endian ordering?
  (b) What is the address of LSB of the word at address 102, , assuming Little-Endian ordering?
  (b) How many memory cycles are required to read the word at address 102?
  (c) How many memory cycles are required to read the half word at address 102?
A:
  (a) MSB of the word at address 102 is 105
  (b) LSB of the word at address 102 is 102
  (c) 2 cycles.
  (d) 1cycle.
Notes: Reading the 32-bit word at address 102 spans addresses 102..105, which cross a 4-byte alignment boundary if the bus expects aligned words at multiples of 4 (e.g., aligned words at 100 and 104). Since 102 is misaligned, the access requires two aligned 32-bit bus cycles (one covering 100..103 and one covering 104..107) with the CPU combining bytes
Reading a 16-bit halfword at address 102 uses bytes 102..103, which reside within the same aligned 32-bit word (100..103). On a 32-bit bus that supports halfword transfers, this is a single bus cycle

## Slide 15: Answer: Memory Cycles
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide.
  It takes ____ memory cycle(s) to read a Byte from memory
  It takes ____ memory cycle(s) to read a half-word from memory
  It takes ____ memory cycle(s) to read a word from memory
  It takes ____ memory cycle(s) to read a double word from memory

## Slide 16: Answer: Memory Cycles
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide.
  It takes ____ memory cycle(s) to read a Byte from memory
  It takes ____ memory cycle(s) to read a half-word from memory
  It takes ____ memory cycle(s) to read a word from memory
  It takes ____ memory cycle(s) to read a double word from memory
A:
  It takes __1__ memory cycle(s) to read a Byte from memory
  It takes __1 or 2__ memory cycle(s) to read a half-word from memory
  It takes __1 or 2__ memory cycle(s) to read a word from memory
  It takes __2 or 3__ memory cycle(s) to read a double word from memory (a double word may span at most 3 consecutive words in memory)

## Slide 17: Question: Arrays
Q: If the first element of a one-dimensional array x[] is stored at memory address 0x12345678, what is address of the second element if the array x[] contains
  (a) chars
  (b) shorts
  (c) ints
  (c) longs

## Slide 18: Answer: Arrays
Q: If the first element of a one-dimensional array x[] is stored at memory address 0x12345678, what is address of the second element if the array x[] contains
  (a) chars
  (b) shorts
  (c) ints
  (c) longs
A: x[1]’s address is x’s address plus the data type size in Bytes
  (a) chars: 0x12345678+1= 0x12345679
  (b) shorts: 0x12345678+2= 0x1234567A
  (c) ints: 0x12345678+4= 0x1234567C
  (c) longs: 0x12345678+8= 0x12345680

## Slide 19: Load Multiple Registers

## Slide 20: LDM
Memory Address | Memory Data
0x8010 | 0x00000001
0x800c | 0xFEEDDEAF
0x8008 | 0x00008888
0x8004 | 0x12340000
0x8000 | 0xBABE0000
r3
Assume that memory and registers r0 through r3 appear as follows. Suppose r3 = 0x8000. Describe the memory and register contents after executing each instruction (individually, not sequentially):
  LDMIA r3!, {r0, r1, r2}
  Or LDMIB r3!, {r2, r1, r0}
Notes: Address Register[1] 0x8010 0x00000001 0x13 r0[1] 0x800c 0xFEEDDEAF 0xFFFFFFFF r1[1] 0x8008 0x00008888 0xEEEEEEEE r2[1] 0x8004 0x12340000 0x8000 r3[1] 0x8000 0xBABE0000[1]

## Slide 21: LDM ANS
Memory Address | Memory Data
0x8010 | 0x00000001
0x800c | 0xFEEDDEAF
0x8008 | 0x00008888
0x8004 | 0x12340000
0x8000 | 0xBABE0000
r3
Assume that memory and registers r0 through r3 appear as follows. Suppose r3 = 0x8000. Describe the memory and register contents after executing each instruction (individually, not sequentially):
  LDMIA r3!, {r0, r1, r2}
  Or LDMIB r3!, {r2, r1, r0}
ANS:
  After LDMIA r3!, {r0, r1, r2}
  r0 = 0xBABE0000 (loaded from 0x8000)
  r1 = 0x12340000 (loaded from 0x8004)
  r2 = 0x00008888 (loaded from 0x8008)
  r3 = 0x800C (auto-incremented)
  Or after LDMIB r3!, {r2, r1, r0}
  r0 = 0x12340000 (loaded from 0x8004)
  r1 = 0x00008888 (loaded from 0x8008)
  r2 = 0xFEEDDEAF (loaded from 0x800c)
  r3 = 0x800C (auto-incremented)
Notes: Address Register[1] 0x8010 0x00000001 0x13 r0[1] 0x800c 0xFEEDDEAF 0xFFFFFFFF r1[1] 0x8008 0x00008888 0xEEEEEEEE r2[1] 0x8004 0x12340000 0x8000 r3[1] 0x8000 0xBABE0000[1]

## Slide 22: LDR
Suppose R2 and R5 hold the values 8 and 0x23456789 After following code runs on a Big-Endian system, what value is in R7? How about in a little-endian system?
  STR R5, [R2, #0]
  LDRB R7, [R2, #1]
  LDRSH R7, [R2, #1]
  LDRSH R7, [R2, #2]
Notes: You are absolutely correct! For LDRSH R7, [R2, #2] in little-endian, the result is 0x00002345.image.jpg
After STR stores 0x23456789 at address 8:
Big-endian layout:
Address 8: 0x23, Address 9: 0x45, Address 10: 0x67, Address 11: 0x89
Little-endian layout:
Address 8: 0x89, Address 9: 0x67, Address 10: 0x45, Address 11: 0x23
Results for each instruction:
LDRB R7, [R2, #1] (byte at address 9):
Big-endian: R7 = 0x00000045
Little-endian: R7 = 0x00000067
LDRSH R7, [R2, #1] (halfword at addresses 9-10):
Big-endian: bytes 0x45, 0x67 → 0x4567 → R7 = 0x00004567
Little-endian: bytes 0x67, 0x45 → 0x4567 → R7 = 0x00004567
LDRSH R7, [R2, #2] (halfword at addresses 10-11):
Big-endian: bytes 0x67, 0x89 → 0x6789 → R7 = 0x00006789
Little-endian: bytes 0x45, 0x23 → 0x2345 → R7 = 0x00002345
I was wrong earlier - in little-endian, the halfword at offset +2 consists of bytes 0x45 (at address 10) and 0x23 (at address 11), which reconstructs to 0x2345, not 0x4523.

## Slide 23: LDRB R7, [R2, #1] ANS
ANS after LDRB R7, [R2, #1] (detailed explanations not needed for exam):
  STR stores a 32-bit register value to memory at base-plus-immediate without changing the base, and LDRB loads a single byte and zero-extends to 32 bits, so endianness only affects which byte resides at offset +1.
  R2 holds 8 (base address), and R5 holds 0x23456789; first the store writes that 32-bit word to memory at address R2+0, and then a byte load reads one byte from address R2+1 into R7.
  Big-endian: the word 0x23456789 is laid out in memory as bytes 23 45 67 89 at addresses A, A+1, A+2, A+3 respectively, so LDRB R7,[R2,#1] reads 0x45 and zero-extends it to R7 = 0x00000045.
  Little-endian: the same word is laid out as 89 67 45 23 at addresses A, A+1, A+2, A+3 respectively, so LDRB R7,[R2,#1] reads 0x67 and zero-extends it to R7 = 0x00000067.
Memory Address | Memory Data
0x0000000B | 0x89
0x0000000A | 0x67
0x00000009 | 0x45
0x00000008 | 0x23
Memory Address | Memory Data
0x0000000B | 0x23
0x0000000A | 0x45
0x00000009 | 0x67
0x00000008 | 0x89
R2
R2
Notes:   [1](https://azeria-labs.com/memory-instructions-load-and-store-part-4/)
  [2](https://developer.arm.com/documentation/ddi0403/d/Application-Level-Architecture/Instruction-Details/Alphabetical-list-of-ARMv7-M-Thumb-instructions/STR--immediate-)
  [3](https://developer.arm.com/documentation/den0042/latest/Coding-for-Cortex-R-Processors/Endianness)
  [4](http://netwinder.oregonstate.edu/pub/netwinder/docs/arm/Apps04vC.html)
  [5](https://developer.arm.com/documentation/ddi0192/a/amba-interface/little-endian-and-big-endian-operation/byte-operations)
  [6](https://developer.arm.com/documentation/dui0801/g/A32-and-T32-Instructions/STR--immediate-offset-)
  [7](https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/f7203996-0950-40fd-8a70-2a8620379d03/image.jpg?AWSAccessKeyId=ASIA2F3EMEYE3R7YOA4A&Signature=FpDzt4OypItBaZAcIbAU8055MR8%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEPb%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FwEaCXVzLWVhc3QtMSJHMEUCIQCD6wIV7ZQsrRKtLcsD2ILQWTe49vXv8PCZOBQLcawpTgIgbl1d9M%2F94eFVLN39uGn0JoPKRKF5bqt1b49GdG9YFh4q8QQIfhABGgw2OTk3NTMzMDk3MDUiDFSwzJTcAyTfOdiIEirOBPbxxRa5qZQA%2BCiHUZzGhazSu8CnmwfmvOsWjGIK7IT0CN8yJdlOrt7q09UAV5GjElVPyAy2LYjvQWXbHA4EqBFtoI%2BZ7mHFyPVgrkLq5xRKwa1uSZTW32fbBBe9cxfvbjIgFpfp7iE2DeWkIeYIJ6EnlFljFVUajrD%2FRA0SEaaR%2FzWK31hOzpXzk7sjzJgWM%2BcNJYR9%2BzsRvujpl81hFq8GYYr4PVAhyWipiGB3HP%2BVYzbKSyHlfSCmVpPf4itnB0Nv8CBNJNaepLZdXmdr21sSXbemQMxgxQw7gX6Xt3Cpn7kg4YgOGnMhAVTsOmrpsAdtOWvqLtwD8VRnp7yM%2FASyaTLOFIQgftx9prPKBCDdM613R2C5d%2B8pLod0S9wmx%2FDEXZf91AHhkWjxKy4XfApJ5aOowVP22U05YvUz%2B23S49a%2BfUmS98UURVFU7QFCGw1iF5NoGLZalykazqyhUq1Ef%2FL0FDRsR7FlxCyW6cP9ehmravO8QEDucaffun9Fn%2FyWQ5Nv1TP8g6u2MkBsKBc7MRocOI9hjExEraF%2Fg74MUV9vUmynpt3RzwBwQ%2BzhsiVC3kWDM4KPPGPkuds2kWpZAX%2BJHmwQ9SUa2B7Npe%2F290lDeN4b16yoVd7jgluVXMoiSW8mvJXMO0ixYOwf1Fo9ldfxzSO1FTp8j8ZRVipY99AmY54cdXjKULaz9DPmHaO85KZxpGgkeZcJMBzvSuIT%2BbQpy2DxH4x94WFnYVwFZl%2Fxgxcn3ziCIT0tqjx9Zto8Vp39ksY09KbGKU91MMfe1sYGOpoB1fyabXFy1WRNJ0hNyV9j3Wb4mltoiB4Bfg9K8XrBduW8weTuvQldGR3gkn%2FTfV5kthjAawy8ZXmap0UaAW7nN2MlRxeM8McdOL1RCXG2qMmfxl8CmunFyuT74FMOqqKLARH0KrJNVULNHT6kUGfuDFSb5KKNQ1qwO3iRBraFogouHjxVGjDWWF%2FlVT6tK2uMqtQYvNOTYYB4Zg%3D%3D&Expires=1758836303)
  [8](https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf)
  [9](https://stackoverflow.com/questions/78984911/how-is-data-loaded-in-big-endian-format-on-arm7tdmi-armv4t)
  [10](https://www.doulos.com/knowhow/arm-embedded/efficient-byte-swapping-using-armv6-and-armv7-ar-instructions/)
  [11](https://mariokartwii.com/armv8/ch9.html)
  [12](https://betterexplained.com/articles/understanding-big-and-little-endian-byte-order/)
  [13](http://computerscience.chemeketa.edu/armTutorial/Memory/Endianness.html)
  [14](https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf)

## Slide 24: LDRSH R7, [R2, #1] ANS
ANS after LDRSH R7, [R2, #1]:
  Big-endian: the word 0x23456789 is laid out in memory as bytes 23 45 67 89 at addresses A, A+1, A+2, A+3 respectively, so LDRSH R7, [R2, #1] reads 0x4567 and sign-extends it to R7 = 0x00004567. (Sign bit is 0 for 0x4567)
  Little-endian: the same word is laid out as 89 67 45 23 at addresses A, A+1, A+2, A+3 respectively, so LDRSH R7, [R2, #1] reads 0x4567 and sign-extends it to R7 = 0x00004567. (Sign bit is 0 for 0x4567)
Memory Address | Memory Data
0x0000000B | 0x89
0x0000000A | 0x67
0x00000009 | 0x45
0x00000008 | 0x23
Memory Address | Memory Data
0x0000000B | 0x23
0x0000000A | 0x45
0x00000009 | 0x67
0x00000008 | 0x89
R2
R2
Notes:   [1](https://azeria-labs.com/memory-instructions-load-and-store-part-4/)
  [2](https://developer.arm.com/documentation/ddi0403/d/Application-Level-Architecture/Instruction-Details/Alphabetical-list-of-ARMv7-M-Thumb-instructions/STR--immediate-)
  [3](https://developer.arm.com/documentation/den0042/latest/Coding-for-Cortex-R-Processors/Endianness)
  [4](http://netwinder.oregonstate.edu/pub/netwinder/docs/arm/Apps04vC.html)
  [5](https://developer.arm.com/documentation/ddi0192/a/amba-interface/little-endian-and-big-endian-operation/byte-operations)
  [6](https://developer.arm.com/documentation/dui0801/g/A32-and-T32-Instructions/STR--immediate-offset-)
  [7](https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/f7203996-0950-40fd-8a70-2a8620379d03/image.jpg?AWSAccessKeyId=ASIA2F3EMEYE3R7YOA4A&Signature=FpDzt4OypItBaZAcIbAU8055MR8%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEPb%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FwEaCXVzLWVhc3QtMSJHMEUCIQCD6wIV7ZQsrRKtLcsD2ILQWTe49vXv8PCZOBQLcawpTgIgbl1d9M%2F94eFVLN39uGn0JoPKRKF5bqt1b49GdG9YFh4q8QQIfhABGgw2OTk3NTMzMDk3MDUiDFSwzJTcAyTfOdiIEirOBPbxxRa5qZQA%2BCiHUZzGhazSu8CnmwfmvOsWjGIK7IT0CN8yJdlOrt7q09UAV5GjElVPyAy2LYjvQWXbHA4EqBFtoI%2BZ7mHFyPVgrkLq5xRKwa1uSZTW32fbBBe9cxfvbjIgFpfp7iE2DeWkIeYIJ6EnlFljFVUajrD%2FRA0SEaaR%2FzWK31hOzpXzk7sjzJgWM%2BcNJYR9%2BzsRvujpl81hFq8GYYr4PVAhyWipiGB3HP%2BVYzbKSyHlfSCmVpPf4itnB0Nv8CBNJNaepLZdXmdr21sSXbemQMxgxQw7gX6Xt3Cpn7kg4YgOGnMhAVTsOmrpsAdtOWvqLtwD8VRnp7yM%2FASyaTLOFIQgftx9prPKBCDdM613R2C5d%2B8pLod0S9wmx%2FDEXZf91AHhkWjxKy4XfApJ5aOowVP22U05YvUz%2B23S49a%2BfUmS98UURVFU7QFCGw1iF5NoGLZalykazqyhUq1Ef%2FL0FDRsR7FlxCyW6cP9ehmravO8QEDucaffun9Fn%2FyWQ5Nv1TP8g6u2MkBsKBc7MRocOI9hjExEraF%2Fg74MUV9vUmynpt3RzwBwQ%2BzhsiVC3kWDM4KPPGPkuds2kWpZAX%2BJHmwQ9SUa2B7Npe%2F290lDeN4b16yoVd7jgluVXMoiSW8mvJXMO0ixYOwf1Fo9ldfxzSO1FTp8j8ZRVipY99AmY54cdXjKULaz9DPmHaO85KZxpGgkeZcJMBzvSuIT%2BbQpy2DxH4x94WFnYVwFZl%2Fxgxcn3ziCIT0tqjx9Zto8Vp39ksY09KbGKU91MMfe1sYGOpoB1fyabXFy1WRNJ0hNyV9j3Wb4mltoiB4Bfg9K8XrBduW8weTuvQldGR3gkn%2FTfV5kthjAawy8ZXmap0UaAW7nN2MlRxeM8McdOL1RCXG2qMmfxl8CmunFyuT74FMOqqKLARH0KrJNVULNHT6kUGfuDFSb5KKNQ1qwO3iRBraFogouHjxVGjDWWF%2FlVT6tK2uMqtQYvNOTYYB4Zg%3D%3D&Expires=1758836303)
  [8](https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf)
  [9](https://stackoverflow.com/questions/78984911/how-is-data-loaded-in-big-endian-format-on-arm7tdmi-armv4t)
  [10](https://www.doulos.com/knowhow/arm-embedded/efficient-byte-swapping-using-armv6-and-armv7-ar-instructions/)
  [11](https://mariokartwii.com/armv8/ch9.html)
  [12](https://betterexplained.com/articles/understanding-big-and-little-endian-byte-order/)
  [13](http://computerscience.chemeketa.edu/armTutorial/Memory/Endianness.html)
  [14](https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf)

## Slide 25: LDRSH R7, [R2, #2] ANS
ANS after LDRSH R7, [R2, #1]:
  Big-endian: the word 0x23456789 is laid out in memory as bytes 23 45 67 89 at addresses A, A+1, A+2, A+3 respectively, so LDRSH R7, [R2, #1] reads 0x6789 and sign-extends it to R7 = 0x00006789.
  Little-endian: the same word is laid out as 89 67 45 23 at addresses A, A+1, A+2, A+3 respectively, so LDRSH R7, [R2, #1] reads 0x2345 and sign-extends it to R7 = 0x00002345.
Memory Address | Memory Data
0x0000000B | 0x89
0x0000000A | 0x67
0x00000009 | 0x45
0x00000008 | 0x23
Memory Address | Memory Data
0x0000000B | 0x23
0x0000000A | 0x45
0x00000009 | 0x67
0x00000008 | 0x89
R2
R2
Notes:   [1](https://azeria-labs.com/memory-instructions-load-and-store-part-4/)
  [2](https://developer.arm.com/documentation/ddi0403/d/Application-Level-Architecture/Instruction-Details/Alphabetical-list-of-ARMv7-M-Thumb-instructions/STR--immediate-)
  [3](https://developer.arm.com/documentation/den0042/latest/Coding-for-Cortex-R-Processors/Endianness)
  [4](http://netwinder.oregonstate.edu/pub/netwinder/docs/arm/Apps04vC.html)
  [5](https://developer.arm.com/documentation/ddi0192/a/amba-interface/little-endian-and-big-endian-operation/byte-operations)
  [6](https://developer.arm.com/documentation/dui0801/g/A32-and-T32-Instructions/STR--immediate-offset-)
  [7](https://ppl-ai-file-upload.s3.amazonaws.com/web/direct-files/attachments/images/92151853/f7203996-0950-40fd-8a70-2a8620379d03/image.jpg?AWSAccessKeyId=ASIA2F3EMEYE3R7YOA4A&Signature=FpDzt4OypItBaZAcIbAU8055MR8%3D&x-amz-security-token=IQoJb3JpZ2luX2VjEPb%2F%2F%2F%2F%2F%2F%2F%2F%2F%2FwEaCXVzLWVhc3QtMSJHMEUCIQCD6wIV7ZQsrRKtLcsD2ILQWTe49vXv8PCZOBQLcawpTgIgbl1d9M%2F94eFVLN39uGn0JoPKRKF5bqt1b49GdG9YFh4q8QQIfhABGgw2OTk3NTMzMDk3MDUiDFSwzJTcAyTfOdiIEirOBPbxxRa5qZQA%2BCiHUZzGhazSu8CnmwfmvOsWjGIK7IT0CN8yJdlOrt7q09UAV5GjElVPyAy2LYjvQWXbHA4EqBFtoI%2BZ7mHFyPVgrkLq5xRKwa1uSZTW32fbBBe9cxfvbjIgFpfp7iE2DeWkIeYIJ6EnlFljFVUajrD%2FRA0SEaaR%2FzWK31hOzpXzk7sjzJgWM%2BcNJYR9%2BzsRvujpl81hFq8GYYr4PVAhyWipiGB3HP%2BVYzbKSyHlfSCmVpPf4itnB0Nv8CBNJNaepLZdXmdr21sSXbemQMxgxQw7gX6Xt3Cpn7kg4YgOGnMhAVTsOmrpsAdtOWvqLtwD8VRnp7yM%2FASyaTLOFIQgftx9prPKBCDdM613R2C5d%2B8pLod0S9wmx%2FDEXZf91AHhkWjxKy4XfApJ5aOowVP22U05YvUz%2B23S49a%2BfUmS98UURVFU7QFCGw1iF5NoGLZalykazqyhUq1Ef%2FL0FDRsR7FlxCyW6cP9ehmravO8QEDucaffun9Fn%2FyWQ5Nv1TP8g6u2MkBsKBc7MRocOI9hjExEraF%2Fg74MUV9vUmynpt3RzwBwQ%2BzhsiVC3kWDM4KPPGPkuds2kWpZAX%2BJHmwQ9SUa2B7Npe%2F290lDeN4b16yoVd7jgluVXMoiSW8mvJXMO0ixYOwf1Fo9ldfxzSO1FTp8j8ZRVipY99AmY54cdXjKULaz9DPmHaO85KZxpGgkeZcJMBzvSuIT%2BbQpy2DxH4x94WFnYVwFZl%2Fxgxcn3ziCIT0tqjx9Zto8Vp39ksY09KbGKU91MMfe1sYGOpoB1fyabXFy1WRNJ0hNyV9j3Wb4mltoiB4Bfg9K8XrBduW8weTuvQldGR3gkn%2FTfV5kthjAawy8ZXmap0UaAW7nN2MlRxeM8McdOL1RCXG2qMmfxl8CmunFyuT74FMOqqKLARH0KrJNVULNHT6kUGfuDFSb5KKNQ1qwO3iRBraFogouHjxVGjDWWF%2FlVT6tK2uMqtQYvNOTYYB4Zg%3D%3D&Expires=1758836303)
  [8](https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf)
  [9](https://stackoverflow.com/questions/78984911/how-is-data-loaded-in-big-endian-format-on-arm7tdmi-armv4t)
  [10](https://www.doulos.com/knowhow/arm-embedded/efficient-byte-swapping-using-armv6-and-armv7-ar-instructions/)
  [11](https://mariokartwii.com/armv8/ch9.html)
  [12](https://betterexplained.com/articles/understanding-big-and-little-endian-byte-order/)
  [13](http://computerscience.chemeketa.edu/armTutorial/Memory/Endianness.html)
  [14](https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf)