## Slide 1: Zonghua Gu
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 5
Memory Access
Exercises
Fall 2025
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Question: Endianness
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Bytes
Addr.
0003
0002
0001
0000
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
What are the memory address of these four words?
Word 3
Word 2
Word 1
Word 0

## Slide 3: Question: Endianness
Q: Assume Big-Endian ordering. If a 32-bit word resides at memory address N, what is the address of:
  (a) The MSB (Most Significant Byte)
  (b) The 16-bit half-word corresponding to the most significant half of the word
Q: Redo the question assuming Little-Endian ordering.
MSB
LSB
Big-Endian
N
N+1
N+2
N+3
LSB
MSB
Little-Endian
N
N+1
N+2
N+3

## Slide 4: Question: Endianness
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
?
The word stored at address 0x20008000
with Big-Endian ordering is
?
The word stored at address 0x20008000
with Little-Endian ordering is
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 5: Endianness
LDR r11, [r0]
; r0 = 0x20008000
Memory Address | Memory Data
0x20008003 | 0xA7
0x20008002 | 0x90
0x20008001 | 0x8C
0x20008000 | 0xEE
r11 before load
0x12345678
r11 after load w/ Big-Endian ordering
r11 after load w/ Little-Endian ordering
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 6: Data Alignment
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand:
Review

## Slide 7: Question: Data Alignment
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each). How many memory cycles are required to read each of the following from memory?
  (a) A 2-Byte operand read from decimal address 5
  (b) A 2-Byte operand read from decimal address 15
  (c) A 4-Byte operand read from decimal address 10
  (d) A 4-Byte operand read from decimal address 20

## Slide 8: Question: Data Align
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide. Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each).
  (a) What is the address of MSB of the word at address 102, , assuming Little-Endian ordering?
  (b) What is the address of LSB of the word at address 102, , assuming Little-Endian ordering?
  (b) How many memory cycles are required to read the word at address 102?
  (c) How many memory cycles are required to read the half word at address 102?

## Slide 9: Answer: Memory Cycles
Q: Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide.
  It takes ____ memory cycle(s) to read a Byte from memory
  It takes ____ memory cycle(s) to read a half-word from memory
  It takes ____ memory cycle(s) to read a word from memory
  It takes ____ memory cycle(s) to read a double word from memory

## Slide 10: Question: Arrays
Q: If the first element of a one-dimensional array x[] is stored at memory address 0x12345678, what is address of the second element if the array x[] contains
  (a) chars
  (b) shorts
  (c) ints
  (c) longs