## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Flow Control in Assembly
Exercises ANS
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Q1
Write ARMv7 assembly for pseudocode
  if (r0 != r1) r2 = r2 + r2
ANS A:
  CMP r0, r1
  BEQ skip
  ADD r2, r2, r2
  skip:
ANS B:
  CMP r0, r1 ; Compare r0 and r1
  ADDNE r2, r2, r2 ; r2 = r2 + r2 if Not Equal
Notes: Compare r0 and r1
@ Branch to skip if r0 == r1 (skip the addition)
@ r2 = r2 + r2 (only executed if r0 != r1)

## Slide 3: Q1 ANS
Write ARMv7 assembly for pseudocode
  r1 = (r0 >> 4) & 15
ANS:
  MOV r1, r0, LSR #4
  AND r1, r1, #15
Notes: Alternative solution:
  AND r1, r0, #0xF0
  MOV r1, r1, LSR #4

## Slide 4: Q2
What is r0 equal to after running this program:
  MOV r0, #10
  MOV r1, #7
  MOV r2, #5
  CMP r1, r2
  ADDGT r0, r0, #100

## Slide 5: Q2 ANS
What is r0 equal to after running this program:
  MOV r0, #10 @ Load immediate value 10 into r0
  MOV r1, #7 @ Load immediate value 7 into r1
  MOV r2, #5 @ Load immediate value 5 into r2
  CMP r1, r2 @ Compare r1 and r2 (compute r1-r2, set flags)
  ADDGT r0, r0,100 @ Add 100 to r0 only if r1 > r2 (Greater Than)
This code sets r0 to 10, compares 7 and 5. Since 7 > 5, adds 100 to the base value of 10 to get 110
Notes: bx lr @ Branch and exchange, return to caller

## Slide 6: Q3
save[] is an array of 32-bit integers. Assume that i and k correspond to registers r1 and r2, and the base of the array save is in r0. Write the ARMv7 assembly code corresponding to this C code.
  while (save[i] == k)
  i += 1;

## Slide 7: Q3 ANS
C code:
  while (save[i] == k)
  i += 1;
ANS:
  @ r0 = &save[0] (base address of array)
  @ r1 = i (index)
  @ r2 = k (value to compare)
  loop:
  LDR r3, [r0, r1, LSL #2] @ r3 = save[i], 32-bit loads with index scaled by 4
  CMP r3, r2 @ compare save[i] with k
  BNE done @ exit loop if save[i] != k
  ADD r1, r1, #1 @ i += 1
  B loop @ repeat
  done: