## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Subroutines
Exercises ANS

## Slide 2: What is Wrong?
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r1, r3 BX pc ENDP

## Slide 3: What is Wrong? ANS
Return result should be put into r0, not r1
BX lr returns to caller
Caller Program
Extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3); int main(void){ int32_t s ... s = sum3(-1, -2, -3) + sum3(4, 5, 6); ...
Callee Program
sum3 PROC EXPORT sum3 ; r3 = sum ADD r3, r0, r1 ; sum = a1 + a2 ADD r3, r0, r2 ; sum += a3 MOV r0, r3 BX lr ENDP