## Slide 1: Zonghua Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 4
ARM Arithmetic and Logic Instructions
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a word at address 0x20000002.
  Word-address mod 4 = 0
  Can we store a word anywhere in memory?
  NO on most computers!
  A word can only be stored at an address that's divisible by 4.

## Slide 3: Logic View of Memory
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
We cannot store a halfword at address 0x20000001.
  Can you store a halfword anywhere? NO.
  A halfword can only be stored at an address that's divisible by 2.
  Memory address of a halfword is the lowest address of its two bytes.
  Halfword-address mod 2 = 0

## Slide 4: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Typically, Barrel shifters are implemented as a cascade of parallel 2-to-1 multiplexers.

## Slide 5: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
Example: S1S0 = 00
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3

## Slide 6: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
Example: S1S0 = 01
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3

## Slide 7: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Example: S1S0 = 10

## Slide 8: Implementation of Barrel Shifter
Example four-bit Barrel shifter that performs rotate right
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | D3 | D2 | D1 | D0
0 | 1 | D0 | D3 | D2 | D1
1 | 0 | D1 | D0 | D3 | D2
1 | 1 | D2 | D1 | D0 | D3
Example: S1S0 = 11

## Slide 9: ADR Pseudo-instruction
ADR: loads a program-relative or register-relative address into a register
start MOV r0,#10 ; 32-bit instruction
ADR r4,start ; 32-bit instruction
; => SUB r4,pc,#0xc

## Slide 10: 64-bit Logic Shift Left

## Slide 11: 64-bit Logic Shift Left
Example of Logic Shift Left by 3

## Slide 12: 64-bit Logic Shift Right

## Slide 13: 64-bit Logic Shift Right
Example of Logic Shift Right by 3