## Slide 1: L4 (CHAPTER 7) Programming in Assembly Part 3: Control Structures
Acknowledgement: some slides taken from instructor resources of Daniel Lewis textbook

## Slide 2: ARM programming model
31
0
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13: Stack Pointer (SP)
R14: Link Register (LR)
R15: Program Counter (PC)
N
Z
C
V
CPSR (Current Program Status Register)
Every arithmetic, logical, or shifting operation sets CPSR bits:
  N (negative), Z (zero), C (carry), V (overflow).

## Slide 3: Comparison Instructions
These instructions set only the NZCV bits of CPSR, with no other effect.
  CMP : compare
  CMN : negated compare
  TST : bit-wise test
  TEQ : bit-wise negated test

## Slide 4
Condition Code | Meaning | Requirements
EQ | Equal | Z = 1
NE | Not equal | Z = 0
CS | Carry set | C = 1
CC | Carry clear | C = 0
MI | Minus/negative | N = 1
PL | Plus/positive or zero (non-negative) | N = 0
VS | Overflow | V = 1
VC | No overflow | V = 0
HI | Unsigned > (“Higher”) | C = 1 && Z = 0
LS | Unsigned ≤ (“Lower or Same”) | C = 0 ¦¦ Z = 1
GE | Signed ≥ (“Greater than or Equal”) | N = V
LT | Signed < (“Less Than”) | N ≠ V
GT | Signed > (“Greater Than”) | Z = 0 && N = V
LE | Signed ≤ (“Less than or Equal”) | Z = 1 ¦¦ N ≠ V
AL | Always (unconditional) | only used with IT instruction
The condition is described as the state of a specific bit in the CPSR register. For example, when we compare two numbers a and b, and they turn out to be equal, we set the Zero bit (Z = 1), because a – b = 0. In this case we have EQual condition. If the first number was bigger, we would have a Greater Than condition and in the opposite case – Lower Than. There are more conditions, like Lower or Equal (LE), Greater or Equal (GE) and so on. Any one of these may be appended to any instruction mnemonic when used inside an If-Then-Else (IT) block.
Condition Codes
Notes: Exceptions: CBZ, CBNZ, CMP, CMN, NEG, TST, or TEQ.
. (E.g., “IT NE followed by ADDNE” would add only if Z ≠ 0.)

## Slide 5: ARM flow of control
All operations can be performed conditionally, testing CPSR:
  EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE
  You should never access CPSR bits directly. Always use condition codes for control flow decisions.
Branch operation:
  B fblock ;branch to code line with label ;“fblock”
  Can be performed conditionally.
  BNE fblock ;branch to code line with label ;“fblock” if NE bit is set in CPSR

## Slide 6: Branch Instructions
Branch Instructions | Operation | {S} | Notes
B{c} label | PC  PC + imm | n/a | “c” is an optional condition code (see next slide)
ITc1c2c3 cond | Each ci is one of T, E, or empty | n/a | Controls 1-4 instructions in “IT block”
BL label | PC  PC + imm; LR  rtn adr | n/a | Subroutine call
BX reg | PC  reg | n/a | “BX LR” often used as function return

## Slide 7: B{c} Instructions
Compare | Signed | Unsigned
== | BEQ | BEQ
!= | BNE | BNE
> | BGT | BHI
>= | BGE | Reverse Operands & Use BLS
< | BLT | Reverse Operands & Use BHI
<= | BLE | BLS

## Slide 8: If-Then Statement with Branch Instruction
LDR R0, [addr(a)] CMP R0,#0 ;Compare a with 0 BNE L1 ;branch to L1 if not ;equal (a!=0) LDR R0,=1 STR R0, [addr(b)] L1:
a == 0?
b = 1
Yes
No
L1:
if (a == 0) {b = 1;}
BNE L1
True Block
{b = 1;}
L1
Compare a vs. 0
ADR R1, a
LDR R0, [R1]
Shorthand notation

## Slide 9: If-Then-Else Statement with Branch Instruction: Option 1
LDR R0, [addr(a)] LDR R1, [addr(b)] CMP R0,R1 BGT L1 LDR R0,=0
B L2 L1: LDR R0,=1 L2: STR R0, [addr(c)] …
a<=b?
c = 1
c = 0
>
≤
if (a <= b) {c = 0;} else {c=1;}
BGT L1
True Block
{c = 0;}
Compare a vs. b
False Block
{c = 1;}
L1
B L2
L2

## Slide 10: If-Then-Else Statement with Branch Instruction: Option 2
LDR R0, [addr(a)] LDR R1, [addr(b)] CMP R0,R1 BLE L1 LDR R0,=1 B L2 L1: LDR R0,=0 L2: STR R0, [addr(c)] …
a<=b?
c = 1
c = 0
>
≤
if (a <= b) {c = 0;} else {c=1;}
BLE L1
False Block
{c = 1;}
Compare a vs. b
True Block
{c = 0;}
L1
B L2
L2

## Slide 11: Another Example:
C code:
  if (a < b) {x = 5; y = c + d;} else {x = c - d;}
Assembler code:
True Block
{x=5;y=c+d;}
False Block
{x=c-d;}
BGE fblock
fblock
Compare a vs. b
after
B after
True Block
{x=5;y=c+d;}
False Block
{x=c-d;}
BLT tblock
tblock
Compare a vs. b
after
B after

## Slide 12: Assembler Part 1: Compute and Test condition
; compute and test condition
ADR R4,a ; get address for a
LDR R0,[R4] ; get value of a
ADR R4,b ; get address for b
LDR R1,[R4] ; get value for b
CMP R0,R1 ; compare a and b; set GE bit in CPSR to 1 if a>=b
BGE fblock ; Branch-if-GE: if GE bit is 1 (a>=b), branch to ; label fblock (false block)

## Slide 13: Assembler Part 2: True Block
; true block: { x = 5; y = c + d; }
MOV R0,#5 ; set register R0=5
ADR R4,x ; get address for variable x
STR R0,[R4] ; store value 5 into x
ADR R4,c ; get address for variable c
LDR R0,[R4] ; get value of c
ADR R4,d ; get address for variable d
LDR R1,[R4] ; get value of d
ADD R0,R0,R1 ; compute c+d
ADR R4,y ; get address for y
STR R0,[R4] ; store c+d into y
B after ; branch around false block

## Slide 14: Assembler Part 3: False Block
; false block {x = c - d;}
fblock ADR R4,c ; get address for variable c
LDR R0,[R4] ; get value of c
ADR R4,d ; get address for variable d
LDR R1,[R4] ; get value for d
SUB R0,R0,R1 ; compute a-b
ADR R4,x ; get address for x
STR R0,[R4] ; store value of x
after ...

## Slide 15: IT Instruction
The structure of the IT instruction is “IF-Then-(Else)” and the syntax is a construct of the two letters T and E:
IT refers to If-Then (next instruction is conditional)
ITT refers to If-Then-Then (next 2 instructions are conditional)
ITE refers to If-Then-Else (next 2 instructions are conditional)
ITTE refers to If-Then-Then-Else (next 3 instructions are conditional)
ITTEE refers to If-Then-Then-Else-Else (next 4 instructions are conditional)

## Slide 16: If-Then Statement with IT Instruction
LDR R0,address(a) CMP R0,#0 ;Compare R0 with 0 ITT EQ ;If-Then-Then: next 2
;instructions are conditional
LDREQ R0,=1 ; in case EQ=1 STREQ R0,address(b); in case EQ=1
a == 0?
b = 1
Yes
No
L1:
if (a == 0) b = 1 ;

## Slide 17: If-Then-Else Statement with IT Instruction
LDR R0, [addr(a)] LDR R1, [addr(b)] CMP R0, R1 ;Compare R0 with R1 ITE GT ;If-Then-Else: next 2 ;instructions are conditional
LDRGT R0,=1 ; in case GT=1 LDRLE R0,=0 ; in case LE=1 STR R0, [addr[c])
a<=b?
c = 1
c = 0
>
≤
if (a <= b) {c = 0;} else {c=1;}

## Slide 18: IT Instruction: More Examples
ITE GT ; Next 2 instructions are conditional
ADDGT R1, R0, #55 ; in case GT(Greater-Than)=1
ADDLE R1, R0, #48 ; in case GT=0 (LE: Less-or-Equal)
ITTE NE ; Next 3 instructions are conditional
ANDNE R0, R0, R1 ; in case NE(Not-Equal)=1
ADDSNE R2, R2, #1 ; in case NE(Not-Equal)=1
MOVEQ R2, R3 ; in case NE=0 (EQ: Equal)
ITTEE EQ ; Next 4 instructions are conditional
MOVEQ R0, R1 ; in case EQ(Equal)=1
ADDEQ R2, R2, #10 ; in case EQ(Equal)=1
ANDNE R3, R3, #1 ; in case EQ=0 (NE: Not-Equal)
BNE L1 ; in case EQ=0 (NE: Not-Equal), branch to statement with label L1. Branch can only be used as the last instruction of an IT block
Notes: ITTE NE ; Next 3 instructions are conditional ANDNE R0, R0, R1 ; ANDNE does not update condition flags ADDSNE R2, R2, #1 ; ADDSNE updates condition flags MOVEQ R2, R3 ; Conditional move ITE GT ; Next 2 instructions are conditional ADDGT R1, R0, #55 ; Conditional addition in case the GT is true ADDLE R1, R0, #48 ; Conditional addition in case the GT is not true ITTEE EQ ; Next 4 instructions are conditional MOVEQ R0, R1 ; Conditional MOV ADDEQ R2, R2, #10 ; Conditional ADD ANDNE R3, R3, #1 ; Conditional AND BNE.W dloop ; Branch instruction can only be used in the last instruction of an IT block

## Slide 19: Compound Conditionals: Example 1
if (lower_limit <= x && x <= upper_limit) y = x ;
if (!(lower_limit <= x && x <= upper_limit)) goto L1
y = x ;
L1:
lower_limit
upper_limit
x
If x falls within this range, execute “y=x”
lower_limit
upper_limit
x
If x falls outside of this range, skip “y=x”
Equivalent C code:
C code:

## Slide 20
if (x < lower_limit) goto L1
if (x > upper_limit) goto L1
y = x ;
L1:
if (x < lower_limit || x > upper_limit) goto L1
y = x ;
L1:
Equivalent C code (with DeMorgan’s law):
Equivalent C code:
Assembler code:
Compound Conditionals: Example 1
LDR R0,[addr(x)] LDR R1,lower_limit
CMP R0,R1
BLT L1 LDR R1,upper_limit
CMP R0,R1
BGT L1
STR R0,[addr(y)]
L1: ...

## Slide 21: Compound Conditionals: Example 2 (Option 1)
if (x < lower_limit || upper_limit < x) y = x ;
lower_limit
upper_limit
x
If x falls outside of this range, execute “y=x”
C code:
if (x < lower_limit) goto L1
if (x > upper_limit) goto L1
goto L2
L1: y = x ;
L2:
Equivalent C code:
Assembler code:
LDR R0,[addr(x)] LDR R1,lower_limit
CMP R0,R1
BLT L1 LDR R1,upper_limit
CMP R0,R1
BGT L1
B L2
L1: STR R0,[addr(y)]
L2: ...

## Slide 22: Compound Conditionals: Example 2 (Option 2)
if (x < lower_limit || upper_limit < x) y = x ;
lower_limit
upper_limit
x
If x falls outside of this range, execute “y=x”
C code:
if (x < lower_limit) goto L1
if (x <=upper_limit) goto L2
L1: y = x ;
L2:
Equivalent C code:
Assembler code:
LDR R0,[addr(x)] LDR R1,lower_limit
CMP R0,R1
BLT L1 LDR R1,upper_limit
CMP R0,R1
BLE L2
L1: STR R0,[addr(y)]
L2: ...
More efficient, with fewer branch instructions

## Slide 23: Loops: Basic Structure
initialization
cond?
body of loop
B{!cond} done
Loop Body
done
top: CMP
B top
top: CMP
CMP
B{cond} top
Loop Body
false
true
Assembler code (option 1):
Assembler code (option 2):
C code flowchart:

## Slide 24: Loops: Predetermined #Iterations
for (n = 0; n < 100; n++) { … //Loop body }
LDR R0,=0 top: CMP R0,#100 BGE done ;Branch greater than or equal to (n>=100) … ADD R0,R0,#1 B top done: | LDR R0,=0 top: … ADD R0,R0,#1 CMP R0,#100 BLT top ;Branch less than (n<100) done:
Assembler code (option 1):
Assembler code (option 2):
C code:
More efficient, with fewer branch instructions.

## Slide 25
Option 2 Caveat
Option 2 executes the loop for at least one iteration
Not correct for loops with 0 iterations!
    for (n = 0; n < 0; n++) {
    … //Loop body is never executed
    }
But this is a pathological example
  Normal loops should have at least 1 iteration

## Slide 26: Larger Example: FIR filter
C:
  for (int i=0, f=0; i<N; i++)
  f = f + c[i]*x[i];
Assembler:
; loop initiation code
MOV R0,#0 ; use R0 for loop index i
MOV R8,#0 ; use R8 for array offset
ADR R2,N ; get address for variable N
LDR R1,[R2] ; get value of N and put in register R1
MOV R2,#0 ; use R2 for f
ADR R3,c ; load R3 with base address of int array c
ADR R5,x ; load R5 with base address of int array x
; loop body
loop LDR R4,[R3,R8] ; load c[i] at memory address R3+R8
; into R4
LDR R6,[R5,R8] ; load x[i] at memory address R5+R8
; into R6
MUL R4,R4,R6 ; compute c[i]*x[i] and store result in R4
ADD R2,R2,R4 ; add into running sum f
ADD R8,R8,#4 ; add 4 (one word) to array offset R8
ADD R0,R0,#1 ; add 1 to loop index i
CMP R0,R1 ; Compare i and N
BLT loop ; if i < N, continue and go back to label “loop”
Reg | Meaning
R0 | Loop index i, incremented by 1 at each loop iteration
R1 | Loop bound N
R2 | Running sum f
R3 | Base address of array c
R4 | c[i]
R5 | Base address of array x
R6 | x[i]
R8 | Array offset, incremented by 4 at each loop iteration since both c and x are 4-byte int arrays

## Slide 27: Loops: Variable # Iterations
//GCD(a,b) computes the Greatest Common Divisor of a and b while (a != b) { if (a > b) a = a – b ; else b = b – a; } | LDR R0, [addr(a)] LDR R1, [addr(b)] top: CMP R0, R1 BEQ done ITE GT ;If-Then-Else: next ;2 instructions are conditional SUBGT R0,R0,R1 ;in case GT=1 SUBLE R1,R1,R0 ;in case GT=0 B top ;go back to top done: STR R0, [addr(a)] STR R1, [addr(b)]

## Slide 28
Summary
ARM programming model
Two alternative control flow schemes:
  Branch (conditional) instructions
  ITE family of instructions
Loops
  Two options