## Slide 1: L2 (CHAPTER 5) Programming in Assembly Part 1: Computer Organization

## Slide 2: von Neumann Architecture
Memory holds data, instructions.
CPU fetches instructions from memory.
CPU registers: program counter (PC), instruction register (IR), general-purpose registers, etc.
Notes: Separate CPU and memory distinguishes programmable computer.

## Slide 3: CPU + Memory
memory
CPU
PC
address
data
IR
ADD r5,r1,r3
200
200
ADD r5,r1,r3

## Slide 4: Harvard Architecture
CPU
PC
data memory
program memory
address
data
address
data

## Slide 5: von Neumann vs. Harvard
Harvard allows two simultaneous memory fetches.
Most DSPs use Harvard architecture for streaming data:
  greater memory bandwidth;
  more predictable bandwidth.
Harvard can’t use self-modifying code.
  Instruction memory is read-only

## Slide 6: A Typical Desktop Processor (von Neumann Arch. as example)
CPU
(Arithmetic and Logic Unit, Control Logic, and Registers)
Memory
(Instructions and Data)
I/O
(Disk, keyboard, display, etc.)
Memory Data Transfers
DMA Controller
I/O Data Transfers
Three major components:
  (1) CPU , where operations are performed,
  (2) memory , where data is stored, and
  (3) input/output (I/O) system, to gather input data or to output results.
The three units are interconnected by groups of wires called buses.
Data transferred between memory and I/O devices normally goes through and is coordinated by the CPU. Direct Memory Access (DMA) controller can be added to perform these transfers without involving the CPU

## Slide 7: A Typical Embedded Processor (von Neumann Arch. as Example)
CPU
(Arithmetic and Logic Unit, Control Logic, and Registers)
Memory
(Instructions and Data)
I/O
(Disk, keyboard, display, etc.)
Memory and I/O Data Transfers
DMA Controller
Memory-mapped I/O
  A 32-bit memory address is capable of referencing 4 GB (232 bytes) of information
  A portion of the address space is reserved for and decoded by the I/O devices. This eliminates the need for separate I/O instructions since all of the regular instructions for accessing memory can then be used to access I/O devices.
DMA controller is often not present, since most embedded applications do not require very high data transfer rates
Notes: Memory-Mapped Peripherals

## Slide 8: Memory
2N bytes
Organized into
groups of 4 bytes
Address Bus: N wires
Data Bus: 4x8 wires
Content is 1’s and 0’s.
Control Bus:
Read vs Write,
Initiate Cycle,
Data Ready
Information flows between the CPU and memory over three sets of wires called the address bus , the data bus , and the control bus.
  The CPU places information on the address bus to tell the memory which data to access
  uses the control bus to determine the direction of information transfer and to coordinate timing
  The data itself is transferred over the data bus
Address bus has N wires, where N is # bits in each address (8,16,32,64…)
Data bus has 4x8 wires, hence each data transfer is 4 Bytes (also called 1 word)

## Slide 9: Memory Byte Ordering
Two possible byte orderings: “little endian” and “big endian”
  Little-endian: the LSB (Least Significant Byte) is stored at the lowest address.
  Big-endian: the LSB (Least Significant Byte) is stored at the highest address.
  Intel processors use Little-Endian; ARM processors can be configured as either Little- or Big-endian.
Below are examples of Little Endian ordering (A 32-bit entity can contain one 32-bit word, or two 16-bit half-words, or four 8-bit Bytes)

## Slide 10: Data Alignment
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand:

## Slide 11: Single Accumulator Architecture
A CPU consists of several components, including the arithmetic and logic unit (ALU) , a set of registers, and a control unit . One or more data and address buses interconnect these components.
Instruction registers hold the current instruction; a program counter (PC) to specify the address of the next instruction to be executed, and others
Data registers hold the operands and the result. In the simplest configuration, a single data register called the accumulator (ACC) is used
Notes: a status register to hold information about the most recent result produced
by the ALU.

## Slide 12: The Fetch-Execute Cycle
(There is typically an instruction decode stage that is omitted here for simplicity)

## Slide 13: Instruction Fetch
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC
1. Memory_Address_Bus  Program_Counter
2. Start Memory Read Operation
3. Increment Program_Counter
4. Wait for Memory Read to Complete
5. Instruction_Register  Memory_Data_Bus
6. Go to execute phase.
Notes: While waiting for the memory read to complete,
the control unit increments the PC in preparation for the retrieval of the next instruction
byte. When the memory has completed its read, the control unit copies the data
from the memory data bus into the instruction register

## Slide 14
Execution Phase: Load ACC
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC
An instruction that loads data from memory into the accumulator takes the address of the memory operand from the instruction register, places it on the address bus, initiates a memory read operation, and then transfers the memory data through the ALU to the accumulator.

## Slide 15
Execution Phase: ADD
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC
Once an operand has been loaded into the accumulator, a subsequent instruction can perform an addition between it and a second operand, taking one operand from memory, a second from the accumulator

## Slide 16
Execution Phase: Store ACC
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC
Replaces content of ACC with the result of ADD.

## Slide 17: Execution Phase: Branch
Memory
IR
Address Bus
Data Bus
ALU
ACC
PC
A branch instruction loads a new address into the PC during the execute phase. This address may have been stored as a constant, as a value retrieved from a register or read from memory, or as the result of some calculation performed during the execute phase of the branch instruction

## Slide 18: result  op1 + op2
ACC  MEM[adrs_of_op1]
ACC  ACC + MEM[adrs_of_op2]
MEM[adrs_of_result]  ACC
REG[R1]  MEM[adrs_of_op1] ;Copy 1st operand from memory into register ‘R1'
REG[R2]  MEM[adrs_of_op2] ;Copy 1st operand from memory into register ‘R2'
REG[R3]  REG[R1] + REG[R2] ;Perform the addition, leaving the result in a 3rd register
MEM[adrs_of_result]  REG[R3] ;Store contents of register ‘R3' into memory
Single Accumulator Architecture:
Load/Store Architecture(almost all modern CPUs):
The past slides illustrate the single-accumulator machine, where an ALU instruction can perform arithmetic operation between register and memory in a single cycle;
Modern CPUs are typically register machines, where an ALU instruction can only perform arithmetic operation between two registers; separate load/store instructions are used to transfer data between register and memory.

## Slide 19: The ARM Processor Family

## Slide 20: Three Instruction Sets
ARM Instruction Set
  Instructions are 32 bits wide
  Original RISC (lots of parallelism)
  “Load/Store” Architecture
Thumb Instruction Set
  Subset of ARM instructions, some restrictions
  Instructions are 16 bits wide
  Less parallelism, longer instruction sequences
  but total code size is 30% smaller
Jazelle Instruction Set
  Java byte codes
Hardware Decoder
16-bit Thumb Instruction
32-bit ARM Instruction

## Slide 21: Three Instruction Sets
* LM3S811 (a Cortex M3 variation) uses the Thumb2 set
 | ARM | Thumb | Jazelle
Instruction Size | 32 bits | 16 bits | 8 bits
Core instructions | 58 | 30 | > 60% of Java byte codes in hardware; rest in software
Conditional Execution | most | Only branch instructions or in an IT block | N/A
Data processing instructions | Access to barrel shifter and ALU | Separate barrel shifter and ALU instructions | N/A
Program status register | Read/write in privileged mode | No direct access | N/A
Register usage | 15 general purpose registers + pc | 8 general purpose registers + 7 high registers + pc | N/A

## Slide 22: Code Density vs. Performance

## Slide 23: The ARMv7-M “Cortex-M3” Architecture

## Slide 24: ARM Cortex-M3 CPU
Registers
R0 – R15
Barrel Shifter
Sign Extender
Incrementer
MAC
Data Bus
Address Bus
R15 (pc)
Rn
Rd
Result Bus
ALU
Address Register
Rm
Load-store architecture
A barrel shifter allows operand Rm to be shifted left or right any number of bit positions before being combined with operand Rn in the ALU, thus allowing calculations of the form Rn +/- 2kRm.
A MAC (Memory Address Calculator) prepares subscripted and relative address references for memory access, and a special incrementer can adjust the memory address on subsequent instructions without having to recalculate the address.

## Slide 25: Pipelined Instruction Execution
Fetch
Decode
Execute
Read register(s) from Register Bank,
Shift and ALU operation,
Write register(s) back to Register Bank
Decompress thumb instruction, Decode ARM instruction Select registers
16-bit Instruction fetched from memory
PC
PC - 2
PC - 4
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
Pipelining allows three instructions to be in progress simultaneously during any one processor clock cycle. While one instruction is fetched, another is decoded, and a third is executed. Thumb instructions are 16 or 32 bits wide, with the majority being 16 bits. Thus, while the address held in PC is being used to read one 16-bit instruction from memory, the previous instruction (from address PC-2) is decoded, and the one before that (from address PC-4) is executed. One instruction completed every cycle.

## Slide 26: Non-Pipelined Instruction Execution (hypothetical)
2nd Instruction (Adrs: PC+2)
Fetch
Decode
Execute
1st Instruction (Adrs: PC)
Fetch
Decode
Execute
3rd Instruction (Adrs: PC+4)
Fetch
Decode
Execute
Time
One instruction completed every 3 cycles. Performance is much lower than pipelined execution.

## Slide 27: ARM Cortex-M3 Bus Structure (Harvard arch.)
Code and data are stored in separate and independent hardware; instructions are fetched over the I-Code bus from a nonvolatile flash memory while the system bus is used to access data in static read/write memory (or peripherals). Since the two memories are physically separate, overall performance is enhanced by a Harvard –style architecture with separate data paths that allow simultaneous instruction and data access

## Slide 28
Summary
von Neumann vs. Harvard architectures
Instruction fetch/execute cycle
Instruction sets for ARM processors
  ARM, Thumb, Thumb-2
Pipelined Instruction Execution