## Slide 1
Acknowledgement: some slides taken from Yifeng Zhu’s courseware
L5 functions
Exercises
Zonghua Gu, 2018

## Slide 2: PUSH/POP Multiple Registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
PUSH/POP multiple registers in a single statement: the order in which registers listed in the {register list} does not matter
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
Review

## Slide 3: Question: Stack
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx
R1==0x11111111
R2==0x22222222
Before execution
Question:
  What is content of stack, and position of SP, after PUSH {R2,R1}?
  What are the values of R1/R2 after POP {R2}?

## Slide 4: Answer: Stack
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1,R2}
POP {R1}
POP {R2}
memory
Address
0x22222222
0x11111111
R1==0x11111111
R2==0x22222222
Before execution
Answer:
  Shown in figure
  After POP {R2}, R1==0x11111111, R2==0x22222222

## Slide 5: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 6: Passing Arguments via Registers R0-R3
Review

## Slide 7: Additional Arguments Passed on Stack
Each argument of 8-bit char, or 16-bit short, is passed in a 32-bit register
R0 | R1 | R2 | R3
Registers
Stack in Memory
foo (int i0, int i1, int i2, int i3)
i0 | i1 | i2 | i3
Registers
Stack in Memory
foo (int i0, char a1, double D)
i0 | a1 | D
Registers
Stack in Memory
foo (int i0, int i1, double D, int i2, int i3)
i0 | i1 | D
i2 | i3 |  |  |  |  | 
Registers
Stack in Memory
Caller passes arguments i0, i1, D in registers R0-R3 directly; pushes additional arguments i2 and i3 onto the stack before function call (details not covered in this lecture)
Review

## Slide 8: Question: Argument Passing
Which registers are used to pass the arguments and return the result?
long fun (short a1, char a2, double a3, int a4, char a5)
Registers
Stack in Memory

## Slide 9: Answer: Argument Passing
Which registers are used to pass the arguments and return the result?
Each argument of 8-bit char, or 16-bit short, is passed in 1 32-bit register; cannot use 1 register to pass more than 1 arguments
long fun (short a1, char a2, double a3, int a4, char a5)
a1 | a2 | a3
a4 | a5 |  |  |  |  | 
Registers
Stack in Memory