## Slide 1
Acknowledgement: some slides taken from Yifeng Zhu’s courseware
L5 functions
Zonghua Gu, 2018

## Slide 2: Stack
A Last-In-First-Out data structure
Only allow to access the most recently added item
  Also called the top of the stack
Key operations:
  push (add item to stack)
  pop (remove top item from stack)

## Slide 3: Tower of Hanoi
Only one disk may be moved at a time.
Each move consists of taking the upper disk from one of the rods and sliding it onto another rod, on top of the other disks that may already be present on that rod.
No disk may be placed on top of a smaller disk.

## Slide 4: Tower of Hanoi
http://en.wikipedia.org/wiki/File:Tower_of_Hanoi_4.gif
STACK: Last In First Out
Stack 1
Stack 2
Stack 3

## Slide 5: Cortex-M Stack
Descending stack
  Grows from top to bottom
Stack Pointer (SP) (R13) contains memory address of top element of the stack
  decremented on PUSH
  incremented on POP
The assembly file startup.s defines stack space and initializes SP.
Notes: A stack is a “Last-In, First-Out” (LIFO) data structure in which data is retrieved in the
opposite order from which it was written. Processors implement stacks by allocating a
region of memory for the stack and maintaining a “stack pointer” (SP) register that
holds the address of the next stack location to be accessed, called the top of the stack.
Stack grows down (towards lower memory addresses). A “push” operation writes data to the
top of the stack and a “pop” operation reads data from the top of the stack. Push and pop
operations adjust the SP so that the location designated as the top of the stack automatically
moves up and down in memory as push and pop instructions are executed

## Slide 6: Stack
PUSH {Rd}
  SP = SP-4 ⟶ Stack grows downward
  (*SP) = Rd ⟶ Rd is pushed and assigned to top element of stack (C Syntax)
POP {Rd}
  Rd = (*SP) ⟶ Top element of stack is popped and assigned to Rd (C Syntax)
  SP = SP + 4 ⟶ Stack shrinks upward
Notes: The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.

## Slide 7: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx
R1==0x11111111
R2==0x22222222
Before execution

## Slide 8: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
xxxxxxxx

## Slide 9: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 10: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 11: Example: Swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x11111111
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222
R1==0x11111111
R2==0x22222222
Before execution
R1==0x22222222
R2==0x11111111
After execution
Not an efficient approach for swapping numbers! Incurs 4 memory
accesses. Much more efficient to use another register to do swap.

## Slide 12: PUSH/POP Multiple Registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
PUSH/POP multiple registers in a single statement: the order in which registers listed in the {register list} does not matter
  When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
  When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.
PUSH {register list} followed by POP{register list} leaves the values in register list unchanged. Useful for saving and restoring register values in functions.
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}

## Slide 13: Quiz
Are the values of R1 and R2 swapped?
  PUSH {R1, R2}
  POP {R1, R2}
Answer: No. This code is equivalent to:
  PUSH {R2}
  PUSH {R1}
  POP {R1}
  POP {R2}
This leaves R1 and R2 unchanged
The following programs perform swap:
  PUSH {R1, R2}
  POP {R2}
  POP {R1}
or
  PUSH {R1}
  PUSH {R2}
  POP {R1, R2}

## Slide 14: Function
A function, also called a subroutine or a procedure
  Single-entry, single-exit
  Returns to caller after it exits
When a function is called, the Link Register (LR) holds the memory address of the next instruction to be executed after the function exits.
  PC + 4

## Slide 15: Link Register
Link Register (LR) holds the return address of the current function call.
MSP: Main Stack Pointer
PSP: Process Stack Pointer

## Slide 16: Calling a function: Two Ways
Caller Program
... BL foo ...
function/Callee
foo PROC ... ... BX LR ENDP
BL label
Equiv. operation:
  LR = PC + 4
  PC = label
PUSH{LR}
...
POP{PC}
Equiv. operation:
  PC = LR
BL label
Equiv. operation:
  LR = PC + 4
  PC = label
BX LR
Equiv. operation:
  PC = LR
Caller Program
... BL foo ...
function/Callee
foo PROC PUSH {LR} ... POP {PC} ENDP
Notes: After call, LR holds return address (the instruction following the call)
Notes:
  label is name of function
  The PROC/ENDP directives mark the start/end of a function
    For programmer’s convenience only, they are not present in the final machine code

## Slide 17: Notes on Previous Slide
foo is name of function
The PROC/ENDP directives mark the start/end of a function
  For programmer’s convenience only, they are not present in the final machine code
  Equivalently: FUNC/ENDFUNC
The two approaches (BX or PUSH{LR}+POP{PC} in callee) are functionally equivalent
  BX approach is more efficient since it does not access memory

## Slide 18: Calling a function: BX LR
Compiler
void foo(void);
Main() {
● ● ●
foo();
● ● ●}
● ● ●
BL foo
● ● ●
export foo
foo PROC
● ● ●
BX LR
ENDP
C Code:
Assembler Code:

## Slide 19: Calling a function: PUSH(LR)+POP(PC)
Compiler
void foo(void);
Main() {
● ● ●
foo();
● ● ●}
● ● ●
BL foo
● ● ●
export foo
foo PROC
PUSH {LR}
● ● ●
POP {PC}
ENDP
C Code:
Assembler Code:

## Slide 20: Calling a function w/ Saving/Restoring R4-R11
export foo
foo PROC
PUSH {R4,R5}
● ● ●
POP {R4,R5}
BX LR
ENDP
export foo
foo PROC
PUSH {R4,R5, LR}
● ● ●
POP {R4,R5, PC}
ENDP
Since LR is R14, the above is equivalent to:
export foo
foo PROC
PUSH {LR}
PUSH {R4,R5}
● ● ●
POP {R4,R5}
POP {PC}
ENDP
Option 1 with BX LR
Option 2 with PUSH{LR}+POP{PC}

## Slide 21: Nested Function Call w/ BX in Callee
Using the BL+BX approach: since register LR can hold only a single return address, a function that calls other functions must preserve LR at its entry point and restore its original content before returning, by using PUSH(LR) and POP(LR) instructions to store and load the first caller’s return address LR in memory.
● ● ●
BX LR

## Slide 22: Nested Function Call w/ PUSH(LR)+POP(PC) in Callee
POP{PC}
Using the PUSH{LR}+POP{PC} approach, every function has the same form, so you don’t have to modify the code if you add one more level of nested function call

## Slide 23: Nested Function Call: R0 = R04
MAIN PROC
MOV R0,#2
BL QUAD
ENDL ...
ENDP
QUAD PROC
PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDP
SQ PROC
MUL R0,R0,R0
BX LR
ENDP
function MAIN
function QUAD
function SQ
MAIN calls QUAD, QUAD calls SQ
Register R0 is used to pass both the argument and the return result (R0 = R04)
Assume 32-bit memory address. Every item (register, instruction, data on stack) is 32 bits = 4 Bytes.

## Slide 24: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
R0
PC
0x08000138
LR
SP
0x20000200
SQ
QUAD
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 25: Example: R0 = R04
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x02
R0
PC
0x0800013C
LR
SP
0x20000200
SQ
QUAD
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 26: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x02
R0
PC
0x0800014C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Preserve
Link Register (LR)
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 27: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x08000140
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x02
R0
PC
0x08000150
LR
SP
0x200001FC
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 28: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x02
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 29: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x04
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 30: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x04
R0
PC
0x08000154
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 31: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x04
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 32: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x10
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 33: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x10
R0
PC
0x08000158
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 34: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x10
R0
PC
0x0800015C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Recover
Link Register (LR)
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
0x08000140
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 35: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0…
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0…
0x10
R0
PC
0x08000140
LR
SP
0x20000200
0x08000140
0x08000140
SQ
QUAD
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
Stack in Data Memory
CPU Registers
Program in Instruction memory

## Slide 36: Arguments and Return Values
Hold arguments, results, or temporary values. Caller doesn’t expect them to be preserved. Also called “scratch registers”.
Link Register
Caller expects these values to be preserved.
Callee either does not use them, or must preserve their original value if it uses them.
Notes:   R0-R3: scratch registers that can be changed by callee
  R4-R11: caller expects their value to stay unchanged before and after a function call

## Slide 37: On Conventions
“Callee must preserve values of R4-R11, but not R0-R3”
  This is a programming convention adopted by ARM compilers and assemblers that helps with interoperability among software written by different people (the processor hardware doesn’t care how you use the registers)
  Like driving on the right side of the road in North America (the road doesn’t care how cars are driven on it)
What if you don’t respect this convention?
  If you write everything (assembler code, compiler toolchain…) by yourself, free to adopt your own convention, but your code or tool will not interoperate with the rest of the world

## Slide 38: Calling a Function without Preserving R4-R11
Caller Program | function/Callee
MOV R4, #100 ... BL foo % R4 has the incorrect value of 10 ... ADD R4, R4, #1 | foo PROC ... MOV R4, #10 ; foo changes R4 ... BX LR ENDP
Callee must preserve values of R4-R11

## Slide 39: Calling a Function, Preserving r4-r11
Caller Program | function/Callee
MOV R4, #100 ... BL foo % R4 has the correct value of 100 ... ADD R4, R4, #1 | foo PROC PUSH {R4} ; preserve R4 ... MOV R4, #10 ; foo changes R4 ... POP {R4} ; Recover R4 BX LR ENDP
Callee must preserve values of R4-R11

## Slide 40: Passing Arguments via Registers R0-R3

## Slide 41: Additional Arguments Passed on Stack
Each argument of 8-bit char, or 16-bit short, is passed in a 32-bit register
R0 | R1 | R2 | R3
Registers
Stack in Memory
foo (int i0, int i1, int i2, int i3)
i0 | i1 | i2 | i3
Registers
Stack in Memory
foo (int i0, char a1, double D)
i0 | a1 | D
Registers
Stack in Memory
foo (int i0, int i1, double D, int i2, int i3)
i0 | i1 | D
i2 | i3 |  |  |  |  | 
Registers
Stack in Memory
Caller passes arguments i0, i1, D in registers R0-R3 directly; pushes additional arguments i2 and i3 onto the stack before function call (details not covered in this lecture)

## Slide 42: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
...
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
...
int SSQ(int x, int y){
int z;
z = x * x + y * y;
return z;
}
R0: first argument
R1: second argument
R0: Return Value

## Slide 43: Redundancy?
This program does not use the stack
  No nested function calls
  All arguments fit in R0-R3
Why do you have “MOV R0, R2” in the callee, and “MOV R2,R0” in the caller? Aren’t they redundant?
  Return value must be in R0, hence must have “MOV R0, R2” in the callee before return
  The specification says “R2=R0*R0+R1*R1”, hence “MOV R2, R0” in the caller after function return
Actually the program can be rewritten to improve efficiency. See next slide.

## Slide 44: Example simplified: R0 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
B ENDL
...
SSQ MUL R0,R0,R0
MUL R1,R1,R1
ADD R0,R0,R1
BX LR
...
int SSQ(int x, int y){
int z;
z = x * x + y * y;
return z;
}
R0: first argument
R1: second argument
R0: Return Value
This version uses fewer registers and is more efficient.
But we use the previous version for illustration purpose

## Slide 45: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
R0
R1
0x08000128
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 46: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
R1
0x08000128
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 47: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x0800012B
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 48: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x0800012F
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address

## Slide 49: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
Address of the next instruction after the branch is saved into LR.
CPU Registers
Program in Instruction memory

## Slide 50: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x0800013B
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 51: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x0800013F
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 52: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
3
R0
4
R1
0x08000144
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 53: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
25
R0
4
R1
0x08000146
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 54: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
25
R0
4
R1
0x0800014A
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 55: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
25
R0
4
R1
0x08000134
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
Copy LR to PC when returning from a function!
CPU Registers
Program in Instruction memory

## Slide 56: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
25
R0
4
R1
0x08000134
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 57: Example: R2 = R0*R0+R1*R1
MOV R0,#3
MOV R1,#4
BL SSQ
MOV R2,R0
B ENDL
SSQ MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOV R0,R2
BX LR
ENDL ...
25
R0
4
R1
0x08000138
PC
MOV R0,R2
0x08000128
0x0800012C
0x0800012F
MUL R3,...
MOV R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
0x08000134
0x08000138
0x08000144
BX LR
0x0800013B
0x0800013F
16
R3
SSQ
MOV R0,#3
0x08000146
0x0800014A
MOV R1,#4
Memory Address
CPU Registers
Program in Instruction memory

## Slide 58: Summary
Stack
  PUSH and POP operations
Calling a function
  Either BX, or PUSH(LR)+POP(PC) in callee
Calling conventions
  R0-R3: scratch registers that can be changed by callee
  R4-R11: caller expects their value to stay unchanged before and after a function call
Passing arguments and returning a value
  Arguments passed in R0-R3, plus stack if necessary
  Value returned in R0-R3, depending on its size