## Slide 1: Z. Gu
Fall 2025
ECE271
Final Review

## Slide 2: Character String
Memory Address | Memory Content | Letter
str + 12 | 0x00 | \0
str + 11 | 0x79 | y
str + 10 | 0x6C | l
str + 9 | 0x62 | b
str + 8 | 0x6D | m
str + 7 | 0x65 | e
str + 6 | 0x73 | s
str + 5 | 0x73 | s
str + 4 | 0x41 | A
str + 3 | 0x20 | space
str + 2 | 0x4D | M
str + 1 | 0x52 | R
str  | 0x41 | A
char str[13] = “ARM Assembly”;

## Slide 3: Data Representation
Integers
  Binary in different bases: binary, octal, hex, decimal
  Signed Integers
    Signed magnitude
    One’s complement
    Two’s complement
  Arithmetic Operations
    N, V, C, Z flags
  Big Endian vs Little Endian
ASCII values
  Null-terminated string
  Converting between numbers and ASCII
  Upper case, lower case
Fixed pointer numbers
  Qm.n format
  Addition, subtract, multiplication, division

## Slide 4: Basic Assembly Programming
Load-modify-store sequence
Accessing nemory
  Memory addressing mode
    Pre-index
    Post-index
    Pre-index with update
Data processing
  Arithmetic, Logic, Comparison, Data Movement
  Barrel Shifter:
    ADD r1, r0, r0, LSL 2
  Bit operations
    Set a bit, Reset a bit, Toggle a bit, Check a bit
  LSL, LSR, ASR, ROR, RRX
Flow control: if, if-then-else, for loop, while loop
  Unconditional Branch: B
  Conditional Branch: CMP, TEQ,TST, BEQ, BNE, BMI, BLS, BHI, etc.
  Conditional Execution: MOVEQ, MOVNE

## Slide 5: Subroutine Without Floating Numbers
Calling Subroutine & Exiting Subroutine
  BL and BX
  How PC, LR, and SP registers are updated?
Embedded application binary interface (EABI) Protocol
  Save and restore R4-R11,LR if your subroutine wishes to modify
  Parameters passing in registers R0,R1,R2,R3
  Extra parameters passing in stack
  Return parameter in R0
Recursive functions
  How does the stack work?
  Pay special attention to LR register

## Slide 6: Subroutine with Float Arguments
Each number is assigned in turn to the next free register of the corresponding type
Example:
  double fun(double a1, float a2, double a3, float a4, float a5, double a6, float a7, double a8)

## Slide 7: Unsigned Fixed-point Representation UQm.n

## Slide 8: Signed Fixed-point Representation Qm.n
where

## Slide 9: Fixed-point Multiplication in Q15.16
SMULL r2, r3, r0, r1 ; Unsigned long multiply
; r2 = low word, r3 = high word
LSLS r3, r3, #16 ; Shift left high word
LSRS r2, r2, #16 ; Shift right low word
ORR r4, r2, r3 ; Pack two halfwords into a word
; r0 = fixed-point number A
; r1 = fixed-point number B
; r4 = fixed-point product = A × B

## Slide 10: Fixed-point Division in UQ16.16 or Q15.16
ASRS r1, r0, #31 ; r1[31:0] = sign bits of A
LSLS r1, r1, #16 ; put sign bits in upper half word
ORR r1, r1, r0, LSR #16
LSLS r0, r0, #16 ; [r1:r0] stores sign extended A
ASRS r3, r2, #31 ; [r4:r3] stores sign extended B
BL division_64_bits ; Take four input register (r0:r1, r3:r4)
MOV r4, r0 ; division_64_bits places result in r0
r4 = fixed-point quotient
= A ÷ B

## Slide 11: IEEE Std 754
IEEE 754 value:
where Bias = 127 for single precision
Bias = 1023 for double precision

## Slide 12: Decoding 0xC1FF0000 into a floating-point number
0.9921875

## Slide 13: Encoding 14.5 into IEEE Std 754 Single-Precision
14.5 = 01000001011010000000000000000000 in binary or 0x41680000 in hex
Normalization:

## Slide 14: Timer’s Clock
Current Count
Reload Value
TIMx_CNT
fCL_PSC
ISR
Resume
Interrupt
Reload
TIMx_PSC
TIMx_ARR
Prescaler
fCL_CNT
clock

## Slide 15: PWM Duty Cycle = Ton/Time Period