## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 7
Structured Programming
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Divide and Conquer
"Nothing is particularly hard if you divide it into small jobs."
Henry Ford
Founder of Ford Motor

## Slide 3: Basic Control Structures
Sequence Structure
Selection Structure
Loop Structure

## Slide 4: History
Spaghetti Code
  Before the 1980s, program flow bounces around anywhere the programmer wanted.
  Culprit: overusing “GOTO” statements
1 i=0
2 i=i+1
3 PRINT i; "squared=";i*i
4 IF i>=100 THEN GOTO 6
5 GOTO 2
6 PRINT "Program Completed."
7 END
Spaghetti code in BASIC
Structured programming in BASIC
1 FOR i=1 TO 100
2 PRINT i;"squared=";i*i
3 NEXT i 'termination of loop body
4 PRINT "Program Completed."
5 END
Notes: https://en.wikipedia.org/wiki/Spaghetti_code
https://commons.wikimedia.org/wiki/File:Spagetti_code_structural_graphic.GIF

## Slide 5: Importance of Structured Programming
Assembly is not a structured programming language
  Does not directly support selection and loop
  Branch in assembly = “goto” in C
  Break the single-entry single-exit rule
Easy to generate spaghetti code in assembly
  Twisted and tangled
  Difficult to debug & maintain
One strategy to alleviate the challenge
  Use flowcharts to facilitate assembly programming
  That is why textbook has many flowcharts
  How to build flowcharts?

## Slide 6: Software Design Strategy: Top-Down Design
Three common design strategies
  Top-down, also known as stepwise refinement
  Bottom up
  Object oriented
Top-down: Repeatedly break down tasks into smaller and smaller pieces until they are easy to solve
Example: Planning a picnic
  Task 1: Where
  Task 2: When
  Task 3: Who
  Task 4: Food

## Slide 7: Top-Down Design Example
Find all Armstrong numbers less than 10,000
  Given a positive integer that has n digits, it is an Armstrong number if the sum of the nth powers of its digits equals the number itself.

## Slide 8: Top-Down Design Example

## Slide 9: Top-Down Design Example

## Slide 10: Top-Down Design Example

## Slide 11: Top-Down Design Example

## Slide 12: Top-Down Design Example: Counting digits

## Slide 13: Reuse Registers
int A = 0; // 0x00000000
int B = -1; // 0xFFFFFFFF
int C = -2; // 0xFFFFFFFE
int D = 2; // 0x00000002
void main(void){
A = B + C – D;
return;
}

## Slide 14: Reuse Registers
int A = 0; // 0x00000000
int B = -1; // 0xFFFFFFFF
int C = -2; // 0xFFFFFFFE
int D = 2; // 0x00000002
void main(void){
A = B + C – D;
return;
}
AREA myCode, CODE
EXPORT __main
ENTRY
__main PROC
LDR r2, =B ; r2 = 0x2000,0004
LDR r3, [r2] ; r3 = B = -1
LDR r4, =C ; r4 = 0x2000,0008
LDR r5, [r4] ; r5 = C = -2
LDR r6, =D ; r6 = 0x2000,000B
LDR r7, [r6] ; r7 = D = 2
ADD r1, r3, r5 ; r1 = B + C
SUB r1, r1, r7 ; r1 = B + C - D
LDR r0, =A ; r0 = 0x2000,0000
STR r1, [r0] ; Save A
ENDP
AREA myData, DATA
A DCD 0
B DCD -1
C DCD -2
D DCD 2
END
Eight registers are used:
R0,r1,r2,r3,r4,r5,r6,r7

## Slide 15: Reuse Registers

## Slide 16: Example 1: Factorial Numbers

## Slide 17: Example 1: Factorial Numbers
C Program | Assembly Program
int main(void) { int result, n, i; | AREA factorial, CODE, READONLY EXPORT __main ENTRY __main PROC
result = 1; n = 5; | MOV r0, #1 ; r0 = result MOV r1, #5 ; r1 = n
for (i = 1; i <= n; i++) result = result * i; | MOV r2, #1 ; r2 = i = 1 loop CMP r2, r1 ; compare i and n BGT stop ; if i > n, stop MULS r0, r2, r0 ; result *= i ADD r2, r2, #1 ; i++ B loop
while(1); } | stop B stop ENDP END

## Slide 18: Example 2: Counting Ones in a Word
Assembly Program
AREA Count_Ones, CODE
EXPORT __main
ALIGN
ENTRY
__main PROC
; r0 = Input = x
; r1 = Number of ones = counter
LDR r0, =0xAAAAAAAA
; r1 = r0 >> 31
MOV r1, r0, LSR #31
; r0 = r0 << 2 and change Carry
loop MOVS r0, r0, LSL #2
; r1 = r1 + r0 >> 31 + Carry
ADC r1, r1, r0, LSR #31
BNE loop
stop B stop
ENDP
END
At the end of the first loop: r1 = b31 + b30 + b29
After LDR: r0=10101010101010101010101010101010 (Load input data into r0) After MOV: r1=r0 >> 31 = 1 (Initialize r1 with the most significant bit of r0. r0 logical shift right by 31 bits, take the leftmost bit b31) After MOVS: r0 = r0 << 2 =10101010101010101010101010101000 (Logical shift left r0 by 2 bits and update C = 0, as the last shifted out bit b30) After ADC: r1 = r1 + r0 >> 31 + Carry = b31 + b29 + b30 =1 + 1 + 0 = 2 2nd iteration: r1 = r1 + b28 + b27 = 2 + 1 + 0 = 3 If after MOVS, the result in r0 is zero, (no more 1’s), Z flag is set to 1 and the loop exits
Notes: LDR r0, =0xAAAAAAAA: Load the input data into r0.
MOV r1, r0, LSR #31: Initialize r1 with the most significant bit of r0.
MOVS r0, r0, LSL #2: Logical shift left r0 by 2 bits and update the carry flag.
ADC r1, r1, r0, LSR #31: Add with carry the count in r1 and the current bit from r0.
BNE loop: The loop ends when the result is zero (Zero flag set).

## Slide 19: Example 2: Counting Ones in a Word: Explanations
Iteration | Shifted r0 value (MSB bit) | Carry bit (last shifted out) | r1 (accumulated count) | Notes
0 (init) | — | — | b31 = 1 | r1 initialized with b31
1 | b29 = 1 | b30 = 0 | 1 (b31) + 1 (b29) + 0 (b30) = 2 | r0 shifted left by 2 bits
2 | b27 = 1 | b28 = 0 | 2 + 1 (b27) + 0 (b28) = 3 | 
3 | b25 = 1 | b26 = 0 | 3 + 1 (b25) + 0 (b26) = 4 | 
4 | b23 = 1 | b24 = 0 | 4 + 1 (b23) + 0 (b24) = 5 | 
in r0 0xAAAAAAAA, bits at odd positions (31, 29, 27, ..., 1) are all 1, bits at even positions (30, 28, 26, ..., 0) are all 0.
Carry bit is always the even bit index at each iteration.
At each iteration, r1 accumulates 1 (highest bit, odd index) + 0 (carry bit, even index).
The loop ends when r0 becomes zero after the last shift, triggering the Zero flag and exiting the branch.
The count accumulates to 16, consistent with the fact that 0xAAAAAAAA has exactly 16 ones in 32 bits.
This program counts two bits per loop iteration, leveraging the Carry bit, and will take 16 iterations for a 32-bit word.

## Slide 20: Stop B stop
“stop B stop” means an infinite loop that repeatedly branches to the label "stop".
  B is the branch instruction in ARM, which causes the program to jump to the specified label or address.
  Here, the label and destination are both "stop". This creates a loop where execution never moves past this point.
  It is commonly used to halt the program or wait indefinitely, often when the program completes or to prevent it from running into uninitialized memory.

## Slide 21: Example 2: Counting Ones in a Word: Simpler Programs
LDR r0, =0xAAAAAAAA ; Load input data into r0
MOV r2, #0 ; Initialize count (r2) to 0
loop:
MOV r1, r0, LSR #31 ; Extract leftmost bit of r0 into r1 (0 or 1)
ADD r2, r2, r1 ; Add extracted bit to count in r2
MOVS r0, r0, LSL #1 ; Shift r0 left by 1 bit, update flags
BNE loop ; If r0 != 0, repeat loop
Algo 1: use MOV r1, r0, LSR #31 to extract the highest bit from r0 and accumulates the per-bit count. (Carry flag is set but ignored.)
Algo 2: use MOVS r0, r0, LSL #1 to shift left by 1 bit and update the carry flag with the bit shifted out (the leftmost bit of the original value). Use ADC (Add with Carry) to add the carry bit to accumulator r2 without needing to move the leftmost bit explicitly.
Both programs count one bit per loop iteration, discarding the Carry bit, and will take 32 iterations for a 32-bit word.
LDR r0, =0xAAAAAAAA ; Load input data into r0
MOV r2, #0 ; Initialize bit count accumulator (r2) to 0
loop:
MOVS r0, r0, LSL #1 ; Shift left by 1 bit, carry gets old MSB
ADC r2, r2, #0 ; Add carry (0 + carry) to r2
BNE loop ; Loop while r0 != 0 (Zero flag clear)
Algo 1
Algo 2
Notes: LDR r0, =0xAAAAAAAA: Load the input data into r0.
MOV r1, r0, LSR #31: Initialize r1 with the most significant bit of r0.
MOVS r0, r0, LSL #2: Logical shift left r0 by 2 bits and update the carry flag.
ADC r1, r1, r0, LSR #31: Add with carry the count in r1 and the current bit from r0.
BNE loop: The loop ends when the result is zero (Zero flag set).

## Slide 22: Quiz
Q: In Algo 1 and Algo 2, can we change MOVS r0, r0, LSL #1 to MOV r0, r0, LSL #1?
ANS:
Q: In Algo 1, can we change MOV r1, r0, LSR #31 to MOVS r1, r0, LSR #31
ANS:
Q: In Algo 1, can we change ADD r2, r2, r1 to ADC r2, r2, r1
ANS:
Q: In Algo 2, can we change ADC r2, r2, #0 to ADD r2, r2, #0?
ANS:
Notes: No, you cannot simply replace MOVS r0, r0, LSL #1 with MOV r0, r0, LSL #1 if you want to use the carry flag for bit counting, because:
MOVS shifts and updates the condition flags, including the carry flag (which captures the leftmost bit shifted out).
MOV just copies/moves the value without updating any status flags (Carry, Zero, Negative, etc.).
Without status flag updates, the carry flag won't track the bit shifted out, so the later ADC instruction would not add the correct carry bit.
Thus, for counting bits by carry from shifts, MOVS is required to update the carry flag each time shifting left.
The plain MOV can only move data without affecting flags and is insufficient for this purpose.
No, you cannot replace ADC r2, r2, #0 with ADD r2, r2, #0 if you want to add the carry bit from the previous operation.
Why?
ADC (Add with Carry) adds two operands plus the carry flag.
ADD only adds the two operands without considering the carry flag.
Since the bit count relies on the carry flag (set by the previous MOVS shift left), replacing ADC with ADD would ignore the carry bit, causing incorrect counting.
In ADC r2, r2, #0, the immediate #0 means the register r2 plus 0 plus carry are summed, effectively adding carry to r2.
Using ADD r2, r2, #0 adds zero and ignores carry, so no bit would be counted from the carry.
Hence, keep using ADC to accumulate the bits from the carry flag properly.

## Slide 23: Example 3: Finding Max of an Array
// Initialize max and location maxLocation = 0; maxValue = array[0];
// Loop through the array for (i = 0; i < arraySize; i++){ if (array[i] > maxValue) { maxValue = array[i]; maxLocation = i; } }

## Slide 24: Example 3: Finding Max of an Array
C Program | Assembly Program
int array[10] = {-1, 5, 3, 8, 10, 23, 6, 5, 2, -10}; int size = 10; | AREA myData, DATA ALIGN array DCD -1,5,3,8,10,23,6,5,2,-10 size DCD 10
int main(void) { int i, maxLocation, maxValue; | AREA findMax, CODE EXPORT __main ALIGN ENTRY __main PROC ; Identify the array size LDR r3, =size LDR r3, [r3] ; array size SUB r3, r3, #1
// Initialize max and location maxLocation = 0; maxValue = array[0]; | ; Initialize max value and location LDR r4, =array LDR r0, [r4] ; r0 = default max MOV r1, #0 ; r1 = max location
// Loop through the array for (i = 0; i < size; i++){ if (array[i] > maxValue) { maxValue = array[i]; maxLocation = i; } } | ; Loop over the array MOV r2, #0 ; loop index i loop CMP r2, r3 ; compare i & size BGE stop ; stop if i ≥ size LDR r5, [r4,r2,LSL #2] ; array[i] CMP r5, r0 ; compare with max MOVGT r0, r5 ; update max value MOVGT r1, r2 ; update location ADD r2, r2, #1 ; update index i B loop
while(1); //dead loop } | stop B stop ; dead loop ENDP END
Notes: The ARM assembly instruction
text
LDR r5, [r4, r2, LSL #2]
means the following:
LDR (Load Register) loads a 32-bit word from memory into the register r5.
The memory address it loads from is computed as the sum of the value in register r4 plus the value in register r2 shifted left by 2 bits.
The "LSL #2" is a logical shift left by 2 bits, which is equivalent to multiplying r2 by 4.
Since ARM usually addresses memory in bytes and each array element (like an integer) is usually 4 bytes, shifting the index by 2 adjusts for byte addressing versus word indexing.
This allows accessing the memory element at array base address stored in r4 plus an offset equal to the element index (r2) times 4 bytes.
In short, it loads into r5 the value of the element located at index r2 in an integer array whose base address is in r4.
This is commonly used to read array elements in ARM assembly efficiently by using scaled offsets in the load instruction.
azeria-labs+1
https://developer.arm.com/documentation/dui0041/latest/Babbfdih
https://developer.arm.com/documentation/ddi0406/c/Application-Level-Architecture/Instruction-Details/Alphabetical-list-of-instructions/LDR--immediate--ARM-
https://azeria-labs.com/memory-instructions-load-and-store-part-4/
https://stackoverflow.com/questions/62563750/ldr-and-equ-in-arm-assembly
https://duetorun.com/blog/20230606/arm-ldr/
https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf
https://www.youtube.com/watch?v=fJcdt7WMQCs
https://www.reddit.com/r/asm/comments/x6icyg/arm_difference_between_ldr_and_str/

## Slide 25: Quiz
Instruction LDR r5, [r4,r2,LSL #2] has the form:
LDR <destination register>, [<base register>, <index register>, LSL #<shift amount>]
Address=value in r4+(value in r2×22 )
  The memory address is calculated by taking the value in the <base register> (here r4) plus the value in the <index register> (here r2) shifted left (logical shift left, LSL) by a certain number of bits (#2 means shifted by 2 bits, or multiplied by 4).
Q: why do we perform r2×22 here?
ANS:
Notes: Since each element is a 32 bit word, we need to multiply by 4 to convert from array index to memory address