## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 12
Fixed-point and Floating-point Arithmetic

## Slide 2: ARM Cortex-M Instruction Sets
from arm.com
Digital Signal Processing
Advanced data processing
Bit field manipulations
Basic data processing
I/O control tasks
Floating Point

## Slide 3: FPU on Cortex-M4
from arm.com
FPU is optional
Cortex-M4 = Cortex-M3 + DSP + FPU (optional)

## Slide 4: FPU on Cortex-M4
“float” in C
“double” in C
Cortex-M4
FPU
FPU only support single precision.

## Slide 5: Floating-point Multiplication
float area_of_rectangle(float length, float width) { float area; area = length * width; return area; }
Software-based FP Multiplication
; Inputs: ; r0 = length ; r1 = width ; Return: ; r0 = area area_of_rectangle PROC PUSH {lr} ; call software library BL __aeabi_fmul POP {pc} ; return area in r0 ENDP
r0
r1
r0
Hardware-based FP Multiplication
; Inputs: ; s0 = length ; s1 = width ; Return: ; s0 = area area_of_rectangle PROC ; Call FPU instructions VMUL.F32 s0, s0, s1 BX lr ; return area in s0 ENDP
s0
s1
s0

## Slide 6: ARM Keil
Not Used
  FP operations are performed by software FP library
Single Precision
  Single-precision performed by FPU hardware directly
  Double-precision performed by software FP library

## Slide 7: Enable FPU
from arm.com
CPACR
Coprocessor Access Control Register (CPACR) in System Control Block (SCB)
SCB->CPACR |= (0xF<<20);

## Slide 8: Enable FPU
C Program | Assembly Program
// Enable FPU by setting CP10 and // CP11 fields in System Control // Block (SCB) SCB->CPACR ¦= (0xF << 20); | ; Load SCB base address (0xE000ED00) LDR r0, = SCB_BASE ; Read SCB->CPACR LDR r1, [r0, #SCB_CPACR] ; Enable full access to CP10 and CP11 ORR r1, r1, #(0xF << 20) ; Write SCB->CPACR STR r1, [r0, #SCB_CPACR];
00 = Access denied (default). Any attempted access generates a NOCP (no co-processor) fault.
01 = Privileged access only. An unprivileged access generates a NOCP fault.
10 = Reserved.
11 = Full access.

## Slide 9: Floating-point Unit (FPU)
Floating-point Unit
Registers s0–s31
ARM Cortex-M
Registers r0–r15
Memory
STR
PUSH
LDR
POP
VLDR
VPOP
VSTR
VPUSH
FPU coprocessor
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13(SP)
r14(LR)
xPSR
r15(PC)
Cortex-M Registers
PRIMASK
FAULTMASK
BASEPRI
CONTROL
s1
s3
s5
s7
s9
s11
s13
s15
s17
s19
s21
s23
s25
s27
s29
s31
s0
s2
s4
s6
s8
s10
s12
s14
s16
s18
s20
s22
s24
s26
s28
FPSCR
s30
FPU Registers
FPCAR
FPCCR
Notes: The FPU has 32 single-precision general registers.
Floating-Point Context Address Register (FPCAR)
Floating-Point Context Control Register (FPCCR)
Floating-Point Status Control Register (FPSCR)

## Slide 10: Floating-Point Registers
s1
s3
s5
s7
s9
s11
s13
s15
s17
s19
s21
s23
s25
s27
s29
s31
s0
s2
s4
s6
s8
s10
s12
s14
s16
s18
s20
s22
s24
s26
s28
s30
FPU Registers
d0
d1
d2
d3
d4
d5
d6
d7
d8
d9
d10
d11
d12
d13
d14
d15
s0
s1
d0
upper
32 bits
lower
32 bits
64 bits
s = single precision (32 bits)
d = double precision (64 bits)
Load a float from address in r0
VLDR.F32 s0, [r0]
Load a double from address in r0
; stored into s1 and s0
VLDR.F64 d0, [r0]
Stack operations
VPUSH.64 {d0,d1}
VPUSH.32 {r4,r6}

## Slide 11: FPU Instructions
 | ARM Cortex-M | FPU
Accessing memory | LDR, STR, LDM, STM, PUSH, POP | VLDR, VSTR, VLDM, VSTM, VPUSH, VPOP
Copying registers | MOV, MRS, MSR | VMOV, VMRS, VMSR
Arithmetic | ADD, SUB, MULS, SDIV/UDIV, | VADD, VSUB, VMUL, VDIV
Multiply-Accumulation | MLA, MLS | VMLA, VMLS
Comparison | CMP | VCMP
Advanced Arithmetic |  | VABS, VNEG, VSQRT
VMLA Sd, Sn, Sm ; Sd = Sd + Sn * Sm
VMLS Sd, Sn, Sm ; Sd = Sd - Sn * Sm

## Slide 12: Register Usages across Function Calls

## Slide 13: Register Usages across Function Calls
A PROC
...
VPUSH {s3, s5}
BL B ; call function B
VPOP {s3, s5}
...
ENDP
B PROC
...
ENDP

## Slide 14: Register Usages across Function Calls
A PROC
...
VPUSH {s3, s5}
BL B ; call function B
VPOP {s3, s5}
...
ENDP
B PROC
VPUSH {s17}
VLDR.F32 s17, [r0]
...
VPOP {s17}
ENDP

## Slide 15: Passing Arguments to a Procedure
s1
s3
s5
s7
s9
s11
s13
s15
s17
s19
s21
s23
s25
s27
s29
s31
s0
s2
s4
s6
s8
s10
s12
s14
s16
s18
s20
s22
s24
s26
s28
s30
FPU Registers
d0
d1
d2
d3
d4
d5
d6
d7
d8
d9
d10
d11
d12
d13
d14
d15
Each argument is assigned in turn to the next free register of the corresponding type
Example:
  double fun(double a1, float a2, double a3, float a4, float a5, double a6, float a7, double a8)
a4
a2
a1
a6
a8
a3
a5
a7

## Slide 16: Example 1: Area of Circle
r
float area(float radius){
float pi = 3.14;
float area;
area = pi * radius * radius;
return area;
}
Implementation in assembly
area PROC
EXPORT area
VLDR.F32 s1, =3.1416 ; Pseudo-instruction
VMUL.F32 s1, s1, s0 ; r0 = radius (input argument)
VMUL.F32 s0, s1, s0 ; return area in s0
BX LR
ENDP

## Slide 17: Transfer data between FPU and ARM
Floating-point Unit
Registers s0–s31
ARM Cortex-M
Registers r0–r15, APSR
VMOV
VMOV r0, s0 ; Copy s0 into r0
VMOV s1, r1 ; Copy r1 into s0
VMRS: Move into ARM register from FPU special register
VMSR: Move into FPU special register from ARM register
Floating-point Unit
Special Registers
ARM Cortex-M
Registers r0–r15, APSR
VMRS
VMSR
FPSCR, FPCAR, FPCCR
VMRS r0, FPSCR ; Read current FPSCR
ORR r0, r0, #(3<<22) ; Set bits 22 and 23 to 1
VMSR FPSCR, r0 ; Save into FPSCR
Example:
Example: Change the rounding mode to round toward zero
Notes: Rounds to the nearest value. This is the default configuration.

## Slide 18: Floating-point Status Control Register (FPSCR)
FPSCR[23:22]
  00: Round to nearest (default)
  01: Round towards
  10: Round towards
  11: Round towards 0

## Slide 19: Example 2: Comparison
float max(float a, float b){
if (a > b)
return a;
else
return b;
}
max PROC
; Update NZCV in FPSCR
VCMP.F32 s0, s1
; Copy NZCV flags to APSR
VMRS APSR_nzcv, FPSCR
VMOVLE.F32 s0, s1
ENDP
Floating-point Unit
FPSCR
ARM Cortex-M
APSR
VMRS
Copy N, Z, C, V flags from FPU status register to ARM core APSR
VMRS APSR_nzcv, FPSCR

## Slide 20: Convert Integer to Floating Point
signed integer
unsigned integer
single precision
double precision
VCVT.F32.S32
VCVT.F32.U32
VCVT.F64.U32
VCVT.F64.S32
VCVT.F64.U32 d2, s0 ; Convert unsigned integer to double
Example:

## Slide 21: Convert Floating Point to Integer
signed integer
unsigned integer
single precision
double precision
VCVT.S32.F32
VCVT.U32.F32
VCVT.U32.F64
VCVT.S32.F64
VCVT.U32.F64 s0, d2 ; Convert double to unsigned integer
Example:

## Slide 22: Convert between Fixed-Point and Single Precision
N: the number of fraction bits in fixed point
Td: type and size of fixed point
  S32: signed 32-bit value
  U32: unsigned 32-bit value
  S16: signed 16-bit value
  U16: unsigned 16-bit value
VCVT.Td.F32 Sd, Sm, #n
VCVT.Td.F32 Sd, Sd, #n
VCVT.F32.Td Sd, Sm, #n
VCVT.F32.Td Sd, Sd, #n
Example:
VCVT.F32.S32 s0, s0, #10 ; Convert a 32-bit fixed point to float
; Fraction part of the fixed point has 10 bits

## Slide 23: Automatic Stacking & Unstacking
Interrupt Handler
Interrupt
Request
User Program
User Program
Stacking
Unstacking
Interrupt
Exit
Time

## Slide 24: Automatic Stacking & Unstacking
xxxxxxxx
xPSP
PC (r15)
LR (r14)
r12
r3
r2
r1
r0
Old SP
Auto
Stacking
New SP
xxxxxxxx
FPSCR
s15
s14
s13
...
...
s0
xPSP
PC (r15)
LR (r14)
r12
r3
r2
r1
r0
Old SP
Auto
Stacking
New SP
FPCAR
Without FPU
With FPU
17 FPU registers

## Slide 26: Passing Arguments
Each number is assigned in turn to the next free register of the corresponding type
Example:
  double fun(double a1, float a2, double a3, float a4,
  float a5, double a6, float a7, double a8)
a1
a2
a4
a3
a6
a8
a7
a6

## Slide 27: Precision Conversion
VCVT{R}.S32.F32 Sd, Sm | Convert from single-precision float to signed 32-bit (S32) or unsigned 32-bit (U32) integer.
VCVT{R}.U32.F32 Sd, Sm | 
VCVT{R}.F32.S32 Sd, Sm | Convert to single-precision float from signed 32-bit (S32) or unsigned 32-bit (U32) integer.
VCVT{R}.F32.U32 Sd, Sm | 
VCVT{R}.Td.F32 Sd, Sm, #n | Convert between single-precision and fixed-point. Td can be S16 (signed 16-bit), U16 (unsigned 16-bit), S32 (signed 32-bit), and U32 (unsigned 32-bit). #n is the number of fraction bits in the fixed-point number.
VCVT{R}.Td.F32 Sd, Sd, #n | 
VCVT{R}.F32.Td Sd, Sm, #n | 
VCVT{R}.F32.Td Sd, Sd, #n | 
VCVT<B¦T>.F32.F16 Sd, Sm | Converts half-precision float to single-precision (B = bottom half of Sm, T = top half of Sm)
VCVT<B¦T>.F16.F32 Sd, Sm | Converts single-precision float to half-precision (B = bottom half of Sd, T = top half of Sd)
{R}: R is optional, and it means conversion with Rounding

## Slide 28: Floating-point Status Control Register (FPSCR)
FPSCR[23:22]
  00: Round to nearest (default)
  01: Round towards
  10: Round towards
  11: Round towards 0

## Slide 29: Floating-point Context Control Register (FPCCR)
Three FPU context save/restore configurations:
  Lazy save/store (default): LSPEN = 1, ASPEN = x
  No FPU register saving: LSPEN = 0, ASPEN = 0
  Automatic save/restore: LSPEN = 0, ASPEN = 1

## Slide 30: Automatic Stacking and Unstacking upon Interrupt

## Slide 31: Load and Store Floating-point Numbers
VLDR.F32 Sd, [Rn] | Load one single-precision float
VLDR.F64 Dd, [Rn] | Load one double-precision float
VSTR.32 Sd, [Rn] | Store one float registers
VSTR.64 Dd, [Rn] | Store one double register
VLDM.32 Rn{!}, list | Load multiple single-precision floats
VLDM.64 Rn{!}, list | Load multiple double-precision floats
VSTM.32 Rn{!}, list | Store multiple float registers
VSTM.64 Rn{!}, list | Store multiple double registers
VPOP.32 list | Pop float registers from stack
VPOP.64 list | Pop double registers from stack
VPUSH.32 list | Push float registers to stack
VPUSH.64 list | Push double registers to stack
Examples:
VLDR.F32 s0, [r0, #4] ; Pre-index, s0 = mem[r0 + 4]
VLDR.F32 s0, [r0], #4 ; Post-index, s0 = mem[r0], r0 += 4
VLDR.F32 s0, [r0, #4]! ; Pre-index with update, s0 = mem[r0 + 4], r0 += 4
VLDM.64 r0, {d0-d7} ; Load 8 double precision numbers
VSDM.64 r0, {d0-d7} ; Store 8 double precision numbers
VPUSH.32 {s16-s31} ; Save floating point registers
VPOP.32 {s16-s31} ; Restore floating point registers

## Slide 32: Copy Floating-point Numbers
VMOV.F32 Sd, #imm | Move immediate to float-register
VMOV.F32 Sd, Sm | Copy from single-precision register to single-precision register
VMOV.F64 Dd, Dm | Copy from double-precision register to double-precision register
VMOV Sn, Rt | Copy ARM core register to float register
VMOV Sm1, Sm2, Rt1, Rt2 | Copy 2 ARM core registers to 2 float registers
VMOV Dd[x], Rt | Copy ARM core register to a half of a double-precision floating-point register, where x is 0 or 1.
VMOV Rt, Dn[x] | Copy a half of a double-precision floating-point register to ARM core register, where x is 0 or 1.
Examples:
VMOV s0, s1, r0, r1 ; s0 = r0, s1 = r1
VMOV r1, d0 [1] ; r1 = d0 [1] = s1
VMOV.F32 s1, #3.25 ; s1 = 3.25

## Slide 33: Single-precision Arithmetic Operations
VADD.F32 {Sd,} Sn, Sm | Add floating points, Sd = Sn + Sm
VSUB.F32 {Sd,} Sn, Sm | Subtract float, Sd = Sn - Sm
VDIV.F32 {Sd,} Sn, Sm | Divide single-precision floats, Sd = Sn/Sm
VMUL.F32 {Sd,} Sn, Sm | Multiply float, Sd = Sn * Sm
VNMUL.F32 {Sd,} Sn, Sm | Negate and multiply float, Sd = -1 * Sn * Sm
VNEG.F32 Sd, Sm | Negate float, Sd = -1 * Sm
VABS.F32 Sd, Sm | Absolute value of floats, Sd = ¦Sm¦
VSQRT.F32 Sd, Sm | Square-root of float
C Function | Assembly Function
float area_of_circle(float radius){ float PI = 3.14; float area; area = PI * radius * radius; return area; } | area_of_circle PROC EXPORT area_of_circle VLDR.F32 s1,=3.14 ; Pseudo-instruction VMUL.F32 s1,s1,s0 ; r0 = radius VMUL.F32 s0,s1,s0 ; return area in s0 ENDP

## Slide 34: Single-precision Arithmetic Operations
VLMA.F32 {Sd,} Sn, Sm | Multiply float, then accumulate float, Sd = Sd + Sn*Sm
VLMS.F32 {Sd,} Sn, Sm | Multiply float, then subtract float, Sd = Sd - Sn*Sm
VNMLA.F32 Sd, Sn, Sm | Multiply float, then accumulate, then negate float, Sd = -1 * (Sd + Sn * Sm)
VNMLS.F32 Sd, Sn, Sm | Multiply float, then subtract, then negate float, Sd = -1 * (Sd - Sn * Sm)
Fused MAC instructions: intermediate result are not rounded. ⟹ Better accuracy
VFMA.F32 {Sd,} Sn, Sm | Multiply (fused) then accumulate float, Sd = Sd + Sn*Sm
VFMS.F32 {Sd,} Sn, Sm | Multiply (fused) then subtract float, Sd = Sd - Sn*Sm
VFNMA.F32 {Sd,} Sn, Sm | Multiply (fused) then accumulate then negate float, Sd = -1 * Sd + Sn * Sm
VFNMS.F32 {Sd,} Sn, Sm | Multiply (fused) then subtract then negate float, Sd = -1 * Sd - Sn * Sm

## Slide 35: Single-precision Arithmetic Operations
VADD.F32 {Sd,} Sn, Sm | Add floating points, Sd = Sn + Sm
VSUB.F32 {Sd,} Sn, Sm | Subtract float, Sd = Sn - Sm
VDIV.F32 {Sd,} Sn, Sm | Divide single-precision floats, Sd = Sn/Sm
VMUL.F32 {Sd,} Sn, Sm | Multiply float, Sd = Sn * Sm
VNMUL.F32 {Sd,} Sn, Sm | Negate and multiply float, Sd = -1 * Sn * Sm
VNEG.F32 Sd, Sm | Negate float, Sd = -1 * Sm
VABS.F32 Sd, Sm | Absolute value of floats, Sd = ¦Sm¦
VSQRT.F32 Sd, Sm | Square-root of float
C Function | Assembly Function
float area_of_circle(float radius){ float PI = 3.14; float area; area = PI * radius * radius; return area; } | area_of_circle PROC EXPORT area_of_circle VLDR.F32 s1,=3.14 ; Pseudo-instruction VMUL.F32 s1,s1,s0 ; r0 = radius VMUL.F32 s0,s1,s0 ; return area in s0 ENDP

## Slide 36: Single-precision comparisons
VCMP.F32 Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero
VCMPE.F32 Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero, and raise exception for a signaling NaN
C Program | Assembly Program
float max(float a, float b){ if (a > b) return a; else return b; } | max PROC VCMPE.F32 s0, s1 ; Copy NZCV flags to APSR VMRS APSR_nzcv, FPSCR BGT exit VMOV.F32 s0, s1 exit BX LR ENDP

## Slide 37: Single-precision comparisons
VCMP.F32 Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero
VCMPE.F32 Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero, and raise exception for a signaling NaN
C Program | Assembly Program
float max(float a, float b){ if (a > b) return a; else return b; } | max PROC VCMPE.F32 s0, s1 ; Copy NZCV flags to APSR VMRS APSR_nzcv, FPSCR BGT exit VMOV.F32 s0, s1 exit BX LR ENDP

## Slide 38: Precision Conversion
VCVT{R}.S32.F32 Sd, Sm | Convert from single-precision float to signed 32-bit (S32) or unsigned 32-bit (U32) integer.
VCVT{R}.U32.F32 Sd, Sm | 
VCVT{R}.F32.S32 Sd, Sm | Convert to single-precision float from signed 32-bit (S32) or unsigned 32-bit (U32) integer.
VCVT{R}.F32.U32 Sd, Sm | 
VCVT{R}.Td.F32 Sd, Sm, #n | Convert between single-precision and fixed-point. Td can be S16 (signed 16-bit), U16 (unsigned 16-bit), S32 (signed 32-bit), and U32 (unsigned 32-bit). #n is the number of fraction bits in the fixed-point number.
VCVT{R}.Td.F32 Sd, Sd, #n | 
VCVT{R}.F32.Td Sd, Sm, #n | 
VCVT{R}.F32.Td Sd, Sd, #n | 
VCVT<B¦T>.F32.F16 Sd, Sm | Converts half-precision float to single-precision (B = bottom half of Sm, T = top half of Sm)
VCVT<B¦T>.F16.F32 Sd, Sm | Converts single-precision float to half-precision (B = bottom half of Sd, T = top half of Sd)

## Slide 39: Passing Arguments
Each number is assigned in turn to the next free register of the corresponding type
Example:
  double fun(double a1, float a2, double a3, float a4, float a5, double a6, float a7, double a8)

## Slide 40: Example: Square Root
C Code | Assembly Code
float my_sqrt(float x){ float root, root_old = 1.0; do { root = root_old; root_old = (root + x / root) / 2; } while(root_old != root); return root; } | __asm float my_sqrt_assembly(float x){ VMOV.F32 s2,s0 ; s0 = x VMOV.F32 s3,#1 ; s3 = root_old VMOV.F32 s1,s3 loop VMOV.F32 s0, s1 ; root = root_old; VDIV.F32 s3,s2,s0 VADD.F32 s3,s3,s0 VMOV.F32 s4,#2 VDIV.F32 s5,s3,s4 VMOV.F32 s1,s5 VCMP.F32 s1,s0 VMRS APSR_nzcv,FPSCR BNE loop BX lr }