## Slide 1: Zonghua Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 3
ARM Instruction Set Architecture
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: History

## Slide 3: ARM Processors
ARM Cortex-A family:
  Applications processors
  Support OS and high-performance applications
  Such as Smartphones, Smart TV
ARM Cortex-R family:
  Real-time processors with high performance and high reliability
  Support real-time processing and mission-critical control
ARM Cortex-M family:
  Microcontroller
  Cost-sensitive, support SoC

## Slide 4: ARM Family

## Slide 5: Instruction Sets
Instructions:
  Encoded to binary machine code by assembler
  Executed at runtime by hardware
Early 32-bit ARM vs Thumb/Thumb-2
  Early ARM has larger power consumption and larger program size
  16-bit Thumb, first used in ARM7TDMI processors in 1995
  Thumb-2: a mix of 16-bit (high code density) and 32-bit (high performance) instructions
ARM Cortex-M:
  Subset of Thumb-2

## Slide 6: ARM Processors

## Slide 7: Processor Registers
Fastest way to read and write
Registers are within the processor chip
Each register has 32 bits
ARM Cortex-M4 has
  Register Bank: R0 – R15
    R0-R12: 13 general-purpose registers
    R13: Stack pointer (Shadow of MSP or PSP)
    R14: Link register (LR)
    R15: Program counter (PC)
  Special registers
    xPSR, BASEPRI, PRIMASK, etc
Register Bank
Special Registers

## Slide 8: Processor Registers
Register Bank
Special Registers
Low Registers (R0 – R7)
  Can be accessed by any instruction
High Register (R8 – R12)
  Can only be accessed by some instructions
Stack Pointer (R13)
  Cortex-M4 supports two stacks
  Main SP (MSP) for privileged access (e.g. exception handler)
  Process SP (PSP) for application access
Program Counter (R15)
  Memory address of the current instruction

## Slide 9: Processor Registers vs Peripheral Registers
ARM Cortex-M Core
Registers
ALU
Control Unit
Registers
GPIO A
Registers
GPIO B
Registers
UART1
Registers
SPI
Registers
ADC

## Slide 10: Processor Registers vs Peripheral Registers
Processor can directly access processor registers
  ADD r3,r1,r0 ; r3 = r1 + r0
Processor access peripheral registers via memory mapped I/O
  Each peripheral register is assigned a fixed memory address at the chip design stage
  Processor treats peripherals registers the same as data memory
  Processor uses load/store instructions to read from/write to memory (to be covered in future lectures)

## Slide 11: C vs Assembly

## Slide 12: Load-Modify-Store
Translating C to assembly
Load values from memory into registers
Modify value by applying arithmetic operations
Store result from register to memory

## Slide 13: Load-Modify-Store

## Slide 14: ARM Cortex-M4 Organization (STM32L4)
System-on-a-chip

## Slide 15: Assembly Instructions
Arithmetic and logic
  Add, Subtract, Multiply, Divide, Shift, Rotate
Data movement
  Load, Store, Move
Compare and branch
  Compare, Test, If-then, Branch, compare and branch on zero
Miscellaneous
  Breakpoints, wait for events, interrupt enable/disable, data memory barrier, data synchronization barrier

## Slide 16: Instruction Format: Labels
label mnemonic operand1, operand2, operand3 ; comments

## Slide 17: Instruction Format: Labels
label mnemonic operand1, operand2, operand3 ; comments
Place marker, marking the memory address of the current instruction
Used by branch instructions to implement if-then or goto
Must be unique

## Slide 18: Instruction Format: Mnemonic
label mnemonic operand1, operand2, operand3 ; comments
The name of the instruction
Operation to be performed by processor core

## Slide 19: Instruction Format: Operands
label mnemonic operand1, operand2, operand3 ; comments
Operands
  Registers
  Constants (called immediate values)
Number of operands varies
  No operands: DSB
  One operand: BX LR
  Two operands: CMP R1, R2
  Three operands: ADD R1, R2, R3
  Four operands: MLA R1, R2, R3, R4
Normally
  operand1 is the destination register, and operand2 and operand3 are source operands.
  operand2 is usually a register, and the first source operand
  operand3 may be a register, an immediate number, a register shifted to a constant number of bits, or a register plus an offset (used for memory access).

## Slide 20: Instruction Format: Comments
label mnemonic operand1, operand2, operand3 ; comments
Everything after the semicolon (;) is a comment
Explain programmers’ intentions or assumptions

## Slide 21: ARM Instruction Format
label mnemonic operand1, operand2, operand3 ; comments
  target ADD r0, r2, r3 ; r0 = r2 + r3
label
mnemonic
comment
destination operand
2nd source operand
1st source operand

## Slide 22: ARM Instruction Format
label mnemonic operand1, operand2, operand3 ; comments
Examples: Variants of the ADD instruction
  ADD r1, r2, r3 ; r1 = r2 + r3
  ADD r1, r3 ; r1 = r1 + r3
  ADD r1, r2, #4 ; r1 = r2 + 4
  ADD r1, #15 ; r1 = r1 + 15

## Slide 23: Example Assembly Program: Copying a String

## Slide 24: Example Assembly Program: Copying a String

## Slide 25: Example Assembly Program: Copying a String

## Slide 26: Logic View of Memory
By grouping bits together we can store more values
  8 bits = 1 byte
  16 bits = 2 bytes = 1 halfword
  32 bits = 4 bytes = 1 word
From software perspective, memory is an addressable array of bytes.
  The byte stored at the memory address 0x20000004 is 0b10000100
  A word can only be stored at an address that‘s divisible by 4 （Word-address mod 4 = 0, binary address ends with 00）
  Memory address of a word is the lowest address of all 4 bytes in that word.
  A halfword can only be stored at an address that‘s divisible by 2 （Halfword-address mod 2 = 0, binary address ends with 0）
  Memory address of a halfword is the lowest address of all 2 bytes in that word.
01110010
00100101
11100010
10000100
01100001
10001111
00010010
10010100
Low Address
High Address
0x20000007
0x20000006
0x20000005
0x20000004
0x20000003
0x20000002
0x20000001
0x20000000
8 bits
0b10000100
0x84
132
Binary
Hexadecimal
Decimal
Notes: 0b10000100 0x84 132

## Slide 27
Two possible byte orderings:
  Little-endian: the LSB (Least Significant Byte) is stored at the lowest address.
  Big-endian: the LSB (Least Significant Byte) is stored at the highest address.
  Intel processors use Little-Endian; ARM processors can be configured as either Little- or Big-endian; STM32 microcontrollers based on ARM Cortex-M3 use little-endian
Example: 4-byte data 0xA1B2C3D4 at memory address 0x100
  (Memory address is Byte address, not bit address)
MSB
LSB
Memory Byte Ordering
D4
C3
B2
A1
Big-Endian
0x100
0x101
0x102
0x103
LSB
MSB
A1
B2
C3
D4
Little-Endian
0x100
0x101
0x102
0x103
Notes: Below are examples of Little Endian ordering (A 32-bit memory range can contain one 32-bit word, or two 16-bit half-words, or four 8-bit Bytes)

## Slide 28
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 FF 00
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 78 56 34 12
Little-Endian
  LSB is at lower address
Big-Endian
  MSB is at lower address
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 00 FF
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 12 34 56 78

## Slide 29: Data Alignment
Assume a byte-addressable memory with a data bus that is 32 bits (4 bytes) wide
Consider 16 bytes of memory (addresses 0 to 15) arranged as four 32-bit words (4 bytes each)
Well-aligned: each word begins on a mod-4 address, which can be read in a single memory cycle
Ill-aligned: a word begins on address 6, not a mod-4 address, which can be read in 2 memory cycles
The first read cycle would retrieve 4 bytes from addresses 4 through 7; of these, the bytes from addresses 4 and 5
are discarded, and those from addresses 6 and 7 are moved to the far right;
The second read cycle retrieves 4 bytes from addresses 8 through 11; the bytes from addresses 10 and 11 are discarded, and those from addresses 8 and 9 are moved to the far left;
Finally, the two halves are combined to form the desired 32-bit operand: