## Slide 1: L8 Cache Part I
Zonghua Gu, 2018
5/3/2018
Acknowledgement: some slides taken from UC Berkeley CS61C

## Slide 2: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 3: Why are Large Memories Slow? Library Analogy
Time to find a book in a large library
  Search a large card catalog – (mapping title/author to index number)
  Round-trip time to walk to the stacks and retrieve the desired book
Larger libraries worsen both delays
Electronic memories have same issue, plus the technologies used to store a bit slow down as density increases (e.g., SRAM vs. DRAM vs. Disk)
However what we want is a large yet fast memory!
5/3/2018

## Slide 4: Processor-DRAM Gap (Latency)
1980 microprocessor executes ~one instruction in same time as DRAM access
2017 microprocessor executes ~1000 instructions in same time as DRAM access
Memory wall: memory access likely to be the performance bottleneck
5/3/2018
Notes: Why doesn’t DRAM get faster?

## Slide 5: What To Do: Library Analogy
Write a report using library books
Go to library, look up relevant books, fetch from stacks, and place on desk in library
If need more, check them out and keep on desk
  But don’t return earlier books since might need them
You hope this collection of ~10 books on desk enough to write report, despite 10 being only 0.00001% of all books in the library
5/3/2018

## Slide 6: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 7: Memory Hierarchy
Cache
Small, Fast
(SRAM)
Capacity: register << cache (typically on-chip) << memory (off-chip)
Latency: register << cache (typically on-chip) << memory (off-chip)
On a data access:
  if data Î cache  cache hit  low latency access (SRAM)
  if data Ï cache  cache miss  high latency access (DRAM)
  Goal: create the illusion of accessing as much memory as is available in the slow memory at the speed of the fast cache
CPU
Big, Slow Memory
(DRAM)
holds frequently used data
Registers
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)
When accessing a memory address, one of two things can happen:
  Cache hit: cache block is valid and refers to the proper memory address, so read from cache (fast)
  Cache miss: cache block is invalid, or refers to the wrong memory address, so read from memory (slow)

## Slide 8: Memory Hierarchy Technologies
Caches use SRAM (Static Random Access Memory) for speed and technology compatibility
  Fast (typical access times of 0.5 to 2.5 ns)
  Low density (6 transistor cells), higher power, expensive
  Static: content will last as long as power is on
Main memory uses DRAM (Dynamic RAM) for size and density
  Slower (typical access times of 50 to 70 ns)
  High density (1 transistor cells), lower power, cheaper
  Dynamic: needs to be “refreshed” regularly (every ~8 ms)
    Consumes 1% to 2% of the active cycles of the DRAM
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
http://parts.digikey.com/1/parts/1211303-ic-sram-1mbit-10ns-32soj-cy7c109d-10vxi.html
Quantity discount 10ns 1MBit SRAM $2.24, $17/Mbyte, $1700/100 Mbyte, $17000/GByte
http://www.frys.com/template/harddrives
DRAM: 4GB @ $70 or $17.50 per GB
24GB@$800 = $33/Gbyte
http://www.frys.com/category/Outpost/Hard+Drives+&+Memory/Memory/Notebook+Memory/Apple+-+Mac++Memory/
DDR2 1GB @ $25 per
DDR3 1 GB @ $37.5 per
FLASH Media
Approx. $2 per Gbyte

## Slide 9
Cache Blocks
Larger, slower, cheaper memory.
Smaller, faster, more expensive memory
Typical block size: 1 – 4 words (4 – 16 Bytes)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
14
CPU

## Slide 10
General Cache Concepts: Hit
Data in block b is needed
Block b is in cache:
Hit!
Data is loaded from cache into CPU register
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Request: 14
14
CPU

## Slide 11
General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is loaded from cache into CPU register
CPU

## Slide 12: Chip Photos
5/3/2018

## Slide 13: Memory Hierarchy Speed vs. Size
Second
Level
Cache
(SRAM)
CPU Control
CPU
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100B’s 10KB’s MB’s GB’s TB’s
Cost/bit: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).
Programmer-invisible hardware mechanism gives illusion of speed of fastest memory with size of largest memory
  Works even if you have no idea what a cache is
  Performance-oriented programmers sometimes “reverse engineer” cache organization to design data structures and access patterns optimized for a specific cache design

## Slide 14: How is the Hierarchy Managed?
Registers  memory hierarchy
  By compiler (or assembler programmer)
Cache  main memory
  By the cache controller hardware
  Focus of this lecture
Main memory  disks (secondary storage)
  By the operating system (virtual memory)
  By the programmer (files)
Notes: Virtual to physical address mapping assisted by the hardware (Translation LB)

## Slide 15: Principle of Locality
Principle of Locality: Programs access small portion of address space at any instant of time (spatial locality) and repeatedly access that portion (temporal locality)
Temporal Locality (locality in time)
  Go back to same book on desk multiple times
  If a memory location is referenced, then it will tend to be referenced again soon
    Keep recently-accessed blocks in the cache
Spatial Locality (locality in space)
  When go to book shelf, pick up multiple books around the book you want, since library stores related books together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
    When fetching a block into cache, also fetch blocks around it
5/3/2018
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 16: Quiz: What locality does this program have?
Data:
  Temporal locality: variable sum is referenced in each iteration
  Spatial locality: array a[] is accessed with stride-1 in each iteration (assuming a[] is stored in contiguous addresses in memory)
Instructions:
  Temporal locality: the loop body is executed repeatedly for n times
  Spatial locality: instructions are accessed sequentially (with 1 branch in each iteration) (assuming instructions are stored in contiguous addresses in memory)
int sum = 0, a[n];
…
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 17: Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality
5/3/2018

## Slide 18: Memory Reference Patterns
Address
Time
Instruction
fetches
Stack
accesses
Data
accesses
n loop iterations
subroutine call
subroutine return
argument access
vector access
scalar accesses
5/3/2018

## Slide 19: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 20: Processor with Cache
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache
5/3/2018
Processor organized around words and bytes
Memory (including
cache) organized around blocks, which are typically multiple words

## Slide 21: Cache vs. Memory
Cache size << memory size
  Smaller cache is faster
1-to-many correspondence between cache blocks and memory blocks
  Use Tags in the cache to match cache and memory blocks
A cache block is also called a cache line

## Slide 22: Block Must be Aligned in Memory
If each cache block is 4 Bytes (1 word), then binary address each cache block always ends in 00two
How to take advantage of this to save hardware and energy?
Don’t need to compare last 2 bits of 32-bit byte address (comparator can be narrower)
  Don’t need to store last 2 bits of 32-bit byte address in Cache Tag (Tag can be narrower)
If each cache block is 8 Bytes (2 words), then binary address each cache block always ends in 000two
5/3/2018

## Slide 23: Tradeoffs of Cache Block Sizes
Smaller cache blocks  more fine-grained caching  take better advantage of temporal locality
  A given data item stays in the cache longer before getting replaced
Larger cache blocks  more coarse-grained caching, take better advantage of spatial locality
  Fetching each cache block brings in lots of data at nearby addresses into the cache
In either case, if the program has poor temporal or spatial locality, then lots of junk may be brought into cache

## Slide 24: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 25: Alternative Cache Organizations
A memory block is mapped to one cache set, which may contain one or more cache blocks
Direct Mapped (DM)
  Each cache set has 1 cache block; # cache sets = # cache blocks
  A memory block is mapped to 1 possible cache block
Fully Associative (FA)
  A single cache set contains all cache blocks; # cache sets = 1
  A memory block can be mapped to any cache block
N-way Set Associative (SA)
  Each cache set has N cache blocks; # cache sets = # cache blocks / N
  N is also called associativity
  A memory block can be mapped to one of N possible cache blocks
DM and FA are special cases of SA
  DM = 1-way SA (N = 1)
  FA = N-way SA (N = total number of cache blocks)
5/3/2018

## Slide 26
0 1 2 3
Set Number
Cache
(4 blocks)
DM 2-way SA FA (4-way SA)
In set 0 In set 0 In set 0
(1 block) (2 blocks) (4 blocks)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
(32 blocks)
Block Number
Alternative Cache Organizations (4-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
0 1 0 1
0
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 4=0) (12 mod 2=0)

## Slide 27: Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Data
Byte
Data
Byte
A Cache Block
100
304
6848
416
Data
Byte
Data
Byte
Tag
Valid
0
1
0
1
1
1
A “valid bit” indicates of a cache block contains valid data
  e.g., upon startup, the cache is “cold”: all cache blocks are invalid
  The cache is “warmed-up” gradually by bringing content into the cache
A tag helps identify the memory block contained in the cache block;
  Disambiguate among multiple possible memory blocks that may be mapped to the same cache block
Cache capacity refers to the total size of cache blocks (not including Tag and Valid bits)
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 28
Set Number
Cache
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
Alternative Cache Organizations（8-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
DM 2-way SA 4-way SA FA(8-way SA)
In set 4 In set 0 In set 0 In set 0
(1 block) (2 blocks) (4 blocks) (8 blocks)
0 1 2 3
4
5
6
7
0 1 2 3
0
1
2
3
0 1 0 1
0
1
0
1
0 1 0 1
0
1
0
1
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 8=4) (12 mod 4=0) (12 mod 2=0)

## Slide 29: Processor Address Fields Used by Cache Controller
Offset: Byte address within a cache block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Set Index (SI) = log2(number of sets)
Size of Offset = log2(number of bytes/block)
Size of Tag = Address size – Size of SI - Size of Offset
Memory Address
5/3/2018
Offset
Tag
Set Index
Notes: For class handout

## Slide 30: Direct-Mapped Cache
Cache
Main Memory
Q: Given a memory block, which cache block is it mapped to?
A: Use 2 middle index bits in memory address to determine which cache block it is mapped to
00: mapped to blue block in cache
01: mapped to green block in cache
10: mapped to pink block in cache
11: mapped to grey block in cache
Tag
Data
6-bit memory address: 2-bit Tag, 2-bit Set Index, 2-bit Offset (4 Bytes/block).
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Q: Is the exact memory block in the cache?
A: Compare 2 higher tag bits in memory address to the cache tag to tell if the memory block is in the cache (provided valid bit is set)
Q: Which exact Byte address in a given cache block of 4 Bytes?
A: Use the Offset
0
5
1
Offset
2
3
4
Tag
Set Index
Set
Way
0
0
1
2
3
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 31: DM Cache Example
Cache
Main Memory
Q: Given memory address 001110, is it in the cache?
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
3
4
0
1
1
1
01
11
10
00
Q: Given memory address 0100xx, is it in the cache?
Q: Given memory address 1110xx, is it in the cache?
0
0
1
2
3
Tag
Data
Valid
Set
Way
Offset
Tag
Set Index
6-bit memory address: 2-bit Tag, 2-bit Set Index, 2-bit Offset (4 Bytes/block).
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes)

## Slide 32
Cache
Main Memory
Q: Given memory address 001110, is it in the cache?
A: Yes. First, 2 middle index bits (11) means that it is mapped to grey block in cache; Second, the 2 higher tag bits (00) matches the tag in the grey block, with valid bit of 1; Finally, to get the exact Byte address, use the Offset of 10
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
3
4
0
1
1
1
01
11
10
00
Q: Given memory address 0100xx, is it in the cache?
A: No. First, 2 middle bits (00) means that it is mapped to blue block in cache; Second, the 2 higher tag bits (01) matches the tag in the blue block, with valid bit of 0.
Q: Given memory address 1110xx, is it in the cache?
A: No. First, 2 middle index bits (10) means that it is mapped to pink block in cache, with valid bit of 1; Second, the 2 higher tag bits (11) does not match the tag (10) in the pink block.
0
0
1
2
3
Tag
Data
Valid
Set
Way
Offset
Tag
Set Index
6-bit memory address: 2-bit Tag, 2-bit Set Index, 2-bit Offset (4 Bytes/block).
DM Cache Example
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes)

## Slide 33: 2-Way Set-Associative Cache
Cache
Main Memory
Q: Given a memory block, which cache set is it mapped to?
A: Use 1 middle index bits in memory address to determine which cache set it is mapped to
0: mapped to blue set in cache
1: mapped to pink set in cache
Tag
Data
6-bit memory address: 3-bit Tag, 1-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
Q: Is the exact memory block in the cache?
A: Compare 3 higher tag bits in memory address to the cache tag to tell if the memory block is in the cache (provided valid bit is set)
Q: Which exact Byte address in a given cache block of 4 Bytes?
A: Use the Offset
0
5
1
2
3
Each memory block is mapped to a cache set with the same color
Way
0
1
0
1
0
1
Offset
Tag
Set Index
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 34: 2-Way SA Cache Example
Main Memory
6-bit memory address: 3-bit Tag, 1-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
3
Q: Given memory address 0111xx, is it in the cache?
Q: Given memory address 0100xx, is it in the cache?
Q: Given memory address 1110xx, is it in the cache?
Cache
Tag
Data
Valid
Set
Way
0
1
0
1
0
1
010
111
101
001
Offset
Tag
Set Index
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 35: 2-Way SA Cache Example
Q: Given memory address 0111xx, is it in the cache?
A: No. First, 1 middle index bit (1) means that it is mapped to pink set in cache; Second, the 3 higher tag bits (011) does not match any tag in the pink set (101 and 001).
Q: Given memory address 0100xx, is it in the cache?
A: No. First, 1 middle index bit (0) means that it is mapped to blue set in cache; Second, the 3 higher tag bits (010) matches one of the tags in the blue set (010 and 111); Third, the valid bit of the corresponding cache block is 0.
Q: Given memory address 1110xx, is it in the cache?
A: Yes. First, 1 middle index bit (0) means that it is mapped to blue set in cache; Second, the 3 higher tag bits (111) matches one of the tags in the blue set (010 and 111); Third, the valid bit of the corresponding cache block is 1.
Main Memory
6-bit memory address: 3-bit Tag, 1-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
3
Cache
Tag
Data
Valid
Set
Way
0
1
0
1
0
1
010
101
111
001
Offset
Tag
Set Index
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 36: Fully-Associative Cache (4-way SA)
Main Memory
Q: Given a memory block, which cache set is it mapped to?
A: There is only a single blue set.
6-bit memory address: 4-bit Tag, 0-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Q: Is the exact memory block in the cache?
A: Compare 4 higher tag bits in memory address to the cache tag to tell if the memory block is in the cache (provided valid bit is set)
Q: Which exact Byte address in a given cache block of 4 Bytes?
A: Use the Offset
0
5
1
Offset
2
Tag
Cache
Tag
Data
Valid
Set
Way
0
1
0
2
3
Each memory block is mapped to a cache set with the same color
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 37: FA Cache Example
Main Memory
6-bit memory address: 3-bit Tag, 1-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
Q: Given memory address 0011xx, is it in the cache?
Q: Given memory address 0100xx, is it in the cache?
Q: Given memory address 0101xx, is it in the cache?
Cache
Tag
Data
Valid
Set
Way
0
1
0
2
3
0101
1110
1010
0011
Offset
Tag
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 38
Main Memory
6-bit memory address: 4-bit Tag, 0-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
Q: Given memory address 0011xx, is it in the cache?
A: Yes. The 4 higher tag bits (0011) matches one of the tags in the blue set, and the valid bit of the corresponding cache block is 1.
Q: Given memory address 0100xx, is it in the cache?
A: No. The 4 higher tag bits (0011) does not match any of the tags in the blue set.
Q: Given memory address 0101xx, is it in the cache?
A: No. The 4 higher tag bits (0101) matches one of the tags in the blue set, but the valid bit of the corresponding cache block is 0.
Cache
Tag
Data
Valid
Set
Way
0
1
0
2
3
0101
1110
1010
0011
Offset
Tag
FA Cache Example
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 39: Hypothetical Cache Design
What if we flip positions of Tag and Index? Have Index as higher-order bits, and Tag as lower-order bits?

## Slide 40: Hypothetical DM Cache Design (BAD)
Cache
Main Memory
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
3
4
0
1
1
1
0
0
1
2
3
Tag
Data
Valid
Set
Way
Offset
Tag
Set Index
Bad idea: Neighboring blocks in memory are mapped to the same cache line, since they share the same Set Index value
  If memory blocks are accessed sequentially, then each new incoming cache block will immediately replace the previous block at the same cache line, causing cache thrashing  cannot exploit spatial locality.
6-bit memory address: 2-bit Set Index, 2-bit Tag, 2-bit Offset (4 Bytes/block).

## Slide 41: Hypothetical 2-Way SA Cache Design
Cache
Main Memory
Tag
Data
6-bit memory address: 3-bit Tag, 1-bit Set Index, 2-bit Offset (each cache block is 4 Bytes/1 Word).
Valid
Set
Each memory block is mapped to a cache set with the same color
Way
0
1
0
1
0
1
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
5
1
2
4
Offset
Tag
Set Index
Still a likely bad idea, but not as bad as the DM cache in the last slide
  Each set (color) has 2 possible addresses in the cache
As associativity increases, this Tag-in-the-Middle approach becomes more feasible
0
1
1
1
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block One word blocks
Two low order bits (xx) define the byte in the block (1 word = 4 Byes) (i.e., modulo the number of blocks in the cache)

## Slide 42: Quiz: # Cache Misses for DM Cache
Consider the following (silly) program that repeatedly accesses an array of 4-Byte ints A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a DM cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model? (Assuming that LDR is used to load elements of A[] in every iteration, instead of keeping them in CPU registers.)
Notes: 4 cache misses:

## Slide 43: Answer: # Cache Misses for DM Cache
Consider the following program that repeatedly accesses an array of words A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a DM cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model?
For Tag-Set Index-Offset model: 4 misses
1st cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0]
2nd cache miss brings into cache a block with address 0001xx into Set 1, which contains A[1]
3rd cache miss brings into cache a block with address 0010xx into Set 2, which contains A[2]
4th cache miss brings into cache a block with address 0011xx into Set 3, which contains A[3]
9996 cache hits.
For Set Index-Tag-Offset model: 10000 misses
1st cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0]
2nd cache miss brings into cache a block with address 0001xx into Set 0, which contains A[1], and replaces A[0]
3rd cache miss brings into cache a block with address 0010xx into Set 0, which contains A[2], and replaces A[1]
4th cache miss brings into cache a block with address 0011xx into Set 0, which contains A[3], and replaces A[2]
5th cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0], and replaces A[3]
…
Tag-Set Index-Offset model has better spatial locality!
Notes: 4 cache misses:

## Slide 44: Quiz: # Cache Misses for 2-Way SA Cache
Consider the following program that repeatedly accesses an array of words A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a 2-way SA cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model?
Notes: 4 cache misses:

## Slide 45: Answer: # Cache Misses for 2-Way SA Cache
Consider the following program that repeatedly accesses an array of words A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a 2-way SA cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model?
For Tag-Set Index-Offset model: 4 misses
1st cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0]
2nd cache miss brings into cache a block with address 0001xx into Set 1, which contains A[1]
3rd cache miss brings into cache a block with address 0010xx into Set 0, which contains A[2]
4th cache miss brings into cache a block with address 0011xx into Set 1, which contains A[3]
9996 cache hits.
For Set Index-Tag-Offset model: 10000 misses for LRU (Least-Recently-Used) replacement policy
1st cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0]
2nd cache miss brings into cache a block with address 0001xx into Set 0, which contains A[1]
3rd cache miss brings into cache a block with address 0010xx into Set 0, which contains A[2], and replaces A[0].
4th cache miss brings into cache a block with address 0011xx into Set 0, which contains A[3], and replaces A[1].
5th cache miss brings into cache a block with address 0000xx into Set 0, and replaces A[2].
Similar process repeats for Set 1.
(MRU (Most-Recently-Used) replacement policy can keep A[0] and A[2] in cache, leading to lower Miss rate. Details omitted)
Tag-Set Index-Offset model has better spatial locality!
Notes: 4 cache misses:

## Slide 46: Quiz: # Cache Misses for FA Cache
Consider the following program that repeatedly accesses an array of words A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a FA cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model?
Notes: 4 cache misses:

## Slide 47: Answer: # Cache Misses for FA Cache
Consider the following program that repeatedly accesses an array of words A[4]
  for (int i=0; i++, i<10000) {sum += A[0]+A[1]+A[2]+A[3];}
Suppose A[0] starts at memory address 000000, how many cache misses due to reading array A[] for a FA cache with either 1) the Tag-Set Index-Offset model; or 2) the Set Index-Tag-Offset model?
For either model: 4 misses
1st cache miss brings into cache a block with address 0000xx into Set 0, which contains A[0]
2nd cache miss brings into cache a block with address 0001xx into Set 0, which contains A[1]
3rd cache miss brings into cache a block with address 0010xx into Set 0, which contains A[2]
4th cache miss brings into cache a block with address 0011xx into Set 0, which contains A[3]
9996 cache hits.
Trick question! There is no Set Index, so the two models are the same!
Notes: 4 cache misses:

## Slide 48: Key Equations
5/3/2018
Offset
Tag
Set Index
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
SI size determines # sets = 2SI size
Offset size determines Bytes/block = 2Offset size
Tag size does not affect cache capacity; depends on memory address length
Notes: Total # cache blocks = Associativity * # sets = #ways (blocks/set) × # sets × Bytes/block C = N × S × B

## Slide 49: 2D Visualization of Cache Organization
#blocks = #ways * #sets
# ways (associativity)
# sets

## Slide 50: Cache Example
Assume: DM cache; 6-bit memory address: 2-bit Tag, 2-bit index, 2-bit Offset. Compute cache capacity and memory size.
  2-bit Offset => Bytes/block = 4;
  # sets = 2SI Size = 4
  # cache blocks = # ways * # sets = 1*4 = 4
  cache capacity = # cache blocks * Bytes/block = 4*4 = 16B
Memory size: 2^4 (2-bit tag +2-bit SI) = 16 blocks = 64 Bytes
0
5
1
Byte Within Block
Offset
2
3
Block Within $
4
Mem Block Within $Block
Tag
Set Index
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
Notes: 16 Memory blocks = 16 words = 64 bytes => 6 bits to address all bytes (Memory and cache blocks always have the same size) 4 Cache blocks, 4 bytes (1 word) per block
4 sets *1 block per set (direct mapped cache) = 4 blocks =
# Memory blocks (16) >> # Cache blocks (4)
  4 Memory blocks map to each cache block
Given a memory block, how to determine which cache set it is mapped to?
  Look at Set Index: middle two bits
A cache set may contain 1 of 4 possible memory blocks, which exact memory block is mapped to it?
  Look at tag: top two bits

## Slide 51: Range of SA Caches
memory_address_size = tag_size (T) + set_index_size (SI) + block_offset_size (BO)
For a fixed-size cache, and a given block size, if we decrease the size of the index by 1 bit and increases the size of the tag by 1 bit (pushing the red bar to the right by 1 bit) :
  Doubled: #ways = #blocks per cache set = associativity
  Halved: #cache sets
Quiz: what if Tag has 0 bits?
  Then cache has same size as memory  clearly unrealistic!
5/3/2018
Offset
Set Index
Tag
Decreasing associativity, lower way, more sets
Fully associative (only one set)
Tag is all bits in memory address
except Offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity, higher way, less sets
Selects the set
Used for tag compare
Selects the Byte in the block
Notes: each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number of “ways”) and halves the number of sets

## Slide 52: Alternative Cache Organizations
A memory block is mapped to one cache set, which may contain one or more cache blocks
Direct Mapped (DM)
  Each cache set has 1 cache block; # cache sets = # cache blocks
  A memory block is mapped to 1 possible cache block
Fully Associative (FA)
  A single cache set contains all cache blocks; # cache sets = 1
  A memory block can be mapped to any cache block
N-way Set Associative (SA)
  Each cache set has N cache blocks; # cache sets = # cache blocks / N
  N is also called associativity
  A memory block can be mapped to one of N possible cache blocks
DM and FA are special cases of SA
  DM = 1-way SA (N = 1)
  FA = N-way SA (N = total number of cache blocks)
5/3/2018
Review

## Slide 53: 4-Block Cache Summary (Valid Bit Omitted)
Tag
Data
Set
0
1
2
3
Tag
Data
Set
0
1
0
1
Tag
Data
Set
0
1
Tag
Data
Set
Way
0
1
0
2
3
0101
1110
1010
0011
Tag
Data
Set 0
Tag
Data
Tag
Data
Tag
Data
Way 0
Way 1
Way 2
Way 3
Tag
Data
Redraw
Redraw
Way 0
Way 1
DA Cache
2-way SA Cache
FA Cache (4-way SA)
0
5
1
2
3
Offset
Tag
Set Index
0
5
1
Offset
2
3
4
Tag
Set Index
0
5
1
2
Offset
Tag
  # cache blocks = 1 way * 4 sets = 4
  # cache blocks = 2 ways * 2 sets = 4
  # cache blocks= 4 ways * 1 set = 4
Notes: Total size of $ in blocks is equal to number of sets x associativity. For fixed $ size, increasing associativity decreases number of sets while increasing number of elements per set. With eight blocks, an 8-way set-associative $ is same as a fully associative $.

## Slide 54: 8-Block Cache
Each color denotes a cache set
54
Set 0
Set 1
Set 2
DM:
8 sets
1 way
Set 4
Set 5
Set 6
Set 7
Set 0
Set 0
Set 0
Set 0
FA: 1 set
1 set,
8 ways
Set 0
Set 0
Set 0
Set 0
2-Way SA: 4 sets,
2 ways
Set 0
Set 1
Set 2
Set 3
4-Way SA: 2 sets,
4 ways
Set 0
Set 1
0
N-1
1
O
2
4
5
Tag
S.I
O
O
O
0
N-1
1
2
3
4
0
N-1
1
2
3
0
N-1
1
2
Tag
  # cache blocks = 1 way * 8 sets =8
  # cache blocks = 2 ways * 4 sets =8
  # cache blocks = 4 ways * 2 sets =8
  # cache blocks = 8 ways * 1 set =8
Tag
S.I
Tag
S.I
Set 0
Set 1
Set 2
Set 3
Set 0
Set 1
Set 2
Set 3
Set 3
Set 0
Set 1
Set 0
Set 0
Set 1
Set 0
Set 1
Set 1
Notes: Direct Mapped: 1 way, 8 sets, 8 blocks
2 Way Set Associative: 2 ways, 4 sets, 8 blocks
4 Way Set Associative: 4 ways, 2 sets, 8 blocks
Fully Associative: 8 ways, 1 set, 8 blocks

## Slide 55: 8-Block Cache Summary
More ways (associativity)  fewer cache sets  cache structure is more “short (vertically) and fat (horizontally)”
Fewer ways (associativity)  more cache sets  cache structure is more “tall (vertically) and skinny (horizontally)”
Notes: Total size of $ in blocks is equal to number of sets x associativity. For fixed $ size, increasing associativity decreases number of sets while increasing number of elements per set. With eight blocks, an 8-way set-associative $ is same as a fully associative $.

## Slide 56: DM Cache Hardware (6-bit Memory)
2
Tag
2
Index
5/3/2018
Cache
Tag
Data
Valid
Set
0
1
2
3
0
5
1
Offset
2
3
4
Tag
Set Index
2
1. Set selection: the cache set index is used to select a set (1 block) from the cache.
2. Tag comparison: The tag of that block is compared with the higher bits of the memory address with HW comparator
3. Data output: If the tag matches, and the block’s Valid bit is 1, we have a cache hit; select and output 32-bit data of that cache block; Otherwise, we have a cache miss.
Total of 4 cache sets
A cache set contains 1 cache block with 4B of data
Comparator compares cache tag with higher part of memory address to see if it’s a Hit
Data
32
Output 32-bit data if Hit
AND gate
Hit?
Set selection
Tag comparison
Data output
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
What kind of locality are we taking advantage of?
The cache set index is used to select a set from the cache
The tags of 2 cache blocks in the set are compared in parallel with the higher bits of the memory address with HW comparator
If no tags match, we have a cache miss.
Otherwise, we have a cache hit, and we will select and output 32-bit data of the cache clock from the way where the tag match occurred, with 2x1 Mux
Temporal!

## Slide 57: 2-way SA Cache Hardware (6-bit Memory)
1
Index
Tag
Data
Set
0
1
Tag
Data
Valid
0
5
1
2
3
Offset
Tag
Set Index
3
3
Tag
3
AND gate
AND gate
Total of 2 cache sets
A cache set contains 2 blocks with 8B of data
Hit
OR Gate
Hit?
32
32
32
2x1 Mux
Output 32-bit data if Hit, from the way where the Tag matched
Set selection
Tag comparison
Data output
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
What kind of locality are we taking advantage of?
Need to compare every tag in each set to the Processor address
Tag comparators are expensive
Optimization: use two “sets” of data with a total of only 2 comparators
Use one Address bit to select which set
Compare only tags from selected set
Generalize to more sets
Temporal!

## Slide 58: Notes on 2-Way SA Cache
1. Set selection: the cache set index is used to select a set (2 blocks) from the cache.
2. Tag comparison: Tags of the 2 blocks in the set are compared with the higher bits of the memory address with 2 HW comparators in parallel
3. Data output: If one of the tags matches (the OR gate outputs true if any input is true), and that block’s Valid bit is 1, we have a cache hit; select and output 32-bit data of that cache block from the way where the tag matched, with 2x1 Mux. Otherwise, we have a cache miss
  The cache controller hardware always returns a 32-bit word; the application software can use the Offset bits for Byte-addressing into the word.
Think of 2-way SA cache as two DM caches working in parallel
  More hardware needed than DM cache: 2 comparators; 1 Mux
Notes: Essentially, you have 4 direct-mapped cache working in parallel.

## Slide 59: DM Cache Hardware (32-bit Memory)
32-bit memory address: 20-bit Tag, 10-bit set index, 2-bit Offset (each cache block is 4 Bytes).
  Cache size: 1 way * 2^10 (10-bit set index) = 1K blocks = 1K Words (4 KB)
  Memory size: 2^30 (20-bit tag +10-bit set index) =1G blocks = 1G Words (4 GB)
10
Index
31 30 . . . 13 12 11 . . . 2 1 0
20
5/3/2018
Data
Set
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
Total of 1024 cache sets
Data
32
Output 32-bit data if Hit
A cache set contains 1 cache block with 4B of data
20
Tag
Hit
AND gate
Hit?
Set selection
Tag comparison
Data output
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
What kind of locality are we taking advantage of?
Temporal!

## Slide 60: Multi-Word Block DM Cache
Index
8
Data
Set
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
20
5/3/2018
32-bit memory address: 20-bit Tag, 8-bit set index, 4-bit Offset (each cache block is 16 Bytes/4 Words).
  Cache size: 1 way * 2^8 (8-bit set index) = .25K blocks = 1K Words (4 KB)
  Memory size: 2^28 (20-bit tag +8-bit set index) =.25G blocks = 1G Words (4 GB)
A 4x1 Mux is needed to select a 32-bit word from 4 words in the hit cache block, controlled by the 4-bit Offset
A cache set contains 1 cache block with 16B of data
4
32
Byte offset
4x1 Mux
Output 32-bit data if Hit, taking into account Byte offset
20
Tag
AND gate
Hit?
Set selection
Tag comparison
Data output
Total of 256 cache sets
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size. What kind of locality are we taking advantage of?

## Slide 61: 4-Way SA Cache Hardware (32-bit Memory)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Set
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Way 0
Way 1
Way 2
Way 3
5/3/2018
Assume: 32-bit memory address: 22-bit Tag, 8-bit set index, 2-bit Offset (each cache block is 4 Bytes/1 Word). Cache size: 4 ways * 2^8 (8-bit set index) = 1K blocks = 1K Words (4 KB)
A cache set contains 4 cache blocks
Total of 256 cache sets
32
4x1 mux
Hit?
32
Output 32-bit data if Hit, from the way where the Tag matched
Set selection
Tag comparison
Data output
Notes: This is simple enough. What is its disadvantages?
28 = 256 sets each with four ways (each with one block)
+1 = 36 min. (Y:16)

## Slide 62: DM Cache HW Structure (Generic)
Tag
Data
V
Mux
=
BOffset
Tag
Set Index
t
k
b
t
Hit?
Data
2k
sets
Set selection
Tag comparison
Data output

## Slide 63: SA Cache HW Structure (Generic)
Tag
Data
V
=
Offset
Tag
Index
t
k
b
Tag
Data
V
=
t
Hit?
Mux
Data
Set selection
Tag comparison
Data output
63
Notes: Compare latency to direct mapped case? (jse)

## Slide 64: Alternative Cache Organizations: HW Costs
Need to compare every tag in each cache set to the memory address; no need to compare tags in different cache sets
  # HW comparators == # cache blocks in each cache set = # ways = associativity
Direct Mapped: a memory block is mapped to one address in cache
  # cache sets = # cache blocks; each cache set has 1 cache block
  # HW comparators = 1
Fully Associative: a memory block can be mapped to any address in cache
  # cache sets = 1; it contains all cache blocks
  # HW comparators = # cache blocks, plus a HW mux
N-way Set Associative: a memory block can be mapped to one of N possible addresses in cache
  # cache sets = # cache blocks / N; each cache set has N cache blocks
  Fully Associative: N = total number of cache blocks
  Direct Mapped: N = 1
  N HW comparators, plus a HW mux
5/3/2018

## Slide 65: N-way SA Cache: Performance Costs
Performance costs
  N-way SA cache: N HW comparators make Hit/Miss decision; Mux selects a way out of N ways (the hit cache block); output data
  DM cache: single HW comparator makes Hit/Miss decision; output data
    Speculative execution optimization: output cache block data before Tag comparison makes Hit/Miss decision; execute optimistically assuming it is a hit; recover later if it turns out to be a miss; works well if hit rate is high
      Instead of 1) Set selection; 2) Tag comparison; 3) Data output,
      we have 1) Set selection; 2) (Data output & Tag comparison) in parallel
    This optimization for DM cache does not work for N-way SA cache. Why?
      For N-way SA cache, data is available only after Hit/Miss decision; if hit, the Mux selects a block from one of N ways
      N possible hit cache blocks before Mux finishes selection
But SA cache reduces miss rate by having more flexible cache block placement
  When miss occurs, which block is selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
In summary: higher associativity  higher hit time & lower miss rate
5/3/2018
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
+2 = 38 min. (Y:18)
  (delay and area)
  Mux delay (set selection) before data is available

## Slide 66: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 67: Handling Stores with Write-Through
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: two policies
1) Write-Through Policy: write cache and write through the cache to memory
  Every write updates both cache and memory
  Optimization: insert a small write buffer between cache and memory to allow processor to continue once data in Buffer; memory is updated from write buffer in parallel to processor execution
5/3/2018

## Slide 68: Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when the block is evicted from cache
  Multiple writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only update memory if bit is set
    Called “Dirty” bit (writing makes it “dirty”)
5/3/2018

## Slide 69: Write-Back Cache
Store/cache hit, write data in cache only and set dirty bit
  Memory has stale value
Store/cache miss, read data from memory, then update and set dirty bit
  “Write-allocate” policy
Load/cache hit, use value from cache
On any miss, write back evicted block, only if it is dirty. Update cache with new block and clear dirty bit
5/3/2018
Notes: TODO: add examples?

## Slide 70: Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Memory always has copy of all data in cache
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Sometimes cache has only copy of data that is not in memory
  Reduces write traffic  write-back is the dominant approach in modern processors
5/3/2018

## Slide 71: Outline
Memory Hierarchy and Latency
Cache Principles
Basic Cache Organization
Different Kinds of Caches
Write Back vs. Write Through
Summary
5/3/2018
Fall 2017 – Lecture #14

## Slide 72: Summary
Cache – copy of data in lower level of memory hierarchy
Principle of locality:
  Program likely to access a relatively small range of memory addresses at any instant of time.
    Temporal locality vs. spatial locality
Cache organizations:
  Direct Mapped: 1 block per set
  N-way Set Associative: N blocks per set
  Fully Associative: all blocks in 1 set
Increasing associativity helps to reduce miss rate
  N-way: N possible places in cache to hold a given memory block
5/3/2018
Notes: Direct Mapped to find block in cache using Tag field and Valid bit for Hit Memory block maps into more than 1 cache block