## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 20
Analog-to-Digital Converter (ADC)

## Slide 2: Analog-to-Digital Converter (ADC)
x(t)
Analog signal
x(n)
Digital values
  Resolution
  Quantization error
  Sampling rate
continuous time
continuous amplitude
discrete time
discrete amplitude
ADC
clock
VREF
Notes: An ADC converts a continuous-time and continuous-amplitude analog signal, such as a sensor output, to a discrete-time and discrete-amplitude digital signal. The performance of an ADC is primarily characterized by its resolution, sampling rate, and power dissipation.

## Slide 3: ADC: Resolution
Resolution: number of binary bits in ADC output.
ADC
clock
VREF
Vinput
N: resolution
VREF: the maximum input voltage that can be converted by the ADC
Example: for 10-bit ADC, Vinput = 1V, VREF = 5V

## Slide 4: ADC: Quantization Error
Resolution N: number of binary bits in ADC output.
½ LSB
Least significant bit (LSB) voltage
Example: 3-bit ADC and input range [0, 5V]
Example: Resolution = 3 bits
Max quantization error = ±½ LSB
1 LSB

## Slide 5: Example of Quantization Error
Marek Gasior, Analog digital conversion, CERN Beam Instrumentation Group, BI CAS 2018, Tusula, Finland
LSB
½ LSB
- ½ LSB
Notes: A – input signal amplitude
n – number of bits
q – one bit amplitude:

## Slide 6: ADC: Sampling rate
Number of ADC output samples available per unit time.

## Slide 7: What sampling rate do we need?
http://195.134.76.37/applets/AppletNyquist/Appl_Nyquist2.html
Nyquist–Shannon Sampling Theorem

## Slide 8: ADC Architecture
https://www.analog.com/en/analog-dialogue/articles/the-right-adc-architecture.html
Popular ADC Architectures:
  Successive-approximation (SAR)
  Sigma-delta (Σ-Δ),
  Pipeline

## Slide 9: Successive-approximation (SAR)

## Slide 10: Determining Minimum Sampling Time
Sampling time is software programmable
Sampling time must large enough to settle within ½ LSB
½ LSB
R
C
VIN
VC
sampling time

## Slide 11: Programming ADC Sampling Time
Prescaler
/1, /2, /4
HSI Clock
16 MHz
ADC Clock
2.5 cycles
6.5 cycles
12.5 cycles
24.5 cycles
47.5 cycles
92.5 cycles
247.5 cycles
640.5 cycles
Selection
ADC sample time registers
(SMPR1 and SMPR2)
default prescaler = 1

## Slide 12: Successive-approximation (SAR) ADC
Binary search algorithm to gradually approaches the input voltage
Settle into ±½ LSB bound within the time allowed
N cycles for N-bit ADC
Notes: In the conversion phase, the device uses a binary search strategy to find the desired digital output.
The binary search starts with the most significant bit decision, and the tests are repeated for each binary bit until the least significant bit decision is made. The value of each binary bit is based on whether the analog input voltage is higher or lower than the DAC voltage. It gradually approaches the input value and eventually settles within the half LSB error bound.
One way to under the binary search algorithm mis to recall how to play the high low game. You are asked to guess a secrete number says between 0 to 100. At every guess, you will be told whether your guess is higher or lower than the secrete number. To minimize the number of guesses, we should select the middle value between the largest and smallest possible numbers. Thus, our first guess should be 50.
In this 4-bit ADC example, the conversion phase takes four clock cycles. During the first cycle, the analog input is compred againt 1000, which represents 0.5 times the reference voltage. Since the input is larger, during the second cycle, the analog input is compared with 0.75 of the reference voltage. Since the input is smaller, in the third cycle the input is compared with 0.625 times the reference voltage. And in the last cycle, it compares the input with 0.687.
The ADC total conversion time equals to the sum of the sampling time and the conversion time. The conversion time takes N cycles, where N is the number of bits in the ADC output, i.e., ADC resolution. As discussed previously, software can configure the the samping time.

## Slide 13: ADC Conversion Time
Suppose ADC clock = 16 MHz, and Sampling time = 4 cycles
For 12-bit ADC
For 6-bit ADC

## Slide 14: ADC: Regular vs injected
Notes: This is the ADC module within STM32 microcontrollers. The ADC module itself is a 12-bit successive approximation converter. Each converter can support a total of 16 regular channels and 4 injected channels. The module supports a flexible sequences to convert up to 16 channels in any desired order. Each channel can have different sampling period.

## Slide 15: ADC Conversion Modes
Single Channel Mode
Scan Mode
Notes: The ADC module supports several conversion modes:

## Slide 16: Example 1: ADC with Polling (Busy Waiting)
Main program
(ADC in single conversion mode)
ADC
Software starts one ADC conversion on a single channel.
Wait until EOC_MST is set in ADC common status register (CSR)
Result = ADC1->DR;
Repeat if more conversions are needed
ADC1->CR |= ADC_CR_ADSTART;
Hardware sets EOC_MST if done.

## Slide 17: Example 2: ADC with Interrupts
Main program
Configure and Starts ADC
void ADC1_2_IRQHandler(void){
if (ADC1->ISR | ADC_ISR_EOC){
buffer[i] = ADC1->DR;
i++;
}
...
}
An ADC interrupt request arrives.

## Slide 18: Example 3: ADC Triggered by a Timer
ADC clock
VREF
Vinput
Digital Output
TRGO
trigger
Timer clock
ADC
clock
clock
Channel #1
OC1REF
Timer

## Slide 19: Example 3: ADC Triggered by a Timer
main program
ADC
Timer
start timer
TRGO signals
interrupt request
Wait for ADC_Done = 1
Process Data
Repeat
ADC ISR
volatile uint ADC_Done = 0;
void ADC1_2_IRQHandler(void){
if (ADC1->ISR | ADC_ISR_EOC){
result[i] = ADC1->DR;
i++;
if (i >= N)
ADC_Done = 1;
}
...
}
Make N sampling

## Slide 20: Example 4: ADC Triggered by a Timer with DMA
main program
ADC
Timer
start timer
TRGO signals
DMA
request
Wait for DMA_Done = 1
Process Data
Repeat
DMA
controller
interrupt
request
DMA ISR
volatile uint DMA_Done = 0;
void DMA1_Channel1_IRQHandler(void){
...
DMA_Done = 1;
...
}
Make N sampling
DMA copies ADC DR register to memory after each conversion.

## Slide 21: Backup Slides

## Slide 22: ADC: Single Conversion Mode
Regular channel:
Set SWSTART in ADC_CR2
The channel is selected by SQ1[4:0] in SQR5
Result is stored in ADC_DR
EOC is set after conversion
Interrupt is generated if EOCIE is set
Injected channel:
Set JSWSTART in ADC_CR2
The channel is selected by JSQ1[4:0] in JSQR
Result is stored in ADC_JDR1
JEOC is set after conversion
Interrupt is generated if JEOCIE is set

## Slide 23: ADC: Scan Conversion Mode
Channels are selected by ADC_SQRx registers for regular channels, and by ADC_JSQR register for injected channel
All channels in a regular group share the same result register ADC_DR. Make sure to read data between consecutive sampling.
Notes: In the scan mode, a set of pre-defined input channels are sampled in single-short or continuous mode.

## Slide 24: Analog Watchdog
If V < VLTR or V > VHTR, the analog watchdog (AWD) flag (in ADC Status Register) is set, generating an interrupt to the processor
The monitor is automatically performed by hardware, not software
Convenient and efficient feature
Help processor detect exceptions and recover from specific situations
  For example, monitor sensor data and raise alarm on some level.
Analog voltage
Higher threshold (HTR)
Lower threshold (LTR)
Guarded Area
Two programmable thresholds

## Slide 25: VREF
Some chips does not expose VREF to a pin
  STM32L LQFP64 does not have VREF pin
  STM32L LQFP100 does
Infer internal VREF
  How?
Corresponds to

## Slide 26: Data Alignment

## Slide 28
Voltage
6
5
4
3
2
1
0
000
001
010
011
100
101
110
1
time (ms)
2
3
4
5
6
7
8
7
111