## Slide 1
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 15
Timer and PWM
Exercises ANS
Z. Gu
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Summary of Equations
Timer clock frequency vs. CPU Clock Frequency
Timer frequency with up-counting or down-counting mode:
PWM duty cycle for Mode 1 (Low-True):
Timer frequency with center-aligned counting mode:
PWM duty cycle for Mode 2 (High-True):
Review

## Slide 3: Calculating ARR
Suppose Timer Clock Frequency = 80MHz
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 4: Calculating ARR ANS
Suppose Timer Clock Frequency = 80MHz
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
But a 16-bit ARR register has value range of [0, 65535], so ARR value of 799999 or 400000 is out of range  cannot generate a 10ms timer from a 80MHz Timer Clock!
Solution: use prescaler (PSC) to reduce Timer Clock Frequency
For up-counting or down-counting mode:
For center-aligned counting mode:
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 5: Calculating ARR with prescaler
Suppose CPU Clock Frequency = 80MHz, PSC=79
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 6: Calculating ARR with prescaler ANS
Suppose CPU Clock Frequency = 80MHz, prescaler PSC=79
Goal: Timer Frequency = 100Hz
What should the ARR value be for 1. up-counting mode; 2. down-counting mode; 3. center-aligned counting mode?
For center-aligned counting mode:
With prescaler, the ARR value of 9999 or 5000 is now within the range of 16-bit ARR register.
For up-counting or down-counting mode:
Notes: {{Pause=2}} Suppose the clock source that drives the timer counter has a frequency of 80 MHz. We want to generate a SysTick interrupt every 10 milliseconds. What is the reload value? {{Pause=2}} Here is the diagram of SysTicks. {{Pause=0.5}} This is the clock signal, which has a frequency of 80 MHz. A SysTick interrupt is generated every 10 milliseconds. {{Pause=0.5}} An interrupt is generated when the counter makes the transition from 1 to 0. {{Pause=1} It takes a total of, reload plus 1, cycles to count down from the reload value to 0. {{Pause=0.5}} The reload value is calculated in this way. Reload value equals to 10 milliseconds, divided by the clock period, minus 1. This is equivalent to 10 milliseconds, multiply the clock frequency, minus 1. {{Pause=0.5}} The final result is 799999.

## Slide 7: Calculating the ARR
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.

## Slide 8: Calculating the ARR ANS
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.
= 0.1 MHz

## Slide 9: Clock Frequency and Timer Frequency
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Clock Frequency, and Timer Frequency, assuming up-counting mode?

## Slide 10: Clock Frequency and Timer Frequency ANS
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Clock Frequency, and Timer Frequency, assuming up-counting mode?
PSC, ARR are both in the range [0, 216-1=65535].
(A realistic Timer Frequency should not be higher than 1KHz, as mentioned before.)
=

## Slide 11: PWM duty cycle
Suppose a 16-bit timer has the following settings
    CPU Clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.

## Slide 12: PWM duty cycle ANS
Suppose a 16-bit timer has the following setting
    CPU clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.
=
PWM output is high on when the counter is 499, 500, 501, …, 1999, a total of 1501 cycles. (This statement is not required in the exam.)