## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Flow Control in Assembly
Exercises
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Pseudocode to Assembly
Write assembly program for pseudocode, one version without Conditional Execution instructions, one version with Conditional Execution.
Pseudocode | Assembly Program
if (r0 != r1) r2 = r2 + r2 | 
Pseudocode | Assembly Program w/Conditional Execution
if (r0 != r1) r2 = r2 + r2 | 
Notes: Compare r0 and r1
; Branch to skip if r0 == r1 (skip the addition)
; r2 = r2 + r2 (only executed if r0 != r1)
; Compare r0 and r1
ANS A:
  CMP r0, r1
  BEQ skip
  ADD r2, r2, r2
  skip:
ANS B:

## Slide 3: Pseudocode to Assembly
Write assembly program for pseudocode.
Pseudocode | Assembly Program 1
r1 = (r0 >> 4) & 15 | 
Notes: Alternative solution:

## Slide 4: Assembly Program Understanding
What is r0 equal to after running this program:
  MOV r0, #10
  MOV r1, #7
  MOV r2, #5
  CMP r1, r2
  ADDGT r0, r0, #100

## Slide 5: C to Assembly
Write the equivalent assembly program for this piece of code in C.
save[] is an array of 32-bit integers. Assume that i and k correspond to registers r1 and r2, and the base of the array save is in r0. Write assembly code corresponding to this C code.
C code | Assembly Program
while (save[i] == k) i += 1; | ; r0 = &save[0] (base address of array) ; r1 = i (index) ; r2 = k (value to compare) ...

## Slide 6: C to Assembly
Write the equivalent assembly program for this piece of code in C.
C code | Assembly Program
for (i=0; i<8; i++){ a[i] = b[7-i]; } | ; Assume r0 = base address of a, r1 = base address of b
Notes:   for (i=0; i<8; i++){
  a[i] = b[7-i];
  }
ANS:
  ; for (i=0; i<8; i++) { a[i] = b[7-i]; }
  ; Assume r0 = base address of a, r1 = base address of b
  MOV r2, #0 ; i = 0
  loop_start:
  …
  loop_end:

## Slide 7: C to Assembly: What is wrong?
C Program | Assembly Program
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: CMP r0, #10 ; Compare x0 with 10 while x0 <=10 BEQ end ; If cnt == 10, branch to end ADD r0, r0, #1 ; cnt = cnt + 1 B loop ; Repeat the loop done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUB r0, r0, #1 ; cnt--; sets flags BNE loop ; repeat until cnt == 0 (10 times) done:

## Slide 8: C to Assembly
C Program | Assembly Program
int cnt = 1; while (cnt <= 10) { // loop body cnt++; } | MOV r0, #1 ; cnt = 1 loop: ; loop body ADD ??? ; cnt++ CMP ??? BLE ??? ; while (cnt <= 10) continue done:
C Program | Assembly Program
int cnt = 10; while (cnt != 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS ??? ; cnt--; sets Z flag if r0=0 BNE ??? ; repeat until cnt == 0 (10 times) done:
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS ???; cnt--; sets Z flag if r0=0 BGT ??? ; repeat until cnt == 0 (10 times) done:

## Slide 9: C to Assembly: What is wrong?
C Program | Assembly Program
int cnt = 10; while (cnt > 0) { // loop body cnt--; } | MOV r0, #10 ; remaining iterations loop: ; loop body SUBS r0, r0, #1 ; cnt--; sets Z flag if r0=0 BPL loop ; repeat until cnt == 0 (10 times) done:
Notes: No—do not replace BNE with BPL in that loop.image.jpg
Why BNE is correct
After SUB r0, r0, #1, the Zero flag Z is set only when r0 becomes 0, so BNE (“branch if not equal to zero”) repeats exactly until the counter hits 0, giving 10 iterations from an initial value of 10.image.jpg
Why BPL is wrong here
BPL tests the Negative flag N=0 (i.e., “plus/non‑negative”), not whether the value is nonzero. Starting from 10 and decrementing, N stays 0 for 10 down to 0, so BPL would still branch at r0=0 and continue into −1
If using “plus” logic
To stop before going negative, the condition would need to be “branch while r0 > 0,” which is achieved with BGT after a CMP r0,#0 or by keeping BNE after SUBS. Using BPL alone does not encode “greater than zero.”

## Slide 10: C to Assembly
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i = i - 1) { array[i] = array[i] * 8; } | % R0 = base address of array, R1 = i MOV R0, 0x60000000 ; base address where array resides MOV R1, #199 ; i = 199 …

## Slide 11: C to Assembly
C Program | Assembly Program
//Calculate x such that 2^x=128 int pow = 1; int x = 0; while (pow != 128) { pow = pow * 2; x = x + 1; } | ; r0 = pow, r1 = x MOV r0, #1 ; pow = 1 MOV r1, #0 ; x = 0 WHILE DONE

## Slide 12: C to Assembly
For an array of 32‑bit ints, each element is 4 bytes, so element i lives at base + i*4, which is implemented as base + (i << 2) via LSL #2 in the addressing mode
BPL “Branch if PLus” branches when the N (negative) flag N == 0, meaning the prior result was positive or zero
C Program | Assembly Program
int array[200]; int i; for (i = 199; i >= 0; i=i-1) array[i] = array[i] * 8; | ; R0 = array base address, R1 = i MOV R0, 0x60000000 MOV R1, #199 FOR

## Slide 13: Assembly Programming
Write a program that reverses the bits in a register, such that the register containing d31,d30,d29...d1,d0 now contains d0,d1,...d29,d30,d3.

## Slide 14: Test for Equal
Give the different methods to test if two values held in registers r0 and r1 are equal.

## Slide 15: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Review
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 16: Conditional Instructions
Write the following ARMv7 instructions:
  Add registers r3 and r6 only if N is clear (from a previous instruction). Store the result in register r7.
  Multiply registers r7 and r12, put the results in register r3 only if C is set and Z is clear (from a previous instruction)
  Compare registers r6 and r8 only if Z is clear (from a previous instruction)
Notes: After a CMP/CMN or SUBS/ADDS used as an unsigned compare where the first operand is strictly greater than the second; for example, after CMP r0, r1, HI means r0 > r1 when treated as unsigned.

## Slide 17: Assembly to C
Write the equivalent C program for the following assembly code, assuming registers and C variables are related as (x=r0, y=r1). ( Variables in C are in memory, and load/store assembly instructions are omitted here for brevity.) For example:
Assembly Program | C Program
CMP r0, #5 MOVEQ r0, #10 BLEQ fn | if (x == 5) { x = 10; fn(x); }
Assembly Program | C Program
CMP r0, #0 MOVLE r0, #0 MOVGT r0, #1 | 
Assembly Program | C rogram
CMP r0, #'A’ CMPNE r0, #'B' MOVEQ r1, #1 | 

## Slide 18: Conditional Execution
Rewrite the assembly program to use conditional execution statements.
Assembly Program | Assembly Program with Cond. Exec
CMP r3, #0 BEQ next ADD r0, r0, r1 SUB r0, r0, r2 next ... |