## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 4
ARM Arithmetic and Logic Instructions
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Adding Two Integers
z = x + y;
int x = 1;
int y = 2;
int z;
If values are in registers
  Value of x in r0
  Value of y in r1
  Value of z in r2
C Statement
Assembly Statement

## Slide 3: Adding Two Integers
z = x + y;
int x = 1;
int y = 2;
int z;
ADD , ,
Source Operand 2
Source Operand 1
Destination
r2
r1
r0
C Statement
Assembly Statement
If values are in registers
  Value of x in r0
  Value of y in r1
  Value of z in r2

## Slide 4: Adding Two Integers
z = x + y;
uint x = 1;
uint y = 2;
uint z;
If values are in registers
  Value of x in r0
  Value of y in r1
  Value of z in r2
C Statement
Assembly Statement

## Slide 5: Adding Two Integers
z = x + y;
uint x = 1;
uint y = 2;
uint z;
ADD , ,
r2
r1
r0
If values are in registers
  Value of x in r0
  Value of y in r1
  Value of z in r2
C Statement
Assembly Statement
ADD works for both signed and unsigned add operations.

## Slide 6: Adding Two Integers
z = x + y;
int x = 1;
int y = 2;
int z;
If addresses are in registers
  Address of x in r0
  Address of y in r1
  Address of z in r2
C Statement
Assembly Statements

## Slide 7: Adding Two Integers
z = x + y;
int x = 1;
int y = 2;
int z;
If addresses are in registers
  Address of x in r0
  Address of y in r1
  Address of z in r2
LDR r3, [r0] ; Read x
LDR r4, [r1] ; Read y
ADD r5, r3, r4
STR r5, [r2] ; Write z
C Statement
Assembly Statements
Load, modify, and store

## Slide 8: Example Arithmetic Instructions
ADD r0, r1, r2 ; r0 = r1 + r2
ADC r0, r1, r2 ; Add with carry, r0 = r1 + r2 + carry
SUB r0, r1, r2 ; r0 = r1 - r2
SBC r0, r1, r2 ; Subtract with borrow, r0 = r1 - r2 – (1 – carry)
MUL r0, r1, r2 ; r0 = r1 * r2, product limited to 32 bits
UDIV r0, r1, r2 ; Unsigned divide, r0 = r1 / r2
SDIV r0, r1, r2 ; Signed divide, r0 = r1 / r2
SMULL r0, r1, r2, r3 ; Signed multiply (64-bit product), r1:r0 = r2 * r3
UMULL r0, r1, r2, r3 ; Unsigned multiply (64-bit product), r1:r0 = r2 * r3

## Slide 9: Example Logical Instructions
AND r0, r1, r2 ; Bitwise AND, r0 = r1 AND r2
ORR r0, r1, r2 ; Bitwise OR, r0 = r1 OR r2
EOR r0, r1, r2 ; Bitwise Exclusive OR, r0 = r1 EOR r2
ORN r0, r1, r2 ; Bitwise OR NOT, r0 = r1 ORN r2
BIC r0, r1, r2 ; Bit clear, r0 = r1 & ~r2
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
32 bits
r1
r2
r0
Bit-wise Logic AND
AND r0, r1, r2

## Slide 10: Example Shift & Rotate Instructions
LSL r0, r1, r2 ; Logical shift left,
r0 = r1 << r2
LSR r0, r1, r2 ; Logical shift right,
r0 = r1 >> r2
ASR r0, r1, r2 ; Arithmetic shift right, r0 = r1 >> r2
ROR r0, r1, r2 ; Rotate right,
r0 = r1 rotate by r2 bits
RRX r0, r1, r2 ; Extended rotate right, {C, r0} = {C, r1} rotate by r2 bits
Logical Shift Right (LSR)
Rotate Right (ROR)
Rotate Right Extended (RRX)
Logical Shift Left (LSL)
Arithmetic Shift Right (ASR)

## Slide 11: Example Data Transfer Instructions
MOV r0, r1 ; Move, r0 = r1
MVN r0, r1 ; Move NOT, r0 = bitwise NOT r1
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
r1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
r0
MVN r0, r1
Bit-wise Logic NOT

## Slide 12: Overview: Arithmetic and Logic Instructions
Shift : LSL (logic shift left), LSR (logic shift right), ASR (arithmetic shift right), ROR (rotate right), RRX (rotate right with extend)
Logic: AND (bitwise and), ORR (bitwise or), EOR (bitwise exclusive or), ORN (bitwise or not), MVN (move not)
Bit set/clear: BFC (bit field clear), BFI (bit field insert), BIC (bit clear), CLZ (count leading zeroes)
Bit/byte reordering: RBIT (reverse bit order in a word), REV (reverse byte order in a word), REV16 (reverse byte order in each half-word independently), REVSH (reverse byte order in each half-word independently)
Addition: ADD, ADC (add with carry)
Subtraction: SUB, RSB (reverse subtract), SBC (subtract with carry)
Multiplication: MUL (multiply), MLA (multiply-accumulate), MLS (multiply-subtract), SMULL (signed long multiply-accumulate), SMLAL (signed long multiply-accumulate), UMULL (unsigned long multiply-subtract), UMLAL (unsigned long multiply-subtract)
Division: SDIV (signed), UDIV (unsigned)
Saturation: SSAT (signed), USAT (unsigned)
Sign extension: SXTB (signed), SXTH, UXTB, UXTH
Bit field extract: SBFX (signed), UBFX (unsigned)
Syntax
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Notes: BIC bit clear
ORR bit set
AND bit mask
EOR bit invert
Comparisons produce no results - just set condition codes.
CMP like SUB
CMN like ADD (subtract of a negative number is the same as add)
TST like AND
TEQ like EOR (eor of identical numbers gives result of zero)
Generally single-cycle execution (except write to PC and register-controlled shift). Mention ARM NOP & Thumb NOP.
Explain RSB and RSC which do subtract in other order (e.g. y-x not x-y)
Does not include multiply (separate instr format). No divide - compiler uses run-time library or barrel shifter to perform division.
Can combine “S” bit with conditional execution, e.g.
ADDEQS r0, r1, r2

## Slide 13: Example: Add
  Unified Assembler Language (UAL) Syntax
ADD r1, r2, r3 ; r1 = r2 + r3
ADD r1, r2, #4 ; r1 = r2 + 4
  Traditional Thumb Syntax
ADD r1, r3 ; r1 = r1 + r3
ADD r1, #15 ; r1 = r1 + 15

## Slide 14: Commonly Used Arithmetic Operations
ADD {Rd,} Rn, Op2 | Add Rd  Rn + Op2
ADC {Rd,} Rn, Op2 | Add with carry Rd  Rn + Op2 + Carry
SUB {Rd,} Rn, Op2 | Subtract Rd  Rn - Op2
SBC {Rd,} Rn, Op2 | Subtract with carry Rd  Rn - Op2 + Carry - 1
RSB {Rd,} Rn, Op2 | Reverse subtract Rd  Op2 - Rn
MUL {Rd,} Rn, Rm | Multiply Rd  (Rn × Rm)[31:0]
MLA Rd, Rn, Rm, Ra | Multiply with accumulate Rd  (Ra + (Rn × Rm))[31:0]
MLS Rd, Rn, Rm, Ra | Multiply and subtract Rd  (Ra – (Rn × Rm))[31:0]
SDIV {Rd,} Rn, Rm | Signed divide Rd  Rn ÷ Rm
UDIV {Rd,} Rn, Rm | Unsigned divide Rd  Rn ÷ Rm
SSAT Rd, #n, Rm {,shift #s} | Signed saturate
USAT Rd, #n, Rm {,shift #s} | Unsigned saturate

## Slide 15: ARM Programming Model
31
0
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13: Stack Pointer (SP)
R14: Link Register (LR)
R15: Program Counter (PC)
N
Z
C
V
CPSR (Current Program Status Register)
Four flag bits:
  N (negative), Z (zero), C (carry), V (overflow).
Notes: Every arithmetic, logical, or shifting operation sets xPSR bits:

## Slide 16: Program Status Register (PSR)
Note:
GE flags are only available on Cortex-M4 and M7
Use PSR in code
N
Z
C
V
ISR number
Reserved
Reserved
ICI/IT
Reserved
T
Reserved
ISR number
APSR
IPSR
EPSR
PSR
Q
ICI/IT
T
N
Z
C
V
Q
ICI/IT
ICI/IT
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
31
30
29
28
27
Combine them together into one register (PSR)
GE
Reserved
GE
Reserved
Application PSR (APSR), Interrupt PSR (IPSR), Execution PSR (EPSR)

## Slide 17: NZCV Flags in xPSR
N: 1/0 = Result from ALU is Negative/positive
Z: 1/0 = Result from ALU is Zero/non-zero
C: Three cases:
  1/0 = ALU addition Carry out/no carry out
  1/0 = ALU subtraction no borrow/borrow
  1/0 = Bit shifted/rotated out
V: 1/0 = ALU oVerflowed/no overflow
Borrow and carry share the same flag bit.
For unsigned subtract, Borrow = NOT Carry

## Slide 18: Updating NZCV flags in PSR
Flags not changed |  | Flags updated
ADD | ⟶ | ADDS
SUB | ⟶ | SUBS
MUL | ⟶ | MULS
UDIV | ⟶ | UDIVS
AND | ⟶ | ANDS
ORR | ⟶ | ORRS
LSL | ⟶ | LSLS
MOV | ⟶ | MOVS
Most instructions update NZCV flags
only if S suffix is present
Some instructions update NZCV flags even if no S is specified.
CMP: Compare, like SUBS but without destination register
CMN: Compare Negative, like ADDS but without destination register
TST: Test, like ANDS but without destination register
TEQ: Test equivalence, like EORS but without destination register
CMP r1, r2 vs SUBS r0, r1, r2

## Slide 19: ADD vs ADDS
ADD does not update flags
ADDS updates flags
  xPSR.N = bit 31 of result
  xPSR.Z = IsZero(result)
  xPSR.C = carry, assuming r1 and r2 representing unsigned integers
  xPSR.V = overflow, assuming r1 and r2 representing signed integers
ADD r0, r1, r2 ; r0 = r1 + r2, NZCV flags unchanged
ADDS r0, r1, r2 ; r0 = r1 + r2, NZCV flags updated

## Slide 20: Suffix S: Update Flags
LDR r0, =0xFFFFFFFF
LDR r1, =0x00000001
ADDS r0, r0, r1
N (Negative) = 0
Z (Zero) = 1
C (Carry) = 1
V (oVerflow) = 0
0xFFFFFFFF r0
0x00000001 r1
+
0x00000000 sum
Notes: Combined Program Status Register (xPSR)

## Slide 21: Example: 64-bit Addition
0 0 0 0 0 0 0 2 F F F F F F F F
0 0 0 0 0 0 0 4 0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 7 0 0 0 0 0 0 0 0
Most-significant (Upper) 32 bits
Least-significant (Lower) 32 bits
+
Carry out
A register can only store 32 bits
A 64-bit integer needs two registers
Split 64-bit addition into two 32-bit additions

## Slide 22: Example: 64-bit Addition
start
; C = A + B
; Two 64-bit integers A (r1,r0) and B (r3,r2).
; Result C (r5, r4)
; A = 00000002FFFFFFFF
; B = 0000000400000001
LDR r0, =0xFFFFFFFF ; A’s lower 32 bits
LDR r1, =0x00000002 ; A’s upper 32 bits
LDR r2, =0x00000001 ; B’s lower 32 bits
LDR r3, =0x00000004 ; B’s upper 32 bits
; Add A to B
ADDS r4, r2, r0 ; C[31..0] = A[31..0] + B[31..0], update Carry
ADC r5, r3, r1 ; C[64..32] = A[64..32] + B[64..32] + Carry
stop B stop
r1
r0
r3
r2
r5
r4
Addend1
Addend2
Sum
Upper 32 bits
Lower 32 bits
Carry out

## Slide 23: Example: 64-bit Subtraction
start
; C = A - B
; Two 64-bit integers A (r1,r0) and B (r3,r2).
; Result C (r5, r4)
; A = 00000002FFFFFFFF
; B = 0000000400000001
LDR r0, =0xFFFFFFFF ; A’s lower 32 bits
LDR r1, =0x00000002 ; A’s upper 32 bits
LDR r2, =0x00000001 ; B’s lower 32 bits
LDR r3, =0x00000004 ; B’s upper 32 bits
; Subtract B from A
SUBS r4, r0, r2 ; C[31..0]= A[31..0] - B[31..0], update Carry
SBC r5, r1, r3 ; C[64..32]= A[64..32] - B[64..32] – (1 – Carry)
stop B stop
r1
r0
r3
r2
r5
r4
A
B
C

## Slide 24: Example: 96-bit Subtraction
SUBS r6, r0, r3
SBCS r7, r1, r4
SBC r8, r2, r5

## Slide 25: Example: Short Multiplication and Division
MUL: Signed multiply
MUL r6, r4, r2 ; r6 = LSB32( r4 × r2 )
UMUL: Unsigned multiply
UMUL r6, r4, r2 ; r6 = LSB32( r4 × r2 )
MLA: Multiply with accumulation
MLA r6, r4, r1, r0 ; r6 = LSB32( r4 × r1 ) + r0
MLS: Multiply with subtract
MLS r6, r4, r1, r0 ; r6 = LSB32( r4 × r1 ) - r0
LSB32: Least significant 32 bits

## Slide 26: Example: Long Multiplication
UMULL RdLo, RdHi, Rn, Rm | Unsigned long multiply RdHi,RdLo  unsigned(Rn × Rm)
SMULL RdLo, RdHi, Rn, Rm | Signed long multiply RdHi,RdLo  signed(Rn × Rm)
UMLAL RdLo, RdHi, Rn, Rm | Unsigned multiply with accumulate RdHi,RdLo  unsigned(RdHi,RdLo + Rn × Rm)
SMLAL RdLo, RdHi, Rn, Rm | Signed multiply with accumulate RdHi,RdLo  signed(RdHi,RdLo + Rn × Rm)
UMULL r3, r4, r0, r1 ; r4:r3 = r0  r1, r4 = MSB bits, r3 = LSB bits
SMULL r3, r4, r0, r1 ; r4:r3 = r0  r1
UMLAL r3, r4, r0, r1 ; r4:r3 = r4:r3 + r0  r1
SMLAL r3, r4, r0, r1 ; r4:r3 = r4:r3 + r0  r1
The result has 64 bits, placed in two registers.

## Slide 27: Bitwise Logic
AND {Rd,} Rn, Op2 | Bitwise logic AND Rd  Rn & operand2
ORR {Rd,} Rn, Op2 | Bitwise logic OR Rd  Rn ¦ operand2
EOR {Rd,} Rn, Op2 | Bitwise logic exclusive OR Rd  Rn ^ operand2
ORN {Rd,} Rn, Op2 | Bitwise logic NOT OR Rd  Rn ¦ (NOT operand2)
BIC {Rd,} Rn, Op2 | Bit clear Rd  Rn & NOT operand2
BFC Rd, #lsb, #width | Bit field clear Rd[(width+lsb–1):lsb]  0
BFI Rd, Rn, #lsb, #width | Bit field insert Rd[(width+lsb–1):lsb]  Rn[(width-1):0]
MVN Rd, Op2 | Move NOT, logically negate all bits Rd  0xFFFFFFFF EOR Op2

## Slide 28: Example: AND r2, r0, r1
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
32 bits
r0
r1
r2
Bit-wise Logic AND

## Slide 29: Example: ORR r2, r0, r1
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
32 bits
r0
r1
r2
Bit-wise Logic OR

## Slide 30: Example: BIC r2, r0, r1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
r0
NOT r1
r2
Bit Clear
r2 = r0 & NOT r1
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
r1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
NOT r1
Step 1:
Step 2:

## Slide 31: Example: BFC and BFI
Bit Field Clear (BFC) and Bit Field Insert (BFI).
Syntax
  BFC Rd, #lsb, #width
  BFI Rd, Rn, #lsb, #width
Examples:
  BFC R4, #8, #12
  ; Clear bit 8 to bit 19 (a total of 12 bits) of R4
  BFI R9, R2, #8, #12
  ; Replace bit 8 to bit 19 (12 bits) of R9
  ; with bit 0 to bit 11 from R2.

## Slide 32: Bit Operators (&, |, ~) vs Boolean Operators (&& ,||, !)
The Boolean operators perform word-wide operations, not bitwise.
For example,
  “0x10 & 0x01” = 0x00, but “0x10 && 0x01” = 0x01. (true && true = true, any non-zero value is logical true)
  “~0x01” = 0xFFFFFFFE, but “!0x01” = 0x00. (!true = false)
A && B | Boolean and | A & B | Bitwise and
A¦¦B | Boolean or | A¦B | Bitwise or
!B | Boolean not | ~B | Bitwise not

## Slide 33: Saturating Instruction: SSAT and USAT
Syntax:
  op{cond} Rd, #n, Rm{, shift}
SSAT saturates a signed value to the signed range -2n-1 ≤ x ≤ 2n-1 -1.
USAT saturates a signed value to the unsigned range 0 ≤ x ≤ 2n - 1.
Examples:
  SSAT r2, #11, r1 ; output range: -210  r2  210
  USAT r2, #11, r3 ; output range: 0  r2  211

## Slide 34: Example of Saturation
Without saturation
With saturation
Assume data are limited to 16 bits

## Slide 35: Reverse Order
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF
RBIT Rd, Rn
Rn
Rd
LDR r0, =0x12345678 ; r0 = 0x12345678
RBIT r1, r0 ; Reverse bits, r1 = 0x1E6A2C48
Example:

## Slide 36: Reverse Order
REV Rd, Rn
Rn
Rd
LDR R0, =0x12345678 ; R0 = 0x12345678
REV R1, R0 ; R1 = 0x78563412
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF

## Slide 37: Reverse Order
REV16 Rd, Rn
Rn
Rd
LDR R0, =0x12345678 ; R0 = 0x12345678
REV16 R2, R0 ; R2 = 0x34127856
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF

## Slide 38: Reverse Order
REVSH Rd, Rn
Rn
Rd
LDR R0, =0x33448899 ; R0 = 0x33448899
REVSH R1, R0 ; R0 = 0xFFFF9988
Example:
RBIT Rd, Rn | Reverse bit order in a word for (i = 0; i < 32; i++) Rd[i]  RN[31– i]
REV Rd, Rn | Reverse byte order in a word Rd[31:24]  Rn[7:0], Rd[23:16]  Rn[15:8], Rd[15:8]  Rn[23:16], Rd[7:0]  Rn[31:24]
REV16 Rd, Rn | Reverse byte order in each half-word Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:24]  Rn[23:16], Rd[23:16]  Rn[31:24]
REVSH Rd, Rn | Reverse byte order in bottom half-word and sign extend Rd[15:8]  Rn[7:0], Rd[7:0]  Rn[15:8], Rd[31:16]  Rn[7] & 0xFFFF

## Slide 39: Sign and Zero Extension
int8_t a = -1; // a signed 8-bit integer, a = 0xFF
int16_t b = -2; // a signed 16-bit integer, b = 0xFFFE
int32_t c; // a signed 32-bit integer
c = a; // sign extension required, c = 0xFFFFFFFF
c = b; // sign extension required, c = 0xFFFFFFFE

## Slide 40: Sign and Zero Extension
LDR R0, =0x55AA8765
SXTB R1, R0 ; R1 = 0x00000065
SXTH R1, R0 ; R1 = 0xFFFF8765
UXTB R1, R0 ; R1 = 0x00000065
UXTH R1, R0 ; R1 = 0x00008765
SXTB {Rd,} Rm {,ROR #n} | Sign extend a byte Rd[31:0]  Sign Extend((Rm ROR (8 × n))[7:0])
SXTH {Rd,} Rm {,ROR #n} | Sign extend a half-word Rd[31:0]  Sign Extend((Rm ROR (8 × n))[15:0])
UXTB {Rd,} Rm {,ROR #n} | Zero extend a byte Rd[31:0]  Zero Extend((Rm ROR (8 × n))[7:0])
UXTH {Rd,} Rm {,ROR #n} | Zero extend a half-word Rd[31:0]  Zero Extend((Rm ROR (8 × n))[15:0])

## Slide 41: Move Data between Registers
MOV r4, r5 ; Copy r5 to r4
MVN r4, r5 ; r4 = bitwise logical NOT of r5
MOV r1, r2, LSL #3 ; r1 = r2 << 3
MOV r0, PC ; Copy PC (r15) to r0
MOV r1, SP ; Copy SP (r14) to r1
MOV | Rd  operand2
MVN | Rd  NOT operand2
MRS Rd, spec_reg | Move from special register to general register
MSR spec_reg, Rm | Move from general register to special register

## Slide 42: Move Immediate Number to Register
MOVW r0, #0x4321 ; r0 = 0x00004321
MOVT r0, #0x8765 ; r0 = 0x87654321
MOVW Rd, #imm16 | Move Wide, Rd  #imm16
MOVT Rd, #imm16 | Move Top, Rd  #imm16 << 16
MOV Rd, #const | Move, Rd  const
MOVW will zero the upper halfword
MOVT won’t zero the lower halfword
MOVT r0, #0x8765 ; r0 = 0x8765xxxx
MOVW r0, #0x4321 ; r0 = 0x00004321
Order does matter!
Example: Load a 32-bit number into a register

## Slide 43: Flexible 2nd Source Operand
ADD r0, r1, Operand2
Add r0, r1, r2 ; r0 = r1 + r2
Add r0, r1, #1 ; r0 = r1 + 1
Add r0, r1, r2 LSL #2 ; r0 = r1 + r2 << 2
LSL,LSR,ASR,
ROR,RRX

## Slide 44: Use Shifts To Implement Multiplication And Division
Use Barrel shifter to speed up multiplication and division
  Shifting left 1 bit <=> multiplication by 2
Examples:
  r1 = 9 × r0 = r0 + 8 × r0
  ADD r1, r0, r0, LSL #3 <=> MOV r2, #9 ; r2 = 9
  MUL r1, r0, r2 ; r1 = r0 * 9
ADD r1, r0, r0, LSR #3
; r1 = r0 + r0 >> 3 = r0 + r0/8 (unsigned)
ADD r1, r0, r0, ASR #3
; r1 = r0 + r0 >> 3 = r0 + r0/8 (signed)
MUL instruction takes only registers, not an immediate, so “MUL r1, r0, #9” is invalid syntax
Notes: Since multiplication is a slow operation, we can shift i’s value left two bit positions. r0 + r0 << 3 = r0 + 8 × r0

## Slide 45: Barrel Shifter
Logical Shift Left (LSL)
Arithmetic Shift Right (ASR)
Logical Shift Right (LSR)
Rotate Right (ROR)
Rotate Right Extended (RRX)
Why is there rotate right but no rotate left?
Rotate left can be replaced by a rotate right with a different rotate offset.

## Slide 46: Updating APSR Flags
N | Z | C | V
R<31> | IsZeroBit(R) | carry | unchanged
If “S” is present, the instruction update flags. Otherwise, the flags are not updated.
Let R be the final 32-bit result
LSLS
LSRS
RRXS
ASRS
RORS

## Slide 47: Barrel Shifter: Explanations
LSL (logical shift left): shifts left, fills zeros on the right; C gets the last bit shifted out of bit 31. This is multiply by .
LSR (logical shift right): shifts right, fills zeros on the left; C gets the last bit shifted out of bit 0. This is unsigned division by .
ASR (arithmetic shift right): shifts right, fills the sign bit on the left to preserving the sign; C gets the last bit shifted out of bit 0. This is signed division by with sign extension
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C gets the bit hat was rotated from bit 0 to bit 31. This is a pure rotation without data loss.
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0.
Notes: Useful for multiword shifts and certain crypto/bit-manip patterns
LSR (used here): Always fills with zeros, converting the negative value to a large positive number
ASR: Would preserve the sign bit, maintaining the negative value (-4096)
The carry flag captures the last bit shifted out of the register during shift operations, when the instruction explicitly updates flags (using S suffix like MOVS, LSLS, ASRS)
  LSLS (Logical Shift Left): Carry = the last bit shifted out from the MSB position (bit 31)
  LSRS (Logical Shift Right), ASRS (Arithmetic Shift Right): Carry = the last bit shifted out from the LSB position (bit 0)
  RORS (Rotate Right): Carry = bit that was rotated from bit 0 to bit 31

## Slide 48: Examples (shifting by 4)
Logical Shift Left (LSL)
Logical Shift Right (LSR)
Arithmetic Shift Right (ASR)
Notes: https://www.davespace.co.uk/arm/introduction-to-arm/barrel-shifter.html

## Slide 49: Examples (rotate)
Rotate Right (ROR) (rotate by 4)
Rotate Right Extended (RRX)
(can only rotate by 1)

## Slide 50: Shift Operations
Logical Shift Left (LSL)
LSL {S} Rd, Rn, <shift>
moves all the bits of a register by n positions to the left and inserts n zeros in the right end
0 ≤ n ≤ 31
Example 1
; r2 = 0x0000_0001 (#1)
LSL r3, r2, #3
Example 2
; r2 = 0x0000_0003 (#3)
LSL r3, r2, #2
Example 3
; r3 = 0xFFFF_0000 (#-65536)
LSLS r2, r3, #1
; r3 = 0x0000_0008 (#8)
; 8 =
; r3 = 0x0000_000C (#12)
; 12 =
; r2 = 0xFFFE_0000 (#-131072)
; -131072 =
C=1, N=1, Z=0, V=not updated
Note: If the suffix S is used, the carry flag is updated to the value of the last shifted bit.

## Slide 51: Shift Operations
Logical Shift Right (LSR)
moves all the bits of a register by n positions to the right and inserts n zeros in the left end
1 ≤ n ≤ 32
Example 1
; r2 = 0x0000_0010 (#16)
LSR r1, r2, #3
Example 2
; r2 = 0x8000_0000 (# -2,147,483,648)
LSR r2, r2, #2
Example 3
; r2 = 0x0000_0001 (#1)
LSRS r3, r2, #1
LSR{S} Rd, Rn, <shift>
; r1 =0x0000_0002 (#2)
; 2 =
; r2 = 0x2000_0000 (# 536,870,912)
; 536,870,912 = -2,147,483,648/
with LSR sign bit is lost (if r2 is a signed integer). So do not use logical shifts for signed integers!
; r3 = 0x0000_0000 (#0)
; 0=
C=1, N=0, Z=1, V=not updated
Note: If the suffix S is used, the carry flag is updated to the value of the last shifted bit.

## Slide 52: Shift Operations
moves all the bits of a register by n positions to the right and inserts n copies of the sign bit in the left end
1 ≤ n ≤ 32
Example 1
; r0 = 0xFFF8_0000 (-524288)
ASR r1, r0, #3
Example 2
; r2 = 0x8000_0000 (-2,147,483,648)
ASR r2, r2, #2
Example 3
; r2 = 0xFFFF_F001 (#-4095)
ASRS r3, r2, #1
Arithmetic Shift Right (ASR)
ASR{S} Rd, Rn, <shift>
; r1 = 0xFFFF_0000 (-65536)
; -65536=
; r2 = 0xE000_0000 (# -536,870,912)
; -536,870,912= -2,147,483,648/
ASR is equivalent to signed integer division
; r3 = 0xFFFF_F800 (#-2048)
; -2048 =
C=1, N=1, Z=0, V=not updated
Note: If the suffix S is used, the carry flag is updated to the value of the last shifted bit.

## Slide 53: Rotate Operations
Circular shifts of all the bits of a register by n positions to the right as if the right end of the register is joined with its left end. The last shifted bit updates the carry bit
1 ≤ n ≤ 31
Example 1
; r2 = 0x0008_0000
ROR r2, r2, #10
Example 2: rotate left by 12 bits
; r0 = 0xF000_0000
ROR r2, r0, #20
Example 3
;r2 = 0xF0F0_F001 (binary: 1111 0000 1111 0000 1111 0000 0000 0001)
;r1 = 0x0000_000E (rotate right by 14 bits)
RORS r3, r2, r1
Rotate left by m bits is equivalent to rotate right ROR by 32-m bits
Rotate Right (ROR)
ROR{S} Rd, Rn, <shift>
; r2 = 0x0000_0200
; r2 = 0x0000_0F00
; r3 = 0xC007_C3C3 (binary: 1100 0000 0000 0111 1100 0011 1100 0011)
C=1, N=1, Z=0, V=not updated
Note: If the suffix S is used, the carry flag is updated to the value of the last shifted bit.

## Slide 54: Rotate Operations
RRX{S} Rd, Rn
This is a one-bit rotate instruction.
Example 1
; r2 = 0x0008_0003, c = 1
RRX r2, r2
Example 2:
; r2 = 0xF000_0001, c = 0
RRX r1, r2
Example 3
; r2 = 0xF0F0_F001, c = 0
RRXS r3,r2
Rotate Right Extended (RRX)
; r2 = 0x8004_0001, c = 1
; r1 = 0x7800_0000, c = 1
; r3 = 0x7878_7800, c = 1
C=1, N=0, Z=0, V= not updated
Note: the carry flag is updated by b0 only if the suffix S is used, otherwise it keeps its original value

## Slide 55: Barrel Shifter More Examples
MOV r0, r0, LSL #1
  r0 = r0 * 2
MOV r1, r1, LSR #2
  r1 = r1 / 4 (unsigned).
MOV r2, r2, ASR #2
  r2 = r2 / 4 (signed).
MOV r3, r3, ROR #16
  Swap the top and bottom halves of r3.
ADD r4, r4, r4, LSL #4
  r4 = r4 * 17 (= r4 + r4 * 16)
RSB r5, r5, r5, LSL #5
  r5 = r5 * 31 (= r5 * 32 – r5)
  Reverse-subtract using barrel shifter on 2nd operand
SUB r5, r5, r5, LSR #5
  r5 = r5 – (r5 / 32)
LDR r9, [r12, r8, LSL #2]
  Load a 32‑bit word into r9 from the memory address computed as r12 + (r8 * 4)
Notes: Subtract using barrel shifter on 2nd operand, giving r5 − (r5 >> n)
RSB r5, r5, r5, LSL #5 computes a reverse-subtract using the barrel shifter on the second operand, giving r5 = (r5 << 5) − r5.
RSB is “Reverse SuBtract”: result = Operand2 − Rn, not Rn − Operand2.
Here, Rn is r5, and Operand2 is r5 logically shifted left by 5 bits.
Thus Operand2 = r5 × 2^5 = 32·r5, so the operation is r5 = 32·r5 − r5 = 31·r5.
No flags are updated because there is no S suffix.
Intuition and uses
It’s a strength-reduction trick: multiply by 31 using one instruction by combining a shift and a subtract in the ALU’s flexible operand path.
Equivalent sequences:
  SUB r5, r5, r5, LSR #? is different; SUB would compute r5 − (r5 >> n).
  RSB r5, r5, r5, LSL #k generally yields r5 = (2^k − 1)·r5. For k=5, multiplier is 31.
https://developer.arm.com/documentation/ddi0597/latest/Base-Instructions/RSB--RSBS--register---Reverse-Subtract--register--
https://developer.arm.com/documentation/dui0231/latest/arm-instruction-reference/arm-general-data-processing-instructions/add--sub--rsb--adc--sbc--and-rsc
https://stackoverflow.com/questions/42042832/what-does-this-rsb-instruction-do-with-an-extra-lsl-1-operand
https://www.csie.ntu.edu.tw/~cyy/courses/assembly/12fall/lectures/handouts/lec09_ARMisa.pdf
https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf
https://web.cs.umass.edu/~weems/homepage/335-Notes/ewExternalFiles/Lecture%2015.pdf
https://cseweb.ucsd.edu/classes/wi14/cse30-c/lectures/PI_WI_14_CSE30_lecture_8_post.pdf
https://keleshev.com/compiling-to-assembly-from-scratch/07-arm-assembly-programming
https://salmanarif.bitbucket.io/visual/supported_instructions.html

## Slide 56: SUB vs. RSB
SUB instruction: SUB Rd, Rn, Operand2 performs Rd = Rn - Operand2
RSB instruction: RSB Rd, Rn, Operand2 performs Rd = Operand2 – Rn
There are equivalent:
  SUB R5, R3, #10 @ R5 = R3 - 10
  RSB R5, R3, #10 @ R5 = 10 - R3
When to use RSB?
Subtracting from constants, since constants can only appear as Operand2 in ARM instructions. For example:
  RSB R2, R4, #1 means R2 = 1 - R4
  This cannot be done with SUB without first loading the constant into a register
Negation Operations by subtracting from zero:
  RSB R0, R0, #0 effectively computes R0 = 0 - R0 = -R0
Complex Operand2 Operations
  RSB is valuable when you want to perform operations on Operand2 before subtraction, such as shifting :
  RSB R1, R2, R3, LSL #1 computes R1 = (R3 << 1) - R2
  This allows you to shift a value and then subtract from it in a single instruction
Notes: The fundamental difference is that RSB reverses the order of the operands in the subtraction operation.
@ Negation
RSB R0, R0, #0 @ R0 = -R0
@ Subtract from constant
RSB R2, R4, #100 @ R2 = 100 - R4
@ Shift and subtract
RSB R1, R2, R3, LSL #2 @ R1 = (R3 << 2) - R2
@ Compare with SUB equivalent
SUB R5, R3, #10 @ R5 = R3 - 10
RSB R5, R3, #10 @ R5 = 10 - R3

## Slide 57: Integer Array Access with LSL
To calculate the address of element array[i] of 32-bit integers, we calculate (base address of array) + i*4 for an array of words. For example:
  ADR r3, ARRAY @ load base address of ARRAY into r3 (ARRAY contains 4-byte ints)
  MOV r2, #6 @ Suppose we want to access ARRAY[6]
  MOV r4, r2, LSL #2 @ logical shift i’s value in r2 by 2 to multiply its value by 4
  ADD r5, r3, r4 @ finish calculation of the address of element array[i] in r5
  LDR r6, [r5] @ load value of array[i] into r6 using the address in r5
Alternatively, we can perform this same address calculation with a single ADD:
  ADD r5, r3, r2, LSL #2 @ calculate address of array[i] in r5 with single ADD
  LDR r6, [r5] @ load value of array[i] into r4 using the address in r5
Alternatively, ARM has some nice addressing modes to speedup array item access:
  LDR r6, [r3, r2, LSL #2]

## Slide 58: Example 1: ANDS
Updates carry flag,
since ANDS does not update carry flag
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ANDS r2, r1, r0, LSL #1
N = 0, Z = 1, C = 1, V = not updated
AND{S}<c><q> {<Rd>,} <Rn>, <Rm> {,<shift>}
r0 = 0xFFFFFF00
r1 = 0x00000001
r0, LSL #1 = 0xFFFFFE00
r2 = r1 AND (r0 << 1) = 0x00000001 AND 0xFFFFFE00 = 0x00000000
ANDS sets flags:
Z = 1 (result r2 is zero)
N = 0 (bit 31 of result r2 is 0)
C is unaffected by ANDS, since logical operations don't affect overflow. It was set by previous shift “r0, LSL #1” to be C=1
V is unaffected by either ANDS or shift (left unchanged from its previous value)
Note: LSL updates the C flag when it is used within the ANDS instruction. This is not a valid instruction: “ANDS r2, r1, r0, LSLS #1”, since LSL forms part of the second operand - it’s not a standalone instruction.
Notes: , logical operations don't affect overflow

## Slide 59: Example 2: ADDS
Does NOT update carry flag,
since ADDS updates flags
LDR r0, =0xFFFFFF00
LDR r1, =0x00000001
ADDS r2, r1, r0, LSL #1
N = 1, Z = 0, C = 0, V = 0
ADD{S}<c><q> {<Rd>,} <Rn>, <Rm> {,<shift>}
r0 = 0xFFFFFF00
r1 = 0x00000001
r0, LSL #1 = 0xFFFFFE00
r2 = r1 + (r0 << 1) = 0x00000001 + 0xFFFFFE00 = 0xFFFFFE01
ADDS sets flags:
Z = 0 (result r2 is non-zero)
N = 1 (bit 31 of result r2 is 1)
C = 0 (there is no carry out from bit 31 for unsigned addition, when adding 0x00000001 and 0xFFFFFE00)
V = 0 (there is no overflow for signed addition, when adding 0x00000001 and 0xFFFFFE00. Recall: adding a positive (1) to a negative (0xFFFFFE00) cannot cause overflow.)
Note: LSL updates the C flag when it is used within the ADDS instruction. However, its update of the C flag is overwritten by ANDS, or equivalently, we say that LSL does not update the C flag.

## Slide 60: Set a Bit in C
a |= (1 << k)
a = a | (1 << k)
or
a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
a7 | a6 | 1 | a4 | a3 | a2 | a1 | a0
Example: k = 5
a
1 << k
a | (1 << k)
The other bits should not be affected.

## Slide 61: Set a Bit in Assembly
a |= (1 << 5)
Solution 2:
MOV r4, #1 ; r4 = 1
ORR r0, r0, r4, LSL #5 ; r0 = r0 & not (1<<5)
Solution 1:
MOV r4, #1 ; r4 = 1
LSL r4, r4, #5 ; r4 = 1<<5
ORR r0, r0, r4 ; r0 = r0 | 1<<5
Solution 3:
ORR r0, r0, # (1 << 5) ; r0 = r0 & not (1<<5)

## Slide 62: Clear a Bit in C
a &= ~(1<<k)
a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
a7 | a6 | 0 | a4 | a3 | a2 | a1 | a0
Example: k = 5
a
~(1 << k)
a & ~(1<<k)
The other bits should not be affected.

## Slide 63: Clear a Bit in Assembly
a &= ~(1<<5)
Solution 2:
MOV r4, #1 ; r4 = 1
MVN r4, r4, LSL #5 ; r4 = not (1<<5)
AND r0, r0, r4 ; r0 = r0 & not (1<<5)
Solution 3:
MOV r4, #1 ; r4 = 1
BIC r0, r0, r4, LSL #5 ; r0 = r0 & not (1<<5)
Solution 1:
MOV r4, #1 ; r4 = 1
LSL r4, r4, #5 ; r4 = 1<<5
MVN r4, r4 ; r4 = not (1<<5)
AND r0, r0, r4 ; r0 = r0 & not (1<<5)
Solution 4:
BIC r0, r0, # (1 << 5) ; r0 = r0 & not (1<<5)
Notes: Here we can remove the S suffix for all instructions, unless the flags are used by later instructions.

## Slide 64: Toggle a Bit in C
a ^= 1<<k
a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
a7 | a6 | NOT(a5) | A4 | a3 | a2 | a1 | a0
Example: k = 5
a
1 << k
a ^ (1<<k)
Without knowing the initial value, a bit can be toggled by XORing it with a “1”
Truth table of Exclusive OR
m | n | m⊕n
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: A bit can be ‘toggled’ (changed) – without knowing its initial value – by XORing it with a “1”.

## Slide 65: Toggle a Bit in Assembly
a ^= 1<<5
Solution:
MOV r4, #1 ; r4 = 1
EOR r0, r0, r4, LSL #5 ; r0 = r0 ^ 1<<5
Here we can use MOVS and EORS instead of MOV and EOR, if the flags are used by later instructions.
Notes: A bit can be ‘toggled’ (changed) – without knowing its initial value – by XORing it with a “1”.

## Slide 66: Mask
Bits 8-11 and bits 16-23 are masked.
All the rest bits are unmasked

## Slide 67: Clear all unmasked bits
Data &= Mask;

## Slide 68: Clear all masked bits
Data &= ~Mask;

## Slide 69: Set all masked bits
Data |= Mask;

## Slide 70: Toggle all tasked bits
Data ^= Mask;

## Slide 71: Carry and Overflow Flags w/ Arithmetic Instructions
71
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs; Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0
Tip: Convert subtraction to addition with Two’s complement.
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 Borrow flag=0 (Result incorrect) | true result < 0  Carry flag=0 Borrow flag=1 (Result incorrect) | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1 Overflow flag=1 (Result incorrect)
Notes: Convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0.”
convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; for all other cases, V = 0
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. ) or smaller than the minimum signed integer (i.e. ) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. 2^(𝑛−1)−1) or smaller than the minimum signed integer (i.e. 〖−2〗^(𝑛−1)) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 72: Example
0 | 1 | 1 | 0 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
Carry
Op1: 0x35
Op2: 0x19
Result: 0x4E
C = 0
V = 0
For an 8-bit system, calculate 0x35 + 0x19, setting C and V flags
ANS:
  Convert to binary and perform addition as in table
  C = 0 since there is no carry-out from MSB b7
  V = 0 since Op1, Op2 and result are all positive (sign bit = 0)
  In decimal (not needed for exam):
    Unsigned addition: 53 + 25 = 78 (result correct)
    Signed addition: 53 + 25 = 78 (result correct)

## Slide 73: Example
1 | 1 | 1 | 1 | 1 | 1 | 1 | 
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Carry
Op1: 0x35
Op2: 0x5B
Result: 0x90
C = 0
V = 1
For an 8-bit system, calculate 0x35 + 0x5B, setting C and V flags
ANS:
  Convert to binary and perform addition as in table
  C = 0 since there is no carry-out from MSB b7
  V = 1 since Op1, Op2 are positive, result is negative
  In decimal:
    Unsigned addition: 53 + 91 = 144 (result correct)
    Signed addition: true sum = 53 + 91 = 144 → result = -112 (result incorrect, V=1)

## Slide 74: Example
1 | 1 | 1 | 0 | 1 | 1 | 1 | 
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Carry
Op1: 0x35
Op2: 0xD3
Result: 0x08 (drop 1 in 0x108)
C = 1
V = 0
For an 8-bit system, calculate 0x35 - 0x2D, setting C and V flags
ANS:
  Convert to binary and perform addition as in table (another way is to perform subtraction in binary, but we do not cover it here)
    0x2D = 00101101, its negation TC(00101101) = 11010011 = 0xD3
  C = 1 since there is carry-out from MSB b7
  V = 0 since Op1 is positive, Op2 is negative, result is negative
    Overflow cannot occur when adding 2 operands with different signs
  In decimal:
    Unsigned subtraction: 53 – 45 = 8 (result correct, C=1, Borrow Flag=0)
    Signed: 53 - 45 = 8 (result correct)

## Slide 75: Example
0 | 0 | 1 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 0 | 1
Carry
Op1: 0x9E
Op2: 0xD3
Result: 0x71 (drop 1 in 0x171)
C = 1
V = 1
For an 8-bit system, calculate 0x9E - 0x2D, setting C and V flags
ANS:
  Convert to binary and perform addition as in table
    0x2D = 00101101, its negation TC(00101101) = 11010011 = 0xD3
  C = 1 since there is carry-out from MSB b7
  V = 1 since Op1, Op2 are both negative, result is positive
  In decimal:
    Unsigned subtraction: 158 − 45 = 113 (result correct, C=1, Borrow Flag=0)
    Signed subtraction: true sum = −98 − 45 = −143 → result = +113 (wrong, V=1)
Notes: 01110001 in decimal0x62 = 01100010, its negation TC(01100010) = 10011110 = 0x9E

## Slide 77: ARM Immediate Values
You can’t fit an arbitrary 32-bit value into a 32-bit instruction word. ARM data processing instructions have 12 bits of space for values in their instruction word. This is arranged as a 4 rotate value and an 8 immediate value. The real immediate = ROR(immediate8, rotate4 × 2).
  The 4-bit rotate value stored in bits 11-8 is multiplied by two giving a range of 0-30 in steps of two.
Using this scheme we can express immediate constants such as:
  0x000000FF
  0x00000FF0
  0xFF000000
  0xF000000F
But these immediate constants are not possible:
  0x000001FE
  0xF000F000
  0x55550000
  0xFFFFFFFF
An assembler will convert big values to the rotated form. Impossible values will cause an error. For example, this instruction is invalid:
  AND R2, R0, #0xFFFFFF8F
Notes: https://www.davespace.co.uk/arm/introduction-to-arm/immediates.html

## Slide 78: Encoding #4080 as Immediate
ADD r1, r2, #4080
  4080 = 1111111110000 in binary
The encoding is:
  immediate8 = 0x000000FF (11111111 in binary)
  rotate4 = 1110 (14*2 = 28)
ROR(0x000000FF, 28) = 0x00000FF0 (4080 in decimal)
  rotate left by 4 = rotate right by 28
Notes: indicates a literal, in this case the immediate value for the instruction
add 4080 to r2 and put the result in r1
▸ but only if if the CPSR flags show Z=1

## Slide 79: Loading Wide Values
You can form constants wider than those available in a single instruction by using a sequence of instructions to build up the constant. For example:
  MOV r2, #0x55 ; R2 = 0x00000055
  ORR r2, r2, r2, LSL #8 ; R2 = 0x00005555
  ORR r2, r2, r2, LSL #16 ; R2 = 0x55555555
Or load the value from memory with pseudo-instruction LDR Rx,=const
  LDR r2, =0x55555555
Or use MVN instead of MOV:
  The invalid instruction MOV r0,#0xFFFFFFFF can be implemented as MVN r0,#0
Notes: https://www.davespace.co.uk/arm/introduction-to-arm/immediates.html

## Slide 80: References
Lesson 45b - Adders Carry and Overflow, LBEbooks
  https://www.youtube.com/watch?v=9cXe_T99nL4
Lecture 25. Arithmetic and Logical Instructions
  https://www.youtube.com/watch?v=H-vOP2yRUj4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=25
Lecture 26. Updating NZCV bit flags
  https://www.youtube.com/watch?v=SGJibM1D2_A&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=26