## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 10
Preserve Environment via Stack
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/
Notes: Embedded application binary interface (EABI) Protocol

## Slide 2: Overview
How to call a subroutine?
How to return the control back to the caller?
How to pass arguments into a subroutine?
How to return a value in a subroutine?
How to preserve the running environment for the caller?

## Slide 3: Stack
A Last-In-First-Out memory model
Only allow to access the most recently added item
  Also called the top of the stack
Key operations:
  push (add item to stack)
  pop (remove top item from stack)
Example: Tower of Hanoi
  Only one disk may be moved at a time.
  Each move consists of taking the upper disk from one of the rods and sliding it onto another rod, on top of the other disks that may already be present on that rod.
  No disk may be placed on top of a smaller disk.
http://en.wikipedia.org/wiki/File:Tower_of_Hanoi_4.gif

## Slide 4: Typical Usage of Stack
Why need stack?
  Saving the original contents of processor’s registers at the beginning a subroutine (Contents are restored at the end of a subroutine)
  Storing local variables in a subroutine
  Passing extra arguments to a subroutine
  Saving processor’s registers upon an interrupt

## Slide 5: Stack Growth Convention: Ascending vs Descending
  Descending stack: Stack grows towards low memory address
  Ascending stack: Stack grows towards high memory address

## Slide 6: Stack Growth Convention: Full vs Empty
  Full stack: SP points to the last item pushed onto the stack
  Empty stack: SP points to the next free space on the stack

## Slide 7: Cortex-M Stack
Cortex-M uses full descending stack
Example:
PUSH/POP {r0,r6,r3}
Stack pointer (SP, aka R13)
  decremented on PUSH
    SP = SP – 4 * # of registers
  incremented on POP
    SP = SP + 4 * # of registers
  SP starts at 0x20000200 for STM32-Discovery by default (can be changed in startup.s)

## Slide 8: Addressing Modes for Load/Store Multiple Registers
STMxx rn{!}, {register_list}
LDMxx rn{!}, {register_list}
xx = IA, IB, DA, or DB
Addressing Modes | Description | Instructions
IA | Increment After | STMIA, LDMIA
IB | Increment Before | STMIB, LDMIB
DA | Decrement After | STMDA, LDMDA
DB | Decrement Before | STMDB, LDMDB
IA: address is incremented by 4 after a word is loaded or stored.
IB: address is incremented by 4 before a word is loaded or stored.
DA: address is decremented by 4 after a word is loaded or stored.
DB: address is decremented by 4 before a word is loaded or stored.
Review

## Slide 9: Load/Store Multiple Registers
The following are synonyms.
  STM = STMIA (Increment After) = STMEA (Empty Ascending)
  LDM = LDMIA (Increment After) = LDMFD (Full Descending)
The order in which registers are listed does not matter
  For STM/LDM, the lowest-numbered register is stored/loaded at the lowest memory address.
Review

## Slide 10: Store Multiple Registers
Review

## Slide 11: Load Multiple Registers
Review

## Slide 12: Full Descending Stack

## Slide 13: Stack Implementation
Stock Name | Push |  | Pop | 
 | Equivalent | Alternative | Equivalent | Alternative
Full Descending(FD) | STMFD SP!,list | STMDB SP!,list | LDMFD SP!,list | LDMIA SP!,list
Empty Descending(ED) | STMED SP!,list | STMDA SP!,list | LDMED SP!,list | LDMIB SP!,list
Full Ascending(FA) | STMFA SP!,list | STMIB SP!,list | LDMFA SP!,list | LDMDA SP!,list
Empty Ascending(EA) | STMEA SP!,list | STMIA SP!,list | LDMEA SP!,list | LDMDB SP!,list
Notes: Assembler aliases: STMFD = STMDB, LDMFD = LDMIA; STMEA = STMIA; LDMEA = LDMDB,

## Slide 14: Stack
PUSH {Rd} == STMDB SP!, {Rd} == STMFD SP!, {Rd}
  SUB SP, SP, #4 @ SP = SP-4 (descending stack)
  STR Rd, [SP] @ (*SP) = Rd (full stack)
Push multiple registers
PUSH {r1, r2, r3, r7}
They are equivalent.
PUSH {r7}
PUSH {r3}
PUSH {r2}
PUSH {r1}
PUSH {r7, r2, r3, r1}
SP is decremented before PUSH (pre-decrement).
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.
Notes: PUSH => SUB SP, SP, #4 STR RN, [SP]
POP => LDR RN, [SP] ADD SP, #4
PUSH {R1, R2} ==
STMFD SP!, {R1, R2} ; or STMDB SP!, {R1, R2}
SP is decremented before PUSH (pre-decrement), and incremented after POP (post-increment).

## Slide 15: Stack
POP {Rd} == LDMIA SP!, {Rd} == LDMFD SP!, {Rd}
  LDR Rd, [SP] @ Rd = (*SP) (full stack)
  ADD SP, #4 @ SP = SP + 4 (Stack shrinks)
Pop multiple registers
POP {r7, r3, r2, r1}
They are equivalent.
POP {r1}
POP {r2}
POP {r3}
POP {r7}
POP {r1, r2, r3, r7}
SP is incremented after POP (post-increment).
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.

## Slide 16: Stack Recap
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}
Pop to the smallest-numbered register first.
Largest-numbered register is pushed first but popped last.

## Slide 17: Cortex-M Stack
PUSH {register list}
POP {register list}
  Eligible registers for PUSH: r0 – r12, LR
  Eligible registers for POP: r0 – r12, LR, PC
  Order specified in the list does not matter
    Largest-numbered register is always pushed first and popped last
    Lowest-numbered register stored at lowest memory address
r0 | 
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Register
Instruction format for PUSH:

## Slide 18: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx

## Slide 19: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
xxxxxxxx

## Slide 20: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 21: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 22: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x11111111
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 23: Quiz
Are the values of R1 and R2 swapped?
PUSH {R1, R2}; POP {R2, R1}
Or
PUSH {R1, R2}; POP {R2}; POP {R1}
Or
PUSH {R1}; PUSH {R2}; POP {R1, R2}

## Slide 24: Quiz ANS
Are the values of R1 and R2 swapped?
PUSH {R1, R2}; POP {R2, R1}
Or
PUSH {R1, R2}; POP {R2}; POP {R1}
Or
PUSH {R1}; PUSH {R2}; POP {R1, R2}
PUSH {R1, R2}; POP {R2, R1}
  is equivalent to
  PUSH {R2}; PUSH {R1}; POP{R1}; POP{R2}
  Values of R1 and R2 are unchanged
PUSH {R1, R2}; POP {R2}; POP {R1}
  is equivalent to
  PUSH {R2}; PUSH {R1}; POP{R2}; POP{R1}
  Values of R1 and R2 are swapped
PUSH {R1}; PUSH {R2}; POP {R1, R2}
  is equivalent to
  PUSH {R1}; PUSH {R2}; POP{R1}; POP{R2}
  Values of R1 and R2 are swapped

## Slide 25: Subroutine
A subroutines, also called a function or a procedure,
  single-entry, single-exit
  Return to caller after it exits
When a subroutine is called, the Link Register (LR) holds the return address of the current subroutine call, i.e., memory address of the next instruction to be executed after the subroutine exits.
Notes: Link Register (LR) holds the return address of the current subroutine call.

## Slide 26: Calling a Subroutine
Caller Program | Subroutine/Callee | 
... BL foo ... | foo PROC ... BX LR EDP | foo PROC PUSH {LR} ... POP {PC} ; pops LR into PC (returns) EDP
Caller: BL label (Branch and Link)
Step 1: LR = PC + 4
Step 2: PC = label
  label is name of subroutine
  Compiler translates label to memory address
  After call, LR holds return address (the instruction following the call)
Callee: BX LR (Branch and Exchange) at end of procedure
PC = LR
  Return to caller by setting PC to LR
Equivalently:
  PUSH {LR} at start of procedure
  POP {PC} at end of procedure

## Slide 27: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | YES | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes/No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 28: Caller-saved Registers vs Callee-saved Registers
Not saved by subroutine
Hold arguments/result
Caller expects their values are retained
Callee must save and store it if callee modifies it
Register Bank
Special Registers
Caller-saved registers
Callee-saved registers
Callee-saved registers

## Slide 29: Embedded Application Binary Interface (EABI) Protocol
Role | Must Preserve | Notes
Caller | R0–R3, R12, CPSR (if needed) | Caller-saved (scratch)
Callee | R4–R11, R13 (SP), R14 (LR) | Must be saved/restored if modified
Return | R0 | Return value
Caller-saved registers:
  R0–R3: Arguments/return registers.
  R12 (IP): Intra-procedure scratch register.
  CPSR: — caller must preserve its state if needed.
Callee-saved registers:
  R4–R11: Must be saved/restored by the callee if used.
  R14 (LR): Must be saved if the callee makes nested calls.
  R13 (SP): Stack pointer — must be preserved.
Extra parameters passed on stack:
  When more than four arguments exist.
Return value in R0
Notes: Caller should save these registers if callers needs to re-use their original values:

## Slide 30
Embedded application binary interface (EABI) Protocol

## Slide 31
Top code:
  Callee foo does MOV R4, #10 → this overwrites whatever the caller had in R4.
  foo does BX LR → returns to caller, and R4 remains 10 in the caller.
Middle code:
  Caller expects callee does not modify r4.
  Callee should preserve r4 by saving and restores R4 by PUSH and POP on the stack
Bottom code:
  Callee saves and restores R4 by PUSH and POP
  Callee uses PUSH{LR} and POP{PC}, equivalent to BX LR
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 11 | foo PROC ... MOV r4, #10 ; foo changes r4 ... BX LR EDP
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101 | foo PROC PUSH {R4} ; save caller's R4 MOV R4, #10 POP {R4} ; restore caller's R4 BX LR EDP
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101 | foo PROC PUSH {R4, LR} MOV R4, #10 POP {R4, PC} ; pops LR into PC (returns) EDP

## Slide 32: Nested Subroutines: What is wrong?
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4} ... MOV r4, #10 ... BL bar ... POP {r4} BX LR ENDP | bar PROC ... BX LR ENDP
Caller does BL foo → LR = return address back into the caller.
foo does PUSH {r4} (saves r4) but does not save LR.
foo does BL bar → this instruction overwrites LR with the return address back into foo (i.e. the instruction after BL bar).
bar returns (BX LR) into foo (normal), but the original LR that pointed back to the caller was lost.
foo does POP {r4} then BX LR — but LR now points to the instruction inside foo (not to the caller), so foo does not return to the caller

## Slide 33: Nested Subroutines: Solution #1
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4, LR} ... MOV r4, #10 ... BL bar ... POP {r4, LR} BX LR ENDP | bar PROC ... BX LR ENDP
foo saves and restores its LR for returning to its caller, before calling bar.

## Slide 34: Nested Subroutines: Solution #1

## Slide 35: Nested Subroutines: Solution #2
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4, LR} ... MOV r4, #10 ... BL bar ... POP {r4, PC} BX LR ENDP | bar PROC ... BX LR ENDP
POP {r4, PC} is equivalent to POP {r4, LR} followed by BX LR.

## Slide 36: Subroutine Calling Another Subroutine
MAIN
MOV R0,#2
BL QUAD
ENDL ...
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
SQ MUL R0,R0
BX LR
Function MAIN
Function QUAD
Function SQ

## Slide 37: Subroutine Calling Another Subroutine
MAIN PROC
MOV R0,#2
BL QUAD
ENDL ...
ENDP
QUAD PROC
PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
EDP
SQ PROC
MUL R0,R0
BX LR
EDP
Function MAIN
Function QUAD
Function SQ

## Slide 38: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
R0
PC
0x08000138
LR
SP
0x20000200
SQ
QUAD

## Slide 39: Example: R0 = R04
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800013C
LR
SP
0x20000200
SQ
QUAD
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 40: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800014C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Preserve
Link Register (LR)
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 41: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x08000140
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000150
LR
SP
0x200001FC
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 42: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 43: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 44: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000154
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 45: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 46: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 47: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000158
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 48: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x0800015C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Restore
Link Register (LR)
0x08000140
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 49: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000140
LR
SP
0x20000200
0x08000140
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 50: Stack Pointer (SP)
SP is the shadow of MSP (Main SP) or PSP (Process SP)
If there is no embedded OS, PSP is not used
Determined by the ASP (Active SP) bit in the CONTROL register (ASP is always 0 in handler mode).
  0 = MSP (default)
  1 = PSP
Before using the stack, software has to define stack space and initialize the stack pointer (SP).
The program startup.s defines stack space and initializes SP.
Register Bank
Special Registers
Bit 31 - 3 | 2 | 1 | 0
Reserved |  | ASP | 
CONTROL Register |  |  | 

## Slide 51: Passing Arguments into a Subroutine
Review

## Slide 52: Passing Arguments into a Subroutine
a16
b16
c8
d32
Subroutine
Register R0
Register R1
Register R2
Register R3
Return Value
Register R0
int32_t sum(int16_t a16, int16_t b16, int8_t c8, int32_t d32);
Review

## Slide 53: Passing 4 Arguments
Caller
s = sum(1, 2, 3, 4);
MOVS r0, #1 ; a16
MOVS r1, #2 ; b16
MOVS r2, #3 ; c8
MOVS r3, #4 ; d32
BL sum
Callee
sum PROC
ADD r0, r0, r1 ; a16 + b16
ADD r0, r0, r2 ; add c8
ADD r0, r0, r3 ; add d32
BX LR ; return
ENDP
int32_t sum(int16_t a16, int16_t b16, int8_t c8, int32_t d32);
Review

## Slide 54: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d, int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Caller
MOVS r0, #5
MOVS r1, #6
MOVS r2, #7
MOVS r3, #8
PUSH {r0, r1, r2, r3}
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum
...
POP {r0, r1, r2, r3}
Version 1
sum PROC
EXPORT sum
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r1,r2, [sp] ; r1=mem[sp],r2=mem[sp+4]
ADD r0, r0, r1 ; add h
ADD r0, r0, r2 ; add i
LDRD r1,r2, [sp, #8] ; r1=mem[sp+8],r2=mem[sp+12]
ADD r0, r0, r1 ; add j
ADD r0, r0, r2 ; add k
BX LR
ENDP
sum PROC
EXPORT sum
PUSH {r5, r6, lr}
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r5,r6, [sp, #12] ;r5=mem[sp+12],r6=mem[sp+16]
ADD r0, r0, r5 ; add h
ADD r0, r0, r6 ; add i
LDRD r5,r6, [sp, #20] ;r5=mem[sp+20],r6=mem[sp+24]
ADD r0, r0, r5 ; add j
ADD r0, r0, r6 ; add k
POP {r5, r6, pc}
ENDP
Version 2

## Slide 55: Explanations
Version 1:
Callee reads the extra args directly from the caller’s push with LDRD: Load Register Doubleword:
  LDRD r1,r2, [sp] → loads 5th & 6th args (h, i)
  LDRD r1,r2, [sp,#8] → loads 7th & 8th args (j, k)
It returns with BX LR.
Version 2:
Callee pushes r5, r6, and lr on entry: PUSH {r5, r6, lr}.
Because it pushed, the extra-argument addresses are shifted, so it uses offsets like [sp,#12] and [sp,#20] to read the caller’s arguments into r5,r6.
  LDRD r5,r6, [sp, #12]
  LDRD r5,r6, [sp, #20]
It returns via POP {r5, r6, pc} (popping lr into pc returns directly).
Ladder analogy:
  Think of the stack like a ladder: The ladder = one shared stack in memory.
  The rung each function stands on = its current SP value.
  When a function “pushes,” it steps down a few rungs (SP decreases).
  The caller’s pushed data remains up above — just higher up the same ladder.
Address | Contents | Access
0x0FFC | arg8 (k=8) | [sp,#12]
0x0FF8 | arg7 (j=7) | [sp,#8]
0x0FF4 | arg6 (i=6) | [sp,#4]
0x0FF0 | arg5 (h=5) | [sp] ← SP
Address | Contents | Access
0x0FFC | arg8 (k=8) | [sp,#24]
0x0FF8 | arg7 (j=7) | [sp,#20]
0x0FF4 | arg6 (i=6) | [sp,#16]
0x0FF0 | arg5 (h=5) | [sp,#12]
0x0FEC | saved lr | [sp,#8]
0x0FE8 | saved r6 | [sp,#4]
0x0FE4 | saved r5 | [sp] ← SP
Version 1 stack after Caller PUSH
Version 2 stack after Caller PUSH and Callee PUSH
Notes: Callee does no PUSH on entry.
Returns with BX LR (it never changed LR).

## Slide 56: Version 2 is Better Programming Practice
Caller pushes extra arguments (5th to 8th) onto the stack before calling the function.
Version 1: Callee accesses those extra arguments directly from the stack using LDRD instructions at specific offsets from SP. It demonstrates the basic mechanism for handling extra arguments on the stack.
Version 2: Callee begins by pushing registers r5, r6, and the link register (LR) onto the stack to preserve them. After addition operations, it pops r5, r6, and the program counter (PC) to return, restoring the preserved registers and the return address. This ensures that the subroutine does not unintentionally overwrite or lose the caller's data and return address, maintaining program correctness during and after the function call.
Notes: 8 arguments are passed: Registers r0-r3 hold the first 4 arguments (a, b, c, d with values 1, 2, 3, 4). The last 4 arguments (h, i, j, k with values 5, 6, 7, 8) are pushed onto the stack by the caller before calling the function.
In callee (subroutine) code, the subroutine saves registers r5, r6, and the link register LR via push at the start. It adds the first 4 arguments from registers r0-r3. It then loads the extra arguments from specific stack offsets with LDRD instructions (load register double), adding these to the result. The subroutine ends by popping saved registers r5, r6 and PC (program counter) to return.

## Slide 57: Summary
ARM Cortex-M uses full descending stack
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
What registers should be preserved?
  Caller-saved registers vs callee-saved registers
How to preserve the running environment for the caller?
  Via stack

## Slide 58: References
Lecture 31. Preserving registers in a Subroutine
  https://www.youtube.com/watch?v=DGKjFKjxAYs&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=31