## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Flow Control in Assembly
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Three Control Structures
Sequence Structure
  Computer executes statements (instructions), one after another, in the order listed in the program
Selection Structure
  If-then-else
Loop Structure
  while loop
  for loop
Sequence Structure
Selection Structure
Loop Structure

## Slide 3: Condition Flags
Negative bit
  N = 1 if most significant bit of result is 1
Zero bit
  Z = 1 if all bits of result are 0
Carry bit
  For unsigned addition, C = 1 if carry takes place
  For unsigned subtraction, C = 0 (carry = not borrow) if borrow takes place
  For shift/rotation, C = last bit shifted out
oVerflow bit
  V = 1 if adding 2 same-signed numbers produces a result with the opposite sign
    Positive + Positive = Negative, or
    Negative + negative = Positive
  Non-arithmetic operations does not touch V bit, such as MOV,AND,LSL,MUL
Reserved
ISR number
Program Status Register (PSR)
ICI/IT
T
N
Z
C
V
Q
ICI/IT
GE
Reserved
Review
Notes: N (negative) – set (1) when a signed result is negative, otherwise cleared (0).
Z (zero) – set (1) when a result is 0, otherwise cleared (0).
C (carry) – set (1) when an add-based operation produces an overflow, when a subtract-based operation doesn’t require a borrow; when shifting, holds the last bit that’s been shifted out; otherwise cleared (0).
V (overflow) – set (1) when an add- or subtract-based operation generates a signed overflow, otherwise cleared (0).

## Slide 4: Carry and Overflow Flags
4
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 Borrow flag=0 (Result incorrect) | true result < 0  Carry flag=0 Borrow flag=1 (Result incorrect) | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1 Overflow flag=1 (Result incorrect)
Review
Notes: C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 5: Updating Condition Flags
Method 1: append “S”: updates destination register, and sets flags
  ADD r0,r1,r2 → ADDS r0,r1,r2
  SUB r0,r1,r2 → SUBS r0,r1,r2
  Performs operation, writes the result into Rd, and also updates NZCV flags
Method 2: compare instructions: sets flags only
  CMP/CMN/TEQ/TST: performs operation to update NZCV flags, but the computation result is not saved and discarded
Instruction | Description | Flags
CMP | Compare | N,Z,C,V
CMN | Compare Negative | N,Z,C,V
TEQ | Test Equivalence | N,Z,C
TST | Test | N,Z,C
Notes: it’s a “compare-only” operation for branching or predication.
; it both computes and compares in one step

## Slide 6: Updating Condition Flags
Update the status flags
  No need to add S.
  No need to specify destination register.
Operations are:
  CMP Rn – Op2: Same as SUBS, except result discarded (not written to destination register)
  CMN Rn + Op2: Same as ADDS, except result discarded
  TST Rn & Op2: Same as ANDS, except result discarded
  TEQ Rn ^ Op2: Same as EORS, except result discarded
Examples:
  CMP r0, r1
  TST r2, #5
Instruction | Operands | Brief description | Flags
CMP | Rn, Op2 | Compare | N,Z,C,V
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C
Notes: SUBS Rd, Rn, Op2: performs subtraction , writes the result into Rd, and also updates NZCV flags; it both computes and compares in one step.
CMP/CMN/TEQ/TST: performs operations to update NZCV flags, but the computation result is not saved and discarded; it’s a “compare-only” operation for branching or predication.
CMP Rn, Operand2
CMN Rn, Operand2
Update N, Z, C and V according to the result
CMP subtracts Operand2 from Rn.
  Same as SUBS, except result is discarded.
CMN adds Operand2 to Rn.
  Same as ADDS, except result is discarded.
SUBS Rd, Rn, Op2: performs subtraction 𝑅𝑛 − 𝑂𝑝2, writes the result into Rd, and also updates NZCV flags; it both computes and compares in one step.
CMP/CMN/TEQ/TST: performs operations to update NZCV flags, but the computation result is not saved and discarded; it’s a “compare-only” operation for branching or predication.
CMP Rn, Operand2
CMN Rn, Operand2
Update N, Z, C and V according to the result
CMP subtracts Operand2 from Rn.
  Same as SUBS, except result is discarded.
CMN adds Operand2 to Rn.
  Same as ADDS, except result is discarded.

## Slide 7: Example of CMP
Area absolute, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
CMP r1, #0
RSBLT r0, r1, #0
done B done ; deadloop, end of program
ENDP
END
Assume register r1 holds x’s value.
RSBLT r1, r1, #0:: conditional execution of the RSB instruction with condition code LT. If r1 < 0, then set r1=−r1
Notes: Note: RSB = Reverse SuBtract

## Slide 8: Updating Condition Flags: TST and TEQ
TST Rn, Operand2 ; Bitwise AND
TEQ Rn, Operand2 ; Bitwise Exclusive OR
Update N and Z according to the result
Can update C during the calculation of Operand2 (w/ shifting)
Do not affect V
TST performs bitwise AND on Rn and Operand2.
  Same as ANDS, except result discarded.
  Use Operand2 as a mask; Z=0 implies “some masked bit(s) are set, so result is non-zero” Z=1 implies “none of the masked bit(s) are set, so result is zero.” For a single-bit mask, Z=0 means “that bit in Rn is 1,” and Z=1 means “that bit is 0.”
TEQ performs bitwise Exclusive OR on Rn and Operand2.
  Same as EORS, except result discarded.
  If Rn and Operand2 are equal, then is zero, and Z is set to 1; otherwise Z is cleared.
x | y | x AND y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x XOR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: It computes logical operation internally, writes no result to a register, and updates the condition flags based on that XOR.
If is 0x0, then Rn and Operand2 are equal, Z is set to 1; otherwise Z is cleared.
It computes logical operation 𝑅𝑑⊕𝑂𝑝 internally, writes no result to a register, and updates the condition flags based on that XOR.
If 𝑅𝑛" ∧ " 𝑂𝑝𝑒𝑟𝑎𝑛𝑑2 is 0x0, then Rn and Operand2 are equal, Z is set to 1; otherwise Z is cleared.

## Slide 9: Example of TEQ
Translate C code into assembly:
TEQ r0, #‘!’ performs a test-equal by computing and setting condition flags; Z=1 when r0 equals ‘!’.
TEQNE r0, #‘?’ executes only if the previous Z=0 (i.e., char was not ‘!’); it tests r0 against ‘?’ and sets Z accordingly. This achieves the logical OR without branches by conditionally running the second test only when needed (short-circuit evaluation).
ADDEQ r1, r1, #1 executes only if Z=1 after the tests, meaning char matched either ‘!’ or ‘?’, so it increments found in r1
C Code | Assembly
if (char==‘!’¦¦char==‘?’) found++; | TEQ r0, #‘!’ TEQNE r0, #‘?’ ADDEQ r1, r1, #1

## Slide 10: Unconditional Branch Instructions
B label
  cause a branch to label.
BL label
  copy the address of the next instruction into r14 (lr, the link register), and
  cause a branch to label.
BX Rm
  branch to the address held in Rm
BLX Rm:
  copy the address of the next instruction into r14 (lr, the link register) and
  branch to the address held in Rm
Instruction | Operands | Brief description
B | label | Branch
BL | label | Branch with Link
BLX | Rm | Branch indirect with Link
BX | Rm | Branch indirect

## Slide 11: Unconditional Branch Instructions: A Simple Example
A label marks the location of an instruction
Labels helps human to read the code
In machine program, labels are converted to numeric offsets by assembler
MOVS r1, #1
B target ; Branch to target
MOVS r2, #2 ; Not executed
MOVS r3, #3 ; Not executed
MOVS r4, #4 ; Not executed
target MOVS r5, #5

## Slide 12: Signed vs. Unsigned Comparison
Conditional codes applied to branch instructions
Compare | Signed | Unsigned
> | BGT | BHI
>= | BGE | BHS
< | BLT | BLO
<= | BLE | BLS
== | BEQ | 
!= | BNE | 
Compare | Signed | Unsigned
> | GT | HI
≥ | GE | HS
< | LT | LO
≤ | LE | LS
== | EQ | 
≠ | NE | 

## Slide 13: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 14: Condition Codes
The possible condition codes are listed below:
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Clear
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z==0
C==1
C==0
Z==1
Flags tested
N==1
N==0
V==1
V==0
C==1 and Z==0
C==0 or Z==1
N==V
N!=V
Z==0 and N==V
Z==1 or N!=V
    Note AL is the default and does not need to be specified
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 15: Unsigned and Signed Compares
CMP a, b computes a - b and sets flags without keeping the result. For unsigned subtraction, borrow happens when a < b. ARM encodes “no borrow” (a ≥ b) as C=1, and “borrow” (a < b) as C=0, while Z distinguishes equality.
  HI (unsigned higher >): the subtraction needs no borrow, so C=1, and it’s not equal, so Z=0.
  HS/CS (higher or same/carry set ≥) : no borrow → C=1; equality allowed.
  LO/CC (unsigned lower/carry clear <): subtraction borrows → C=0.
  LS (unsigned lower or same ≤): “lower or same” means either borrowed or equal → C=0 or Z=1.
For signed subtraction a - b, the sign bit N is correct if a ≥ b (no overflow, V = 0); the sign bit N is incorrect if a < b (overflow, V = 1).
  GE (signed greater or equal ≥): N == V. If there’s no overflow (V=0), non‑negative (N=0) means ≥; if there is overflow (V=1), N=1 (incorrect) also indicates the ≥ relation.
  LT (signed less than <): N != V. If there’s no overflow (V=0), negative (N=1) means <; if there is overflow (V=1), N=0 (incorrect) also indicates the < relation.
  GT (signed greater than >): N==V and Z=0. Strictly greater excludes equality, so combine GE with not equal.
  LE (signed less or equal ≤): N != V or Z=1. Either strictly less, or equal.
Notes: alone is unreliable when overflow occurs, so ARM uses N and V together:
Why this works: for signed a − b, overflow flips the apparent sign; comparing N to V “unflips” it. Equality is still just Z=1 because zero is unambiguous.

## Slide 16: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | No overflow, implying the result is correct. The result is non-negative, Thus r0 – r1 ≥ 0, i.e., r0 ≥ r1 | No overflow, implying the result is correct. The result is negative. Thus r0 – r1 < 0, i.e., r0 < r1
V = 1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as non-negative and in fact it should be negative. Thus r0 – r1 < 0 in reality, i.e., r0 < r1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as negative and in fact it should be non-negative. Thus r0 – r1 ≥ 0 in reality., i.e. r0 ≥ r1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 17: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | r0 ≥ r1 | r0 < r1
V = 1 | r0 < r1 | r0 ≥ r1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 18: Signed Greater or Equal (N == V)
 | N = 0 | N = 1
V = 0 | 1 | 0
V = 1 | 0 | 1
CMP r0, r1
perform subtraction r0 – r1, without saving the result
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 19: Number Interpretation
If they represent signed numbers, the latter is greater.
(1 > -1).
If they represent unsigned numbers, the former is greater.
(4294967295 > 1).
Which is greater?
0xFFFFFFFF or 0x00000001

## Slide 20: Which is Greater: 0xFFFFFFFF or 0x00000001?
signed int x, y ; x = -1;
y = 1; if (x > y)
...
unsigned int x, y ;
x = 4294967295;
y = 1;
if (x > y)
...
BLE: Branch if less than or equal, signed ≤
BLS: Branch if lower or same, unsigned ≤
It’s software’s responsibility to tell computer how to interpret data:
If written in C, declare the signed vs unsigned variable
If written in Assembly, use signed vs unsigned branch instructions
MOVS r5, #0xFFFFFFFF MOVS r6, #0x00000001
CMP r5, r6 BLE Then_Clause
...
MOVS r5, #0xFFFFFFFF MOVS r6, #0x00000001
CMP r5, r6 BLS Then_Clause
...

## Slide 21: If-then Statement
C Program
// a is signed integer if (a < 0 ) { a = 0 – a; } x = x + 1;
; r1 = a (signed integer), r2 = x
CMP r1, #0 ; Compare a with 0
BGE endif ; Go to endif if a ≥ 0
then RSB r1, r1, #0 ; a = - a
endif ADD r2, r2, #1 ; x = x + 1
Implementation 1:

## Slide 22: If-then Statement
; r1 = a, r2 = x
CMP r1, #0 ; Compare a with 0
RSBLT r1, r1, #0 ; a = 0 - a if a < 0
ADD r2, r2, #1 ; x = x + 1
Implementation 2:
C Program
// a is signed integer if (a < 0 ) { a = 0 – a; } x = x + 1;

## Slide 23: Compound Boolean Expression
x > 20 && x < 25
x == 20 || x == 25
!(x == 20 || x == 25)
C Program | Assembly Program
// x is a signed integer if(x <= 20 ¦¦ x >= 25){ a = 1 } | ; r0 = x CMP r0, #20 ; compare x and 20 BLE then ; go to then if x ≤ 20 CMP r0, #25 ; compare x and 25 BLT endif ; go to endif if x < 25 then MOV r1, #1 ; a = 1 endif

## Slide 24: If-then-else
C Program
if (a == 1) b = 3; else b = 4;
; r1 = a, r2 = b
CMP r1, #1 ; compare a and 1
BNE else ; go to else if a ≠ 1
then MOV r2, #3 ; b = 3
B endif ; go to endif
else MOV r2, #4 ; b = 4
endif

## Slide 25: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
B check
loop ADD r1, r1, r0 ; sum += i
ADD r0, r0, #1 ; i++
check CMP r0, #10 ; check whether i < 10
BLT loop ; loop if signed less than
endloop
Implementation 1:

## Slide 26: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
loop CMP r0, #10 ; check whether i < 10
BGE endloop ; skip if ≥
ADD r1, r1, r0 ; sum += i
ADD r0, r0, #1 ; i++
B loop
endloop
Implementation 2:

## Slide 27: Combined Program Status Registers (xPSR)
Notes: The Q flag is sticky in that, when set to 1 by an instruction, it remains set until explicitly cleared to 0 by an MSR instruction writing to the CPSR. Instructions cannot execute conditionally on the status of the Q flag.
Saturation arithmetic is a version of arithmetic in which all operations such as addition and multiplication are limited to a fixed range between a minimum and maximum value. If the result of an operation is greater than the maximum it is set ("clamped") to the maximum, while if it is below the minimum it is clamped to the minimum. The name comes from how the value becomes "saturated" once it reaches the extreme values; further additions to a maximum or subtractions from a minimum will not change the result.
For example, if the valid range of values is from -100 to 100, the following operations produce the following values:
60 + 43 = 100
(60 + 43) − 150 = −50
43 − 150 = −100
60 + (43 − 150) = −40
10 × 11 = 100
99 × 99 = 100
30 × (5 − 1) = 100
30×5 − 30×1 = 70
Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 28: Condition Codes
The possible condition codes are listed below:
    Note AL is the default and does not need to be specified
Not equal
Unsigned higher or same
Unsigned lower
Negative
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Signed Less than
Signed Greater than
Signed Less than or equal
Always
Signed Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 29: Conditional Execution
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 30: Conditional Execution
if (a <= 0)
y = -1;
else
y = 1;
CMP r0, #0
MOVLE r1, #-1 ; executed if LE
MOVGT r1, #1 ; executed if GT
LE: Signed Less than or Equal
GT: Signed Greater Than
a ⟶ r0
y ⟶ r1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 31: Conditional Execution
if (a==1 || a==7 || a==11)
y = 1;
else
y = -1;
CMP r0, #1
CMPNE r0, #7 ; executed if r0 != 1
CMPNE r0, #11 ; executed if r0 != 7
MOVEQ r1, #1
MOVNE r1, #-1
NE: Not Equal
EQ: Equal
a ⟶ r0
y ⟶ r1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 32: Compound Boolean Expression
C Program | Assembly Program
// x is a signed integer if(x <= 20 ¦¦ x >= 25){ a = 1; } | ; r0 = x, r1 = a CMP r0, #20 ; compare x and 20 MOVLE r1, #1 ; a=1 if less or equal CMP r0, #25 ; CMP if greater than MOVGE r1, #1 ; a=1 if greater or equal endif

## Slide 33: Example 1: Greatest Common Divider (GCD)
; suppose r0 = a and r1 = b
gcd CMP r0, r1 ; a > b?
BEQ end ; if a = b, done
BLO less ; a < b
SUB r0, r0, r1 ; a = a – b
B gcd
less SUB r1, r1, r0 ; b = b – a
B gcd
end
Euclid’s Algorithm
gcd CMP r0, r1
SUBHI r0, r0, r1
SUBLO r1, r1, r0
BNE gcd
uint32_t a, b;
while (a != b ) {
if (a > b)
a = a – b;
else
b = b – a;
}

## Slide 34: Example 2
// x in r0, y in r1
if ( x + y < 0 )
x = 0;
else
x = 1;
ADDS r0, r0, r1
BPL PosOrZ
MOV r0, #0
B done
PosOrZ MOV r0, #1
done
ADDS r0, r0, r1 ; r0 = x + y, setting CCs
MOVMI r0, #0 ; return 0 if n bit = 1
MOVPL r0, #1 ; return 1 if n bit = 0

## Slide 35: Combination
Except that it does not change the status flags, CBZ Rn,label is equivalent to:
  CMP Rn, #0
  BEQ label
Except that it does not change the status flags, CBNZ Rn,label is equivalent to:
  CMP Rn, #0
  BNE label
Instruction | Operands | Brief description
CBZ | Rn, label | Compare and Branch if Zero
CBNZ | Rn, label | Compare and Branch if Non Zero

## Slide 36: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: ?? | Output: ??

## Slide 37: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: 0, 1 | Output: 0, 1, 3, 4

## Slide 38: Break and Continue
C Program | Assembly Program
// Find string length char str[] = "hello"; int len = 0; for( ; ; ) { if (*str == '\0') break; str++; len++; } | ; r0 = string memory address ; r1 = string length MOV r1, #0 ; len = 0 loop LDRB r2, [r1] CBNZ r2, notZero B endloop notZero ADD r0, r0, #1 ; str++ ADD r1, r1, #1 ; len++ B loop endloop

## Slide 39: IT (If-Then) instruction
IT{x{y{z}}} {cond}
where the x, y, and z specify the existence of the optional second, third, and fourth conditional instruction respectively.
x, y, and z are either T (Then) or E (Else)
ITTE NE ; IT can be omitted
ANDNE r0,r0,r1 ; 16-bit AND, not ANDS
ADDNE r2,r2,#1 ; 32-bit ADDS
MOVEQ r2,r3 ; 16-bit MOV
ITT AL ; emit 2 non-flag setting 16-bit instructions
ADDAL r0,r0,r1 ; 16-bit ADD, not ADDS
SUBAL r2,r2,#1 ; 16-bit SUB, not SUB
ADD r0,r0,r1 ; expands into 32-bit ADD, and is not in IT block
ITT EQ
MOVEQ r0,r1
BEQ dloop ; branch at end of IT block is permitted
ITT EQ
MOVEQ r0,r1
ADDEQ r0,r0,#1
Examples:

## Slide 40: IT (If-Then) instruction
You do not need to write IT instructions in your code.
The assembler generates them for you automatically according to the conditions specified.
IT{x{y{z}}} {cond}
where the x, y, and z specify the existence of the optional second, third, and fourth conditional instruction respectively.
x, y, and z are either T (Then) or E (Else)

## Slide 41: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 42: Summary: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 43: Summary: Conditionally Executed
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V