## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Stack and Recursive Functions
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Recursive Functions
A recursive function is one that solves its task by calling itself on smaller pieces of data.
An effective tactic is to
  divide a problem into sub-problems of the same type as the original,
  solve those sub-problems, and
  combine the results

## Slide 3: Defining Factorial(n)
1 × 2 × 3 × … × n
factorial(0)
= 1
factorial(1)
= 1
= 1 × factorial(0)
factorial(2)
= 2×1
= 2 × factorial(1)
factorial(3)
= 3×2×1
= 3 × factorial(2)
factorial(4)
= 4×3×2×1
= 4 × factorial(3)
factorial(n)
= n×(n-1)×…×1
= n × factorial(n-1)
Product of the first n numbers

## Slide 4: Classic Example: Factorial
Factorial is the classic example:
  6! = 6  5!
  6! = 6  5 x 4!
  ...
  6! = 6  5  4  3  2  1
The factorial function can be easily written as a recursive function:
int Factorial(int n) {
if (n < 2)
return 1; /* base case */
return (n * Factorial(n – 1));
}

## Slide 5: Classic Example: Fibonacci Numbers
f(n) = f(n-1) + f(n-2)
f(0) = 1
f(1) = 1
1, 1, 2, 3, 5, 8, 13, 21, 34, 55, 89, 144, 233, 377, 610, 987, …
int Fibonacci(int n) {
if (n <= 1)
return 1; /* base case */
return (Fibonacci(n-1) + Fibonacci(n-2));
}

## Slide 6: Analysis of fib(5)
int fib(int n)
if(n == 0 || n == 1)
return n;
else
return fib(n-1) + fib(n-2);
fib(5)
fib(4)
fib(3)
fib(3)
fib(2)
fib(1)
fib(0)
fib(2)
fib(1)
fib(0)
fib(1)
fib(2)
fib(1)
fib(0)
fib(1)
1
1
1
1
1
0
0
0
1
1
2
1
3
2
5

## Slide 7: Example of Recursive Function: Testing Palindrome
bool isPalindrome(char* s, int len) {
if(len < 2)
return TRUE;
else
return s[0] == s[len-1] && isPalindrome(&s[1], len-2);
}

## Slide 8: Recursion vs Iteration
Any problem that can be solved recursively can also be solved iteratively (using loop).
Recursive functions vs Iterative functions
Cons:
  Recursive functions are slow
  Recursive function take more memory
Pros
  Recursive functions resembles the problem more naturally
  Recursive function are easier to program, and debug.

## Slide 9: Recursive Factorial in C
factorial(5)
5 * factorial(4)
4 * factorial(3)
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6
return 24
return 120
int factorial(int n);
int main(void){
factorial(5);
return 0;
}
int factorial(int n) {
int f;
if(n==1)
return 1;
else
f = n * factorial(n-1);
return f;
}

## Slide 10: Recursive Functions
PUSH LR (& working registers) onto stack before nested call
POP LR (& working registers) off stack after nested return

## Slide 11: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03 ; Set argument n = 3 in r0 (r0 holds first arg)
BL factorial ; Call factorial(n); LR gets return address; ; result returns in r0
stop B stop ; Halt by branching to self (infinite loop)
ENDP
; --- Recursive factorial(n) ---
factorial
PUSH {r4, lr} ; Save callee-used r4 and return address LR on stack
MOV r4, r0 ; Preserve n in r4 across the recursive call
CMP r4, #0x01 ; Check base case: n == 1 ?
BNE NZ ; If n != 1, branch to NZ for recursive case
MOVS r0, #0x01 ; Base case: return 1 in r0
loop POP {r4, pc} ; restore r4, and return by popping PC
NZ SUBS r0, r4, #1 ; Prepare argument r0 = n - 1 for recursive call
BL factorial ; r0 <- factorial(n-1) after return
MUL r0, r4, r0 ; r0 = n * factorial(n-1)
B loop
END

## Slide 12: Trace Function Execution for this Call Sequence
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6

## Slide 13: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
3 * factorial(2)
2 * factorial(1)
1
return 2
return 6
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C

## Slide 14: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03 ; Set argument n = 3 in r0 (r0 holds first arg)
BL factorial ; Call factorial(n); LR gets return address; ; result returns in r0
stop
B stop ; Halt by branching to self (infinite loop)
ENDP
; --- Recursive factorial(n) ---
factorial
PUSH {r4, lr} ; Save callee-used r4 and return address LR on stack
MOV r4, r0 ; Preserve n in r4 across the recursive call
CMP r4, #0x01 ; Check base case: n == 1 ?
BNE NZ ; If n != 1, branch to NZ for recursive case
MOVS r0, #0x01 ; Base case: return 1 in r0
loop
POP {r4, pc} ; restore r4, and return by popping PC
NZ
SUBS r0, r4, #1 ; Prepare argument r0 = n - 1 for recursive call
BL factorial ; r0 <- factorial(n-1) after return
MUL r0, r4, r0 ; r0 = n * factorial(n-1)
B loop
END

## Slide 15: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000130
0xFFFFFFFF
0x20000600
pc
lr
sp
Data
0x12345678
…
…
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
0
3
r4
r0
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Memory
1st recursive call factorial(3), with argument r0 = 3

## Slide 16: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000136
0x08000134
0x20000600
Memory
Data
0x12345678
…
…
0
3
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 17: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000138
0x08000134
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
3
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 18: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000144
0x08000134
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
2nd recursive call factorial(2), with argument r0 = 2

## Slide 19: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000136
0x08000148
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 20: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000138
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 21: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000144
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
1
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
3rd recursive call 2 * factorial(1)
3rd recursive call factorial(1), with argument r0 = 1

## Slide 22: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000136
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
1
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 23: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000138
0x08000148
0x200005E8
Memory
Data
0x08000134
0
0x08000148
3
0x08000148
2
0x12345678
…
…
1
1
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 24: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x0800013E
0x08000148
0x200005E8
Memory
Data
0x08000134
0
0x08000148
3
0x08000148
2
0x12345678
…
…
1
1
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Compute factorial(1)=1

## Slide 25: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000148
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
1
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Return from factorial(1)

## Slide 26: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000148
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Compute 2 * factorial(1) = 2

## Slide 27: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000140
0x08000148
0x200005F0
Memory
Data
0x08000134
0
0x08000148
3
0x12345678
…
…
2
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Return from factorial(2)

## Slide 28: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000148
0x08000148
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
2
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 29: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000148
0x08000148
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
6
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Compute 3 * factorial(2) = 6

## Slide 30: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000148
0x08000148
0x200005F8
Memory
Data
0x08000134
0
0x12345678
…
…
3
6
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0
Return from factorial(3)

## Slide 31: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000134
0x08000148
0x20000600
Memory
Data
0x12345678
…
…
0
6
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0

## Slide 32: Recursive Factorial in Assembly
AREA main, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
MOV r0, #0x03
BL factorial
stop B stop
ENDP
factorial
PUSH {r4, lr}
MOV r4, r0
CMP r4, #0x01
BNE NZ
MOVS r0, #0x01
loop POP {r4, pc}
NZ SUBS r0, r4, #1
BL factorial
MUL r0, r4, r0
B loop
END
0x08000134
0x08000148
0x20000600
Memory
Data
0x12345678
…
…
0
6
…
…
0x08000130
0x08000134
0x08000136
0x08000144
0x08000148
0x08000140
0x08000142
0x08000138
0x0800013A
0x0800013C
0x0800013E
0x0800014C
Address
0x00000000
0xFFFFFFFF
0x20000600
0x200005FC
0x200005F8
0x200005F4
0x200005F0
0x200005EC
0x200005E8
0x200005E4
0x200005E0
0x200005DC
0x200005D8
0x200005D4
pc
lr
sp
r4
r0