## Slide 1: L1 (CHAPTER 2) Data Representation Exercises
Acknowledgement: some slides taken from Yifeng Zhu’s courseware

## Slide 2: Decimal, Binary and Hex
Decimal | Binary | Hex
0 | 0000 | 0x0
1 | 0001 | 0x1
2 | 0010 | 0x2
3 | 0011 | 0x3
4 | 0100 | 0x4
5 | 0101 | 0x5
6 | 0110 | 0x6
7 | 0111 | 0x7
8 | 1000 | 0x8
9 | 1001 | 0x9
10 | 1010 | 0xA
11 | 1011 | 0xB
12 | 1100 | 0xC
13 | 1101 | 0xD
14 | 1110 | 0xE
15 | 1111 | 0xF
Prefix 0x denotes hex
Review

## Slide 3: Question: Number Conversion
Q: Convert 0x3A56E2F8 into binary
Q: Convert binary number 111010 into hex

## Slide 4: Adding two integers
-9
6
-3
01001
10110
10111
flip
+1
9
-9
00010
00011
flip
+1
3
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1
Hardware Adder
23
6
29
+
Two’s Complement Counterpart
Same bit patterns, different interpretation.
  Unsigned addition: 23+6=29
  Signed addition: -9+6=-3
This example shows that the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers.
Review
Notes: {{Pause=1}} We will use a very simple example to show that, the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers. {{Pause=0.5}}
Suppose we are adding negative nine and six. {{Pause=0.5}} These two signed numbers are represented in two’s complement in computers. {{Pause=0.5}}
Specifically, we can obtain the two’s complement representation of negative nine by flipping all bits and adding one. {{Pause=0.5}} The two’s complement of a positive number is itself. {{Pause=0.5}}
Let’s see what will happen if the hardware treats these two inputs as unsigned numbers. If these binary bits represent unsigned numbers, they are 23 and 6, respectively. Therefore, the hardware adds 23 and 6, and produces 29, in decimal, {{Pause=0.3}} or one, one, one, zero, one, in binary. {{Pause=0.5}}
If the output represents a signed integer in two’s complement, it actually represents negative 3. This can be proved by inverting all the bits and adding one. The result, negative three, is exactly the sum of the original signed inputs. {{Pause=0.5}}
This example shows that, without any modification, the hardware adder designed for adding unsigned numbers, works correctly for adding signed numbers.

## Slide 5: Signed Integers Method 3: Two’s Complement
Two’s Complement ():
TC of a number can be obtained by its bitwise NOT plus one.
 | Binary | Decimal
Original number | 00011 | 3
Step 1: Invert every bit | 11100 | 
Step 2: Add 1 | + 00001 | 
Two’s complement | 11101 | -3
Example 1: TC(3)
Review

## Slide 6: Signed Integer Representation Overview
Three ways to represent signed binary integers:
  Signed magnitude
  One’s complement ()
  Two’s complement ()
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero | Two zeroes () | Two zeroes () | One zero
Unique Numbers |  |  | 
 | Sign-and-Magnitude | One’s Complement | Two’s Complement
Range |  |  | 
Zero |  |  | One zero
Unique Numbers |  |  | 
Review

## Slide 7: Question: 2’s Complement
For each of the following binary numbers, give the corresponding binary number of the negative of its value, for 2’s-complement system
(a) x=01010101
(b) x=10101010
(c) x=10000000

## Slide 8: Question: Number Conversion
Q: What is the decimal value of binary number x=10100111 as either unsigned int, or signed int in 2’s complement representation?
What about x=11100001?
What about x=10000000?

## Slide 9: Question: Number Conversion
Q: Which number is larger: 1001 or 0011 in binary?
Q: Which number is larger: 0xFFFFFFFF or 0x00000001 in hex?

## Slide 10: Question: Number Range
Which range of decimals can be expressed with a 6-bit number (assuming Two’s complement representation)?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 11: Question: Number Range
Which range of decimals can be expressed with a 6-bit unsigned integer?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 12: Question: Integer arithmetic
Q: Consider a 4-bit system. What is the result of 1001 + 0011?

## Slide 13: Summary of Carry and Overflow Flags
13
Carry flag C = 1 upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Bit | Name | Meaning after add or sub
N | negative | result is negative
Z | zero | result is zero
V | overflow | signed overflow
C | carry | unsigned overflow
31
0
N
Z
C
V
CPSR (Current Program Status Register)
Review
Notes: C is cleared upon an unsigned subtract if the answer is wrong

## Slide 14: Signed or unsigned
Whether the carry flag or the overflow flag should be used depends on the programmer’s intention.
uint a;
uint b;
…
c = a + b
…
C Program
Check the carry flag
for unsigned addition
int a;
int b;
…
c = a + b
…
C Program
Check the overflow flag
for signed addition
Review

## Slide 15: Question: Addition
Q: Consider a 4-bit system. What is the result of addition 1011+0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？

## Slide 16: Question: Subtraction
Q: Q: Consider a 4-bit system. What is the result of subtraction 1011-0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？

## Slide 17: Question: Subtraction
Q: Consider a 4-bit system. What is the result of subtraction 0110-1011, assuming either unsigned integers, or signed integers in 2’s-complement representation？

## Slide 18: Question: True or False
1. Borrow=1 is impossible when subtracting one unsigned number from another.
2. Overflow=1 is impossible when subtracting two signed operands of the same sign.
3. There are two representations of zero in 2’s complement representation.
4. In 2’s complement, the absolute values of full-scale negative and full-scale positive are identical