## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 10
Preserve Environment via Stack

## Slide 2: Overview
How to call a subroutine?
How to return the control back to the caller?
How to pass arguments into a subroutine?
How to return a value in a subroutine?
How to preserve the running environment for the caller?

## Slide 3: Stack
A Last-In-First-Out memory model
Only allow to access the most recently added item
  Also called the top of the stack
Key operations:
  push (add item to stack)
  pop (remove top item from stack)

## Slide 4: Tower of Hanoi
Only one disk may be moved at a time.
Each move consists of taking the upper disk from one of the rods and sliding it onto another rod, on top of the other disks that may already be present on that rod.
No disk may be placed on top of a smaller disk.

## Slide 5: Tower of Hanoi
http://en.wikipedia.org/wiki/File:Tower_of_Hanoi_4.gif
STACK: Last In First Out
Stack 1
Stack 2
Stack 3

## Slide 6: Stack Growth Convention: Ascending vs Descending
  Descending stack: Stack grows towards low memory address
  Ascending stack: Stack grows towards high memory address

## Slide 7: Stack Growth Convention: Full vs Empty
  Full stack: SP points to the last item pushed onto the stack
  Empty stack: SP points to the next free space on the stack

## Slide 8: Cortex-M Stack
Cortex-M uses full descending stack
Example:
PUSH/POP {r0,r6,r3}
Stack pointer (SP, aka R13)
  decremented on PUSH
    SP = SP – 4 * # of registers
  incremented on POP
    SP = SP + 4 * # of registers
  SP starts at 0x20000200 for STM32-Discovery by default (can be changed in startup.s)

## Slide 9: Full Descending Stack

## Slide 10: Stack Implementation
Stock Name | Push |  | Pop | 
 | Equivalent | Alternative | Equivalent | Alternative
Full Descending(FD) | STMFD SP!,list | STMDB SP!,list | LDMFD SP!,list | LDMIA SP!,list
Empty Descending(ED) | STMED SP!,list | STMDA SP!,list | LDMED SP!,list | LDMIB SP!,list
Full Ascending(FA) | STMFA SP!,list | STMIB SP!,list | LDMFA SP!,list | LDMDA SP!,list
Empty Ascending(EA) | STMEA SP!,list | STMIA SP!,list | LDMEA SP!,list | LDMDB SP!,list

## Slide 11: Typical Usage of Stack
Why need stack?
  Saving the original contents of processor’s registers at the beginning a subroutine (Contents are restored at the end of a subroutine)
  Storing local variables in a subroutine
  Passing extra arguments to a subroutine
  Saving processor’s registers upon an interrupt
Sound complex? No worry! We will learn them.

## Slide 12: Stack
PUSH {Rd}
  SP = SP-4 ⟶ descending stack
  (*SP) = Rd ⟶ full stack
Push multiple registers
PUSH {r6, r7, r8}
They are equivalent.
PUSH {r8}
PUSH {r7}
PUSH {r6}
PUSH {r8, r7, r6}
The order in which registers listed in the register list does not matter.
When pushing multiple registers, these registers are automatically sorted by name and the lowest-numbered register is stored to the lowest memory address, i.e. is stored last.

## Slide 13: Stack
POP {Rd}
  Rd = (*SP) ⟶ full stack
  SP = SP + 4 ⟶ Stack shrinks
Pop multiple registers
POP {r8, r7, r6}
They are equivalent.
POP {r6}
POP {r7}
POP {r8}
POP {r6, r7, r8}
The order in which registers listed in the register list does not matter.
When popping multiple registers, these registers are automatically sorted by name and the lowest-numbered register is loaded from the lowest memory address, i.e. is loaded first.

## Slide 14: Full Descending Stack
PUSH {r3, r1, r7, r2}

## Slide 15: Full Descending Stack
PUSH {r3, r1, r7, r2}
Largest-numbered register is pushed first.

## Slide 16: Full Descending Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}

## Slide 17: Full Descending Stack
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}
Smallest-numbered register is popped first.

## Slide 18: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
xxxxxxxx
xxxxxxxx

## Slide 19: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
xxxxxxxx

## Slide 20: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001F8
0x22222222
0x11111111
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 21: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x200001FC
0x22222222
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 22: Example: swap R1 & R2
R1
R2
R13 (SP)
0x20000200
0x200001FC
0x200001F8
0x20000200
0x11111111
0x22222222
xxxxxxxx
PUSH {R1}
PUSH {R2}
POP {R1}
POP {R2}
memory
Address
PC
0x11111111
0x22222222

## Slide 23: Quiz
Are the values of R1 and R2 swapped?
  PUSH {R1, R2}
  POP {R2, R1}
Answer: No.
But you can:
  PUSH {R1, R2}
  POP {R2}
  POP {R1}
or
  PUSH {R1}
  PUSH {R2}
  POP {R1, R2}

## Slide 24: Subroutine
A subroutines, also called a function or a procedure,
  single-entry, single-exit
  Return to caller after it exits
When a subroutine is called, the Link Register (LR) holds the memory address of the next instruction to be executed after the subroutine exits.

## Slide 25: Link Register
Link Register (LR) holds the return address of the current subroutine call.

## Slide 26: Call a Subroutine
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101, not 11 | foo PROC ... MOV r4, #10 ; foo changes r4 ... BX LR ENDP

## Slide 27: Calling a Subroutine
BL label
Step 1: LR = PC + 4
Step 2: PC = label
Notes:
  label is name of subroutine
  Compiler translates label to memory address
  After call, LR holds return address (the instruction following the call)
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 28: Exiting a Subroutine
Branch and Exchange
BX LR
PC = LR
Caller Program
MOV r4, #100 ... BL foo ...
Subroutine/Callee
foo PROC ... MOV r4, #10 ... BX LR ENDP

## Slide 29: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | YES | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes/No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 30: Caller-saved Registers vs Callee-saved Registers
Not saved by subroutine
Hold arguments/result
Caller expects their values are retained
Callee must save and store it if callee modifies it
Register Bank
Special Registers
Caller-saved registers
Callee-saved registers
Callee-saved registers

## Slide 31: Preserve Runtime Environment via Stack
Caller Program | Subroutine/Callee
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 ; r4 = 101, not 11 | foo PROC PUSH {r4} ; preserve r4 ... MOV r4, #10 ; foo changes r4 ... POP {r4} ; Recover r4 BX LR ENDP
Callee should preserve r4!
Caller expects callee does not modify r4!

## Slide 32: Preserve Runtime Environment via Stack
Caller Program | Subroutine/Callee
Caller should save these registers if callers needs to re-use their original values: R0 – R3 R12 CPSR | Callee should Preserve R4 – R11 R14 (LR) R13 (SP)

## Slide 33: Preserve Runtime Environment via Stack
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4} ... MOV r4, #10 ... BL bar ... POP {r4} BX LR ENDP | bar PROC ... BX LR ENDP
What is wrong in foo()?

## Slide 34: Preserve Runtime Environment via Stack
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4} ... MOV r4, #10 ... BL bar ... POP {r4} BX LR ENDP | bar PROC ... BX LR ENDP
What is wrong in foo()?

## Slide 35: Preserve Runtime Environment via Stack
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4, LR} ... MOV r4, #10 ... BL bar ... POP {r4, LR} BX LR ENDP | bar PROC ... BX LR ENDP
What is wrong in foo()? Solution #1

## Slide 36: Stacks and Subroutines

## Slide 37: Preserve Runtime Environment via Stack
Caller Program | Subroutine foo | Subroutine bar
MOV r4, #100 ... BL foo ... ADD r4, r4, #1 | foo PROC PUSH {r4, LR} ... MOV r4, #10 ... BL bar ... POP {r4, PC} BX LR ENDP | bar PROC ... BX LR ENDP
What is wrong in foo()? Solution #2

## Slide 38: Subroutine Calling Another Subroutine
MAIN
MOV R0,#2
BL QUAD
ENDL ...
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
SQ MUL R0,R0
BX LR
Function MAIN
Function QUAD
Function SQ

## Slide 39: Subroutine Calling Another Subroutine
MAIN PROC
MOV R0,#2
BL QUAD
ENDL ...
ENDP
QUAD PROC
PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDP
SQ PROC
MUL R0,R0
BX LR
ENDP
Function MAIN
Function QUAD
Function SQ

## Slide 40: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x20000200
0x200001FC
0x200001F8
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C
R0
PC
0x08000138
LR
SP
0x20000200
SQ
QUAD

## Slide 41: Example: R0 = R04
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800013C
LR
SP
0x20000200
SQ
QUAD
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 42: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x0800014C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Preserve
Link Register (LR)
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 43: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
0x08000140
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000150
LR
SP
0x200001FC
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 44: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x02
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 45: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 46: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000154
LR
SP
0x200001FC
0x08000154
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 47: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x04
R0
PC
0x08000144
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 48: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000148
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 49: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000158
LR
SP
0x200001FC
0x08000158
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 50: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x0800015C
LR
SP
0x20000200
0x08000140
SQ
QUAD
Restore
Link Register (LR)
0x08000140
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 51: Example: R0 = R04
MOV R0,#2
BL QUAD
B ENDL
SQ MUL R0,R0
BX LR
QUAD PUSH {LR}
BL SQ
BL SQ
POP {LR}
BX LR
ENDL ...
PUSH {LR}
POP {LR}
BL SQ
B ENDL
BL SQ
BX LR
xxxxxxxx
MOV R0,#2
BL QUAD
BX LR
MUL R0,R0
0x10
R0
PC
0x08000140
LR
SP
0x20000200
0x08000140
0x08000140
SQ
QUAD
0x20000200
0x200001FC
0x200001F8
0x0800014C
0x08000150
0x08000140
0x08000148
0x08000154
0x08000158
0x08000138
0x0800013C
0x08000144
0x0800015C

## Slide 52: Stack Pointer (SP)
SP is the shadow of MSP (Main SP) or PSP (Process SP)
If there is no embedded OS, PSP is not used
Determined by the ASP (Active SP) bit in the CONTROL register (ASP is always 0 in handler mode).
  0 = MSP (default)
  1 = PSP
Register Bank
Special Registers
Bit 31 - 3 | 2 | 1 | 0
Reserved |  | ASP | 
CONTROL Register |  |  | 

## Slide 53: Initializing the stack pointer (SP)
Before using the stack, software has to define stack space and initialize the stack pointer (SP).
The assembly file startup.s defines stack space and initialize SP.

## Slide 54: Passing Arguments into a Subroutine

## Slide 55: Passing Arguments into a Subroutine
a16
b16
c8
d32
Subroutine
Register R0
Register R1
Register R2
Register R3
Return Value
Register R0
int32_t sum(int16_t a16, int16_t b16, int8_t c8, int32_t d32);

## Slide 56: Passing 4 Arguments
Caller
s = sum(1, 2, 3, 4);
MOVS r0, #1 ; a16
MOVS r1, #2 ; b16
MOVS r2, #3 ; c8
MOVS r3, #4 ; d32
BL sum
Callee
sum PROC
ADD r0, r0, r1 ; a16 + b16
ADD r0, r0, r2 ; add c8
ADD r0, r0, r3 ; add d32
BX LR ; return
ENDP
int32_t sum(int16_t a16, int16_t b16, int8_t c8, int32_t d32);

## Slide 57: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Caller
MOVS r0, #5
MOVS r1, #6
MOVS r2, #7
MOVS r3, #8
PUSH {r0, r1, r2, r3}
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum
...
POP {r0, r1, r2, r3}
Callee
sum PROC
EXPORT sum
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r1,r2, [sp] ; r1=mem[sp],r2=mem[sp+4]
ADD r0, r0, r1 ; add h
ADD r0, r0, r2 ; add i
LDRD r1,r2, [sp, #8] ; r1=mem[sp+8],r2=mem[sp+12]
ADD r0, r0, r1 ; add j
ADD r0, r0, r2 ; add k
BX LR
ENDP
LDRD: Load Register Doubleword

## Slide 58: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Caller
MOVS r0, #5
MOVS r1, #6
MOVS r2, #7
MOVS r3, #8
PUSH {r0, r1, r2, r3}
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum
...
POP {r0, r1, r2, r3}
Callee
sum PROC
EXPORT sum
PUSH {r5, r6, lr}
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r5,r6, [sp, #12] ;r5=mem[sp+12],r6=mem[sp+16]
ADD r0, r0, r5 ; add h
ADD r0, r0, r6 ; add i
LDRD r5,r6, [sp, #20] ;r5=mem[sp+20],r6=mem[sp+24]
ADD r0, r0, r5 ; add j
ADD r0, r0, r6 ; add k
POP {r5, r6, pc}
ENDP

## Slide 59: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Caller
MOVS r0, #5
MOVS r1, #6
MOVS r2, #7
MOVS r3, #8
PUSH {r0, r1, r2, r3}
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum
...
POP {r0, r1, r2, r3}
Old SP | <xxxxxxxx>
SP+12 | 0x00000008
SP+8 | 0x00000007
SP+4 | 0x00000006
SP | 0x00000005
Stack

## Slide 60: Passing Extra Arguments via Stack
int32_t sum(int32_t a, int32_t b, int32_t c, int32_t d,
int32_t h, int32_t i, int32_t j, int32_t k);
s = sum(1, 2, 3, 4, 5, 6, 7, 8);
Callee
sum PROC
EXPORT sum
PUSH {r5, r6, lr}
ADD r0, r0, r1 ; add a + b
ADD r0, r0, r2 ; add c
ADD r0, r0, r3 ; add d
LDRD r5,r6, [sp, #12] ; r5=mem[sp+12],r6=mem[sp+16]
ADD r0, r0, r5 ; add h
ADD r0, r0, r6 ; add i
LDRD r5,r6, [sp, #20] ; r5=mem[sp+20],r6=mem[sp+24]
ADD r0, r0, r5 ; add j
ADD r0, r0, r6 ; add k
POP {r5, r6, pc}
ENDP
Old SP | <xxxxxxxx>
SP+24 | 0x00000008
SP+20 | 0x00000007
SP+16 | 0x00000006
SP+12 | 0x00000005
SP+8 | lr
SP+4 | r6
SP | r5
Stack

## Slide 61: Summary
ARM Cortex-M uses full descending stack
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
What registers should be preserved?
  Caller-saved registers vs callee-saved registers
How to preserve the running environment for the caller?
  Via stack