## Slide 1: Dr. Yifeng Zhu
ARM Cortex-M
External Interrupts (EXTI)
Embedded Systems with ARM Cortex-M
Microcontrollers in Assembly Language and C
Visit book website: http://web.eece.maine.edu/~zhu/book
Notes: {{Pause=3}} This lecture will show you how to configure and program, external interrupts (EXTI). External interrupts are generated by peripherals or devices, external to the microcontroller, such as push buttons and key pads.

## Slide 2: Interrupt vs Polling
Polling:
You pick up the phone every few seconds to check whether you are getting a call.
Interrupt:
Do whatever you should do and pick up the phone when it rings.
  Hardware-triggered software action
  espond to external events efficiently, while avoiding busy wait.
  When no events, the processor can run the main program or enter a sleep state to conserve energy
Notes: {{Pause=2}} There are two approaches to monitoring, and responding to external events. One is polling. The other is interrupt. The polling approach is like, picking up your phone every few seconds to check whether you are getting a call.

## Slide 3: Interrupt vs Polling
Polling:
You pick up the phone every few seconds to check whether you are getting a call.
Interrupt:
Do whatever you should do and pick up the phone when it rings.
  Hardware-triggered software action
  Respond to external events efficiently, while avoiding busy wait.
  When no events, the processor can run the main program or enter a sleep state to conserve energy
http://www.istockphoto.com/
Notes: The interrupt approach is like, waiting for the phone to ring. Apparently, interrupt is more efficient than polling. You are free to do whatever you should do, and pick up the phone, only when it rings. {{Pause=1}} Put it simply, an interrupt is essentially, a hardware-triggered software action. {{Pause=1}} The interrupt controller temporally stops the normal flow of program execution, and causes the interrupt service routine to be executed. After the interrupt service routine completes, normal program execution is resumed, at the point where it was last. {{Pause=0.5}} When there are no interrupt events, the processor runs the normal program, or enters a sleep state to conserve energy.

## Slide 4: Joystick
STM32L4 Discovery Kit
Joystick with 4-direction control and selector
STM32L4
Up
Down
Left
Right
Center
Notes: {{Pause=2}} We will use the joystick as an example, to show the basic configuration and programming of external interrupts. {{Pause=1}} Each STM32L4 discovery kit, has a four-direction joystick. The user may push in one of four directions: up, down, left, and right. The user may also press the center of the joystick.

## Slide 5: Joystick
+3V
Internal diagram of joystick
PA3
Notes: {{Pause=2}} Let’s quickly review the schematic diagram of STM32L4 discovery kit. This diagram shows how processor's and joystick's pins are connected. G P I O pins PA 0, PA 1, PA 5, PA 2, PA 3 are connected to the center, left, down, right, and up pin of the joystick, respectively. Each pin is connected to the ground, via a capacitor. These capacitors perform hardware debouncing.
{{Pause=1}} Here is the internal diagram of the joystick. It has five switches. The common terminal is connected to positive 3 volt. When the up of the joystick is pressed, this switch is then closed. As result, PA 3 is then connected to the 3 volt via the common terminal.
{{Pause=1}} Pay attention, the joystick center pin, is pulled down to ground, via a 10K ohms resistor. Therefore, the default voltage on the center pin is zero. However, the other four joystick terminals are not pulled down. If these pins are neither pulled up nor pulled down internally, their voltage is un-deterministic. Their default voltage may be high or low, depending on history usage.

## Slide 6: Joystick
+3V
Internal diagram of joystick
PA3
EXTI0
EXTI1
EXTI3
EXTI5
EXTI2
Notes: {{Pause=2}} We can use external interrupts, to monitor whether the joystick is pressed or not. Each pin can independently trigger an interrupt request signal. Specifically, software can configure the external interrupt controller, such that PA 0 triggers, external interrupt 0, PA 1 triggers, external interrupt 1, PA 5 triggers, external interrupt 5, PA 2 triggers, external interrupt 2, and finally, PA 3 triggers, external interrupt 3.
{{Pause=1}} In the next slide, I will show you how to select the source of external interrupts.

## Slide 7: External Interrupt (EXTI) Sources
PA.3
PB.3
PC.3
PD.3
PE.3
PF.3
EXTI.3
STM32L4
PA.3
EXTI3
NVIC
Cortex-M4
Nested-Vectored Interrupt Controller
SYSCFG external interrupt configuration register (SYSCFG_EXTICR)
PG.3
PH.3
source selection
000
001
010
011
100
101
110
111
Select pin x from Port y as EXTIx
Notes: {{Pause=2}} Both external circuit, and the microcontroller, can supply, a voltage signal on a pin. The external interrupt controller monitors the change of the voltage signal. The rising or falling edge of the voltage signal, can make the external interrupt controller, generate an interrupt request. The interrupt request will be sent to, the N V I C.
{{Pause=1}} The external interrupt controller supports, 16 external interrupts, associated with G P I O pins. These interrupts are named, from external interrupt 0, to external interrupt 15. Each of these interrupts is associated with one specific G P I O pin. However, a processor has more than 16 G P I O pins. How does the controller map G P I O pins to external interrupts?
{{Pause=1}} STM32 takes a simple approach. Specifically, only pins with the pin number x, can be the source of, external interrupt x. For example, the source of external interrupt 3, can be PA 3, PB 3, PC 3, PD 3, etc. {{Pause=0.5}} The source selection bits, in the SYSCFG external interrupt configuration register (E X T I C R), specifies which pin will be selected as external interrupt source. Pay attention. No multiple pins from this group, can be used as the external interrupt source simultaneously. For example, if the pin PA 3 has an external interrupt on it, we cannot use the pins PB 3 or PC 3 as the source for external interrupt 3.

## Slide 8: External Interrupt (EXTI) Sources
PA.x
PB.x
PC.x
PD.x
PE.x
PF.x
EXTIx
STM32L4
Pin.x
EXTIx
NVIC
Cortex-M4
Nested-Vectored Interrupt Controller
SYSCFG external interrupt configuration register (SYSCFG_EXTICR)
PG.x
PH.x
source selection
000
001
010
011
100
101
110
111
x = 0, 1, 2, …, 15
One mux for each of EXTI0, EXTI1, ..., EXTI15
Notes: {{Pause=2}} In summary, the controller has one multiplexer for each of these 16 external interrupts. The microcontroller has a total of 16 multiplexers. As shown here, x is from 0 to 15. A multiplexer, also called MUX, is a simple circuit. It selects one of its inputs, and forwards the selected input to the output.

## Slide 9: Interrupt Vector Table
PA.3
EXTI3
NVIC
Cortex-M4
Nested-Vectored Interrupt Controller (NVIC)
Interrupt Vector Table
Interrupt Number (8 bits) | Memory Address of ISR (32 bits)
... | ...
EXTI0_IRQn = 6 | EXTI0_IRQHandler
EXTI1_IRQn = 7 | EXTI1_IRQHandler
EXTI2_IRQn = 8 | EXTI2_IRQHandler
EXTI3_IRQn = 9 | EXTI3_IRQHandler
EXTI4_IRQn = 10 | EXTI4_IRQHandler
... | ...
EXTI9_5_IRQn = 23 | EXTI9_5_IRQHandler
... | ...
EXTI15_10_IRQn = 40 | EXTI15_10_IRQHandler
... | ...
EXTI3_IRQHandler
Interrupt Vector Table
Notes: {{Pause=2}} The concept of interrupt vector table, has been presented, in the previous lecture. There are five dedicated interrupt handlers, for the first five external interrupts, including external interrupt 0, external interrupt 1, external interrupt 2, external interrupt 3, and, external interrupt 4. {{Pause=1}} For example, pin PA 3 can be mapped to external interrupt 3, and its corresponding interrupt handler is E X T I 3 IRQ Handler. {{Pause=0.5}} External interrupts from number 5 to 9, share the same interrupt handler, E X T I, 9, 5, IRQ Handler. {{Pause=0.5}} External interrupts from number 10 to 15, share the same interrupt handler, E X T I 15, 10, IRQ Handler.

## Slide 10: External Interrupt (EXTI) Controller
IMR
RTSR
FTSR
EMR
0: disabled
1: enabled
SWIER
OR
AND
AND
AND
AND
AND
OR
PR
Configurable External
Interrupts
Direct External Interrupts
GPIO, RTC, COMP, PVD,
PVM
USART/I2C/OTG/LPTIM/LCD wakeup
Notes: {{Pause=2}} This is the basic diagram of the external interrupt controller. {{Pause=1}} The controller supports two types of external interrupts: configurable, external interrupts, and direct external interrupts.
{{Pause=1}} Configurable, external interrupts, include those associated with, G P I O, RTC, comparators, power voltage detector (PVD), and peripheral voltage monitoring (PVM). For these interrupts, the controller has a programmable edge detector, and software can select which active edge generate an interrupt request. An interrupt can be triggered on rising, falling, or both edges. In addition, software can generate an interrupt request by writing 1 to the software interrupt event register (S W I E R).
{{Pause=1}} For direct external interrupts, only rising edge can generate an interrupt request. Direct external interrupts are mostly used for communication peripherals, low-power timer, and LCD.
{{Pause=1}} An interrupt can only be generated, if the corresponding bit, in the interrupt mask register, is 1. The interrupt signal can pass, this ænd gate, if and only if the bit from the IMR register is 1.

## Slide 11: STM32L4 Discovery Kit
Software goal: If the up button is pressed, turn on LED.
EXTI3
Note: PA3 is neither pulled up nor pulled down externally.
+3V
Internal diagram of joystick
PA3
Notes: {{Pause=2}} Now, let’s work on the software part. If we press the up button of the joystick, software turns on the LED. The up button is connected to G P I O pin PA 3, which can generate the external interrupt request 3.

## Slide 12
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
AHB2 peripheral clock enable register (AHB2ENR)
1
GPIOAEN
Clock for Port A
SYSCLK
1
AND
Gate
//stm32l476xx.h
#define RCC_AHB2ENR_GPIOAEN ((uint32_t)0x00000001U)
Notes: {{Pause=2}} Here is the main function. First of all, software must enable the clock of G P I O port A. {{Pause=1}} The constant G P I O A E N is defined in the device header file. {{Pause=1}} This bitwise OR operation, sets the least significant bit to 1, in the A H B 2 E N R register. As result, the clock signal, can pass through, this logic ænd gate, and drive the circuit of port A.

## Slide 13
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11, default)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
Digital Input
Digital Output
Alternative Function
Analog
GPIO Pin
Mode bits = 00
01
10
11
Notes: {{Pause=2}} Then, software configures, the mode of pin PA 3, as digital input. This is achieved by clearing, two bits in the mode register, corresponding to pin 3. Specifically, we clear bit 6, and bit 7, in the mode register of G P I O Port A.

## Slide 14
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
Notes: {{Pause=2}} As discussed previously, pin PA 3 is neither pulled up nor pulled down externally. It was connected to the ground via a capacitor. {{Pause=1}} If the processor does not pulled it down internally, the voltage on pin PA 3 is floating. Its voltage can be high or low, if the up button is not pressed down. Therefore, the processor has to pull the pin down internally. This is to ensure that, the voltage on pin PA 3, is low, under the normal state. Here are two lines of C code, which sets PA 3 as pull down.

## Slide 15
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
15
PA.3
EXTI3
NVIC
Cortex-M4
Nested-Vectored Interrupt Controller (NVIC)
EXTI3_IRQHandler
Interrupt Vector Table
Notes: {{Pause=2}} Next, we enable external interrupt 3, by calling the function, N V I C Enable IRQ.

## Slide 16
PA.3
PB.3
PC.3
PD.3
PE.3
PF.3
EXTI.3
SYSCFG external interrupt configuration register (SYSCFG_EXTICR)
PG.3
PH.3
source selection
000
001
010
011
100
101
110
111
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
Notes: {{Pause=2}} Pin 3 in all ports, can generate, external interrupt 3. {{Pause=1}} These three lines of C code, select PA 3 as the source of external interrupt 3. {{Pause=1}} When PA 3 is selected, the other pins, such as PB 3, PC 3, PD 3, etc., can not be used to generate external interrupts.

## Slide 17
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
while(1);
}
Rising edge triggers EXTI interrupt.
Notes: {{Pause=2}} Under normal state, the voltage on pin PA 3 is low. {{Pause=1}} When the, up button is pressed down, {{Pause=1}} the voltage on PA 3 is raised to high. {{Pause=1}} When the, up button is released, the voltage on pin PA 3 becomes low. {{Pause=1}} This waveform makes two transitions, and has a rising edge, and a falling edge. In this example, we select the rising edge as the active edge, to trigger external interrupts.

## Slide 18
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
while(1);
}
AND
IMR
Notes: {{Pause=2}} Then, software sets the corresponding bit to 1, in the interrupt mask register, in order to enable the interrupt request.

## Slide 19
// Pull PA.3 down internally; Trigger on rising edge
int main(void) {
// Enable GPIO Clock
RCC->AHB2ENR |= RCC_AHB2ENR_GPIOAEN;
// GPIO Mode: Input(00), Output (01),
// AF(10), Analog (11)
GPIOA->MODER &= ~3U << 6;
// GPIO Push-Pull: No pull-up, pull-down (00),
// Pull-up (01), Pull-down (10), Reserved (11)
GPIOA->PUPDR &= ~3U << 6;
GPIOA->PUPDR |= 2U << 6; // Pull down
NVIC_EnableIRQ(EXTI3_IRQn); // Enable Interrupt
// Connect External Line to the GPI
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN;
SYSCFG->EXTICR[0] &= ~SYSCFG_EXTICR1_EXTI3;
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI3_PA;
// Interrupt Mask Register
// 0 = marked, 1 = not masked (enabled)
EXTI->IMR1 |= EXTI_IMR1_IM3;
// Rising trigger selection
// 0 = trigger disabled, 1 = trigger enabled
EXTI->RTSR1 |= EXTI_RTSR1_RT3;
while(1);
}
Processor runs a dead loop forever!
Notes: {{Pause=2}} At the end of the main function, we put a dead loop. After the program perform the initialization of G P I O, and external interrupt, the processor will execute this dead loop forever.

## Slide 20: Interrupt Service Routine (ISR)
void EXTI3_IRQHandler(void) {
if ((EXTI->PR1 & EXTI_PR1_PIF3) != 0) {
// Toggle LED
...
// Cleared flag by writing 1
EXTI->PR1 |= EXTI_PR1_PIF3;
}
}
while(1);
EXTI3_IRQHandler
while(1);
time
Push the up button
stacking
unstacking
Notes: {{Pause=2}} The next important code is the interrupt handler for external interrupt 3. When the up button is pressed down, the rising edge of the voltage, on pin PA 3, triggers, external interrupt 3. After receiving the interrupt request, the N V I C controller, forces the processor, to execute the interrupt handler E X T I 3 IRQ Handler.
{{Pause=1}} One of the most common mistakes many people make, is that, the interrupt handler, does not clear, the interrupt status or pending flag, before it exits. If the interrupt handler does not clear the interrupt pending flag, the interrupt handler will be executed repeatedly by mistake.