## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Spring 2020
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 19
Direct Memory Access (DMA)

## Slide 2: Why need DMA?
Communication Rate
CPU Utilization
Without DMA
With DMA

## Slide 3: Moving Data between Peripheral and Memory
Copy data from peripheral to buffer
Register
Buffer
Data Register
Memory
Peripheral
Processor Core
load
store
Load/store instructions are needed to move data.

## Slide 4: Moving Data between Peripheral and Memory
Copy data from buffer to peripheral
Register
Buffer
Data Register
Memory
Peripheral
Processor Core
store
load
Load/store instructions are needed to move data.

## Slide 5: DMA
Copy data from peripheral to buffer
Register
Buffer
Data Register
Memory
Peripheral
Processor Core
Transferring data without CPU intervention!

## Slide 6: DMA
Copy data from buffer to peripheral
Register
Buffer
Data Register
Memory
Peripheral
Processor Core
Transferring data without CPU intervention!

## Slide 7: DMA: Flow-though vs Fly-by

## Slide 8: DMA Channels
DMA releases CPU from moving data
  between peripherals and memory, or
  between one peripheral and another peripheral.
DMA uses bus matrix to allow concurrent transfers
Peripherals | Channel 1 | Channel 2 | Channel 3 | Channel 4 | Channel 5 | Channel 6 | Channel 7
ADC1 | ADC1 |  |  |  |  |  | 
SPI |  | SPI1_RX | SPI1_TX | SPI2_RX | SPI2_TX |  | 
USART |  | USART3_TX | USART3_RX | USART1_TX | USART1_RX | USART2_RX | USART2_TX
I2C |  |  |  | I2C2_TX | I2C2_RX | I2C1_TX | I2C1_RX
TIM2 | TIM2_CH3 | TIM2_UP |  |  | TIM2_CH1 |  | TIM2_CH2 TIM2_CH4
TIM3 |  | TIM3_CH3 | TIM3_CH4 TIM3_UP |  |  | TIM3_CH1 TIM3_TRIG | 
TIM4 | TIM4_CH1 |  |  | TIM4_CH2 | TIM4_CH3 |  | TIM4_UP
TIM6 DAC_Ch1 |  | TIM6_UP DAC_Ch1 |  |  |  |  | 
TIM7 DAC_CH2 |  |  | TIM7_UP DAC_CH2 |  |  |  | 

## Slide 9: Programmed I/Os
Receiving data from USART serial port without using DMA
Processor executes a lot Loads/Stores to move data
High overhead and slow

## Slide 10: DMA Sets Core Free
Receiving data from USART serial port using DMA
CPU delegates reads/writes to DMA controller
Low overhead and fast

## Slide 11: DMA Controller
Basic Procedures
  DMA device requests bus
  CPU grants bus request
  CPU takes its signals to HiZ
Key DMA Controller Registers
  DMA memory address register (CMAR)
  DMA peripheral address register (CPAR)
  DMA number of data register (CNDTR)
  DMA configuration register (CCR)
DMA are often used together with interrupts

## Slide 12: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 2
incremental mode
memory
DATA
DMA Bus Matrix

## Slide 13: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
DATA
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 1
incremental mode
memory
DATA
1st DMA Transfer
DMA Bus Matrix

## Slide 14: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
DATA
DATA
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 0
incremental mode
memory
DATA
2nd DMA Transfer
DMA Bus Matrix
DMA stops since CNDTR is zero now.

## Slide 15: DMA Mode: Circular Mode
Circular Mode
  handle circular buffers and continuous data flows
  The number of data to be transferred (CNDTR) is automatically reloaded and DMA requests continue to be served
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
memory
DATA
DMA Bus Matrix
incremental mode

## Slide 16: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 2
CIR = 1
incremental mode
memory
DATA
DMA Bus Matrix

## Slide 17: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
DATA
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 1
CIR = 1
incremental mode
memory
DATA
1st DMA Transfer
DMA Bus Matrix

## Slide 18: DMA Mode: Incremental Mode
Peripheral registers/memory
DMA memory address register
DMA peripheral address register
DATA
DATA
non-incremental mode
DIR: Data transfer direction: 0 = Read from peripheral; 1 = Read from memory
DIR = 0
CNDTR = 0
CIR = 1
incremental mode
memory
DATA
2nd DMA Transfer
DMA Bus Matrix
DMA resets and continues to run!

## Slide 19: DMA Request
When does the next DMA transfer start?
  When the peripheral is ready to send or receive data, the peripheral will generate a DMA request signal to the DMA controller to request a data transfer.
Memory
Peripheral
Processor Core
Request
Acknowledge
DMA Controller

## Slide 20: DMA Interrupts
Programmable and Independent source and destination transfer data size:
  Byte, Halfword or Word
Three event flags:
  DMA Half Transfer
  DMA Transfer complete
  DMA Transfer Error
Software programmable priorities:
  Very high, High, Medium, Low

## Slide 21: DMA Request Mapping
DMA
SW TRIGGER
DMA REQUEST
OR
ADC1
TIM2_CC3
TIM4_CC1
SW TRIGGER
OR
USART3_TX
SW TRIGGER
OR
SW TRIGGER
OR
SW TRIGGER
OR
SW TRIGGER
OR
SW TRIGGER
OR
High Priority Request
Low Priority Request
Channel1
Channel2
Channel3
Channel4
Channel5
Channel6
Channel7
TIM1_CC1
TIM2_UP
TIM3_CC3
SPI1_RX
USART3_RX
TIM1_CC2
SPI1_TX
TIM3_CC4
TIM3_UP
SPI2_RX
I2C2_TX
TIM1_CC4
USART1_TX
TIM1_CCU
TIM1_TRIG
TIM4_CC2
USART1_RX
TIM1_UP
SPI2_TX
I2C2_RX
TIM2_CC1
TIM4_CC3
USART2_RX
TIM1_CC3
TIM3_CC1
I2C1_TX
TIM3_TRIG
USART2_TX
TIM2_CC2
TIM2_CC4
TIM4_UP
I2C1_RX
From stm

## Slide 22: DMA Summary
Without DMA, CPU has to execute many load and store instructions, leading to slower performance.
DMA, which makes an automatic data transfer when received a DMA request without involving CPU, accelerates the overall performance.